## Slide 1: CS155 – Z Sweedyk
Digital Images

## Slide 2: Objectives
Color models
Digital images

## Slide 3: Light

## Slide 4: Reflection

## Slide 5: Perception

## Slide 6: Sensation
cones
rods
You’re a real trichromat!

## Slide 7: Light, Reflection, Sensation
Color is in the eye of the beholder

## Slide 8: Human vision
Tristimulus color space
3-paramater, additive color models

## Slide 9: RGB

## Slide 10: RGB Displays (LCD, CRT)
LCD technology
LCD Display

## Slide 11: RGB Gamut

## Slide 12: HSV
Henry Albert Munsell 1898
Gamut same as RGB

## Slide 13: Models
RGB
HSV
HSB/HLS
CIE
CIEXYZ
CIELUB
CIELAB
We’ll use RGB

## Slide 14: Objectives
Color models
Digital images


## Slide 15: Digital image
A digital image is a rectilinear array of sample values. Each sample is a pixel; i.e. a location and a color value

## Slide 16: Digital image fidelity
spatial sampling
color quantization

## Slide 17: Spatial sampling
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
How closely do our samples have to be to spaced in order to realistically represent a continuous image?

## Slide 18: Nyquist criteria
Sample at more than twice the highest frequency to avoid aliasing

## Slide 19: Jaggies

## Slide 20: Digital image fidelity
spatial sampling
color quantization


## Slide 21: Color quantization
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
bits per pixels

## Slide 22: Bits per pixel
1 bit per pixel, grayscale
21 = 2 colors
8 bits per pixel, grayscale
28 = 256 colors
24 bits per pixel, RGB
(8 bits per pixel per channel)
224 colors

## Slide 23: cs155 conventions
IMAGE CLASS
IMAGE FILES
DISPLAY DEVICES

## Slide 24: cs155 conventions
IMAGE CLASS
IMAGE FILES
DISPLAY DEVICES
24 bit bmp/no compression

## Slide 25: bmp files
file header
info header
optional palette
image data

## Slide 26: harry24.bmp
file header
info header
optional palette
image data
bfType: 4d42 Magic number
bfSize: 51130 File size
bfReserved1:0
bfReserved2:0
bfOffBits: 54 Offset to image data

## Slide 27: harry24.bmp
file header
info header
optional palette
image data
Size: 40 Size of header (always 40 bytes)
Width: 150 Image width in pixels
Height: 113 Image height in pixels
Planes: 1
BitCount: 24 Bits per pixel
Compression: 0 0= no compression
SizeImage: 16950 Size of image in pixels
etc.

## Slide 28: harry24.bmp
file header
info header
optional palette
image data
None
24bit RGB

## Slide 29: harry24.bmp image data
Ri,0 | Gi,0 | Bi,0 | ... | Ri,width-1 | Gi,width-1 | Bi,width-1 | padding
Ri+1,0 | Gi+1,0 | Bi+1,0 | ... | Ri+1,width-1 | Gi+1,width-1 | Bi+1,width-1 | padding
row i
row i+1

## Slide 30: cs155 conventions
IMAGE CLASS
IMAGE FILES
DISPLAY DEVICES
Support RGB, 8 bits per channel

## Slide 31: Color values: 8 bit
Option 0: 0, 1, 2, ..., 254,255
Option 1: 0, 1/255, 2/255, ... , 254/255, 1
we use this convention

## Slide 32: Objectives
Color models: RGB, HSV
Digital images: bmp file format, cs155 image class conventions



## Slide 33: Next
Project 1