## Slide 1
CS Today
Minterm Expansion Principle
A circuit for any binary function can be built from three components:
x
x
"not x"
x
y
wxyz
"w and x and y and z"
AND
NOT
w
z
That's minterm, NOT midterm
OR
using the singularity as a problem-solving strategy!
"w or x or y or z"
w+x+y+z
OR
x
y
w
z
hw#5: Circuit design in Logisim

## Slide 2
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto Corner
am guess
bagel: 2
first: 0
hound: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: ?
pm guess
alien: 0
slope: 2
truck: 2
my guess
diner: 2
sassy: 0
thumb: 1
cruel: ?
Madi M.
Lani C.
booed?
sigma?

## Slide 3
Creativity of a sort…

## Slide 4
Cookies!
K. Kohl

## Slide 5
def decipher( S ):
""" TESIJHYDW - je tusyfxuh
jxyi tesijhydw, zkij hkd
tusyfxuh ed yj. """
… code here …
Creativity with Caesar...

## Slide 6
def decipher( S ):
""" DOCSTRING - to decipher
this docstring, just run
decipher on it. """
… code here …
Creativity with Caesar...

## Slide 7
def decipher( S ):
""" This works sometimes """
Creativity with Caesar...

## Slide 8
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
What's in that green box?
read output voltages
set input voltages
perform computation

## Slide 9
Part 1: Represent your f'n as bits…
Truth table for the "odd-parity" function
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
This is odd, but it's also f'n!

## Slide 10
Part 2: Use building blocks ~ logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT

## Slide 11
Physical Logic Gates...
Hex NOT gate
Notes: these quotes are important to yahoo… !

## Slide 12
Better-than-physical Logic Gates...
Notes: these quotes are important to yahoo… !

## Slide 13
Outrageous Claim!
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input

## Slide 14
A circuit with four minterms
A minterm is an AND gate connected to all input bits - directly or through a NOT gate

## Slide 15
A circuit with four minterms
What 3-bit input makes this AND gate output a 1?
A minterm is an input selector!

## Slide 16
Outrageous Claim!
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using what's called the minterm expansion principle.

## Slide 17
Specify a truth table defining any function you want
A constructive proof… !
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
Hey! This is a 3-i'ed proof!

## Slide 18
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
TWO rows ALREADY work – with NO connections at all !
x
y
x
y
We ensure this outputs zero by default.

## Slide 19
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
Does this wire turn on for the red input row?
Does this wire turn on for any other input rows?

## Slide 20
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?

## Slide 21
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!

## Slide 22
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!
But... ALL functions are just functions of bits! (via binary)

## Slide 23
Specify a truth table defining any function you want
Another example
x
y
0
0
0
1
1
0
1
1
fn(x,y)
1
0
0
1
1
2
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together
2 ANDs
1 OR
input
output
x
y
x
y

## Slide 24
"Rails"
What are the differences between these two circuits?
Any advantages of the "rails" approach?
using rails for Not X and Not Y

## Slide 25
Odd parity
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
1, exactly when the number of input bits is odd
Truth table for the "odd-parity" f'n
This is odd, but it's also f'n!

## Slide 26
Odd parity vs. odd parody
Truth table for the "odd-parity" function
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
with Python ties!
1, if the number of input bits is odd

## Slide 27
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 27

## Slide 28
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 28

## Slide 29
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 29

## Slide 30
A full adder sums three input bits to create a 2-bit binary output
3 individual bits of input
2 bits of output: a binary #
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
x
y
0 1
1 0
1 0
1 1
(A 3-bit adder is a full adder)
A full adder
(A 2-bit adder is a half adder)
these columns look familiar!
You'll build this in Lab 5…

## Slide 31
Building a Full Adder
Create a separate circuit for each output bit !
input
output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
0 1
1 0
1 0
1 1
x
y
"Carry-out" Circuit
You'll build this in Lab!
x
y
cin
Full Adder
3 input bits
sum output bit
cout output bit
Remember: this is addition in silicon !
2 output bits
"Rails" of each bit and its inverse

## Slide 32
Your "canvas"

## Slide 33
Two Adders…
It does look fairly wiry to me!
Zombie ripple-carry adder
an actual adder…

## Slide 34
Adders!

## Slide 35
relative scale…

## Slide 36
"Rails" ?
chugging right along…

## Slide 37
What to do with all that extra silicon?

## Slide 38
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 39
Homestate pride…

## Slide 40
Marriage proposals?

## Slide 41
and "secret" messages…

## Slide 42
0 1 1 1
1 1 0 1
Composing circuits
+
Could we use pieces we already have?
FA
x
y
cin
sum
cout
4-bit Ripple-carry Adder
8 input bits
5 output bits

## Slide 43
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-carry Adder

## Slide 44: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield those four "partial products" ??
0

## Slide 45
Division? hw5pr3
Ideas?

## Slide 46
See you in Lab!

## Slide 47
0 1 1 1
1 1 0 1
Composing circuits
+
two 4-bit inputs
How many output bits?
Could we use pieces we already have?
FA
x
y
cin
sum
cout
4-bit Ripple-carry Adder

## Slide 48
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:

## Slide 49
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
input (0 or 1)
+5 v power
Ground
SIGNAL
POWER
Transistors are current switches:
output
input
NOT

## Slide 50
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 51
Here's the truth table defining a function
Quiz
y
c
0
0
0
1
1
0
1
1
odd(x,y,c)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with an OR.
Create NOT "rails" ... if you want to...
x
y
Name(s):
3
Using multiplication for AND and addition for OR, what formula represents this circuit?
0
0
0
1
1
0
1
1
0
1
1
0
x
0
0
0
0
1
1
1
1
c
ExCr
Can you get rid of the ANDs by using only NOTs and ORs?
Notes: 51

## Slide 52
Getting rid of ANDs ?
Can you get rid of the ANDs by using only NOTs and ORs?
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
xy
Notes: 52

## Slide 53
Jotto !
morning class's
our guesses
938 words remaining
630 words remaining
2749 words remaining
2047 words remaining
tower 1
trump 1
462 words remaining
285 words remaining
afternoon class's
our guesses
784 words remaining
303 words remaining
1361 words remaining
1844 words remaining
339 words remaining
206 words remaining
smile 2
bacon 1
happy 1
shyly 2
hairy 2
wasps 2
plane 1
credo 2
gumbo 1
thumb 0
front 1
154 words remaining
deify 1
bunch 1

## Slide 54
The LogiSketch circuit simulator
http://www.cs.hmc.edu/~alvarado/research/sketch/release/LogiSketchFun2011.m4v

## Slide 55
CS labs: safe from zombies!

## Slide 56
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
R
input
NOR's Truth Table

## Slide 57
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
feedback loop

## Slide 58
NOR
S
Q
input
output
feedback loop
Take a look at this circuit.
If S is 1, what will Q be?
NOR's Truth Table
What happens if S becomes 0?
Reminders
NOR outputs 1 only if both inputs are 0
NOR outputs 0 if either inputs is 1

## Slide 59
Is it currently stable or oscillating?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
Follow how the signals will change…
Which signals will change?
How could we change this circuit so that it takes 1 bit of DATA as input?
What will happen if input R is then set to 1?
how do R and S affect Q in general?
The SR latch
NOR
NOR
S
R
0
1
0
input
input
1
0
0
Q
output
NOR's Truth Table
SET
RESET

## Slide 60
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
only one of S or R is high
How could we change this circuit so that it takes 1 bit of DATA as input?
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 61
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
tells when to remember the data!
mutually exclusive ANDs
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 62
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
S sets Q to 1.
R resets Q to 0.
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
The data can be ready any time (or NOT!) But nothing will happen until the strobe says so!
"flip-flop"

## Slide 63
NOR
NOR
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the circuit element
The SR latch

## Slide 64
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 65
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 66
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 67
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 68
See you in Lab…

## Slide 69
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 70
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
Central Processing Unit
Memorable media…
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
"640K ought to be enough for anybody"
- not Bill Gates!
~ 1 billion bits +
< 10,000 bits
~1 trillion bits (or more)
120 gigabyte drive

## Slide 71
Memorable media…
Not Bill Gates, Logic Gates!
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
~1 trillion bits (or more)
120 gigabyte drive
Central Processing Unit
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 1 billion bits +
< 10,000 bits
"Leaky Bucket" capacitors
remagnetizing surfaces
strategies for storage

## Slide 72
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
Price
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 73
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 74
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
If “cycle”
were 1 min
1 min
1.5 hours
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
?
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 75
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1.5 hours
19 YEARS
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
If “cycle”
were 1 min
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 76
See you in Lab!

## Slide 77
Optimization hinders Evolution
- A Perlis

## Slide 78
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm
Integrated Circuits

## Slide 79
The enemy ...
Keeping particles out of the fabrication process is paramount!
Nature still impresses...
Pollen on a memory chip
A ruthless invader...
Ouch!

## Slide 80
It’s totally FAB
How are all of these gates actually realized?
Layering
silicon wafer
silicon dioxide
photoresist
mask w/ circuit (or sailboat)
conductor
Lithography
Etching
Cleaning
x 200 or so
http://www.techfak.uni-kiel.de/matwis/amat/elmat_en/makeindex.html

## Slide 81
CS 101 Today
Minterm Expansion Principle
Hw #5:
Any circuit for any binary function can be built from three components:
x
x
"not x"
x
"w or x or y or z"
w+x+y+z
y
wxyz
"w and x and y and z"
AND
OR
NOT
due 10/11 @ 11:59 pm
Circuit design in Logisim
Extra credit: memory design
to all Grace Hopper-ers
Welcome Back!
Too many inputs !?
start it in lab (perhaps finish!)
w
z
x
y
w
z
Gallery

## Slide 82
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
AND
OR
NOT

## Slide 83
Universal set
output
input
Any function of bits can be built from these three gates:
“Hex NOT gate"
AND
OR
NOT
Notes: these quotes are important to yahoo… !

## Slide 84
Minterm Expansion
… is a proof that AND, OR, and NOT suffice to construct any function!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Build circuits of NOTs and AND that computes each "1" row.
OR them together.
Process
Notes: 84

## Slide 85
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row!
Notes: 85

## Slide 86
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
AND
These are not bubbles, they’re NOT bubbles
KEY
This circuit always outputs 0 - except for the third row!
Notes: 86

## Slide 87
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
Notes: 87

## Slide 88
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
Or you can start here…
3
"the formula"
xy + xy
Notes: 88

## Slide 89
Specify the Truth Table defining the function
"Rails"
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
AND
AND
OR
x
x
y
y
This wire ("rail") carries x's value.
This wire ("rail") carries y's value.
Notes: 89

## Slide 90
The XOR circuit in Logisim
The Logisim circuit simulator
It's no coincidence that the "high-power" lines are lime green!
http://ozark.hendrix.edu/~burch/logisim/
Rails for circuit cleanliness!

## Slide 91
Specify the Truth Table defining the function
x
y
0
0
0
1
1
1
1
<=(x,y)
1
0
1
1
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
How many ANDs will there be?
The "less than or equal to" function…
3
What is the "formula" for this boolean function?
Use these "rails" to help draw your circuit
x
x
y
y
0
Notes: 91

## Slide 92
I'm chomping at the bit to find out…
4
Minterm expansion proves that you need only AND, OR, and NOT gates in order to construct any boolean function.
Can we do without some of the 3? Which?
5
How could we create functions with two bits, or N bits, of output?

## Slide 93
or maybe not so safe…