## Slide 1
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
Jotto ~ no letter left behind!
Hw#5: Circuit design in Logisim
Recursion ~ OK?
OKer than before?
A circuit for any binary function can be built from
only these three logic gates!
Not enough Sakai? Recurse!
am guesses
alien: 2
chord: 2
bumps: 1
my guesses
diner: 0
ghost: 2
plumb: 1
161 words left…
213 words left…
Thanks, Julio!
Notes: jazzy!

## Slide 2
Enjoy GHC!
… as these folks (and 40 other HMCers) did!
Needed: pictures from the 2014 GHC bus!

## Slide 3
def decipher( S ):
Creativity with Caesar...

## Slide 4
def decipher( S ):
""" TESIJHYDW - je tusyfxuh
jxyi tesijhydw, zkij hkd
tusyfxuh ed yj. """
… code here …
Creativity with Caesar...

## Slide 5
def decipher( S ):
""" DOCSTRING - to decipher
this docstring, just run
decipher on it. """
… code here …
Creativity with Caesar...
my favorite not-fully-working decipher…

## Slide 6
def decipher( S ):
""" This works sometimes """
return encipher( S, 3 )
Creativity with Caesar...
and this docstring is 100% correct!

## Slide 7
def decipher( S ):
""" This works sometimes """
return encipher( S, 3 )
Circuits!
Designing physical devices that work all the time!
This week

## Slide 8
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
What's in that green box?
(3) read output voltages
(1) set input voltages
(2) perform computation
Richard Feynman: "Computation is just a physics experiment that always works!"

## Slide 9
Part 1: Represent your f'n as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1

## Slide 10
All computations…
…are simply f'ns of bits
00
00
00
01
00
10
00
11
01
00
01
01
01
10
01
11
10
00
10
01
10
10
10
11
11
00
11
01
11
10
11
11
000
001
010
011
001
010
011
100
010
011
101
100
100
011
101
110
A
B
binary inputs A and B
output, A+B
bitwise
addition function
You'll build this f'n in Logisim this week… !
You already built it in Python last week…
sum

## Slide 11
Part 2: Arrange logic gates to match…
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
not just theoretical models!

## Slide 12
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
How many different input combinations yield an output of 0 here?

## Slide 13
AND
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
fifteen 0s
one 1
AND's truth table:

## Slide 14
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
How many different input combinations yield an output of 1 here?
OR

## Slide 15
OR
inputs
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
0
1
1
1
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
1
fifteen 1s
one 0
OR's truth table:

## Slide 16
NOT
inputs
output
NOT
"NOT bubble" (optional)
x
x
0
1
NOT(x)
1
0
input
output
one 1
one 0
NOT's function:

## Slide 17
Real logic gates
1:31
:41
"It's not real unless it can be done in Minecraft."
- perhaps not a real quote
https://www.youtube.com/watch?v=P7E4K5D834g "Minecraft Logi Gates"
https://www.youtube.com/watch?v=r7N3K8ulEEM "Minecraft Logic Gates Water"
Notes: these quotes are important to yahoo… !

## Slide 18
Real! logic gates...
Hex NOT gate
Notes: these quotes are important to yahoo… !

## Slide 19
Our building blocks: logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT

## Slide 20
The claim!
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input

## Slide 21
The claim!
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using the minterm expansion principle.

## Slide 22
Designing circuits
What inputs make this circuit output 1?
Logisim
What inputs make this circuit output 0?

## Slide 23
Minterm?
A minterm is an AND gate connected to all input bits - either directly or inverted

## Slide 24
Each minterm selects one input:
What 3-bit input makes this AND gate output a 1?
minterm == AND gate that "selects" a single input

## Slide 25
Rails
What are the differences between these two circuits?
Any advantages of this "rails" approach?
using rails for Not X and Not Y
disadvantages?

## Slide 26
(3) Draw the upstream wires that will implement this function as a circuit.
(2) Which line does each AND gate (each minterm) A, B, C, D - implement?
A
B
C
D
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
Name(s)
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) The second circuit has four ANDs (minterms). Could it use fewer ANDs?
(EC) Do you see how these two circuits can implement all binary additions !?
c

## Slide 27
(3) Draw the upstream wires that will implement this function as a circuit.
(2) Which line does each AND gate (each minterm) A, B, C, D - implement?
A
B
C
D
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
Name(s)
(1) Fill in the function values (the truth table) for this circuit…
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) The second circuit has four ANDs (minterms). Could it use fewer ANDs?
(EC) Do you see how these two circuits can implement all binary additions !?
Let's go over these… in a moment

## Slide 28
Our claim!
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using the minterm expansion principle.

## Slide 29
Specify a truth table defining any function you want
A constructive proof… !
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
Hey! This is a 3-i'ed proof!

## Slide 30
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
The ZERO rows ALREADY work – with no connections at all !
x
y
x
y
We ensure this OR outputs zero by default.
0

## Slide 31
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
Does this wire turn on for the red input row?
Does this wire turn on for any other input rows?

## Slide 32
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?

## Slide 33
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!

## Slide 34
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!
but ALL functions are just functions of bits !

## Slide 35
Specify a truth table defining any function you want
Another example
x
y
0
0
0
1
1
0
1
1
fn(x,y)
1
0
0
1
1
2
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together
2 ANDs
1 OR
input
output
x
y
x
y

## Slide 36
(2) Which truth-table line does each AND gate - i.e., each minterm A, B, C, and D - implement?
(1) Fill in the function values (the truth table) for this circuit…
Quiz
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
1
1
0
1
0
0
1

## Slide 37
Odd parity
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
1, exactly when the number of input bits is odd
Truth table for the "odd-parity" f'n
This is odd, but it's also f'n!

## Slide 38
Odd parity vs. odd parody
Truth table for the "odd-parity" function
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
with Python ties!
1, if the number of input bits is odd

## Slide 39
(3) Draw the upstream wires that will implement this function as a circuit.
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) This second circuit has four ANDs (minterms). Could it use fewer ANDs?
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
(EC) Do you see how these two circuits can implement all binary additions !?

## Slide 40
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 40

## Slide 41
(3) Draw the upstream wires that will implement this function as a circuit.
(2) Which line does each AND gate (each minterm) A, B, C, D - implement?
A
B
C
D
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
Name(s)
(1) Fill in the function values (the truth table) for this circuit…
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) The second circuit has four ANDs (minterms). Could it use fewer ANDs?
(EC) Do you see how these two circuits can implement all binary additions !?
Please hand these in…

## Slide 42
A full adder sums three input bits to create a 2-bit binary output
3 individual bits of input
2 bits of output: a binary #
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
x
y
0 1
1 0
1 0
1 1
(A 3-bit adder is a full adder)
Lab5: full adder
(A 2-bit adder is a half adder)
these columns look familiar!
the full adder
FA
x
y
cin
sum
cout

## Slide 43
Building a Full Adder
A separate circuit for each output bit
input
output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
0 1
1 0
1 0
1 1
x
y
"Carry-out" Circuit
You'll build both of these in Lab!
x
y
cin
Full Adder
3 input bits
sum output bit
cout output bit
2 output bits
"Rails" of each bit and its inverse

## Slide 44
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how to use full adders here?

## Slide 45
0 1 1 1
1 1 0 1
Compose!
+
4-bit Ripple-carry Adder
8 bits in
5 bits out
We've used four full adders here… .
This may be less clear than before!

## Slide 46
The "canvas"
These are circuit-based compositions!

## Slide 47
It looks pretty wiry to me!
A zombie-themed ripple-carry adder
an "official" adder…

## Slide 48
relative scale…

## Slide 49
Many adders!
These aren't Easter Eggs, they're adder eggs!

## Slide 50
Ridin' the Rails !
chugging right along…

## Slide 51
What to do with all that extra silicon?

## Slide 52
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 53
Homestate pride…

## Slide 54
Marriage proposals?

## Slide 55
and secret? messages…

## Slide 56
Composing circuits ~ hw5
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider

## Slide 57
Composing circuits
We reuse pieces we already have… !
FA
x
y
cin
sum
cout
0 1 1 1
1 1 0 1
+
4-bit Ripple-carry Adder
8 bits in
5 bits out
abstract these details away…

## Slide 58
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-carry Adder

## Slide 59: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield the four "partial products" ??
0

## Slide 60
Logisim layout…
6 x 7… what else?
the 4-bit ripple-carry adder
one factor horizontal…
one factor vertical…
use labels!
the output
4-bit multiplier

## Slide 61
Division? hw5pr3
Ideas?

## Slide 62
Division! hw5pr3
Only a human would build a circuit like this!
DIVISOR
Error bit
QUOTIENT
DIVIDEND

## Slide 63
CS labs: safe from zombies
See you in Lab!

## Slide 65
0 1 1 1
1 1 0 1
Composing circuits
+
two 4-bit inputs
How many output bits?
Could we use pieces we already have?
FA
x
y
cin
sum
cout
4-bit Ripple-carry Adder

## Slide 66: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield those four "partial products" ??
0

## Slide 67
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 67

## Slide 68
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 68

## Slide 69
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 69

## Slide 70
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 70

## Slide 71
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 71

## Slide 72
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 72

## Slide 73
"Rails"
What are the differences between these two circuits?
Any advantages of the "rails" approach?
using rails for Not X and Not Y

## Slide 74
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:

## Slide 75
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
input (0 or 1)
+5 v power
Ground
SIGNAL
POWER
Transistors are current switches:
output
input
NOT

## Slide 76
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto: Word == ?????
am guess
bagel: 2
first: 0
hound: 2
bendy: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: 2
pm guess
alien: 0
slope: 2
truck: 2
shock: 1
my guess
diner: 2
sassy: 0
thumb: 1
cruel: 2
Madi M.
Lani C.
booed?
sigma?

## Slide 77
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 78
Here's the truth table defining a function
Quiz
y
c
0
0
0
1
1
0
1
1
odd(x,y,c)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with an OR.
Create NOT "rails" ... if you want to...
x
y
Name(s):
3
Using multiplication for AND and addition for OR, what formula represents this circuit?
0
0
0
1
1
0
1
1
0
1
1
0
x
0
0
0
0
1
1
1
1
c
ExCr
Can you get rid of the ANDs by using only NOTs and ORs?
Notes: 78

## Slide 79
Getting rid of ANDs ?
Can you get rid of the ANDs by using only NOTs and ORs?
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
xy
Notes: 79

## Slide 80
Jotto !
morning class's
our guesses
938 words remaining
630 words remaining
2749 words remaining
2047 words remaining
tower 1
trump 1
462 words remaining
285 words remaining
afternoon class's
our guesses
784 words remaining
303 words remaining
1361 words remaining
1844 words remaining
339 words remaining
206 words remaining
smile 2
bacon 1
happy 1
shyly 2
hairy 2
wasps 2
plane 1
credo 2
gumbo 1
thumb 0
front 1
154 words remaining
deify 1
bunch 1

## Slide 81
The LogiSketch circuit simulator
http://www.cs.hmc.edu/~alvarado/research/sketch/release/LogiSketchFun2011.m4v

## Slide 82
One sort of creativity…

## Slide 83
Cookies!

## Slide 84
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
using the singularity as a problem-solving strategy
Hw#5: Circuit design in Logisim
on Th.: guest talk by Don Chamberlin HMC '66
Comparing types of programming languages
recursion seems OK?
or more so than before?
A circuit for any binary function can be built from
only these three logic gates
Also:
Sheldon-approved!

## Slide 85
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
R
input
NOR's Truth Table

## Slide 86
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
feedback loop

## Slide 87
NOR
S
Q
input
output
feedback loop
Take a look at this circuit.
If S is 1, what will Q be?
NOR's Truth Table
What happens if S becomes 0?
Reminders
NOR outputs 1 only if both inputs are 0
NOR outputs 0 if either inputs is 1

## Slide 88
Is it currently stable or oscillating?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
Follow how the signals will change…
Which signals will change?
How could we change this circuit so that it takes 1 bit of DATA as input?
What will happen if input R is then set to 1?
how do R and S affect Q in general?
The SR latch
NOR
NOR
S
R
0
1
0
input
input
1
0
0
Q
output
NOR's Truth Table
SET
RESET

## Slide 89
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
only one of S or R is high
How could we change this circuit so that it takes 1 bit of DATA as input?
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 90
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
tells when to remember the data!
mutually exclusive ANDs
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 91
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
S sets Q to 1.
R resets Q to 0.
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
The data can be ready any time (or NOT!) But nothing will happen until the strobe says so!
"flip-flop"

## Slide 92
NOR
NOR
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the circuit element
The SR latch

## Slide 93
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 94
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 95
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 96
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 97
See you in Lab…

## Slide 98
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 99
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
Central Processing Unit
Memorable media…
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
"640K ought to be enough for anybody"
- not Bill Gates!
~ 1 billion bits +
< 10,000 bits
~1 trillion bits (or more)
120 gigabyte drive

## Slide 100
Memorable media…
Not Bill Gates, Logic Gates!
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
~1 trillion bits (or more)
120 gigabyte drive
Central Processing Unit
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 1 billion bits +
< 10,000 bits
"Leaky Bucket" capacitors
remagnetizing surfaces
strategies for storage

## Slide 101
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
Price
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 102
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 103
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
If “cycle”
were 1 min
1 min
1.5 hours
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
?
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 104
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1.5 hours
19 YEARS
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
If “cycle”
were 1 min
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 105
See you in Lab!

## Slide 106
Optimization hinders Evolution
- A Perlis

## Slide 107
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm
Integrated Circuits

## Slide 108
The enemy ...
Keeping particles out of the fabrication process is paramount!
Nature still impresses...
Pollen on a memory chip
A ruthless invader...
Ouch!

## Slide 109
It’s totally FAB
How are all of these gates actually realized?
Layering
silicon wafer
silicon dioxide
photoresist
mask w/ circuit (or sailboat)
conductor
Lithography
Etching
Cleaning
x 200 or so
http://www.techfak.uni-kiel.de/matwis/amat/elmat_en/makeindex.html

## Slide 110
CS 101 Today
Minterm Expansion Principle
Hw #5:
Any circuit for any binary function can be built from three components:
x
x
"not x"
x
"w or x or y or z"
w+x+y+z
y
wxyz
"w and x and y and z"
AND
OR
NOT
due 10/11 @ 11:59 pm
Circuit design in Logisim
Extra credit: memory design
to all Grace Hopper-ers
Welcome Back!
Too many inputs !?
start it in lab (perhaps finish!)
w
z
x
y
w
z
Gallery

## Slide 111
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
AND
OR
NOT

## Slide 112
Universal set
output
input
Any function of bits can be built from these three gates:
“Hex NOT gate"
AND
OR
NOT
Notes: these quotes are important to yahoo… !

## Slide 113
Minterm Expansion
… is a proof that AND, OR, and NOT suffice to construct any function!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Build circuits of NOTs and AND that computes each "1" row.
OR them together.
Process
Notes: 113

## Slide 114
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row!
Notes: 114

## Slide 115
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
AND
These are not bubbles, they’re NOT bubbles
KEY
This circuit always outputs 0 - except for the third row!
Notes: 115

## Slide 116
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
Notes: 116

## Slide 117
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
Or you can start here…
3
"the formula"
xy + xy
Notes: 117

## Slide 118
Specify the Truth Table defining the function
"Rails"
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
AND
AND
OR
x
x
y
y
This wire ("rail") carries x's value.
This wire ("rail") carries y's value.
Notes: 118

## Slide 119
The XOR circuit in Logisim
The Logisim circuit simulator
It's no coincidence that the "high-power" lines are lime green!
http://ozark.hendrix.edu/~burch/logisim/
Rails for circuit cleanliness!

## Slide 120
Specify the Truth Table defining the function
x
y
0
0
0
1
1
1
1
<=(x,y)
1
0
1
1
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
How many ANDs will there be?
The "less than or equal to" function…
3
What is the "formula" for this boolean function?
Use these "rails" to help draw your circuit
x
x
y
y
0
Notes: 120

## Slide 121
I'm chomping at the bit to find out…
4
Minterm expansion proves that you need only AND, OR, and NOT gates in order to construct any boolean function.
Can we do without some of the 3? Which?
5
How could we create functions with two bits, or N bits, of output?

## Slide 122
or maybe not so safe…