## Slide 1
CS 5
logic gates
switches: transistors
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
Hw 5: be fruitful! multiply, divide, and remember
registers
Python
What could be roiling around under here?
A
B
S
T
R
A
C
T
I
O
N
Fri office hours: 2:30-4:30, LAC lab
Jotto Corner
Mo/Kepa
alien: 2
whole: 1
sloth: 1
grump: 0
diner: 1
savvy: 1
flock: 2
thumb: 1
my guess
AM guess
alien: 2
bears: 2
flour: 1
crazy: 2
diner: 0
savvy: 1
flock: 2
thumb: 1
my guess
PM guess
191
149
94
119
words remaining
D. Chamberlain (next week)
Notes: flash – as in I've guessed this word in a flash!

## Slide 2
SQL

## Slide 3
Past zombie run-ins… Not sure about the tie?!

## Slide 4
Things seem to get messy around here…
An example of a happy RCA solution...
taking
Logisim's "canvas" literally
…
Aaron B.
CS 5
logic gates
switches: transistors
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
registers
Python
A
B
S
T
R
A
C
T
I
O
N
Notes: flash – as in I've guessed this word in a flash!

## Slide 5
Composing circuits ~ hw5
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider
12 nGbits of memory (RAM)
extra credit

## Slide 6
Composing circuits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
let's abstract these details away…

## Slide 7
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder

## Slide 8: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could THREE 4-bit ripple-carry adders help here?
(Q2) What bit would be correct for the starred spot ?
(Q3) What circuits could you use to create the four "partial products" ??
0

## Slide 9: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three (3) ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0

## Slide 10
The "canvas"
These are circuit-based compositions!

## Slide 11
Division? hw5pr3
Ideas?

## Slide 12
Division! hw5pr3
Only a human would build a circuit like this!
DIVISOR
Error bit
QUOTIENT
DIVIDEND
"Make-it-up" design

## Slide 13
bit
principled design
Minterm Division
(0) All computation can be expressed as bits...
(1) Any function of bits can be made a truth table
INPUTS
Y2 Y1 Y0 X1 X0
OUTPUT
Z2 Z1 Z0 E
0 0
anything
0 0 0
0 1
0 0 1
0 1
0 1 0
0 1
0 1 1
0 1
1 0 0
0 1
1 0 1
0 1
1 1 0
0 1
1 1 1
0 1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 1
1 1
1 1
1 1
1 1
1 1
1 1
1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 1 0 0
1 0 1 0
1 1 1 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 1 1 0
0 1 0 0
0 1 1 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 0 1 0
0 1 0 0
(2) Consider the output, one bit at a time...
(4) Use an AND gate to select each input for which the output should be 1. (a minterm)
(3) The circuit will output 0 by default!
(5) OR the outputs from step (4) together.
anything
(6) optimize your circuit later -- or never
To implement the red 1, how many inputs will its minterm AND need?
What division is it?
How many negated?
dividend
divisor
quotient
error

## Slide 14
Circuit Optimization?
Perhaps artistically optimized!
Optimization for what?!
16 gates
7 gates
using a genetic algorithm
try E85 !

## Slide 15
Time-optimized circuits: Carry lookahead adders
The following circuit is called a carry lookahead adder.
By adding more hardware, we reduced the number of levels in the circuit and sped things up.
We can "cascade" carry lookahead adders, just like ripple carry adders.
We'd have to do carry lookahead between the adders too.
How much faster is this?
  For a 4-bit adder, not much. There are 4 gates in the longest path of a carry lookahead adder, versus 9 gates for a ripple carry adder.
  But if we do the cascading properly, a 16-bit carry lookahead adder could have only 8 gates in the longest path, as opposed to 33 for a ripple carry adder.
  Newer CPUs these days use 64-bit adders. That's 12 vs. 129 gates or 10x speedup!
The delay of a carry lookahead adder grows logarithmically with the size of the adder, while a ripple carry adder's delay grows linearly.
The thing to remember about this is the trade-off between complexity and performance. Ripple carry adders are simpler, but slower. Carry lookahead adders are faster but more complex.

## Slide 16
“carry-out”, not “c-zero”
A 4-bit carry-lookahead adder circuit
Sum bits
Carry bits
carry-in
xor
xor
xor
xor
xor
xor
xor
xor
Details!

## Slide 17
A 4-bit carry-lookahead adder circuit
A 4-bit ripple-carry adder circuit
speed vs. complexity tradeoffs ~ cs facets of engineering
What information is needed? Where? How?

## Slide 18
What's inside gates?
What's the other half of computation?

## Slide 19
It looks pretty wiry to me!
A zombie-themed ripple-carry adder
an "official" adder…

## Slide 20
relative scale…

## Slide 21
Many adders!
These aren't Easter Eggs, they're adder eggs!

## Slide 22
Ridin' the Rails !
chugging right along…

## Slide 23
What to do with all that extra silicon?

## Slide 24
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 25
Homestate pride…

## Slide 26
Marriage proposals?

## Slide 27
and secret? messages…

## Slide 28
and secret? messages…
VAX…
When you care enough…
…to steal the very best!

## Slide 29
Today's gates?

## Slide 30
Silicon-based switches (transisors)
a single etched transistor labeled with base (b), emitter (e), and collector (c)

## Slide 31
Transistors
SET transistor
single-electron tunneling
30 nm
voltage here
allows current here
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:
otherwise it's blocked
otherwise it's blocked
Radio Shack transistors

## Slide 32
Building a NOT gate
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
Transistors are current switches:
output
input
NOT
otherwise it's blocked
otherwise it's blocked
(0 or 1)
+5 v
Ground
INPUT
POWER
OUTPUT
(1 or 0)
SIGNAL

## Slide 33
+5 v
Ground
(0 or 1)
+5 v
INPUT
POWER
OUTPUT
(1 or 0)
SIGNAL
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:
otherwise it's blocked
otherwise it's blocked
NOT gate

## Slide 34
(2) the above circuit is one of these gates – which one?
each is 0 or 1 independently
Ground, 0 or 0v
Inputs: X, Y
Output: Z
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
Z
(3) Extra! How could you alter the transistor-level design to make an AND?
Power, 1 or +5v
"exclusive or"
Name(s) __________________________________________
Quiz
(1) Find the circuit's truth table
X
Y
Z
0
0
0
1
1
0
1
1

## Slide 35
water!
legos!!
Gates without Si? Sí!

## Slide 36
Reading this week: molec. computing

## Slide 37
Reading this week: H2O computing !

## Slide 38
NOT gate
Signal Input, A
Signal Output
Q
Spring
Electromechanical "gates" (relays)
1940's computers
External Power (6v)
Electro-magnet
metal plate

## Slide 39
Which gate is this?
Input, A
Signal Output
Q
External Power (6v)
AND
NAND
OR
NOR
XOR
Input, B

## Slide 40
The Mark 1
ran at 0.00001 MHz
5 tons
530 miles of wiring
765,299 distinct parts!
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html
Grace Hopper + Howard Aiken, Harvard ~ 1944
an early, relay-based computer

## Slide 41
The Mark 1
ran at 0.00001 MHz
5 tons
530 miles of wiring
765,299 distinct parts!
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html
Grace Hopper + Howard Aiken, Harvard ~ 1944
an early, relay-based computer
a "modern" relay-based computer

## Slide 42
Transistors as disruptive technology
1947: Bell Labs
seeking amplifiers for phone lines
team of physicists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley Semiconductor Co.
1957: Fairchild Semiconductor Co.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 43
Half a computer: the CPU
transistors
6 x 7… !
arithmetic
gates

## Slide 44
Make no mistake… computers process numbers - not symbols.
We can only automate what we can arithmetize.
- Alan Perlis
True! But it misses 99% of what computers do! What?

## Slide 45
What's inside gates?
What's the other half of computation?

## Slide 46
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
X
NOR
inputs
output
Y
NOR's Truth Table
X
Y
Z
Z
0
0
0
1
1
0
1
1
1
0
0
0
Let's engineer this into 1 bit of memory!
- also Alan Perlis

## Slide 47
Is this circuit stable now?
What happens if R is 0 and S is set to 1?
Memory Circuits
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
Q is 1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0
SR latch
Demo!

## Slide 48
Q is then set to 1
Yes.
What happens if R is 0 and S is set back to 0?
What happens if S is 0 and R is set to 1?
Memory!
Take a look at this circuit:
The D (data) line holds a single bit we want to store (either a 0 or a 1).
How does the strobe bit help store the bit D into Q?
Why does "S" stand for "Set" and R for "Reset" ?
Keep this page, in case you'd like to try the extra credit… .
What happens if S is 0 and R is set back to 1?
Hint: What happens when the "strobe" is 1?
NOR
NOR
S
R
1
0
0
"Set"
"Reset"
1
Q
Q is 1 bit of storage
Is this circuit stable now?
What happens if R is 0 and S is set to 1?
with S == 0, R == 0, and the storage bit Q == 0

## Slide 49
NOR
NOR
inputs
The flip-flop
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
the flip-flop's diagram
Demo!
Q
Q is 1 bit of storage

## Slide 50
NOR
NOR
inputs
The flip-flop
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
the flip-flop's diagram
Demo!
Q
Q is 1 bit of storage
But there's a LOT more than 1 bit of memory… !

## Slide 51
Random Access Memory
Extra this week: Design 12nGbits of RAM
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
Demo!

## Slide 52
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
the value 5 into mem. loc. #1
3 data input bits
write enable line
read enable line
0
1
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
3. How do the * AND gates make sure that the value does go into memory location #1?
*
*
Ex Cr
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
Binary Address Decoder
4. How do the * AND gates make sure that the value does NOT go into memory location #0?
0
1
data address, in binary
A0
A1

## Slide 53
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
take data from mem. location #1
3 data input bits
write enable line
read enable line
data address, in binary
0
1
Binary Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates will ensure bits from memory location #1 are read out?
4. Which gates will ensure bits from memory location #0 are not read out?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high
5. Draw where the "Read Enable" wire should go!
0
1
A0
A1

## Slide 54
Happy Wiring!
Animusic's Fiber Bundles
Friday LAC office hours & lots of weekend grutoring hours…

## Slide 56
The above circuit is one of these gates – which one?
each is 0 or 1 independently
Ground, 0 or 0v
INPUTS
OUTPUT
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
Z
Extra! How could you alter this transistor-level design to create an AND?
Power, 1 or +5v
"exclusive or"
Name(s) __________________________________________
Quiz
Truth Table
X
Y
Z
0
0
0
1
1
0
1
1

## Slide 57
Is this circuit stable or oscillating now?
What will happen if input S is set to 1?
Memory Circuits
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0
SR latch

## Slide 58
Is this circuit stable or oscillating now?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
What will happen if input R is then set to 1?
Memory!
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0
Take a look at the diagram at right. The D (data) line holds a single bit we want to store (either a 0 or a 1).
How does the strobe direct storing the data into Q?
Note: "S" stands for "Set" and R for "Reset"
Keep this page, in case you'd like to try the extra credit… .
What will happen if input R is then set back to 0?
Hint: What happens when the "strobe" is 1?

## Slide 59
The above circuit is one of these gates – which one?
each is 0 or 1 independently
Ground, 0v
INPUTS
OUTPUT
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
Z
Extra! How could you alter this transistor-level design to create an AND?
Power, +5v
"exclusive or"
Name(s) __________________________________________
Quiz
Truth Table
X
Y
Z
0
0
0
1
1
0
1
1

## Slide 60
Is this circuit stable or oscillating now?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
What will happen if input R is then set to 1?
Memory!
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0
Take a look at the diagram at right. The D (data) line holds a single bit we want to store (either a 0 or a 1).
How does the strobe direct storing the data into Q?
Why are S for "Set" and R for "Reset" ?
Keep this page, in case you'd like to try the extra credit… .
What will happen if input R is then set back to 0?
Hint: What happens when the "strobe" is 1?

## Slide 61
Odd parity
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
1, exactly when the number of input bits is odd
Truth table for the "odd-parity" f'n
This is odd, but it's also f'n!

## Slide 62
Odd parity vs. odd parody
Truth table for the "odd-parity" function
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
with Python ties!
1, if the number of input bits is odd

## Slide 63
(3) Draw the upstream wires that will implement this function as a circuit.
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) This second circuit has four ANDs (minterms). Could it use fewer ANDs?
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
(EC) Do you see how these two circuits can implement all binary additions !?

## Slide 64
Past zombie run-ins… Not sure about the tie?!

## Slide 65
Registers
Main Memory
(replaceable RAM)
Disk Drive
magnetic storage
on the Central Processing Unit
More Memory!
"640K ought to be enough for anybody"
- maybe Bill Gates!
~ 10 billion bits +
~ 10,000 bits
~10 trillion bits (or more)
1 TB drive
memory from logic gates
"Leaky Bucket" capacitors
remagnetizing surfaces
100 Registers of 8-64 bits each
s
D
Q
8 flip-flops are an 8-bit register
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
1 GB memory

## Slide 66
~$100
~$100
~$100
1.5 hours
Price
Time
If a cycle ==
1 minute
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
Registers
Main Memory
(replaceable RAM)
100 Registers of 8-64 bits each
Disk Drive
magnetic storage
on the Central Processing Unit
More Memory!
s
D
Q
8 flip-flops are an 8-bit register
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 10 billion bits +
~ 10,000 bits
~10 trillion bits (or more)
1 TB drive
1 GB memory

## Slide 67
~$100
~$100
~$100
1.5 hours
Price
Time
If a cycle ==
1 minute
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
Registers
Main Memory
(replaceable RAM)
Disk Drive
magnetic storage
on the Central Processing Unit
More Memory!
~ 10 billion bits +
~10 trillion bits (or more)
1 TB drive
19 YEARS
100 Registers of 8-64 bits each
s
D
Q
8 flip-flops are an 8-bit register
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 10,000 bits
1 GB memory

## Slide 68
tfw you click "submit"
tfw you want somebody to click "submit"

## Slide 69
principled design
Minterm Division
(0) All computation can be expressed as bits...
(1) Any function of bits can be made a truth table
INPUTS
Y2 Y1 Y0 X1 X0
OUTPUT
Z2 Z1 Z0 E
0 0
anything
0 0 0
0 1
0 0 1
0 1
0 1 0
0 1
0 1 1
0 1
1 0 0
0 1
1 0 1
0 1
1 1 0
0 1
1 1 1
0 1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 1
1 1
1 1
1 1
1 1
1 1
1 1
1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 1 0 0
1 0 1 0
1 1 1 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 1 1 0
0 1 0 0
0 1 1 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 0 1 0
0 1 0 0
(2) Consider the output, one bit at a time...
(4) Use an AND gate to select each input for which the output should be 1. (a minterm)
(3) The circuit will output 0 by default!
(5) OR the outputs from step (4) together.
anything
(6) optimize your circuit later -- or never
To implement the red 1, how many inputs will its minterm AND need?
What division is this?
How many negated?

## Slide 70
Design strategies…
No alien would build a circuit like this!
"Make-it-up" design

## Slide 71
CS 5
logic gates
switches (transistors)
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
Hw 5: be fruitful! multiply, divide, and remember
registers
Python!
Is there anything under here?
An example of a happy lab solution...
am guesses
alien: 2
chord: 2
bumps: 1
lunch: 2
my guesses
diner: 0
ghost: 2
plumb: 1
jazzy: 1
only 44 words left…
still 133 words left…
A
B
S
T
R
A
C
T
I
O
N
Notes: flash – as in I've guessed this word in a flash!

## Slide 72
CS 5
logic gates
switches (transistors)
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
registers
Python!
Is there anything under here?
An example of a happy lab solution...
am guesses
alien: 2
chord: 2
bumps: 1
lunch: 2
my guesses
diner: 0
ghost: 2
plumb: 1
jazzy: 1
only 44 words left…
still 133 words left…
A
B
S
T
R
A
C
T
I
O
N
Bailey picture!!
Notes: flash – as in I've guessed this word in a flash!

## Slide 73
The above circuit is one of these gates – which one?
each is 0 or 1 independently
Ground, 0v
INPUTS
OUTPUT
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
Z
Extra! How could you alter this transistor-level design to make this an AND?
Power, +5v
"exclusive or"
Name(s) __________________________________________
Quiz
Transistor-level circuit design

## Slide 74
Take a look at this circuit.
(Question #1) If S is 1, what will Q be?
(Question #2) What happens if S becomes 0?
NOR
S
input
output
feedback cycle
Q
1-bit of storage?

## Slide 75
Is this circuit stable or oscillating now?
What will happen if input S is set to 1?
Memory Circuits
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0

## Slide 76
Is this circuit stable or oscillating now?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
What will happen if input R is then set to 1?
Memory!
NOR
NOR
S
R
0
1
0
"Set"
"Reset"
1
0
0
Q
1 bit of storage
with S == 0, R == 0, and the storage bit Q == 0
Take a look at the diagram at right. The D (data) line holds a single bit we want to store (either a 0 or a 1). How does the strobe help to store the data into Q?
Why is S called "set" and R called "Reset" ?
Name(s): _________________________
What will happen if input R is then set to 1?

## Slide 77
NOR
NOR
Q
0
1
0
inputs
1
0
0
The flip-flop
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the flip-flop diagram
1 bit of storage

## Slide 78
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto: word == ?????
am guess
bagel: 2
first: 0
hound: 2
bendy: 2
lemon: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: 2
beget: 3
pm guess
alien: 0
slope: 2
truck: 2
shock: 1
proud: 3
my guess
diner: 2
sassy: 0
thumb: 1
cruel: 2
toric: 1
Madi M.
Lani C.
ELUDE
ADOZE
HEDGE
SQUEG
GLEYS
BEGET
words remaining: 62
123 words remaining
SPRUG
POUTY
GLIME
OFTER
TORIC
words remaining: 16
132 words remaining

## Slide 79
CS 5
logic gates
switches (transistors)
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
Hw 5: multiply, divide, and memory
registers
Python!
Is there anything under here?
An example of a happy lab solution...

## Slide 80
CS snapshots…
East '13

## Slide 81
CS snapshots…
East '13

## Slide 82
CS 5 Today
logic gates
switches (transistors)
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm
Our path
Hw 5: multiply, divide, and memory
registers
Python!
Is there anything under here?
An example of a happy lab solution...

## Slide 83
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto: Word == ?????
am guess
bagel: 2
first: 0
hound: 2
bendy: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: 2
pm guess
alien: 0
slope: 2
truck: 2
shock: 1
my guess
diner: 2
sassy: 0
thumb: 1
cruel: 2
Madi M.
Lani C.
booed?
sigma?

## Slide 84
CS snapshots…

## Slide 85
Jotto !
words remaining: 340
722 words remaining
2744 words remaining
words remaining: 2285
words remaining: 153
181 words remaining
words remaining: 238
1275 words remaining
3001 words remaining
words remaining: 679
words remaining: 70
670 words remaining
am guess
alien: 2
sleep: 0
bacon: 2
human: 2
crypt: 0
my guess
syrup: 1
swift: 2
bacon: 0
hedge: 2
weird: 3
pm guess
alien: 3
steam: 3
goody: 1
ghoul: 0
danes: 4
my guess
slyly: 1
queue: 1
bacon: 1
prime: 2
meows: 1
Louis
Ana
words remaining: 65
60 words remaining
words remaining: 8
237 words remaining
EXAMS
LOOIE
MEOWS
YEANS
DEANS
MEANY
MAGIC
AURIC
QUOIN
SIGHS
FLESH
WEIRD

## Slide 86
Jotto !
words remaining: 340
722 words remaining
2744 words remaining
words remaining: 2285
words remaining: 153
181 words remaining
words remaining: 238
1275 words remaining
3001 words remaining
words remaining: 679
words remaining: 70
670 words remaining
am guess
alien: 2
sleep: 0
bacon: 2
human: 2
crypt: 0
my guess
syrup: 1
swift: 2
bacon: 0
hedge: 2
weird: 3
pm guess
alien: 3
steam: 3
goody: 1
ghoul: 0
danes: 4
my guess
slyly: 1
queue: 1
bacon: 1
prime: 2
meows: 1
Louis
Ana
words remaining: 65
60 words remaining
words remaining: 8
237 words remaining
words remaining: 20
19 words remaining
words remaining: 4
76 words remaining

## Slide 87
What's inside gates?
What's the other half of computation?

## Slide 88
What's inside gates?

## Slide 89
Transistors
SET transistor
single-electron tunneling
30 nm
voltage here
allows current here
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:
otherwise it's blocked
otherwise it's blocked

## Slide 90
Building a NOT gate
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
Transistors are current switches:
output
input
NOT
otherwise it's blocked
otherwise it's blocked
(0 or 1)
+5 v
Ground
INPUT
POWER
OUTPUT
(1 or 0)
SIGNAL

## Slide 91
+5 v
Ground
(0 or 1)
+5 v
INPUT
POWER
OUTPUT
(1 or 0)
SIGNAL
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:
otherwise it's blocked
otherwise it's blocked
a NOT gate

## Slide 92
Which of these four gates is above?
each is 0 or 1 independently
+5 v
Ground, 0 v
INPUTS
POWER
OUTPUT
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
!=
Z
Extra! How could you change this page's transistor-level design to create an AND circuit?

## Slide 93
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
the value 5 into mem. loc. #1
3 data input bits
write enable line
read enable line
0
1
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
3. How do the * AND gates make sure that the value does go into memory location #1?
*
*
Ex Cr
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
Binary Address Decoder
4. How do the * AND gates make sure that the value does NOT go into memory location #0?
0
1
data address, in binary
A0
A1

## Slide 94
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
takes data from mem. location #1
3 data input bits
write enable line
read enable line
data address, in binary
0
1
Binary Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates will ensure bits from memory location #1 are read out?
4. Which gates will ensure bits from memory location #0 are not read out?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high
5. Draw where the "Read Enable" wire should go!
0
1
A0
A1

## Slide 95
PC
IR
Reg3
1
1
0
1
0
0
1
1
1
0
0
The instruction
00 = LOAD from memory
01 = STORE to memory
10 = add a constant to a reg. (AIM)
11 = ADD a reg. to a reg.
Argument 1
Argument 2
the same Reg3
the register
the constant
1
1
1
0
0
1
1
1
4
old value of Reg3 = 7
new value of Reg3 = 11
clock
0
0
0
0
0
read enable
RAM
IR
8 data bits
8 address bits
strobe for all IR bits
1
0
0
1
1
1
0
0
D in
Q out
strobe
decode instruction
strobe to finish instruction (to all bits)
ripple8
7+4
8 output bits
flip-flop
strobe for next instruction
Instruction Decoding Guide
a Von Neumann machine
1
2
3
4
5
Reg3

## Slide 96
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Binary Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
Ex Cr
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 97
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Binary Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
Ex Cr
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 99
water!
legos!
Gates without Si? Sí!

## Slide 100
Reading this week: molecular computing
with robots...!

## Slide 101
redstone!!
Gates without Si? Sí!
http://www.youtube.com/watch?v=P7E4K5D834g

## Slide 102
electromechanical relays
Signal Input, A
Signal Output
Q
Spring
Power
Power (6v)
Gates without Si? Sí!

## Slide 103
Which gate is this one?
Input, A
Input, B
Signal Output
Q
Power (6v)
AND
NAND
OR
NOR
XOR

## Slide 104
The Mark 1
Grace Hopper, Howard Aiken at Harvard, 1944
ran at 0.00001 MHz
5 tons, 530 miles of wiring
765,299 distinct parts!
relay-based computer
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html

## Slide 105
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 106
Is it currently stable or oscillating?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
Follow how the signals will change…
Which signals will change?
What will happen if input R is then set to 1?
how do R and S affect Q in general?
Quiz
NOR
NOR
S
R
0
1
0
"SET" input
"Reset" input
1
0
0
Q
output
NOR's Truth Table
(Right now, the inputs S and R are both 0 and the output Q is 0).
Draw the wires and gates upstream of this SR latch to create a Flip Flop (one bit of memory)
We'll show how it works in Logisim...
When strobe is 1, D is stored in the circuit.
When strobe is 0, D has no effect on the circuit at all.
Names(s): __________________
Better not as a quiz…

## Slide 107
Von Neumann Architecture
CPU
RAM
central processing unit
random access memory
programs stored here
instructions executed here
Von Neumann bottleneck
Will the real von Neumann please stand up?
A few, fast registers + arithmetic
“Slow” memory no computation

## Slide 108
Von Neumann Architecture
CPU
RAM
central processing unit
random access memory
the program
the processing
0000100111101000
0
1
2
3
4
5
…
6
Programs are stored in memory in machine language
(bits)
Von Neumann bottleneck
1111110100100001
0001011011111001
1010100111000010
0000000000000000

## Slide 109
Von Neumann Architecture
CPU
RAM
central processing unit
random access memory
read r1
0
1
2
3
4
5
…
6
halt
Assembly language is human-readable machine language
mul r2 r1 r1
add r2 r2 r1
write r2
Von Neumann bottleneck
the program
the processing
substituting words for bits

## Slide 110
the fetch - execute cycle
0000000000000000
1111110100100001
0000100111101000
0001011011111001
1010100111000010
central processing unit registers
random access memory locations
0
1
2
3
4
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2
CPU
RAM
Von Neumann bottleneck

## Slide 111
the fetch - execute cycle
halt
mul r2 r1 r1
read r1
add r2 r2 r1
write r2
central processing unit registers
random access memory locations
0
1
2
3
4
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2
CPU
RAM
Von Neumann bottleneck

## Slide 113
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 114
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 115
Hmmm
CPU
RAM
central processing unit
random access memory
Von Neumann bottleneck
read r1
0
1
2
3
4
5
…
6
255
halt
255 memory locations of 16 bits
r0
…
16 registers,
each 16 bits
r15
they can hold values from -32768 upto 32767
r1
r2
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
The Harvey Mudd Miniature Machine
mul r2 r1 r1
add r2 r2 r1
write r2
0

## Slide 116
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
The D latch
D
data
only one of S or R is high
Here, we change this circuit so that it takes only 1 bit of data as input…
S sets Q to 1.
R resets Q to 0.

## Slide 117
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
these ANDs propagate the data D only when the strobe is high (1)
Here, we can deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.
How does this "strobe" work?

## Slide 118
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
but only if the strobe is 1…
tells when to remember the data!
S sets Q to 1.
R resets Q to 0.

## Slide 119
Demo
of friendly assembly-language programming…

## Slide 120
Assembly Language
read r1
div r1 r1 r1
add r2 r2 r2
register-level programming
reg2 = reg2 + reg2
which is why it is written this way in python!
sub r2 r1 r4
reg2 = reg1 - reg4
reg7 = reg6 * reg2
reg1 = reg1 / reg1
INTEGER division - no remainders
mul r7 r6 r2
Each of these instructions (and many more) get implemented for a particular processor and particular machine… .
write r1
read from keyboard and write to screen
loadn r1 42
you can replace 42 with anything from -128 to 127
addn r1 -1
a shortcut
crazy, perhaps, but used ALL the time
reg1 = 42
reg1 = reg1 - 1

## Slide 121
Hmmm

## Slide 122
Real Assembly Language
Hmmm has a subset common to all real assembly languages.
http://packetstormsecurity.org/unix-humor/AssemblyLanguageCommands.html
DWIMNWIS Do what I mean, not what I say
GFM Go forth and multiply
SQPC Sit quietly and play with your crayons
some of the latest intel instructions (SSE4, 2008)
Operations that should exist:

## Slide 123
Is this enough?
0
1
2
3
4
Could we implement Python using Hmmm Assembly?
halt
mul r2 r1 r1
read r1
add r2 r2 r1
write r2
What’s missing?

## Slide 124
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
input
output
feedback cycle
Q

## Slide 125
Loops and ifs
It's all too linear!
"straight-line code"
jump!
Could we implement Python using our Hmmm Assembly Language so far?
0
1
2
3
4
jump 1
mul r2 r1 r1
read r1
add r2 r2 r1
write r2

## Slide 126
Hmmm, Let's jump !
halt
write r1
loadn r1 42
addn r1 1
jump 1
RAM
CPU
0
1
2
3
4
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2
What if we replace 1 with 2?
screen
random access memory
central processing unit

## Slide 127
jumps
Unconditional jump
Conditional jumps
jump 42
jeqz r1 #
jgtz r1 #
jltz r1 #
jnez r1 #
replaces the PC (program counter) with 42.
"jump to program line number 42"
IF r1 == 0 THEN jump to line number #
IF r1 > 0 THEN jump to the location in #
IF r1 < 0 THEN jump to the location in #
IF r1 != 0 THEN jump to the location in #
Indirect jump
jumpi r1
Jump to the line # stored in reg1!
This IS making me jumpy!

## Slide 128
jgtz
RAM
random access memory
read r1
0
1
2
3
4
5
6
7
8
jgtz r1 7
loadn r2 -1
mul r1 r1 r2
nop
nop
nop
What is this code computing about its input?
Gesundheit!
write r1
halt
CPU
central processing unit
r1
General-purpose register r1
r2
General-purpose register r2
screen

## Slide 129
"Quiz"
Feeling Jumpy?
Name(s)
1
Follow this assembly-language program from top to bottom. Use r1 = 42 and r2 = 5.
Write an assembly-language program that reads one integer as keyboard input. Then, the program should
2
Hint: Take in an input. Next, set up a “result” register starting with 1 in it. Then modify the “result” until it’s right!
compute the factorial of that input and write it out. You may assume without checking that the input will be a positive integer.
r0
r1
r2
r3
r4
read r1
read r2
sub r3 r2 r1
nop
jltz r3 7
write r1
jump 8
(1) What does this program compute in general?
(2) How could you change this program so that, if the original two inputs were equal, it asked the user for new inputs?
Memory - RAM
0
Memory - RAM
Registers - CPU
1
2
3
4
5
6
7
8
9
10
r0
r1
r2
Registers - CPU
0
1
2
3
4
5
6
r5
write r2
halt
7
8
r3
9
r4
0
0

## Slide 130
1
(1) What does this program compute in general?
(2) How could you change this program so that, if the original two inputs were equal, it asked the user for new inputs?
Follow this assembly-language program from top to bottom. Use r1 = 42 and r2 = 5.
read r1
read r2
sub r3 r2 r1
nop
jltz r3 7
write r1
jump 8
Memory - RAM
r0
Registers - CPU
0
1
2
3
4
5
6
write r2
halt
7
8
9
0
r1
r2
r3

## Slide 131
Write an assembly-language program that reads one integer as keyboard input. Then, the program should
2
compute the factorial of that input and write it out. You may assume without checking that the input will be a positive integer.
factorial
plan

## Slide 132
Write an assembly-language program that reads one integer as keyboard input. Then, the program should
2
compute the factorial of that input and write it out. You may assume without checking that the input will be a positive integer.
0
Memory - RAM
1
2
3
4
5
6
7
8
9
10
r0
Registers - CPU
0
r1
r2
r3
factorial

## Slide 134
Bah Hmmmbug!
Randohmmm Numbers…
debugging in Hmmm...
how computers generate "random" numbers
See you there!
This week's lab:

## Slide 135
Why Assembly Language ?
It’s only the foolish who never climb Mt. Fuji -- or who climb it again.
Who writes most of the assembly language used?

## Slide 136
Exam notes
wrap
maxWrapper
binary
bugs
countSL
Do not share these solutions outside of Fall '09 CS 5.

## Slide 138
Jotto
Exams
Mt. Fuji

## Slide 140
Inside gates: Transistors
1947: Bell Labs
seeking cheaper, smaller amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor
1957: Fairchild semiconductor
much more robust, solid state
the "traitorous eight" - ICs
point contact transistor

## Slide 141
Have a relaxing fall break !
drop your feedback into the box…

## Slide 142
Demo & HW
hw6pr1.py
hw6pr2.py
hw6pr3.py
hw6pr4.py
problem 5
Countdown
start from the "count-up" example
Hmmm power!
Fibonacci
1, 1, 2, 3, 5, 8, …
Recursive power
Towers of Hanoi
start from the factorial example
start from the factorial example
start from the recursive factorial example - next time
start from the recursive factorial example - next time
this time
next time

## Slide 143
Assess these HW problems:
How is the class's pace?
black - gold
female - male
circuit design
caesar cipher
audio-based problems
base conversions: baseToBase, …
random walks: rwPos, rwSteps, …
turtle graphics: spiral, svtree, …
Picobot
intro: pigLatin, scrabbleScore …
Circle one of each of these, but don't include your name
What is one thing you'd change about CS 5?
What is one thing you'd keep about CS 5?
image compression
HOW
WORTHWHILE?
HOW
DIFFICULT?
How many hours per week do you spend on CS --outside of lab/class?
too slow
too fast
just right
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
very!
not
1
7
4
Midterm feedback
skip any you did not do…

## Slide 144
Have a relaxing fall break !
drop your feedback into the box…

## Slide 145
Jotto
diner 2
diner 1
ghost 1
ghoul 1
Jessica's word
my word
952 words remaining
1129 words remaining
2319 words remaining
1916 words remaining
quack 0
brown 3
363 words remaining
56 words remaining
badge 1
wacky 0
190 words remaining
9 words remaining

## Slide 146
onward to microprocessors
1968: Intel
Bob Noyce and Gordon Moore decide to go off on their own again, leaving Fairchild to found Intel
1971: the first microprocessor
the Intel 4004 is created by the team of Federico Faggin, Ted Hoff and Stan Mazur. Next up: the 8008, 8080, 8086, 80386, 80486, Pentium, P6
the Intel 4004

## Slide 147
Intel 4004
1971
108 KHz clock
4-bit processor
2300 transistors
10,000 nm wires

## Slide 148
2006
Intel Core 2 Duo
3 GHz clock
64-bit processor
291 million transistors
65 nm wires
I see these designers had excellent taste!

## Slide 149
the compiler
a program that translates from human-usable language into assembly language and machine langauge
x = 6
y = 7
z = x*y
print z
the code
assembly or byte-code
executable machine code
machine code
loadn r1 6
loadn r2 7
mul r3 r1 r2
write r3
0000 0001 0000 0001
1000 0010 0001 0001
0110 0010 0010 0001
0000 0010 0000 0010
0000 0000 0000 0000
0000 0001 …
0010 0001 …
0110 0010 …
1000 0001 …
interpreting byte code
Interpreter
Compiler

## Slide 150
Examples
each processor has its own endearing idiosyncrasies...
Power PC
Core 2 Duo
x = 6
y = 7
z = x*y
print z
the code

## Slide 151
Hmmm reference
memory access
factorial code
for problems 1-3
recursive factorial code

## Slide 152
Assembly Mnemonics

## Slide 154
RISC vs CISC

## Slide 155
Three assembly versions of
lots of machine-dependent details!
main:
pushl %ebp
movl %esp, %ebp
subl $24, %esp
andl $-16, %esp
movl $0, %eax
subl %eax, %esp
movl $42, -4(%ebp)
movl $7, -8(%ebp)
movl -4(%ebp), %eax
movl %eax, -12(%ebp)
movl -8(%ebp), %eax
movl %eax, -4(%ebp)
movl -12(%ebp), %eax
movl %eax, -8(%ebp)
subl $4, %esp
pushl -8(%ebp)
pushl -4(%ebp)
pushl $.LC0
call printf
addl $16, %esp
leave
ret
main:
push {r7, lr}
mov r7, sp
sub sp, sp, #12
mov r0, #2
bl TDInit
ldr r3, .L2
mov r0, r3
bl TDPrintf
sub r2, r7, #4
mov r3, #42
str r3, [r2]
mov r2, r7
sub r2, r2, #8
mov r3, #7
str r3, [r2]
mov r2, r7
sub r2, r2, #12
sub r3, r7, #4
ldr r3, [r3]
str r3, [r2]
sub r2, r7, #4
mov r3, r7
sub r3, r3, #8
ldr r3, [r3]
str r3, [r2]
main:
!#PROLOGUE# 0
save %sp, -128, %sp
!#PROLOGUE# 1
mov 42, %g1
st %g1, [%fp-20]
mov 7, %g1
st %g1, [%fp-24]
ld [%fp-20], %g1
st %g1, [%fp-28]
ld [%fp-24], %g1
st %g1, [%fp-20]
ld [%fp-28], %g1
st %g1, [%fp-24]
sethi %hi(.LLC0), %g1
or %g1, %lo(.LLC0), %o0
ld [%fp-20], %o1
ld [%fp-24], %o2
call printf, 0
nop
mov %g1, %i0
ret
restore
Intel: PC
UltraSparc: Turing
ARM: GBA
mov r2, r7
sub r2, r2, #8
mov r3, r7
sub r3, r3, #12
ldr r3, [r3]
str r3, [r2]
ldr r1, .L2+4
sub r3, r7, #4
ldr r2, [r3]
mov r3, r7
sub r3, r3, #8
ldr r3, [r3]
mov r0, r1
mov r1, r2
mov r2, r3
bl TDPrintf
mov r0, r3
mov sp, r7
@ sp needed for prologue
pop {r7, pc}
def main():
x = 42
y = 7
T = x;
x = y;
y = T;
print x, y

## Slide 157
Computers process numbers - not symbols. We measure our understanding (and control) by the extent to which we can arithmetize an activity.
The Neo-classical view:
- Alan Perlis

## Slide 158
PC
IR
Reg3
1
1
0
1
0
0
1
1
1
0
0
The instruction
00 = LOAD from memory
01 = STORE to memory
10 = add a constant to a reg. (AIM)
11 = ADD a reg. to a reg.
Argument 1
Argument 2
the same Reg3
the register
the constant
1
1
1
0
0
1
1
1
4
old value of Reg3 = 7
new value of Reg3 = 11
clock
0
0
0
0
0
read enable
RAM
IR
8 data bits
8 address bits
strobe for all IR bits
1
0
0
1
1
1
0
0
D in
Q out
strobe
decode instruction
strobe to finish instruction (to all bits)
ripple8
7+4
8 output bits
flip-flop
strobe for next instruction
Instruction Decoding Guide
a Von Neumann machine
1
2
3
4
5
Reg3

## Slide 159
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 160
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 161
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 162
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 163
Von Neumann Architecture
CPU
RAM
central processing unit
random access memory
programs stored here
instructions executed here
Von Neumann bottleneck
read r1
0
1
2
3
4
5
…
6
255
halt
255 memory locations of 16 bits
r0
…
16 registers,
each 16 bits
r15
they can hold values from -32768 upto 32767
r1
r2
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
mul r2 r1 r1
add r2 r2 r1
write r2
0

## Slide 164
Hmmm, Let's jump !
halt
write r1
loadn r1 42
addn r1 1
jump 1
RAM
CPU
central processing unit
random access memory
0
1
2
3
4
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2
Replace 1 with 2? with r1?

## Slide 165
Hmmm, Let's jump !
halt
write r1
loadn r1 42
addn r1 1
jump 1
RAM
CPU
central processing unit
random access memory
0
1
2
3
4
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2
Replace 1 with 2? with r1?

## Slide 166
jgtz
RAM
random access memory
read r1
0
1
2
3
4
5
6
7
8
jgtz r1 7
loadn r2 -1
mul r1 r1 r2
nop
nop
nop
What is this code computing about its input?
Gesundheit!
write r1
halt
CPU
central processing unit
r1
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
General-purpose register r1
r2
General-purpose register r2

## Slide 167
1
(1) What does this program compute in general?
(2) How could you change this program so that, if the original two inputs were equal, it asked the user for new inputs?
Follow this assembly-language program from top to bottom. Use r1 = 42 and r2 = 5.
read r1
read r2
sub r3 r2 r1
nop
jltz r3 7
write r1
jump 8
Memory - RAM
r0
Registers - CPU
0
1
2
3
4
5
6
write r2
halt
7
8
9
0
r1
r2
r3

## Slide 168
Write an assembly-language program that reads one integer as keyboard input. Then, the program should
2
compute the factorial of that input and write it out. You may assume without checking that the input will be a positive integer.
0
Memory - RAM
1
2
3
4
5
6
7
8
9
10
11
r0
Registers - CPU
0
r1
r2
r3
factorial

## Slide 169
I’m checking this with Prof. Townsend…

## Slide 170
I’m checking this with Prof. Townsend…

## Slide 171
Exam notes
wrap
maxWrapper
binary
bugs
countSL
Do not share these solutions outside of Fall '09 CS 5.

## Slide 172
Exam notes
wrap
maxWrapper
binary
bugs
countSL
Do not share these solutions outside of Fall '09 CS 5.

## Slide 173
“NEO”

## Slide 175
Minterm Expansion
(0) All computation can be expressed as bits...
(1) Any function of bits can be made a truth table
INPUTS
Y2 Y1 Y0 X1 X0
OUTPUT
Z2 Z1 Z0 E
0 0
anything
0 0 0
0 1
0 0 1
0 1
0 1 0
0 1
0 1 1
0 1
1 0 0
0 1
1 0 1
0 1
1 1 0
0 1
1 1 1
0 1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 1
1 1
1 1
1 1
1 1
1 1
1 1
1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 1 0 0
1 0 1 0
1 1 1 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 1 1 0
0 1 0 0
0 1 1 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 0 1 0
0 1 0 0
(2) Consider the output, one bit at a time...
(4) Use an AND gate to select each input for which the output should be 1. (a minterm)
(3) The circuit will output 0 by default!
(5) OR the outputs from step (4) together.
anything
Perhaps artistically optimized?
(later) optimize your circuit
How many 1-bit functions here?
To implement the green 1, how many inputs will the AND need?
What is this?

## Slide 176
Without optimizing, how many AND gates and OR gates would this divider need in Logisim?
INPUTS
Y2 Y1 Y0 X1 X0
OUTPUT
Z2 Z1 Z0 E
0 0
anything
0 0 0
0 1
0 0 1
0 1
0 1 0
0 1
0 1 1
0 1
1 0 0
0 1
1 0 1
0 1
1 1 0
0 1
1 1 1
0 1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 1
1 1
1 1
1 1
1 1
1 1
1 1
1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 1 0 0
1 0 1 0
1 1 1 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 1 1 0
0 1 0 0
0 1 1 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 0 1 0
0 1 0 0
anything
(A)
(B)
(C)
(D)
(E)
24 ANDs, 4 ORs
24 ANDs, 7 ORs
24 ANDs, 3 ORs
26 ANDs, 3 ORs
26 ANDs, 7 ORs
Using plain minterm expansion

## Slide 177
Inside Gates?
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:
otherwise it's blocked
otherwise it's blocked
SET transistor
single-electron tunneling
30 nm
voltage here
allows current here

## Slide 178
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
input (0 or 1)
+5 v power
Ground
SIGNAL
POWER
Transistors are current switches:
output
input
NOT
otherwise it's blocked
otherwise it's blocked

## Slide 179
What gate is this?
(0 or 1)
+5 v
Ground, 0 v
SIGNAL
POWER
(A)
output
inputs
X
Y
X
Y
(B)
(C)
(D)
(E)
AND
NAND
"not and"
OR
NOR
XOR
"not or"

## Slide 180
How to get AND, NOT, and OR?
Any way at all !
water
legos

## Slide 181
How to get AND, NOT, and OR?
electromechanical relays
Input, A
Output
Q
Spring
Power

## Slide 182
How to get AND, NOT, and OR?
electromechanical relays
Input, A
Output
Q
Power
Input, B

## Slide 183
The Mark 1
Grace Hopper, Howard Aiken at Harvard
ran at 0.00001 MHz
5 tons, 530 miles of wiring
765,299 distinct parts!
relay-based computer
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html

## Slide 184
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 185
… the movie.
Other disruptive technologies?

## Slide 186
Take a look at this circuit.
If S is 1, what will Q be?
What happens if S becomes 0?
NOR
S
input
output
feedback cycle
Q

## Slide 187
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
The D latch
D
data
only one of S or R is high
Here, we change this circuit so that it takes only 1 bit of data as input…
How could be change the value of our 1 bit of memory at regular time intervals ... ?
S sets Q to 1.
R resets Q to 0.

## Slide 188
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
but only if the strobe is 1…
tells when to remember the data!
S sets Q to 1.
R resets Q to 0.

## Slide 189
NOR
NOR
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the circuit element
The SR latch

## Slide 190
Registers
Main Memory
(replaceable RAM)
100 Registers of 8-64 bits each
Disk Drive
magnetic storage
on the Central Processing Unit
Memory
s
D
Q
8 flip-flops are an 8-bit register
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 10 billion bits +
< 10,000 bits
~10 trillion bits (or more)
1 TB drive
~$100
~$100
~$100
1.5 hours
Price
Time
If “cycle”
were 1 min
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec

## Slide 191
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 192
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Binary Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
Ex CR
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 193
Jotto !
our guesses
M/W's guesses
diner 3
reaps 2
savvy 1
Jesus 1
257 words remaining
1156 words remaining
2334 words remaining
576 words remaining
sines 2
diner 2
105 words remaining
396 words remaining
our guesses
T/Th's guesses
alien 2
alien 1
fjord 0
short 3
910 words remaining
283 words remaining
2326 words remaining
2285 words remaining
musty 0
ducky 1
112 words remaining
97 words remaining
irony 2
icing 0
south 1
shark 3
180 words remaining
50 words remaining
CANOE
ERROR
WOOER
RHYTA
TAROK
HURLS
dicey ?
levee
25 words left
26 words remaining
Notes: 193

## Slide 194
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Binary Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
Ex Cr
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 195
PC
IR
Reg3
1
1
0
1
0
0
1
1
1
0
0
The instruction
00 = LOAD from memory
01 = STORE to memory
10 = add a constant to a reg. (AIM)
11 = ADD a reg. to a reg.
Argument 1
Argument 2
the same Reg3
the register
the constant
1
1
1
0
0
1
1
1
4
old value of Reg3 = 7
new value of Reg3 = 11
clock
0
0
0
0
0
read enable
RAM
IR
8 data bits
8 address bits
strobe for all IR bits
1
0
0
1
1
1
0
0
D in
Q out
strobe
decode instruction
strobe to finish instruction (to all bits)
ripple8
7+4
8 output bits
flip-flop
strobe for next instruction
Instruction Decoding Guide
a Von Neumann machine
1
2
3
4
5
Reg3

## Slide 196
Beyond Python?
Scott Ellsworth, Google Irvine and HMC '89 visiting Wed. ... returning today … other HMC Googlers @ the career fair Friday
Google agrees…

## Slide 197
and are here Fri.
Scott Ellsworth, Google Irvine and HMC '89 visiting yesterday... returning Thursday … with other HMC Google representatives Friday

## Slide 198
Logisim layout…
6 x 7… what else?
the 4-bit ripple-carry adder
one factor horizontal…
one factor vertical…
use labels!
the output
4-bit multiplier