## Slide 1: The CS 5 Times
Penguin Revenge “Rich,”
Gloats Computer Scientist
Upland (AP): A group of penguins celebrated in a
beer garden here after one of their number played an irreverent prank on a rival. “You should have seen it,” chirped one. “Those uppity physics rhinos think they’re better than us because they have spaceships and stuff, but who writes the guidance software? Those guys are all wet—especially now!”
Burping delicately, another bird commented, “Maybe we should insert an, um, insect into their rockets. Who says every booster has to go up?”
A computer science professor in their midst was more restrained. “I did appreciate the retaliatory stunt,” he commented, “but mostly because of the robust flavor of the beer involved.”
CS5 penguins chuckle at their friend’s prank.

## Slide 2: Representing Data
Last time…
  Representing numbers in different bases
  Converting between bases
  Arithmetic in different bases
Today…
  Representing non-integer data
  Boolean functions
  The Minterm Expansion Principle
  Digital logic gates and circuits
  Building an adder!
This stuff is so cool it brings tears to my eyes!

## Slide 3: What’s Up With This!?
>>> .01*10 == .01/.1
False
Notes: Does this seem odd? It should. Mathematically, the two sides are identical. So why is it false? (See next slide).

## Slide 4
Sinking With floats
0.0000
0.0001
0.0010
0.0011
0.1111
0.0100
0.0101
4 bits
In reality, 23 bits or 52 bits will be used to represent the fractional part of a floating-point number
0.1110
0.1101
0.1100
…
0.0000
exact decimal equivalents
0.0625
0.1250
0.1875
0.2500
0.3125
0.7500
0.8125
0.8750
0.9375
…
lots of gaps in here…
2-1
2-2
2-3
2-4
Imagine a computer that uses only 4 bits to represent decimals…
>>> X = 0.1
Notes: This is an oversimplification of how floats really work, but it gives the basic idea. The point is that just as 1/3 is a repeating fraction when expressed in decimal, 1/10 is infinite when expressed in binary. The computer is finite, so it has to deal with an approximation. In this slide, we are using a 4-bit approximation, which shows very clearly that you can’t represent 0.1 accurately. So if we calculate 1.0/0.1, we’re really calculating either 1.0/0.0625 or 1.0/0.1250 (which is the better choice?) and naturally we’re not going to get 10 as the answer.

## Slide 5: Representing Symbols
BINARY HEX DESCRIPTION
0000 0000 00 Null character
0000 0001 01 Start of header
0000 0010 02 Start of text
0000 0011 03 End of text
0000 0100 04 End of transmission
…
0000 1101 0D Carriage return
…
0010 0000 20 Space
0010 0001 21 !
0010 0010 22 “
0010 0011 23 #
0010 0100 24 $
…
0011 0000 30 0
0011 0001 31 1
0011 0010 32 2
…
0100 0001 41 A
0100 0010 42 B
0100 0011 43 C
…
0110 0001 61 a
0110 0010 62 b
0110 0011 63 c
…
ASCII (American Standard Code for Information Interchange)
>>> print "\x21"
!
>>> print "\x63"
c
>>> print "\x63\x61\x62"
cab
In Python…
8 bits are called a “byte”. How many different symbols can be represented with this 1-byte-per-symbol system?
Notes: To represent characters, we can just use numbers. For example, A could be 1, B could be 2, etc. For historical reasons, ASCII won out even though A isn’t 1. This table shows some of the characters in ASCII.
Python strings let you use the strange \xYY notation to insert characters according to their codes. The “x” in python stands for “heXadecimal.”
ASCII can’t handle things like European accented characters or Chinese characters. Unicode is another standard thatallows for encoding of symbols in many alphabets - it’s much larger than ASCII! But we’ll ignore Unicode in CS 5 because it’s complicated.

## Slide 6
HW4: Binary Image Compression
Binary Image
Encoding as raw bits
Just one big string of 64 characters
'01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010'
Notes: An image can be encoded as a bunch of numbers. Here, we use a simple encoding: 0 for a black square and 1 for a white one. This is a checkerboard, but it would be easy to make (for example) the letter “H” by choosing the right pattern of 1’s and 0’s.
When you take a picture, your camera collects “pixels” (short for “picture elements”), which are tiny colored dots. Each dot has a certain amount of red, green, and blue, encoded as numbers. Put them together and you have Taylor Swift!

## Slide 7
HW4: Binary Image Compression!
Binary Image
Encoding as raw bits
Just one big string
'11111111
11111111
00000000
00000000
11111111
11111111
00000000
00000000'
Can we represent this more compactly?
Notes: This image is pretty simple, but it takes the same number of 1’s and 0’s as the previous one. It would be pretty cool to make it smaller without losing the information that makes it be four stripes.

## Slide 8
HW4: Binary Image Compression!
Binary Image
Encoding as raw bits
Just one big string
'11111111
11111111
00000000
00000000
11111111
11111111
00000000
00000000'
An idea:
110000010000110000010000
1 is the next digit
There are 16 of them.
0 is the next digit
Again, there are 16 of them.
And the same for the next two stripes
Notes: This is called “run-length encoding”. It works well on images that have large areas of the same color. The idea is that you count the size of each “run” of all the same color (considering the rows to connect to each other) and encode that as a binary number.

## Slide 9: Algebra with Only 0s and 1s!
George Boole
1815-1864
Real-valued variable Boolean variable
A variable assigned any A variable assigned
real number either 0 or 1
(e.g. x = 3.1234567) (e.g. x = 0 or x = 1)
Real Operators Boolean Operators
+ NOT
 AND
 OR

…
0 and 1 are also called “False” and “True” or “No” and “Yes”
Notes: 0,1 are sometimes referred to as “False” and “True” or even “No” and “Yes” or (if you’re an engineer) “Low” and “High”—or sometimes "High" and "Low" just to confuse people.
George Boole invented the algebra of 0 and 1; it’s called (surprise) Boolean algebra. NOT turns true into false and false into true. We’ll cover AND and OR shortly.

## Slide 10: Functions
Describing a real-valued function…
Words Table Formula
f is a function of TWO real variables s.t. the output is the sum of their squares
f(x) = x2+y2
That table seems to be missing a “few” entries!
x y f(x,y)
0 0 0
1 2 5
1.2 1 2.44
1 1 2
Notes: Real-valued functions are normally described with formulas, but words can work just as well. Sometimes you can describe a function by giving a table of all arguments and all results.
Note: A table isn’t really viable when the domain of the function is infinite!

## Slide 11: Boolean Functions
A Boolean function just takes Boolean arguments and gives a Boolean result.
Example: f(True, True) = True
The most common Boolean functions take 1 or 2 arguments.
There are exactly four 1-argument Boolean functions!
There are 16 two-argument functions, but only 5 are commonly used!
Notes: There's one animation on this slide, giving the alien's second comment.
Why are there four 1-argument functions? Because you have two choices for what to produce given true, and two for what to produce given false. Only one of these functions is useful: NOT. The others are the identity function, the always-false function, and the always-true function.
The commonly used 2-argument functions are AND, OR, and XOR. Hardware engineers also use NAND and NOR because they're actually easier to build in transistor circuits than the 2-argument software-friendly functions. Several of the others are theoretically useful (e.g., EQUIV, which is NOT-XOR) but don’t' get used in practice.

## Slide 12: Boolean Functions
Describing a Boolean function (inputs and outputs: 0 and 1)
Words Table Formula
f is a function of TWO binary (Boolean) variables s.t. the output is 1 if and only if exactly one of the two inputs is 1
x y f(x,y)
0 0 0
0 1 1
1 0 1
1 1 0
?
A table works fine now! It’s called a “truth table.”
Notes: Note that this function is a function of TWO variables!
A table works fine because there is only a finite number of possible input patterns.
What is “the formula”? f(x, y) = x XOR y. We haven’t defined XOR yet – and in fact, this table is the definition!

## Slide 13: NOT, AND, OR
x NOT x
0 1 1 0
x y x AND y
0 0 0
0 1 0
1 0 0
1 1 1
x y x OR y
0 0 0
0 1 1
1 0 1
1 1 1
Also written
x
Also written
xy
Also written
x+y
Notes: The cool thing about AND is that it allows you to force things to zero. Suppose x is the "data" and y is the "mask". Where y is 0, you get zero. Where y is 1, you get the value of x. This allows you to extract information from a string of bits.
The cool thing about OR is that it allows you to force things to one. This allows you to insert information into a string of bits. If x has zeros in a field (which you can arrange with appropriate use of AND), OR-ing in y will cause bits in the matching positions to duplicate the values of y.

## Slide 14: Playing with Functions…
Describe these functions in English:
xx xx x+x (xy + xy)
Worksheet!
Notes: If you refer back to the table of AND, you’ll see that xx = x AND x = x. We’ll leave the second and third ones for you to figure out. The last turns out to calculate equality between x and y; take the time to figure out why.

## Slide 15: Playing with Functions…
How about Boolean formulae (“formulas”) for:
  A function of two variables x,y that evaluates to 1 iff
  x and y are not equal
  A function of two variables x,y that evaluates to 1 iff
  x  y
Notes: We won’t do this on the worksheet. The point here is that finding “closed forms” (functions) is hard! We need a general systematic way of doing this. We’ll see such a method soon!

## Slide 16: XOR
x y x XOR y
0 0 0
0 1 1
1 0 1
1 1 0
Python uses ~, &, |, and ^ to represent NOT, AND, OR, and XOR, respectively.
Notes: This is called a “Truth Table” because when Boole did it, he used T and F, and the table shows when f(x, y) is true.
XOR is useful for selective inversion. Where y is zero, you get the original value of x. Where y is one, you get x-bar.
XOR has the property that x XOR y XOR y = y.

## Slide 17: Properties of Boolean Functions
All the "usual" Boolean functions commute:
f(x, y) = f(y, x)
AND, OR, and XOR associate:
f(f(x, y), z) = f(x, f(y, z))
e.g., (x AND y) AND z = x AND (y AND z)
What about the Unusual ones?
Notes: Commutativity holds for AND, OR, XOR, NAND, and NOR. Some of the other two-argument functions don't commute; for example, the "discard y" function f(x, y) = x doesn't commute. (NAND is “not AND”: calculate x AND y, then invert the result. NOR is “not OR”.)
NAND and NOR don't associate. (0 NOR 0) NOR 1 = 1 NOR 1 = 0, but 0 NOR (0 NOR 1) = 0 NOR 0 = 1

## Slide 18: The Alien’s Life Advice
Don’t get bogged down in a single project.
Get bogged down in at least two!

## Slide 19: Digital Logic Gates
x NOT x
0 1 1 0
x y x AND y
0 0 0
0 1 0
1 0 0
1 1 1
x y x OR y
0 0 0
0 1 1
1 0 1
1 1 1
Also written
x
Also written
xy
Also written
x+y
y
y
x AND y
x OR y
NOT is often shown as just the small circle on another gate.
x
x
x
x
Notes: The purpose of this slide is to show the complete definitions of these three functions, the mathematical notation we’ll use when talking about them, and the symbols we’ll use when we draw electrical circuits.

## Slide 20: Finding the Formula! The Minterm Expansion Principle
Consider this function…
Words Truth Table Formula
A function of
TWO binary
inputs x,y
where the
output is 1 iff
x  y
x y x XOR y
0 0 0
0 1 1
1 0 1
1 1 0
Notes: This slide has six animations. The first four highlight the result-true lines and then the associated formulas. The fifth highlights all the result-false lines. The last highlights the resulting formula.
The principle is that each line in the truth table can be written as an AND of the inputs (and their inverses), such that this term (a "minterm") is one (true) only for that precise set of inputs. By selecting the inputs for which the function is true, and OR-ing them together, we can create an expression that exactly reproduces the truth table.
In this case, the first blue line in the truth table is selected when x = 0 and y = 1. We can write this as (x-bar)y. That’s true when x is 0 (since x-bar is then 1) and y is 1. Convince yourself that it’s true ONLY when x = 0 and y = 1. So that minterm implements just one line of the truth table. Likewise, x(y-bar) is true only for the second blue line. If we OR them together, we get a function that’s true only for the two blue lines. Convince yourself of that fact by plugging all four combinations of x and y into f(x,y) and showing that it produces 1 when x and y are different, and 0 when they are the same.
In general, the minterm expansion of a function is NOT optimal. For example, the expansion of f(x,y) = x is non-minimal because it considers the values of y when they could simply be ignored. There are "minimization techniques" that can help to find a more optimal representation.

## Slide 21: From Formula to Circuit!
Words Table Formula
f is a function of TWO binary (Boolean) variables s.t. the output is 1 if and only if exactly one of the two inputs is 1
x y f(x,y)
0 0 0
0 1 1
1 0 1
1 1 0
xy + xy
Circuit
x
y
Notes: Once we have the formula, we can draw the circuit directly. x, y, z, etc. are just inputs to the circuit. x-bar, y-bar, etc. are the inputs fed through a NOT gate. Any AND operations are just feeding x or x-bar, etc., into an AND gate. Finally, we take the results of all the ANDs and feed them into an OR gate to get f(x, y).

## Slide 22: From Formula to Circuit!
Words Table Formula
f is a function of TWO binary (Boolean) variables s.t. the output is 1 if and only if exactly one of the two inputs is 1
x y f(x,y)
0 0 0
0 1 1
1 0 1
1 1 0
xy + xy
Circuit
Notes: Another way to draw the circuit is to have a line (horizontal or vertical) for each variable and its negation.
Next week we will use a program called Logisim in lab to design circuits and experiment with them! Logisim lets you draw a logic circuit and then try different inputs. It will show you (with clever coloring) exactly how the circuit works and what the results are.
At this point, bring up Logisim and demonstrate the pre-prepared XOR circuit.

## Slide 23: You Try It! The Minterm Expansion Principle
Consider this function…
Words Truth Table Formula
A function of
TWO binary
inputs x,y
where the
output is 1 iff
x ≥ y
Circuit

## Slide 24: Try This One…
Consider this function…
Words Truth Table Formula
A function of
THREE binary
inputs x,y,z
where the
output is 1 iff
the number of 1’s
is odd
Circuit
This is called an “odd parity” circuit
Notes: WORKSHEET.
This is pretty much the same thing, only with three inputs. The truth table will have eight lines. A good way to enumerate the inputs is to think of them as a binary number. Start with 000 and then increment (count) until you have 111.
Your truth table should have exactly four lines where the output is 1. How many AND gates do you need? How many OR gates? (Hint: an OR gate can have more than two inputs; in that case its output is 1 if any input is a 1.)

## Slide 25: A Circuit for Adding!
Base 2 Addition
0
sum
carry out
0 1 0 1
1 0 0 1
+
FA
Notes: This slide has one animation, making the full adder appear.
FA = "Full Adder", so called because it is possible to build it from two identical "Half Adders". We won't do half adders; it's easier to create a full adder directly.
If you have a FA for one bit position, you can wire up a multi-bit adder…see the next slide.

## Slide 26: A Circuit for Adding!
Base 2 Addition
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
Cool, but how do we build a FA?
Notes: If you have a working full adder, you can treat it as a black box that takes three inputs and produces TWO outputs. Then wire a “carry” of zero to the right-most FA, and wire each other FA’s carry to the next higher one. What happens to the final carry?

## Slide 27: A Circuit for Adding!
Base 2 Addition
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0
Notes: Note that a FA has three inputs and TWO outputs. The easy way to build it is to write a separate truth table for each output, and then build a circuit for each. Then just wire the “global” input x to the x input for each sub-circuit, and do the same for y and z!
Notice that one of the columns in the truth table is the odd-parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on next week’s homework/lab.

## Slide 28: A Cool Thing About XOR
x XOR y XOR y = x
Why is that?
Try this on for size:
x = x ^ y
y = x ^ y
x = x ^ y
Notes: The rest of these slides are just for fun, if we have time in lecture.
If y is zero, XOR leaves x unchanged. If y is one, XOR flips x. So applying XOR twice with the same y flips x twice, and you get the original. Also, y XOR y is always zero, and zero XOR anything is always that thing.

## Slide 29: A Cool Thing About XOR
Try this on for size:
x = x ^ y
y = x ^ y
x = x ^ y
Suppose x, y = 0,0 0,1 1,0 1,1
Now x,y = 0,0 1,1 1,0 0,1
0,0 1,0 1,1 0,1
0,0 1,0 0,1 1,1
Notes: Note that the table on the right covers all possible combinations of x and y (if x and y are a single bit).
The original x and y have been swapped!

## Slide 30: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = (x0 ^ y0) ^ y0
x2 = x1 ^ y1
Notes: XOR associates, so…

## Slide 31: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = x0 ^ (y0 ^ y0)
x2 = x1 ^ y1
Notes: Remember that y0^y0 = 0, and anything XOR 0 is the original thing.

## Slide 32: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = x0
x2 = x1 ^ y1

## Slide 33: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = x0
x2 = x1 ^ y1 = x1 ^ x0

## Slide 34: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = x0
x2 = x1 ^ y1 = (x0 ^ y0) ^ x0
Notes: XOR not only associates, it commutes, so…

## Slide 35: A Cool Thing About XOR
x = x ^ y
y = x ^ y
x = x ^ y
We can prove this if we call the original values x0 and y0:
x1 = x0 ^ y0
y1 = x1 ^ y0 = x0
x2 = x1 ^ y1 = y0
That's so cool that last night I got a date with Xhicktlx by telling him about it!
Notes: If y is zero, XOR leaves x unchanged. If y is one, XOR flips x. So applying XOR twice flips x twice, and you get the original.