## Slide 1: 64-Bit Architectures
Topics
  64-bit data
  New registers and instructions
  Calling conventions
CS 105 “Tour of the Black Holes of Computing!”

## Slide 2: Data Representations: IA32 + x86-64
Sizes of C Objects (in Bytes)
  C Data Type Typical 32-bit Intel IA32 x86-64
    unsigned 4 4 4
    int 4 4 4
    long int 4 4 8
    char 1 1 1
    short 2 2 2
    float 4 4 4
    double 8 8 8
    long double 8 10/12 16
    char * 4 4 8 Or any other pointer

## Slide 3: x86-64 Integer Registers
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
  Extend existing registers. Add 8 new ones.
  Make %ebp/%rbp general purpose
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%ax
%bx
%cx
%dx
%si
%di
%sp
%bp
%r8w
%r9w
%r10w
%r11w
%r12w
%r13w
%r14w
%r15w
%dx
%si
%di
%sp
%bp
%r8w
%r9w
%r10w
%r11w
%r12w
ah
al
bh
bl
ch
cl
dh
dl
sil
dil
spl
bpl
r8b
r9b
r10b
r11b
r12b
r13b
r14b
r15b
Oh.
My.
God.

## Slide 4: x86-64 Integer Registers
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
  Extend existing registers. Add 8 new ones.
  Make %ebp/%rbp general purpose
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d

## Slide 5: Instructions
Long word l (4 Bytes) ↔ Quad word q (8 Bytes)
New instructions:
  movl → movq
  addl → addq
  sall → salq
  movzbq, movslq
  etc.
32-bit instructions that generate 32-bit results
  Set higher order bits of destination register to 0
  Example: addl, movl (thus no movzlq)

## Slide 6: Swap in 32-bit Mode
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 12(%ebp),%ecx
movl 8(%ebp),%edx
movl (%ecx),%eax
movl (%edx),%ebx
movl %eax,(%edx)
movl %ebx,(%ecx)
movl -4(%ebp),%ebx
movl %ebp,%esp
popl %ebp
ret
Body
Setup
Finish

## Slide 7: Swap in 64-bit Mode
Operands passed in registers (why useful?)
  First (xp) in %rdi, second (yp) in %rsi
  64-bit pointers
No stack operations required
32-bit data
  Data held in registers %eax and %edx
  movl operation
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movl (%rdi), %edx
movl (%rsi), %eax
movl %eax, (%rdi)
movl %edx, (%rsi)
retq

## Slide 8: Swap Long Ints in 64-bit Mode
64-bit data
  Data held in registers %rax and %rdx
  movq operation
  Otherwise same
void swap_l
(long int *xp, long int *yp)
{
long int t0 = *xp;
long int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap_l:
movq (%rdi), %rdx
movq (%rsi), %rax
movq %rax, (%rdi)
movq %rdx, (%rsi)
retq

## Slide 9: New Calling Conventions
Most procedures no longer need stack frame
First six arguments passed in registers
Register %rbp available for general use
Stack frame accessed via %rsp
128 bytes below %rsp usable by function (“red zone”)