## Slide 1: Computer Systems Introduction
Topics:
  Class Intro
  Data Representation
CS 105
“Tour of the Black Holes of Computing!”
Geoff Kuenning
Fall 2015

## Slide 2: Course Theme
  Abstraction is good, but don’t forget reality!
Many CS Courses emphasize abstraction
  Abstract data types
  Asymptotic analysis
These abstractions have limits
  Especially in the presence of bugs
  Need to understand underlying implementations
Useful outcomes
  Become more effective programmers
    Able to find and eliminate bugs efficiently
    Able to tune program performance
  Prepare for later “systems” classes in CS
    Compilers, Operating Systems, File Systems, Computer Architecture, Robotics, etc.

## Slide 3: Textbooks
Randal E. Bryant and David R. O’Hallaron,
  “Computer Systems: A Programmer’s Perspective”, 2nd Edition, Prentice Hall, 2011.
Brian Kernighan and Dennis Ritchie,
  “The C Programming Language, Second Edition”, Prentice Hall, 1988
Larry Miller and Alex Quilici
  The Joy of C, Wiley, 1997

## Slide 4: Syllabus
  Syllabus on Web: http://www.cs.hmc.edu/~geoff/cs105
  Calendar defines due dates
  Labs: cs105submit for some, others have specific directions

## Slide 5: Notes:
Work groups
  You must work in pairs on all labs
  Honor-code violation to work without your partner!
  Corollary: showing up late doesn’t harm only you
Handins
  Check calendar for due dates
  Electronic submissions only
Grading Characteristics
  Lab scores tend to be high
    Serious handicap if you don’t hand a lab in
  Tests & quizzes typically have a wider range of scores
    I.e., they’re primary determinant of your grade
      …but not the ONLY one
  Do your share of lab work and reading, or bomb tests
  Do practice problems in book

## Slide 6: Facilities
Assignments will use Intel computer systems
  Not all machines are created alike
    Performance varies (and matters sometimes in 105)
    Security settings vary and can matter
  Wilkes: x86/Linux specifically set up for this class
  Log in on a Mac, then ssh to Wilkes
    If you want fancy programs, start X11 first
    Directories are cross-mounted, so you can edit on Knuth or your Mac, and Wilkes will see your files
  …or ssh into Wilkes from your dorm
  All programs must run on Wilkes: that’s where we grade

## Slide 7: CS 105 “Tour of the Black Holes of Computing”
Topics
  Representing information as bits
  Bit-level manipulations
  Integers
    Representation, unsigned and signed
    Conversion, Casting
    Expanding, truncating
    Addition, negation, multiplication, shifting
  Representations in memory, pointers, strings
CS 105
Bits, Bytes, Integers

## Slide 8: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 9: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 10: Example Data Sizes
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 11: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 12: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 13: Example: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 14: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 ➙ 0xBE
    ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF
    ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41
    011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D
    011010012 | 010101012 ➙ 011111012

## Slide 15: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)

## Slide 16: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p (avoids null pointer access)
Watch out for && vs. & (and || vs. |)…
one of the more common oopsies in
C programming

## Slide 17: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 18: C Puzzles
  Taken from old exams
  Assume machine with 32-bit word size, two’s complement integers
  For each of the following C expressions, either:
    Argue that it is true for all argument values, or
    Give example where it is not true
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization

## Slide 19: Encoding Integers
short int x = 15213;
short int y = -15213;
  C short 2 bytes long
Sign Bit
  For 2’s complement, most-significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit

## Slide 20: Encoding Integers (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 21: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s-Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 22: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
    K&R Appendix B11
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform-specific

## Slide 23: An Important Detail
No self-identifying data
  Looking at a bunch of bits doesn’t tell you what they mean
  Could be signed, unsigned integer
  Could be floating-point number
  Could be part of a string
Only theprogram (instructions) knows for sure!

## Slide 24: Unsigned & Signed Numeric Values
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding

## Slide 25: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret

## Slide 26: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 27: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 28: Casting Signed to Unsigned
short int x = 15213;
unsigned short int ux = (unsigned short) x;
short int y = -15213;
unsigned short int uy = (unsigned short) y;
C Allows Conversions from Signed to Unsigned
Resulting Value
  No change in bit representation
  Nonnegative values unchanged
    ux = 15213
  Negative values change into (large) positive values
    uy = 50323

## Slide 29: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 30: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 31: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
    Exception: unsigned, if too big to be signed but fit in unsigned
  Unsigned if have “U” as suffix
    0U, 4294967259u
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;
lowercase is better here

## Slide 32: Casting Surprises
Expression Evaluation
  If you mix unsigned and signed in single expression, signed values are implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32
Constant1 Constant2 Relation Evaluation
  0 0u
  -1 0
  -1 0u
  2147483647 -2147483648
  2147483647u -2147483648
  -1 -2
  (unsigned) -1 -2
  2147483647 2147483648u
  2147483647 (int) 2147483648u

## Slide 33: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If you mix unsigned and signed in single expression, signed values are implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32
Constant1 Constant2 Relation Evaluation
  0 0u
  -1 0
  -1 0u
  2147483647 -2147483648
  2147483647u -2147483648
  -1 -2
  (unsigned) -1 -2
  2147483647 2147483648u
  2147483647 (int) 2147483648u

## Slide 34: Summary: Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!

## Slide 35: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 36: Sign Extension Example
  Converting from smaller to larger integer data type
  C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 37: Negating with Complement & Increment
Claim: Following holds for 2’s complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…112 == -1
Increment
  ~x + x + (-x + 1) == -1 + (-x + 1)
  ~x + 1 == -x
Warning: Be cautious treating int’s as integers
  OK here (associativity holds)
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 38: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 39: Two’s-Complement Addition
TAdd and UAdd have identical bit-level behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 40: Detecting 2’s-Comp. Overflow
Task
  Given s = TAddw(u , v)
  Determine if s = Addw(u , v)
  Example
  int s, u, v;
  s = u + v;
Claim
  Overflow iff either:
    u, v < 0, s  0 (NegOver)
    u, v  0, s < 0 (PosOver)
0
2w –1
2w–1
PosOver
NegOver

## Slide 41: A Fun Fact
Official C standard says overflow is “undefined”
  Intention was to let machine define what happens
Recently compiler writers have decided “undefined” means “we get to choose”
  We can generate 0, biggest integer, or anything else
  Or if we’re sure it’ll overflow, we can optimize out completely
  This can introduce some lovely bugs (e.g., you can’t check for overflow)
Currently fight between compiler community and security community over this issue
Notes: Different hardware algorithms are needed for signed and unsigned.

## Slide 42: Multiplication
Computing exact product of w-bit numbers x, y
  Either signed or unsigned
Ranges
  Unsigned: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
    Up to 2w bits
  Two’s complement min: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
    Up to 2w–1 bits (including 1 for sign)
  Two’s complement max: x * y ≤ (–2w–1) 2 = 22w–2
    Up to 2w bits, but only for (TMinw)2
Maintaining exact results
  Would need to keep expanding word size with each product computed
  Done in software by “arbitrary-precision” arithmetic packages
Notes: Different hardware algorithms are needed for signed and unsigned.

## Slide 43: Power-of-2 Multiply by Shifting
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  u << 5 - u << 3 == u * 24
  Most machines shift and add much faster than multiply
    Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 44: Unsigned Power-of-2 Divide by Shifting
Quotient of unsigned by power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
•••

## Slide 45: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 46: Why Should I Use Unsigned?
Don’t use without understanding implications
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .

## Slide 47: Counting Down with Unsigned
Proper way to use unsigned as loop index
    unsigned i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
See Robert Seacord, Secure Coding in C and C++
  C Standard guarantees unsigned addition will behave like modular arithmetic
    0 – 1  UMax
Even better
    size_t i;
    for (i = cnt-2; i < cnt; i--)
    a[i] += a[i+1];
  Data type size_t is unsigned value with length = word size
  Code will work even if cnt = UMax
  What if cnt is signed and < 0?

## Slide 48: Why Should I Use Unsigned? (cont.)
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 49: Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 50: Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 PB (petabytes) of addressable memory
    That’s 18.4 X 1015
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 51: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 52: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 53: Byte Ordering
So, how are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows
    Least significant byte has lowest address

## Slide 54: Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 55: Representing Strings
char S[6] = "18213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
IA32
Sun
31
38
32
31
33
00
31
38
32
31
33
00