## Slide 1: Internetworking
Topics
  Client-server programming model
  Networks
  Internetworks
  Global IP Internet
    IP addresses
    Domain names
    Connections
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: Computer Networks
A network is a hierarchical system of boxes and “wires” organized by geographical proximity
  LAN (local area network) spans building or campus
    Ethernet
    802.11 (wireless)
  WAN (wide-area network) spans country or world
    Different, usually faster technology
An internetwork (internet) is an interconnected set of networks
  Global IP Internet (uppercase “I”) is most famous example of an internet (lowercase “i”)

## Slide 3: Lowest Level: Ethernet Segment
Ethernet segment consists of collection of hosts connected by wires (twisted pairs) to a switch
All or part of a building
Operation
  Each Ethernet adapter has unique 48-bit address
  Hosts send bits to any other host in chunks called frames
  Switch copies bits to proper destination port
    Dynamically learns which port has which host address
host
host
host
hub
100 Mb/s
100 Mb/s
ports

## Slide 4: Next Level: Bridged Ethernet Seg
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port. How? Frames have source and destination addresses….
host
host
host
host
host
switch
switch
bridge
100 Mb/s
100 Mb/s
host
host
switch
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
switch
A
B
C
X
Y

## Slide 5: Conceptual View of LANs
For simplicity, switches, bridges, and wires are often shown as collection of hosts attached to a single wire:
host
host
host
...
Key: any host can easily talk to any other host on the “wire”

## Slide 6: Next Level: internets
Multiple incompatible LANs can be physically connected by specialized computers called routers
The connected networks are called an internet
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible LANs (e.g., Ethernet and ATM)

## Slide 7: Notion of an internet Protocol
How is it possible to send bits across incompatible LANs and WANs?
Solution: protocol software running on each host and router smooths out differences between different networks
Implements an internet protocol (i.e., set of rules) that governs how hosts and routers should cooperate when they transfer data from network to network
  TCP/IP is protocol (family) for global IP Internet

## Slide 8: What Does an internet Protocol Do?
1. Provides naming scheme
  Defines uniform format for host addresses
  Each host (and router) is assigned at least one internet address that uniquely identifies it
2. Provides delivery mechanism
  An internet protocol defines a standard transfer unit (packet)
  Packet consists of header and payload
    Header: contains info such as packet size, source and destination addresses
    Payload: contains data bits sent from source host
  Encapsulation—key to network messages

## Slide 9: Transferring Data via an internet
protocol
software
client
LAN1
adapter
Host A
data
data
PH
FH1
data
PH
data
PH
FH2
LAN1
LAN2
data
data
PH
data
PH
FH2
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
internet packet
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
FH1
data
PH
protocol
software
server
LAN2
adapter
Host B
Frame

## Slide 10: Other Issues
We are glossing over several important questions:
  What if different networks have different maximum frame sizes? (segmentation)
  How do routers know where to forward frames?
  How do routers learn when the network topology changes?
  What if packets get lost?
These (and other) questions are addressed by the area of systems known as computer networking: CS 125

## Slide 11: Global IP Internet
Most famous example of an internet
Based on TCP/IP protocol family
  IP (Internet protocol) :
    Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host to host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable datagram delivery from process to process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable byte streams from process to process over connections
  …and several more
Accessed via mix of Unix file I/O and functions from the sockets interface

## Slide 12: Hardware and Software Org of an Internet Application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 13: Programmer’s View of Internet
1. Hosts are mapped to a set of 32-bit IP(v4) addresses
  134.173.42.100 is Knuth
2. IP addresses are mapped to set of identifiers called Internet domain names
  134.173.42.2 is mapped to www.cs.hmc.edu
  128.2.203.164 is mapped to www.cs.cmu.edu
  Mapping is many-to-many
3. Process on one Internet host can communicate with process on another via a connection—IP Address, Port Number

## Slide 14: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
As of 2015, vast majority of Internet traffic still carried by IPv4
  Only 4% of users access Google services using IPv6.
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.

## Slide 15: 1. IP (v4) Addresses
32-bit IP addresses are stored in IP address struct
  Always stored in memory in network byte order (big-endian)
  True in general for any integer transferred in packet header from one machine to another.
    E.g., port number used to identify Internet connection
/* Internet address structure */
struct in_addr {
unsigned int s_addr; /* network byte order (big-endian) */
};
Handy network byte-order conversion functions (no-ops on some machines):
  htonl: convert int from host to network byte order
  htons: convert short int from host to network byte order
  ntohl: convert int from network to host byte order
  ntohs: convert short int from network to host byte order

## Slide 16: Dotted-Decimal Notation
By convention, each byte in 32-bit IP address is represented by its decimal value and separated by period
    IP address 0x8002C2F2 = 128.2.194.242
    IPv6 addresses uglier: 2001:1878:301:902:218:8bff:fef9:a407
Functions for converting between binary IP addresses and dotted decimal strings:
  inet_pton: converts dotted-decimal string to IP address in network byte order
  inet_ntop: converts IP address in network byte order to its corresponding dotted-decimal string
  “n” denotes network representation; “p” denotes printable representation

## Slide 17: 2. Internet Domain Names
mil
edu
gov
com
hmc
berkeley
mit
cs
math
mike1
134.173.41.151
unnamed root
Knuth
134.173.42.100
amazon
www
208.216.181.15
Top-level domain names
Second-level domain names
Third-level domain names

## Slide 18: Domain Naming System (DNS)
Internet tracks mapping between IP addresses and domain names in worldwide many-to-many distributed database called DNS.
  Conceptually, programmers can view DNS database as collection of millions of address information structures:
Functions for retrieving host entries from DNS:
  getaddrinfo: query key is DNS domain name
  getnameinfo: query key is IP address (V4 or V6)
/* Address information structure (DNS only has + entries) */
struct addrinfo {
int ai_flags; /* Various options */
int ai_family; /* + AF_INET or AF_INET6 */
int ai_socktype; /* Preferred socket type */
int ai_protocol; /* Preferred protocol */
size_t ai_addrlen; /* Length of address */
struct sockaddr *ai_addr; /* + Encoded IP address */
char *ai_canonname; /* + Canonical host name */
struct addrinfo *ai_next; /* Link to next answer */
};

## Slide 19: Properties of DNS Host Entries
Each host entry is equivalence class of domain names and IP addresses
Each host has a locally defined domain name localhost, which always maps to loopback address 127.0.0.1
Different kinds of mappings are possible:
  Simple case: 1-1 mapping between domain name and IP addr:
    www.cs.hmc.edu maps to 134.173.42.2
  Multiple domain names mapped to the same IP address:
    cs.hmc.edu and knuth.cs.hmc.edu both map to 134.173.42.100
  Multiple domain names mapped to multiple IP addresses:
    aol.com and www.aol.com map to multiple IP addresses
  Some valid domain names don’t map to any IP address:
    For example: research.cs.hmc.edu

## Slide 20: A Program That Queries DNS
int main(int argc, char **argv) { /* argv[1] is a domain name */
struct addrinfo hints, *host, *firsthost = NULL;
struct sockaddr *addr;
char buf[80];
memset(&hints, 0, sizeof hints);
hints.ai_flags = AI_CANONNAME;
hints.ai_family = AF_UNSPEC; /* Or AF_INET or AF_INET6 */
if (getaddrinfo(argv[1], NULL, &hints, &firsthost) != 0)
exit(1);
printf("official hostname: %s\n", firsthost->ai_canonname);
for (host = firsthost; host != NULL; host = host->ai_next) {
addr = host->ai_addr;
inet_ntop(addr->sa_family, addr->sa_data, buf, sizeof buf);
printf("address: %s\n", buf);
}
exit(0);
}

## Slide 21: Querying DNS from the Command Line
Domain Information Groper (dig) provides scriptable command line interface to DNS.
linux> dig +short knuth.cs.hmc.edu
134.173.42.100
linux> dig +short -x 134.173.42.100
Knuth.cs.hmc.edu.
linux> dig +short aol.com
64.12.79.57
64.12.89.186
205.188.100.58
205.188.101.58
207.200.74.38
linux> dig +short -x 64.12.79.57
5minmedia.com.
mightyaol.com.
…

## Slide 22: 3. Internet Connections
Clients and servers communicate by sending streams of bytes over connections:
  Point-to-point, full-duplex (2-way communication), and reliable
Socket is application endpoint of connection
  Socket address is IPaddress:port pair
Port is 16-bit integer that identifies a process:
  Ephemeral port: Assigned automatically on client when client makes connection request
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)
Connection is uniquely identified by socket addresses of its endpoints (socket pair)
  (clientaddr:clientport, serveraddr:serverport)

## Slide 23: Well-known Ports and Service Names
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo server: 7/echo
  ssh servers: 22/ssh
  email server: 25/smtp
  Web servers: 80/http
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 24: Putting it all Together: Anatomy of an Internet Connection
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15

## Slide 25: Next Time
How to use sockets interface to establish Internet connections between clients and servers
How to use Unix I/O to copy data from one host to another over an Internet connection