## Slide 1: Virtual Memory
Topics
  Address translation
  Motivations for VM
  Accelerating translation with TLBs
CS 105 “Tour of the Black Holes of Computing!”

## Slide 2: Physically Addressed System
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 3: Virtually Addressed System
Used in all modern servers, laptops, and smart phones
One of the great ideas in computer science
000:
100:
M-1:
Main memory
MMU
200:
300:
400:
500:
600:
700:
Physical address
(PA)
Data word
800:
...
CPU
Virtual address
(VA)
CPU Chip
400
4100

## Slide 4: What Is Virtual Memory?
If you think it’s there, and it is there…it’s real.
If you think it’s not there, and it really isn't there…it’s nonexistent.
If you think it’s not there, and it really is there…it’s transparent.
If you think it’s there, and it’s not really there…it’s imaginary.
Virtual memory is imaginary memory: it gives you the illusion of a memory arrangement that’s not physically there.

## Slide 5: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}
Clean distinction between data (bytes) and their attributes (addresses)
Every byte in main memory has one physical address and zero or more virtual addresses

## Slide 6: Why Virtual Memory (VM)?
Uses main memory efficiently
  Use DRAM as a cache for parts of a virtual address space
Simplifies memory management
  Each process gets the same uniform linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
  User program can’t access privileged kernel information and code

## Slide 7: VM as Tool for Caching
Conceptually, virtual memory is an array of N contiguous bytes stored on disk.
The contents of the array on disk are cached in physical memory (DRAM cache)
  These cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 8: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
Consequences
  Large page (block) size: typically 4-8 KB, sometimes 4 MB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from CPU caches
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 9: Enabling Data Structure: Page Table
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory-resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 10: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory-resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 11: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 12: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 13: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 14: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 15: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Key point: Waiting until the miss to copy the page to DRAM is known as demand paging

## Slide 16: Allocating Pages
Allocating a new page (VP 5) of virtual memory.
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5

## Slide 17: Locality to the Rescue Again!
Virtual memory seems terribly inefficient, but it works because of locality.
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If working set size < main memory size
  Good performance for one process after compulsory misses
If SUM(working set sizes) > main memory size
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously

## Slide 18: VM as Tool for Memory Management
Key idea: each process has own virtual address space
  Can view memory as a simple linear array
  Mapping function scatters addresses through physical memory
    Well-chosen mappings can improve locality
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 19: VM as Tool for Memory Management
Memory allocation
  Each virtual page can be mapped to any physical page
  A virtual page can be stored in different physical pages at different times
Sharing code and data among processes
  Map virtual pages to the same physical page (here: PP 6)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 20: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, stack, and shared libraries always start at same virtual address
Loading
  execve allocates virtual pages for .text and .data sections & creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
brk
0x400000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from
the
executable
file

## Slide 21: VM as Tool for Memory Protection
Extend PTEs with permission bits
Page fault handler checks these before remapping
  If violated, send process SIGSEGV (segmentation fault)
Process i:
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j:
Yes
USER
Yes
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
USER
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
EXEC
Yes
EXEC
Yes
Yes
Yes
Yes
No

## Slide 22: VM Address Translation
Virtual Address Space
  V = {0, 1, …, N–1}
Physical Address Space
  P = {0, 1, …, M–1}
Address Translation
  MAP: V  P U {}
  For virtual address a:
    MAP(a) = a’ if data at virtual address a is at physical address a’ in P
    MAP(a) =  if data at virtual address a is not in physical memory
      Either invalid or stored on disk

## Slide 23: Summary of Address-Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number

## Slide 24: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1

## Slide 25: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 26: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 27: Integrating VM and Cache
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 28: Speeding up Translation With a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small set-associative hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages

## Slide 29: Accessing the TLB
MMU uses the VPN portion of the virtual address to access the TLB:
TLB tag (TLBT)
TLB index (TLBI)
0
p-1
p
n-1
VPO
VPN
p+t-1
p+t
PTE
tag
v
…
PTE
tag
v
Set 0
PTE
tag
v
PTE
tag
v
Set 1
PTE
tag
v
PTE
tag
v
Set T-1
T = 2t sets
TLBI selects the set
TLBT matches tag of line within set

## Slide 30: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 31: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?

## Slide 32: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 48-bit address space, 8-byte PTE
Problem:
  Would need a 512 GB page table!
    248 * 2-12 * 23 = 239 bytes
Common solution: Multi-level page table
Example: 2-level page table
  Level 1 table (always memory-resident): each PTE points to a page table
  Level 2 table (paged in and out like any other data): each PTE points to a page
Level 1
Table
...
Level 2
Tables
...

## Slide 33: A Two-Level Page Table Hierarchy
Level 1
page table
...
Level 2
page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
32-bit addresses, 4KB pages, 4-byte PTEs

## Slide 34: Translating With a k-level Page Table
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table

## Slide 35: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions