## Slide 1
Computer Networking: A Top Down Approach
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 2 Application Layer
A note on these slides:
The slides used in this class were derived from ones provided by Jim Kurose and Keith Ross, authors of the textbook for the course.
I would like to thank the authors for making the slides available. They retain copyright in all of the original material.
Copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 3: Chapter 2: application layer
our goals:
conceptual, implementation aspects of network application protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
  content distribution networks
learn about protocols by examining popular application-level protocols
  HTTP
  SMTP / POP3 / IMAP
  DNS
creating network applications
  socket API

## Slide 4: Some network apps
e-mail
web
text messaging
remote login
P2P file sharing
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
voice over IP (e.g., Skype)
real-time video conferencing
social networking
search
…
…

## Slide 5: Creating a network app
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
having applications on end systems allows rapid development and propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 6: Application architectures
possible application structures:
client-server
peer-to-peer (P2P)

## Slide 7: Client-server architecture
server:
always-on host
permanent IP address
data centers for scaling
clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
client/server

## Slide 8: P2P architecture
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
peer-peer

## Slide 9: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
aside: applications with P2P architectures have both client & server characteristics
clients, servers

## Slide 10: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 11: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host

## Slide 12: App-layer protocol defines
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype

## Slide 13: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, authentication, …

## Slide 14: Transport service requirements: common apps
application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
time sensitive
no
no
yes, few secs
yes, 100s msec
yes, few secs
yes, 100s msec
yes and no

## Slide 15: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup,
Q: why bother? Why is there a UDP?

## Slide 16: Internet apps: application, transport protocols
application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
application
layer protocol
SMTP [RFC 5321]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP

## Slide 17: Securing TCP
TCP & UDP
no encryption
cleartext info sent into socket traverses Internet in cleartext
SSL
provides encrypted TCP connection
data integrity
end-point authentication
SSL is at app layer
apps use SSL libraries, that “talk” to TCP
SSL socket API
  cleartext passwords sent into socket traverse Internet encrypted
  see Chapter 8

## Slide 18: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 19: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file, …
web page built from base HTML file, which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 20: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 21: HTTP overview (continued)
uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server or client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 22: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 23: Non-persistent HTTP
suppose user enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text,
references to 10
jpeg images)
www.someSchool.edu/someDepartment/index.html

## Slide 24: Non-persistent HTTP (cont.)
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 25: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time =
  2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 26: Persistent HTTP
non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters each referenced object
as little as one RTT for all the referenced objects

## Slide 27: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 28: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~
sp
sp

## Slide 29: Uploading form input
POST method:
web page often includes form input
input is uploaded to server in entity body
suited to large inputs or inputs with binary content
URL method:
uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 30: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 31: HTTP response message
status line
(protocol,
status code,
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 32: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:
Google for “http status cats” or “http status dogs”

## Slide 33: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
after typing this in, hit carriage
return twice. You have sent
a minimal (but complete)
GET request to the HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 34: User-server state: cookies
many Web sites use cookies
four components:
  1) cookie header line of HTTP response message
  2) cookie header line in next HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
example:
Ming always accesses Internet from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 35: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: id=1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
set-cookie: id=1678
ebay 8734
amazon 1678
usual http request msg
cookie: id=1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 36: Cookies (continued)
what cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
aside
how to keep “state”:
protocol endpoints: maintain state at sender and receiver over multiple transactions
cookies: http messages carry state

## Slide 37: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 38: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link
Internet dense with caches: enables “poor” content providers to effectively deliver content (so too does P2P file sharing)

## Slide 39: Caching example:
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 15%
access link utilization = 99%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + usecs
problem!

## Slide 40: Caching example: fatter access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 15%
access link utilization = 99%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + usecs
origin
servers
1.54 Mbps
access link
154 Mbps
154 Mbps
msecs
Cost: increased access link speed (not cheap!)
9.9%
public
Internet
institutional
network
1 Gbps LAN

## Slide 41: Caching example: install local cache
institutional
network
1 Gbps LAN
origin
servers
1.54 Mbps
access link
local web
cache
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 15%
access link utilization = 100%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + usecs
?
?
How to compute link
utilization, delay?
Cost: web cache (cheap!)
public
Internet

## Slide 42: Caching example: install local cache
Calculating access link utilization, delay with cache:
suppose cache hit rate is 0.4
  40% requests satisfied at cache, 60% requests satisfied at origin
origin
servers
1.54 Mbps
access link
access link utilization:
  60% of requests use access link
data rate to browsers over access link
= 0.6*1.50 Mbps = .9 Mbps
  utilization = 0.9/1.54 = .58
total delay
  = 0.6 * (delay from origin servers) +0.4 * (delay when satisfied at cache)
  = 0.6 (2.01) + 0.4 (~msecs) = ~ 1.2 secs
  less than with 154 Mbps link (and cheaper too!)
public
Internet
institutional
network
1 Gbps LAN
local web
cache

## Slide 43: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
  no object transmission delay
  lower link utilization
cache: specify date of cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server

## Slide 44: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 45: Electronic mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, Thunderbird, iPhone mail client, GNUS
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 46: Electronic mail: mail servers
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
  client: sending mail server
  “server”: receiving mail server
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 47: Electronic Mail: SMTP [RFC 5321]
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction (like HTTP)
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII (boo hiss)

## Slide 48: Scenario: Alice sends message to Boris
user
agent
1) Alice uses UA to compose message “to” boris@someschool.edu
2) Alice’s UA sends message to her mail server; message placed in message queue
3) client side of SMTP opens TCP connection with Boris’s mail server
4) SMTP client sends Alice’s message over the TCP connection
5) Boris’s mail server places the message in Boris’s mailbox
6) Boris invokes his user agent to read message
mail
server
mail
server
1
2
3
4
5
6
Alice’s mail server
Bob’s mail server
user
agent

## Slide 49: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <boris@hamburger.edu>
S: 250 boris@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection

## Slide 50: Try SMTP interaction for yourself:
telnet servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT commands
above lets you send email without using email client (reader)
Important notes:
  Start by sending mail to yourself (or me)
  No verification of from address or mail headers
  This is one way spammers forge mail
  Have a bit of fun with your friends, but 7C policy prohibits forgery so be sure they’re in on the joke

## Slide 51: SMTP: (not really) final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: pull
SMTP: push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response message
SMTP: multiple objects sent in multipart message

## Slide 52: Mail message format
SMTP: protocol for exchanging email messages
RFC 822/2822/5322: standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP MAIL FROM, RCPT TO: commands!
Body: the “message”
  ASCII characters only
  …but many modern mailers are “8-bit clean”
header
body
blank
line

## Slide 53: Mail access protocols
SMTP: delivery/storage to receiver’s server
mail access protocol: retrieval from server
  POP: Post Office Protocol [RFC 1939]: authorization, download
  IMAP: Internet Mail Access Protocol [RFC 1730]: more features, including manipulation of stored messages on server
  HTTP: gmail, Hotmail, Yahoo! Mail, etc.
sender’s mail
server
SMTP
SMTP
mail access
protocol
receiver’s mail
server
(e.g., POP,
IMAP)
user
agent
user
agent

## Slide 54: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 1 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user bashir
S: +OK
C: pass still-learning
S: +OK user successfully logged on

## Slide 55: POP3 (more) and IMAP
more about POP3
previous example uses POP3 “download and delete” mode
  Bashir cannot re-read e-mail if he changes client
POP3 “download-and-keep”: copies of messages on different clients
POP3 is stateless across sessions
IMAP
keeps all messages in one place: at server
  No network  no rereading
allows user to organize messages in folders
keeps user state across sessions:
  names of folders and mappings between message IDs and folder name

## Slide 56: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 57: DNS: domain name system
people: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.yahoo.com - used by humans
Q: how to map between IP address and name, and vice versa?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity resides at network’s “edge”

## Slide 58: DNS: services, structure
why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services
hostname to IP address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
A: doesn‘t scale!

## Slide 59: DNS: a distributed, hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
client wants IP for www.amazon.com; 1st approximation:
client queries root server to find .com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
…
…

## Slide 60: DNS: root name servers
contacted by local name server that can’t resolve name
root name server:
  contacts authoritative name server if mapping not known
  gets mapping
  returns mapping to local name server
13 logical root name “servers” worldwide
each “server” replicated many times
a. Verisign, Los Angeles CA
(5 other sites)
b. USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA
(41 other sites)
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo
(5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
g. US DoD Columbus, OH (5 other sites)

## Slide 61: TLD, authoritative servers
top-level domain (TLD) servers:
  responsible for com, org, net, edu, aero, jobs, museums, and all top-level country domains, e.g.: uk, fr, ca, jp
  Network Solutions maintains servers for .com TLD
  Educause for .edu TLD
authoritative DNS servers:
  organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider
  organization can delegate subdomains (e.g., HMC delegates cs.hmc.edu to CS department)

## Slide 62: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
    every entry has expiration time
  acts as proxy, forwards query into hierarchy

## Slide 63: DNS name resolution example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
unix1.cs.umass.edu
7
8
edu DNS server
host at cis.poly.edu wants IP address for gaia.cs.umass.edu
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”

## Slide 64
4
5
6
3
recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
7
authoritative DNS server
unix1.cs.umass.edu
8
DNS name resolution example
TLD DNS
server

## Slide 65: DNS: caching, updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire
  clever sysadmins manipulate TTLs before big changes
update/notify mechanisms in proposed IETF standard (RFC 2136)

## Slide 66: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A or AAAA
  name is hostname
  value is IP[v6] address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  www.ibm.com.cs186.net
  value is canonical name
type=MX
  value is name of mailserver associated with name

## Slide 67: DNS protocol, messages
query and reply messages, both with same message format
message header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 68
name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
DNS protocol, messages
2 bytes
2 bytes

## Slide 69: Inserting records into DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into .com TLD server: (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server type A record for www.networkuptopia.com; type MX record for networkutopia.com

## Slide 70: Attacking DNS
DDoS attacks
bombard root servers with traffic
  not successful to date
  traffic filtering
  local DNS servers cache IPs of TLD servers, allowing root server bypass
bombard TLD servers
  potentially more dangerous
redirect attacks
man-in-middle
  Intercept queries
DNS poisoning
  Send bogus replies to DNS server, which caches them
exploit DNS for DDoS
send queries with spoofed source address: target IP
requires amplification

## Slide 71: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 72: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
examples:
  file distribution (BitTorrent)
  Streaming (KanKan)
  VoIP (Skype)

## Slide 73: File distribution: client-server vs P2P
Question: how much time to distribute file (size F) from one server to N peers?
  peer upload/download capacity is limited resource
us
uN
dN
server
network (with abundant
bandwidth)
file, size F
us: server upload capacity
ui: peer i upload capacity
di: peer i download capacity
u2
d2
u1
d1
di
ui

## Slide 74: File distribution time: client-server
server transmission: must sequentially send (upload) N file copies:
  time to send one copy: F/us
  time to send N copies: NF/us
increases linearly in N
time to distribute F
to N clients using
client-server approach
Dc-s > max{NF/us,,F/dmin}
client: each client must download file copy
  dmin = min client download rate
  min client download time: F/dmin
us
network
di
ui
F

## Slide 75: File distribution time: P2P
server transmission: must upload at least one copy
  time to send one copy: F/us
time to distribute F
to N clients using
P2P approach
us
network
di
ui
F
DP2P > max{F/us,,F/dmin,,NF/(us + Sui)}
client: each client must download file copy
  min client download time: F/dmin
clients: as aggregate must download NF bits
  max upload rate (limiting max download rate) is us + Sui
… but so does this, as each peer brings service capacity
increases linearly in N …

## Slide 76
Client-server vs. P2P: example
client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us

## Slide 77: P2P file distribution: BitTorrent
tracker: tracks peers
participating in torrent
torrent: group of peers exchanging chunks of a file
Sai arrives…
file divided into 256Kb chunks
peers in torrent send/receive file chunks
…obtains list
of peers from tracker
…and begins exchanging
file chunks with peers in torrent

## Slide 78
peer joining torrent:
  has no chunks, but will accumulate them over time from other peers
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
P2P file distribution: BitTorrent
while downloading, peer uploads chunks to other peers
peer may change peers with whom it exchanges chunks
churn: peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain in torrent

## Slide 79: BitTorrent: requesting, sending file chunks
requesting chunks:
at any given time, different peers have different subsets of file chunks
periodically, Sai asks each peer for list of chunks that they have
Sai requests missing chunks from peers, rarest first
sending chunks: tit-for-tat
Sai sends chunks to those four peers currently sending her chunks at highest rate
  other peers are choked by Sai (do not receive chunks from her)
  re-evaluate top 4 every 10 secs
every 30 secs: randomly select another peer, start sending chunks
  “optimistically unchoke” this peer
  newly chosen peer may join top 4

## Slide 80: BitTorrent: tit-for-tat
(1) Sai “optimistically unchokes” Michel
(2) Sai becomes one of Michel’s top-four providers; Michel reciprocates
(3) Michel becomes one of Sai’s top-four providers
higher upload rate: find better trading partners, get file faster !

## Slide 81: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks (CDNs)
2.7 socket programming with UDP and TCP

## Slide 82: Video Streaming and CDNs: context
  Netflix, YouTube: 37%, 16% of downstream residential ISP traffic
  ~1B YouTube users, ~75M Netflix users
challenge: scale—how to reach ~1B users?
  single massive video server won’t work (why?)
challenge: heterogeneity
  different users have different capabilities (e.g., wired versus mobile; bandwidth-rich versus bandwidth-poor)
solution: distributed, application-level infrastructure
video traffic: major consumer of Internet bandwidth

## Slide 83: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 84: Multimedia: video
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, < 1 Mbps)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 85: Streaming stored video:
simple scenario:
video server
(stored video)
client
Internet

## Slide 86: Streaming multimedia: DASH
DASH: Dynamic, Adaptive Streaming over HTTP
server:
  divides video file into multiple chunks
  each chunk stored, encoded at different rates
  manifest file: provides URLs for different chunks
client:
  periodically measures server-to-client bandwidth
  consulting manifest, requests one chunk at a time
    chooses maximum coding rate sustainable given current bandwidth
    can choose different coding rates at different points in time (depending on available bandwidth at time)

## Slide 87: Streaming multimedia: DASH
DASH: Dynamic, Adaptive Streaming over HTTP
“intelligence” at client: client determines
  when to request chunk (so that buffer starvation or overflow does not occur)
  what encoding rate to request (higher quality when more bandwidth available)
  where to request chunk (can request from server that is “close” to client or has high available bandwidth)

## Slide 88: Content distribution networks
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
option 1: single, large “mega-server”
  single point of failure
  point of network congestion
  long path to distant clients
  multiple copies of video sent over outgoing link
….quite simply: this solution doesn’t scale

## Slide 89: Content distribution networks
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
option 2: store/serve multiple copies of videos at multiple geographically distributed sites (CDN)
  enter deep: push CDN servers deep into many access networks
    close to users
    used by Akamai, 1700 locations
  bring home: smaller number (10’s) of larger clusters in POPs near (but not within) access networks
    used by Limelight

## Slide 90
Content Distribution Networks (CDNs)
…
…
…
…
…
…
subscriber requests content from CDN
CDN: stores copies of content at CDN nodes
  e.g. Netflix stores copies of Mad Men
where’s Mad Men?
manifest file
  directed to nearby copy, retrieves content
  may choose different copy if network path congested
Notes: 90
Akamai: 100,000+ servers in 1000+ clusters in 1000+ networks in 70+ countries serving trillions of requests a day.
How many people use Netflix?

## Slide 91
Content Distribution Networks (CDNs)
…
…
…
…
…
…
Internet host-to-host communication as a service
OTT challenges: coping with a congested Internet
  from which CDN node to retrieve content?
  viewer behavior in presence of congestion?
  what content to place in which CDN node?
“over the top”
more ... in chapter 9
Notes: 91
peak load: 7million viewers, 2 Tbytes via

## Slide 92: CDN content access: a closer look
Rolf (client) requests video http://netcinema.com/6Y7B23V
video stored in CDN at http://KingCDN.com/NetC6y&B23V
netcinema.com
KingCDN.com
1
1. Rolf gets URL for video http://netcinema.com/6Y7B23V
from netcinema.com web page
2
2. resolve http://netcinema.com/6Y7B23V
via Rolf’s local DNS
netcinema’s
authoratative DNS
3
3. netcinema’s DNS returns URL
http://KingCDN.com/NetC6y&B23V
4
4&5. Resolve
http://KingCDN.com/NetC6y&B23
via KingCDN’s authoritative DNS,
which returns IP address of KingCDN
server with video
5
6. request video from
KINGCDN server,
streamed via HTTP
KingCDN
authoritative DNS
Rolf’s
local DNS
server

## Slide 93: Case study: Netflix
1
1. Rolf manages Netflix account
Netflix registration,
accounting servers
Amazon cloud
CDN
server
2
2. Rolf browses
Netflix video
3
3. Manifest file
returned for
requested video
4. DASH streaming
upload copies of multiple versions of video to CDN servers
CDN
server
CDN
server

## Slide 94: Chapter 2: outline
2.1 principles of network applications
2.2 Web and HTTP
2.3 electronic mail
  SMTP, POP3, IMAP
2.4 DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 95: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 96: Socket programming
  Two socket types for two transport services:
  UDP: unreliable datagram
  TCP: reliable, byte stream-oriented
  Application Example:
client reads a line of characters (data) from its keyboard and sends data to server
server receives the data and converts characters to uppercase
server sends modified data to client
client receives modified data and displays line on its screen

## Slide 97: Socket programming with UDP
UDP: no “connection” between client & server
no handshaking before sending data
sender explicitly attaches IP destination address and port number to each packet
receiver extracts sender IP address and port number from received packet
UDP: transmitted data may be lost or received out-of-order
Application viewpoint:
UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server

## Slide 98: Client/server socket interaction: UDP
close
clientSocket
read datagram from
clientSocket
create socket:
clientSocket =
socket(AF_INET, SOCK_DGRAM)
Create datagram with server IP and
port=x; send datagram via clientSocket
create socket, port = x:
serverSocket =
socket(AF_INET, SOCK_DGRAM)
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number
Application 2-98
server (running on serverIP)
client

## Slide 99
Example app: UDP client
from socket import *
serverName = ‘hostname’
serverPort = 12000
clientSocket = socket(AF_INET,
SOCK_DGRAM)
message = input('Type lowercase sentence: ')
clientSocket.sendto(message.encode(),
(serverName, serverPort))
modifiedMessage, serverAddress =
clientSocket.recvfrom(2048)
print modifiedMessage.decode()
clientSocket.close()
Python3 UDP Client
include Python’s socket
library
create UDP socket for server
get user keyboard
input
Attach server name, port to message; send into socket
print out received string and close socket
read reply characters from
socket into string

## Slide 100
Example app: UDP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET, SOCK_DGRAM)
serverSocket.bind(('', serverPort))
print("The server is ready to receive")
while True:
message, clientAddress = serverSocket.recvfrom(2048)
modifiedMessage = message.decode().upper()
serverSocket.sendto(modifiedMessage.encode(),
clientAddress)
Python3 UDP Server
create UDP socket
bind socket to local port number 12000
loop forever
Read from UDP socket into message, getting client’s address (client IP and port)
send uppercase string back to this client

## Slide 101: Socket programming with TCP
client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
client contacts server by:
Creating TCP socket, specifying IP address, port number of server process
when client creates socket: client TCP establishes connection to server TCP
when contacted by client, server TCP creates new socket for server process to communicate with that particular client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
byte-stream transfer (“pipe”)
between client and server
application viewpoint:

## Slide 102: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
serverSocket.accept()
create socket,
port = x, for incoming request:
serverSocket = socket()
serverSocket.listen()
create socket,
connect to hostip, port=x
clientSocket = socket()
clientSocket.connect()
server (running on hostip)
client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket

## Slide 103
Example app: TCP client
from socket import *
serverName = ’servername’
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName, serverPort))
sentence = input('Type lowercase sentence: ')
clientSocket.sendall(sentence.encode())
modifiedSentence = clientSocket.recv(1024)
print ('From server:', modifiedSentence.decode())
clientSocket.close()
Python3 TCP Client
create TCP socket for server, remote port 12000
No need to attach server name, port

## Slide 104
Example app: TCP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET, SOCK_STREAM)
serverSocket.bind(('', serverPort))
serverSocket.listen(1)
print("The server is ready to receive")
while True:
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024).decode()
capitalizedSentence = sentence.upper()
connectionSocket.sendall(capitalizedSentence.
encode())
connectionSocket.close()
Python3 TCP Server
create TCP welcoming
socket
server begins listening for incoming TCP requests
loop forever
server waits on accept()
for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this client (but not the welcoming socket)

## Slide 105: Chapter 2: summary
application architectures
  client-server
  P2P
application service requirements:
  reliability, bandwidth, delay
Internet transport service model
  connection-oriented, reliable: TCP
  unreliable, datagrams: UDP
our study of network apps now complete!
specific protocols:
  HTTP
  SMTP, POP, IMAP
  DNS
  P2P: BitTorrent
video streaming, CDNs
socket programming:
TCP, UDP sockets

## Slide 106
typical request/reply message exchange:
  client requests info or service
  server responds with data, status code
message formats:
  headers: fields giving info about data
  data: info(payload) being communicated
important themes:
control vs. messages
  in-band, out-of-band
centralized vs. decentralized
stateless vs. stateful
reliable vs. unreliable message transfer
“complexity at network edge”
Chapter 2: summary
most importantly: learned about protocols!