## Slide 1: Machine-Level Programming IV: Structured Data
Topics
  Arrays
  Structs
  Unions
CS 105
“Tour of the Black Holes of Computing”

## Slide 2: Basic Data Types
Integral
  Stored & operated on in general registers
  Signed vs. unsigned depends on instructions used
    Intel GAS Bytes C
    byte b 1 [unsigned] char
    word w 2 [unsigned] short
    double word l 4 [unsigned] int
    quad word q 8 [unsigned] long
Floating Point
  Stored & operated on in floating point registers
    Intel GAS Bytes C
    Single s 4 float
    Double l 8 double

## Slide 3: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes in memory
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 8
x + 16
x + 24

## Slide 4: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0
Reference Type Value
  val[4] int 3
  val int[5] x (acts like int *)
  val+1 int * x + 4
  &val[2] int * x + 8
  val[5] int ??
  *(val+1) int 5
  val + i int * x + 4 i
1
5
2
1
3
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 5: Array Example
Notes
  Declaration “zip_dig cmu” equivalent to “int cmu[5]”
  Example arrays were allocated in successive 20-byte blocks
    Not guaranteed to happen in general
typedef int zip_dig[5];
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig hmc = { 9, 1, 7, 1, 1 };
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig hmc;
9
1
7
1
1
56
60
64
68
72
76

## Slide 6: Array Accessing Example
Register %rdi contains starting address of array
Register %rsi contains array index
Desired digit at %rdi + 4*%rsi
Use memory reference (%rdi,%rsi,4)
int get_digit
(zip_dig z, int digit)
{
return z[digit];
}
# %rdi = z
# %rsi = digit
movl (%rdi,%rsi,4), %eax # z[digit]
x86-64
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36

## Slide 7: Referencing Examples
Code Does Not Do Any Bounds Checking!
Reference Address Value Guaranteed?
  mit[3] 36 + 4* 3 = 48 3
  mit[5] 36 + 4* 5 = 56 9
  mit[-1] 36 + 4*-1 = 32 3
  cmu[15] 16 + 4*15 = 76 ??
  Out-of-range behavior implementation-dependent
    No guaranteed relative allocation of different arrays
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig hmc;
9
1
7
1
1
56
60
64
68
72
76
Yes
No
No
No

## Slide 8: Referencing Examples
Code Does Not Do Any Bounds Checking!
Reference Address Value Guaranteed?
  mit[3] 36 + 4* 3 = 48 3
  mit[5] 36 + 4* 5 = 56 9
  mit[-1] 36 + 4*-1 = 32 3
  cmu[15] 16 + 4*15 = 76 ??
  Out-of-range behavior implementation-dependent
    No guaranteed relative allocation of different arrays
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig hmc;
9
1
7
1
1
56
60
64
68
72
76

## Slide 9: Array Loop Example
# %rdi = z
movl $0, %eax # i = 0
jmp .L3 # goto middle
.L4: # loop:
addl $1, (%rdi,%rax,4) # z[i]++
addq $1, %rax # i++
.L3: # middle
cmpq $4, %rax # i:4
jbe .L4 # if <=, goto loop
rep; ret
void zincr(zip_dig z) {
size_t i;
for (i = 0; i < ZLEN; i++)
z[i]++;
}

## Slide 10: Multidimensional (Nested) Arrays
Declaration
  T A[R][C];
  2D array of data type T
  R rows, C columns
  Type T element requires K bytes
Array Size
  R * C * K bytes
Arrangement
  Row-Major Ordering
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
int A[R][C];
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C Bytes
Notes: Board: show 3D example: a[2][3][2] to illustrate the idea of row major as enumerating indices from right to left

## Slide 11: Nested Array Example
“zip_dig pgh[4]” equivalent to “int pgh[4][5]”
  Variable pgh: array of 4 elements, allocated contiguously
  Each element is an array of 5 int’s, allocated contiguously
“Row-Major” ordering of all elements in memory
#define PCOUNT 4
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
zip_dig
pgh[4];
76
96
116
136
156
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1

## Slide 12: Nested Array Row Access
• • •
Row Vectors
  A[i] is array of C elements
  Each element of type T requires K bytes
  Starting address A + i * (C * K)
• • •
A
[i]
[0]
A
[i]
[C-1]
A[i]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
A[R-1]
• • •
A
• • •
A
[0]
[0]
A
[0]
[C-1]
A[0]
A+(i*C*4)
A+((R-1)*C*4)
int A[R][C];

## Slide 13: Nested Array Element Access
• • •
Array Elements
  A[i][j] is element of type T, which requires K bytes
  Address A + i * (C * K) + j * K = A + (i * C + j) * K
• • •
A
[i]
[j]
• • •
A[i]
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
A[R-1]
• • •
A
A
[0]
[0]
A
[0]
[C-1]
• • •
A[0]
int A[R][C];
A+i*C*4
A+(R-1)*C*4
A+(i*C+j)*4

## Slide 14: Strange Referencing Examples
Reference Address Value Guaranteed?
  pgh[3][3] 76+20*3+4*3 = 148 2
  pgh[2][5] 76+20*2+4*5 = 136 1
  pgh[2][-1] 76+20*2+4*-1 = 112 3
  pgh[4][-1] 76+20*4+4*-1 = 152 1
  pgh[0][19] 76+20*0+4*19 = 152 1
  pgh[0][-1] 76+20*0+4*-1 = 72 ??
  Code does not do any bounds checking
  Ordering of elements within array guaranteed
zip_dig
pgh[4];
76
96
116
136
156
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
Yes
Yes
Yes
Yes
Yes
No

## Slide 15: Strange Referencing Examples
Reference Address Value Guaranteed?
  pgh[3][3] 76+20*3+4*3 = 148 2
  pgh[2][5] 76+20*2+4*5 = 136 1
  pgh[2][-1] 76+20*2+4*-1 = 112 3
  pgh[4][-1] 76+20*4+4*-1 = 152 1
  pgh[0][19] 76+20*0+4*19 = 152 1
  pgh[0][-1] 76+20*0+4*-1 = 72 ??
  Code does not do any bounds checking
  Ordering of elements within array guaranteed
zip_dig
pgh[4];
76
96
116
136
156
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1

## Slide 16: Multi-Level Array Example
  Variable univ denotes array of 3 elements
  Each element is a pointer
    4 bytes
  Each pointer points to array of int’s
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig hmc = { 9, 1, 7, 1, 1 };
#define UCOUNT 3
int *univ[UCOUNT] = {mit, cmu, hmc};
36
160
16
56
168
176
univ
cmu
1
5
2
1
3
16
20
24
28
32
36
mit
0
2
1
3
9
36
40
44
48
52
56
hmc
9
1
7
1
1
56
60
64
68
72
76

## Slide 17: Element Access in Multi-Level Array
Computation
  Element access Mem[Mem[univ+8*index]+4*digit]
  Must do two memory reads
    First get pointer to row array
    Then access element within array
salq $2, %rsi # 4*digit
addq univ(,%rdi,8), %rsi # p = univ[index] + 4*digit
movl (%rsi), %eax # return *p
ret
int get_univ_digit
(size_t index, size_t digit)
{
return univ[index][digit];
}

## Slide 18: Array Element Accesses
  Similar C references
Nested Array
  Element at
  Mem[pgh+20*index+4*dig]
  Different address computation
Multi-Level Array
  Element at
  Mem[Mem[univ+4*index]+4*dig]
int get_pgh_digit
(int index, int dig)
{
return pgh[index][dig];
}
int get_univ_digit
(int index, int dig)
{
return univ[index][dig];
}
36
160
16
56
168
176
univ
cmu
1
5
2
1
3
16
20
24
28
32
36
mit
0
2
1
3
9
36
40
44
48
52
56
ucb
9
4
7
2
0
56
60
64
68
72
76
36
160
16
56
univ
36
16
56
univ
cmu
1
5
2
1
3
16
20
24
28
32
36
1
5
2
1
3
1
5
2
1
3
16
20
24
28
32
36
mit
0
2
1
3
9
36
40
44
48
52
56
0
2
1
3
9
0
2
1
3
9
36
40
44
48
52
56
hmc
9
4
7
2
0
56
60
64
68
72
76
9
4
7
2
0
9
1
7
1
1
56
60
64
68
72
76

## Slide 19: Strange Referencing Examples
Reference Address Value Guaranteed?
  univ[2][3] 56+4*3 = 68 1
  univ[1][5] 16+4*5 = 36 0
  univ[2][-1] 56+4*-1 = 52 9
  univ[3][-1] ?? ??
  univ[1][12] 16+4*12 = 64 7
  Code does not do any bounds checking
  Ordering of elements in different arrays not guaranteed
36
160
16
56
168
176
univ
cmu
1
5
2
1
3
16
20
24
28
32
36
mit
0
2
1
3
9
36
40
44
48
52
56
hmc
9
1
7
1
1
56
60
64
68
72
76
Yes
No
No
No
No

## Slide 20: Strange Referencing Examples
Reference Address Value Guaranteed?
  univ[2][3] 56+4*3 = 68 1
  univ[1][5] 16+4*5 = 36 0
  univ[2][-1] 56+4*-1 = 52 9
  univ[3][-1] ?? ??
  univ[1][12] 16+4*12 = 64 7
  Code does not do any bounds checking
  Ordering of elements in different arrays not guaranteed
36
160
16
56
168
176
univ
cmu
1
5
2
1
3
16
20
24
28
32
36
mit
0
2
1
3
9
36
40
44
48
52
56
hmc
9
1
7
1
1
56
60
64
68
72
76

## Slide 21: N X N Matrix Code
Fixed dimensions
  Know value of N at compile time
Variable dimensions, explicit indexing
  Traditional way to implement dynamic arrays
Variable dimensions, implicit indexing
  Now supported by gcc
#define N 16
typedef int fix_matrix[N][N];
/* Get element a[i][j] */
int fix_ele(fix_matrix a,
size_t i, size_t j)
{
return a[i][j];
}
#define IDX(n, i, j) ((i)*(n)+(j))
/* Get element a[i][j] */
int vec_ele(size_t n, int *a,
size_t i, size_t j)
{
return a[IDX(n,i,j)];
}
/* Get element a[i][j] */
int var_ele(size_t n, int a[n][n],
size_t i, size_t j) {
return a[i][j];
}

## Slide 22: 16 X 16 Matrix Access
/* Get element a[i][j] */
int fix_ele(fix_matrix a, size_t i, size_t j) {
return a[i][j];
}
# a in %rdi, i in %rsi, j in %rdx
salq $6, %rsi # 64*i
addq %rsi, %rdi # a + 64*i
movl (%rdi,%rdx,4), %eax # M[a + 64*i + 4*j]
ret
Array Elements
  Address A + i * (C * K) + j * K
  C = 16, K = 4

## Slide 23: n X n Matrix Access
/* Get element a[i][j] */
int var_ele(size_t n, int a[n][n], size_t i, size_t j) {
return a[i][j];
}
# n in %rdi, a in %rsi, i in %rdx, j in %rcx
imulq %rdx, %rdi # n*i
leaq (%rsi,%rdi,4), %rax # a + 4*n*i
movl (%rax,%rcx,4), %eax # a + 4*n*i + 4*j
ret
Array Elements
  Address A + i * (C * K) + j * K
  C = n, K = 4
  Must perform integer multiplication

## Slide 24: Structure Representation
Structure represented as block of memory
  Big enough to hold all of the fields
Fields ordered according to declaration
  Even if another ordering could yield a more compact representation
Compiler determines overall size + positions of fields
  Machine-level program has no understanding of the structures in the source code
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 25: Generating Pointer to Structure Member
# r in %rdi, idx in %rsi
leaq (%rdi,%rsi,4), %rax
ret
int *get_ap
(struct rec *r, size_t idx)
{
return &r->a[idx];
}
Generating Pointer to Array Element
  Offset of each structure member determined at compile time
  Compute as r + 4*idx
r+4*idx
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 26: Following Linked List
.L11: # loop:
movslq 16(%rdi), %rax # i = M[r+16]
movl %esi, (%rdi,%rax,4) # M[r+4*i] = val
movq 24(%rdi), %rdi # r = M[r+24]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r != NULL) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
C Code
Register | Value
%rdi | r
%rsi | val
struct rec {
int a[3];
int i;
struct rec *next;
};
Element i
r
i
next
0
16
24
32
a

## Slide 27: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
  Required on some machines; advised on x86-64
Motivation for Aligning Data
  Memory accessed by (aligned) chunks of 4 or 8 bytes (system dependent)
    Inefficient to load or store datum that spans quad word boundaries
    Virtual memory trickier when datum spans 2 pages
Compiler
  Inserts gaps in structure to ensure correct alignment of fields

## Slide 28: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;

## Slide 29: Specific Cases of Alignment (x86-64)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, …
  lowest 2 bits of address must be 002
8 bytes: double, long, char *, …
  lowest 3 bits of address must be 0002
16 bytes: long double (GCC on Linux)
  lowest 4 bits of address must be 00002

## Slide 30: Satisfying Alignment within Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure:
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example:
  K = 8, due to double element
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 31: Meeting Overall Alignment Requirement
For largest alignment requirement K
Overall structure must be multiple of K
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
Multiple of K=8

## Slide 32: Arrays of Structures
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 

## Slide 33: Accessing Array Elements
Compute array offset 12*idx
  sizeof(S3), including alignment spacers
Element j is at offset 8 within structure
Assembler gives offset a+8
  Resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %rdi = idx
leaq (%rdi,%rdi,2),%rax # 3*idx
movzwl a+8(,%rax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[idx] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12*idx |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | i | 2 bytes |  | v |  |  | j | 2 bytes |  |  | 
 |  |  |  | a+12*idx |  |  |  |  |  | a+12*idx+8 |  |  |  |  | 

## Slide 34: Saving Space
Put large data types first
Effect (K=4)
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes

## Slide 35: Union Allocation
Allocate according to largest element
Can only use one field at a time
union U1 {
char c;
int i[2];
double v;
} *up;
struct S1 {
char c;
int i[2];
double v;
} *sp;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  | v |  |  |  |  |  | 
sp+0 |  |  |  | sp+4 |  |  |  | sp+8 |  |  |  |  |  |  | sp+16 |  |  |  |  |  | sp+24 | 
 | c |  |  |  |  |  |  |  | 
 | i[0] |  |  |  | i[1] |  |  |  | 
 | v |  |  |  |  |  |  |  | 
up+0 |  |  | up+4 |  |  |  |  | up+8 | 

## Slide 36: Using Union to Access Bit Patterns
typedef union {
float f;
unsigned u;
} bit_float_t;
float bit2float(unsigned u) {
bit_float_t arg;
arg.u = u;
return arg.f;
}
unsigned float2bit(float f) {
bit_float_t arg;
arg.f = f;
return arg.u;
}
Same as (float) u ?
Same as (unsigned) f ?
 | u |  |  |  | 
 | f |  |  |  | 
0 |  |  |  | 4 | 

## Slide 37: Byte Ordering Revisited
Idea
  Short/long/quad words stored in memory as 2/4/8 consecutive bytes
  Which byte is most (least) significant?
  Can cause problems when exchanging binary data between machines
Big Endian
  Most significant byte has lowest address
  Sparc
Little Endian
  Least significant byte has lowest address
  Intel x86, ARM Android and IOS
Bi Endian
  Can be configured either way
  ARM

## Slide 38: Byte Ordering Example
union {
unsigned char c[8];
unsigned short s[4];
unsigned int i[2];
unsigned long l[1];
} dw;
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
32-bit
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
64-bit

## Slide 39: Byte Ordering Example (Cont).
int j;
for (j = 0; j < 8; j++)
dw.c[j] = 0xf0 + j;
printf("Characters 0-7 == [0x%x,0x%x,0x%x,0x%x,0x%x,0x%x,0x%x,0x%x]\n",
dw.c[0], dw.c[1], dw.c[2], dw.c[3],
dw.c[4], dw.c[5], dw.c[6], dw.c[7]);
printf("Shorts 0-3 == [0x%x,0x%x,0x%x,0x%x]\n",
dw.s[0], dw.s[1], dw.s[2], dw.s[3]);
printf("Ints 0-1 == [0x%x,0x%x]\n",
dw.i[0], dw.i[1]);
printf("Long 0 == [0x%lx]\n",
dw.l[0]);

## Slide 40: Byte Ordering on Sun
Big Endian
Characters 0-7 == [0xf0,0xf1,0xf2,0xf3,0xf4,0xf5,0xf6,0xf7]
Shorts 0-3 == [0xf0f1,0xf2f3,0xf4f5,0xf6f7]
Ints 0-1 == [0xf0f1f2f3,0xf4f5f6f7]
Long 0 == [0xf0f1f2f3]
Output on Sun:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
MSB
LSB
MSB
LSB
Print

## Slide 41: Byte Ordering on x86-64
Little Endian
Characters 0-7 == [0xf0,0xf1,0xf2,0xf3,0xf4,0xf5,0xf6,0xf7]
Shorts 0-3 == [0xf1f0,0xf3f2,0xf5f4,0xf7f6]
Ints 0-1 == [0xf3f2f1f0,0xf7f6f5f4]
Long 0 == [0xf7f6f5f4f3f2f1f0]
Output on x86-64:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
LSB
MSB
Print

## Slide 42: Summary of Compound Types in C
Arrays
  Contiguous allocation of memory
  Aligned to satisfy every element’s alignment requirement
  Pointer to first element
  No bounds checking
Structures
  Allocate bytes in order declared
  Pad in middle and at end to satisfy alignment
Unions
  Overlay declarations
  Way to circumvent type system