## Slide 1: File Systems
Topics
  Design criteria
  History of file systems
  Berkeley Fast File System
  Effect of file systems on programs
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: File Systems: Disk Organization
A disk is a sequence of 4096-byte sectors or blocks
  Used to be 512 bytes
  Backwards compatibility is problematic
First comes boot block and partition table
Partition table divides the rest of disk into partitions
  May appear to operating system as logical “disks”
  Useful for multiple OSes, etc.
  Otherwise bad idea; hangover from earlier days
File system: partition structured to hold files (of data)
  May aggregate blocks into segments or clusters
  Typical size: 8K–128M bytes
  Increases efficiency by reducing overhead

## Slide 3: Disk Geometry
Disks consist of stacked platters, each with two surfaces
Each surface consists of concentric rings called tracks
Each track consists of sectors separated by gaps
spindle
surface
tracks
track k
sectors
gaps

## Slide 4: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder (this view is outdated)
surface 0
surface 1
surface 2
surface 3
surface 4
surface 5
cylinder k
spindle
platter 0
platter 1
platter 2

## Slide 5: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
spindle
By moving radially, arm can position read/write head over any track
Read/write head
is attached to end
of the arm and flies over
disk surface on
thin cushion of air
spindle

## Slide 6: Disk Operation (Multi-Platter View)
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 7: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tseek)
  Time to position heads over cylinder containing target sector
  Typical Tseek = 9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min

## Slide 8: Disk Access Time Example
Given:
  Rotational rate = 7200 RPM (typical desktop; laptops are 5400)
  Average seek time = 9 ms
  Avg # sectors/track = 400
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency
  First bit in a sector is the most expensive, the rest are “free”
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM, and
    2,500 times slower then DRAM

## Slide 9: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller (partly on motherboard, mostly in disk itself)
  Converts requests for logical blocks into (surface,track,sector) triples
Allows controller to set aside spare cylinders for each zone
  Accounts for (some of) the difference in “formatted capacity” and “maximum capacity”

## Slide 10: Aside: Solid-State Disks
They aren’t disks! But for backwards compatibility they pretend to be…
SSDs are divided into erase blocks made up of pages
  Typical page: 4K-8K bytes
  Typical erase block: 128K-512K
Can only change bits from 1 to 0 when writing
  Erase sets entire block to all 1’s
  Erase is slow
  Can only erase 104 to 106 times
  Must pre-plan erases and manage wear-out
Net result:
  Reads are fast (and almost truly random-access)
  Writes are 100X slower (and have weird side effects)

## Slide 11: Design Problems
So, disks have mechanical delays (and SSDs have their own strange behaviors)
Fundamental problem in file-system design: how to hide (or at least minimize) these delays?
Side problems also critical:
  Making things reliable (in face of s/w and h/w failures)
    People frown on losing data
  Organizing data (e.g., in directories or databases)
    Not finding stuff is almost as bad as losing it
  Enforcing security
    System should only share what you want to share

## Slide 12: Important File Systems
FAT: old Windows and MSDOS standard
NTFS: Windows current standard
FFS: Unix standard since 80’s
AFS: distributed system developed at CMU
LFS: Berkeley redesign for high performance
ZFS: redesigned Unix system, recently released by Sun
ISO 9660: CD-ROM standard
EXT2/EXT3/EXT4: Linux standards, variants of FFS
BtrFS: new Linux kid on the block
Other OS’s have own file organization: VMS, MVS, 

## Slide 13: Typical Similarities Among File Systems
A (secondary) boot record
A top-level directory
Support for hierarchical directories
Management of free and used space
Metadata about files (e.g., creation date)
Protection and security

## Slide 14: Typical Differences Between File Systems
Naming conventions: case, length, special symbols
File size and placement
Speed
Error recovery
Metadata details
Support for special files
Snapshot support

## Slide 15: Case Study: Berkeley Fast File System (FFS)
First public Unix (Unix V7) introduced many important concepts in Unix File System (UFS)
  I-nodes
  Indirect blocks
  Unix directory structure and permissions system
UFS was simple, elegant, and slow
Berkeley initiated project to solve the slowness
Many modern file systems are direct or indirect descendants of FFS
  In particular, EXT2 through EXT4

## Slide 16: FFS Headers
Boot block: first few sectors
  Typically all of cylinder 0 is reserved for boot blocks, partition tables, etc.
Superblock: file system parameters, including
  Size of partition (note that this is dangerously redundant)
  Location of root directory
  Block size
Cylinder groups, each including
  Data blocks
  List of inodes
  Bitmap of used blocks and fragments in the group
  Replica of superblock (not always at start of group)

## Slide 17: FFS File Tracking
Directory: file containing variable-length records
  File name
  I-node number
Inode: holds metadata for one file
  Fixed size
  Located by number, using info from superblock
  Integral number of inodes in a block
  Includes
    Owner and group
    File type (regular, directory, pipe, symbolic link, …)
    Access permissions
    Time of last i-node change, last modification, last access
    Number of links (reference count)
    Size of file (for directories and regular files)
    Pointers to data blocks
  Except for pointers, precisely what’s in stat data structure

## Slide 18: FFS Inodes
Inode has 15 pointers to data blocks
  12 point directly to data blocks
  13th points to an indirect block, containing pointers to data blocks
  14th points to a double indirect block
  15th points to a triple indirect block
With 4K blocks and 4-byte pointers, the triple indirect block can address 4 terabytes (242 bytes) in one file
Data blocks might not be contiguous on disk
But OS tries to cluster related items in cylinder group:
  Directory entries
  Corresponding inodes
  Their data blocks
Notes: With 4K blocks and 8-byte pointers, triple indirect can address only 0.5 TB. But 8K and 8-byte gives 8 TB. Some new FSes have quad indirect blocks.

## Slide 19: FFS Free-Space Management
Free space managed by bitmaps
  One bit per block
  Makes it easy to find groups of contiguous blocks
Each cylinder group has own bitmap
  Can find blocks that are physically nearby
  Prevents long scans on full disks
Prefer to allocate block in cylinder group of last previous block
  If can’t, pick group that has most space
  Heuristic tries to maximize number of blocks close to each other

## Slide 20: FFS Fragmentation
Blocks are typically 4K or 8K
  Sector size was only 512
  Amortizes overhead of reading or writing block
  On average, wastes 1/2 block (total) per file
FFS divides blocks into 4-16 fragments
  Free space bitmap manages fragments
  Small files, or tails of files, are placed in fragments
  This turned out to be bad idea
    Complicates OS code
    Didn’t foresee how big disks would get
Linux EXT2/3/4 uses smaller block size (typically 4K) instead of fragments

## Slide 21: File Systems and Data Structures
Almost every data structure you can think of is present in FFS:
  Arrays (of blocks and i-nodes)
  Variable-length records (in directories)
  Heterogeneous records
  Indirection (directories and inodes)
  Reference counting
  Lists (inodes in different cylinder groups)
  Trees (indirect data blocks)
  Bitmaps (free space management)
  Caching

## Slide 22: Effect of File Systems on Programs
Software can take advantage of FFS design
  Small files are cheap: spread data across many files
  Directories are cheap: use as key/value database where file name is the key
  Large files well supported: don’t worry about file-size limits
  Random access adds little overhead: OK to store database inside large file
    But don’t forget you’re still paying for disk latencies and indirect blocks!
FFS design also suggests optimizations
  Put related files in single directory
  Keep directories relatively small
  Recognize that single large file will eat much remaining free space in cylinder group
    Create small files before large ones

## Slide 23: The Crash Problem
File system data structures are interrelated
  Free map implies which blocks do/don’t have data
  Inodes and indirect blocks list data blocks
  Directories imply which inodes are allocated/free
  All live in different places on disk
  Which to update first?
Crash in between updates means inconsistencies
  Block listed as free but really allocated will get reused
  Block listed as allocated but really free means space leak
  Allocated inode without directory listing means lost file

## Slide 24: File System Checking
Traditional solution: verify all structures after a crash
  Look through files to find out what blocks are in use
  Look through directories to find used inodes
  Fix all inconsistencies, put lost files in “lost+found”
Problem: takes a long time
  Following directory tree means random access
  Following indirect blocks is also random
  Random == slow
  Huge modern disks  hours or even days to verify
    System can’t be used during check

## Slide 25: Journaled File Systems
One (not only) solution to checking problem
  Before making change, write intentions to journal
    “I plan to allocate block 42, give it to inode 47, put that in directory entry foo”
    Journal writes are carefully kept in single block  atomic
  After making changes, append “I’m done” to journal
Post-crash journal recovery
  Journal is sequential and fairly small  fast scanning
  Search for last “I’m done” record
  Re-apply any changes past that point
    Atomicity means they can’t be partial
    All changes are arranged to be idempotent
  Write an “I’m done” in case of another crash

## Slide 26: Summary: Goals of Unix File Systems
Simple data model
  Hierarchical directory tree
  Uninterpreted (by OS) sequences of bytes
  Extensions are just strings in long filename
Multiuser protection model
High speed
  Reduce disk latencies by careful layout
  Hide latencies with caching
  Amortize overhead with large transfers
  Sometimes trade off reliability for speed