## Slide 1: CS 1012 Today
Weather: Temperatures around 11000002 F
Sports: CS Professor runs 1002 meter dash in under 310 seconds!
News Briefs
Spam proven to
be even healthier
than chocolate
(page 11001012)
Hoch-Shanahan
to use Spam in
all its dishes
(page 10001012)
Proof of Spam’s
merits proven to
be false
(page 1101012)
Harvey Mudd to adopt Base 2 as Official Number System
(Claremont, AP): Harvey Mudd College, a small science and engineering college in Los Angeles county, has announced that it will henceforth exclusively use base 2. “One obvious advantage is that there will now be 11000 hours in each day.” said a CS professor who first proposed that the college adopt the binary system. Other professors happily noticed that their monthly paychecks are now on the order of $1000000000000.
Students too were excited that they would be able to take 10000 units per semester without overloading. However, one disgruntled student complained that he flexed a friend into the dining hall and he was charged over $110 for the meal. “The food here is good, but $110 for lunch is outrageous!”
Notes: <number>

## Slide 2: A True Story…
Donald Gillies Sr.
A prime example of Gillies’ work!
How big is 211213 ?
Notes: <number>

## Slide 3: Computing Digitally
Adder
5
3
1012
112
10002
8
I would pay anything for such a nice blue box!
Multiplier
CPU
Notes: <number>

## Slide 4: From Description to Circuit!
Words Table Formula
f is a function of TWO binary (Boolean) variables s.t. the output is 1 if and only if exactly one of the two inputs is 1
x y f(x,y)
0 0 0
0 1 1
1 0 1
1 1 0
xy + xy
Circuit
x
y
Abstract
Concrete
That is nothin’ but a two-bit adder!
actually, it’s called a 1-bit adder!
Notes: <number>
One might prefer to draw this circuit by hand on the board or in classroom presenter!

## Slide 5: Digital Logic Gates
x NOT x
0 1 1 0
x y x AND y
0 0 0
0 1 0
1 0 0
1 1 1
x y x OR y
0 0 0
0 1 1
1 0 1
1 1 1
Also written
x
Also written
xy
Also written
x+y
x
y
x
x
y
x
x AND y
x OR y
Notes: <number>

## Slide 6: Try building circuits for these…
x y output
0 0 1
0 1 0
1 0 0
1 1 0
x y output
0 0 1
0 1 0
1 0 0
1 1 1
Circuit 1
Circuit 2
x NOT x
0 1 1 0
x
x
x y x AND y
0 0 0
0 1 0
1 0 0
1 1 1
y
x
x AND y
xy
x y x OR y
0 0 0
0 1 1
1 0 1
1 1 1
y
x
x OR y
x+y
Notes: <number>

## Slide 7: Try This One (In your notes)…
Consider this function…
Words Truth Table Formula
A function of
THREE binary
inputs x,y,z
where the
output is 1 iff
the number of 1’s
is odd
Circuit
This is called an “odd” “parity” circuit.
Just cuz it’s odd doesn’t mean you should parity it!
x y z
output
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 0
1 1 0 0
1 1 1 1
Notes: <number>
Students draw the circuit. Then, instructor draws circuit. Show “pretty” drawing convention in which each input and its negation are connected to a “long” line so that the input can be “tapped” from the line. Suggest that this is a nice way to draw circuits in general.

## Slide 8: A Circuit for Adding!
Base 2 Addition
0 1 0 1
1 0 0 1
+
Notes: <number>

## Slide 9: A Circuit for Adding!
Base 2 Addition
0
sum
carry out
0 1 0 1
1 0 0 1
+
FA
Notes: <number>

## Slide 10: A Circuit for Adding!
Base 2 Addition
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
Cool, but how do we build a FA?
Notes: <number>

## Slide 11: A Circuit for Adding!
Base 2 Addition
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0
Fill the rest of this table in your NOTES. Then, start building the circuit with AND, OR, NOT gates! (The next slide is blank for your work)
Notes: <number>
Notice that one of these columns is the parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on next week’s homework/lab.

## Slide 12: This Slide for Rent (Call 1-800-CS5 Black)

## Slide 13: A Circuit for Adding!
Base 2 Addition
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
Now what!??
Notes: <number>
Notice that one of these columns is the parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on next week’s homework/lab.

## Slide 14: A Circuit for Adding!
Base 2 Addition
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
This looks vaguely familiar…
Notes: <number>
Notice that one of these columns is the parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on next week’s homework/lab.

## Slide 15: A Circuit for Adding!
Base 2 Addition
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
Ah! I know how to do that!
Notes: <number>
Notice that one of these columns is the parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on next week’s homework/lab.

## Slide 16: Logisim: A Digital Logic Simulator
Notes: <number>
Demo Logisim. Explain drawing, deleting, labeling, projects, objects, reusing objects to build larger objects, and simulation. This will likely take 15 minutes.

## Slide 17: LogiSketch!

## Slide 18: Homework 1012
0. Reading (Computing with DNA)
1. Lab: Building a Ripple-Carry Adder
2. Multiplier circuit
3. Division circuit
0
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
22 21 20
1 1
1 0 1


## Slide 19: Implementing Gates with Relays
NOT Gate
Figures courtesy of HowStuffWorks.com
A
Q = A
6v power
Notes: <number>

## Slide 20: And AND…
Figure courtesy of HowStuffWorks.com
A
B
AB
6v power
Notes: <number>
How about an OR gate?

## Slide 21: Integrated Circuits
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm
Notes: <number>

## Slide 22: A real early relay computer
EARLY RELAY?
LEARY!
See the anagram solver at http://www.ssynth.co.uk/~gay/anagram.html
Notes: <number>

## Slide 23
Relays to Vacuum Tubes, …
Images courtesy of en.wikipedia.org
A vacuum tube
Notes: <number>
ENIAC at U. of Penn: http://en.wikipedia.org/wiki/ENIAC
Physically, ENIAC was a monster. It contained 17,468 vacuum tubes, 7,200 crystal diodes, 1,500 relays, 70,000 resistors, 10,000 capacitors and around 5 million hand-soldered joints. It weighed 30 short tons (27 t), was roughly 8 feet (2.4 m) by 3 feet (0.9 m) by 100 feet (30 m), took up 1800 square feet (167 m2), and consumed 150 kW of power. Input was possible from an IBM card reader, while an IBM card punch was used for output. These cards could be used to produce printed output offline using an IBM accounting machine, probably the IBM 405

## Slide 24: Digital Logic with Water and Legos!
Hydraulic Logic Gates!
Lego Logic Gates!
http://goldfish.ikaruga.co.uk/logic.html
http://www.cs.princeton.edu/introcs/lectures/fluid-computer.swf
Notes: <number>

## Slide 25: You’re Stranded on a Desert Island…
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 26: Yay! A Radio Shack!
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 27: And of course…
Can we implement every possible boolean function with
AND, OR, and NOT gates alone???
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 28
AND, OR, NOT is a “Universal” Set!
x y z Output
0 0 0 1
0 0 1 0
0 1 0 1
0 1 1 1
0 0 0
1 0 1 0
0 1 0 0
1 1 1 1
x y z
Notes: <number>

## Slide 29
The Minterm Expansion Principle Revisited!
x1 x2 x3 … x100 output
0 0 0 0 1
0 0 0 1 1
…
1 1 1 1 1
Notes: <number>

## Slide 30
The Minterm Expansion Principle Revisited!
x1 x2 x3 … x100 output
0 0 0 0 1
0 0 0 1 1
…
1 1 1 1 1
“1” (6v)
output
Notes: <number>

## Slide 31: Are other Sets of Gates Universal?
De Morgan’s Laws:
x y = x + y
x+y = x y
What if Radio Shack ran out of OR gates?
Augustus De Morgan: 1806-1871
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 32: Are other Sets of Gates Universal?
De Morgan’s Laws:
x y = x + y
x+y = x y
What if Radio Shack ran out of OR gates?
x y x y x + y
0 0
0 1
1 0
1 1
Augustus De Morgan: 1806-1871
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 33: This Space for Rent
Notes: <number>
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 34: A 1-bit Memory
This stuff is truly unforgettable!
OR + NOT = NOR
Notes: <number>

## Slide 35: From S-R Latches to D-Latches
Notes: <number>

## Slide 36
A Random Access Memory (RAM)
A 512K RAM
(About 4.2 million bits)
Notes: <number>