## Slide 1: Congestion Control
Outline
  Queuing Discipline
  Reacting to Congestion
  Avoiding Congestion
Readings:
Chapter 6

## Slide 2: Goals of Today’s Lecture
Principles of congestion control
  Learning that congestion is occurring
  Adapting to alleviate the congestion
TCP congestion control
  Additive-increase, multiplicative-decrease
  Slow start and slow-start restart
Related TCP mechanisms
  Nagle’s algorithm and delayed acknowledgments
Active Queue Management (AQM)
  Random Early Detection (RED)
  Explicit Congestion Notification (ECN)

## Slide 3: Resource Allocation vs. Congestion Control
Resource allocation
  How nodes meet competing demands for resources
  E.g., link bandwidth and buffer space
  When to say no, and to whom
Congestion control
  How nodes prevent or respond to overload conditions
  E.g., persuade hosts to stop sending, or slow down
  Typically has notions of fairness (i.e., sharing the pain)

## Slide 4: Flow Control vs. Congestion Control
Flow control
  Keeping one fast sender from overwhelming a slow receiver
Congestion control
  Keep a set of senders from overloading the network
Different concepts, but similar mechanisms
  TCP flow control: receiver window
  TCP congestion control: congestion window
  TCP window: min{congestion window, receiver window}

## Slide 5: Issues
Two sides of the same coin
  pre-allocate resources so at to avoid congestion
  control congestion if (and when) it occurs
Two points of implementation
  hosts at the edges of the network (transport protocol)
  routers inside the network (queuing discipline)

## Slide 6: Three Key Features of Internet Service Model
Packet switching
  A given source may have enough capacity to send data
  … and yet the packets may encounter an overloaded link
Connectionless flows
  No notions of connections inside the network
  … and no advance reservation of network resources
  Still, you can view related packets as a group (“flow”)
  … e.g., the packets in the same TCP transfer
Best-effort service
  No guarantees for packet delivery or delay
  No preferential treatment for certain packets

## Slide 7: Congestion is Unavoidable
Two packets arrive at the same time
  The node can only transmit one
  … and either buffer or drop the other
If many packets arrive in a short period of time
  The node cannot keep up with the arriving traffic
  … and the buffer may eventually overflow

## Slide 8: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 9: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
‘

## Slide 10: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
R/2
R/2
lout
lin
Host B
A

## Slide 11: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
A
Host B

## Slide 12: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
A
Host B

## Slide 13: Causes/costs of congestion: scenario 2
A
lin
lout
l'in
copy
free buffer space!
timeout
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Host B
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 14: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 15: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0

## Slide 16: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin’

## Slide 17: Congestion Collapse
Definition: Increase in network load results in a decrease of useful work done
Many possible causes
  Spurious retransmissions of packets still in flight
    Classical congestion collapse
    Solution: better timers and TCP congestion control
  Undelivered packets
    Packets consume resources and are dropped elsewhere in network
    Solution: congestion control for ALL traffic

## Slide 18: What Do We Want, Really?
High throughput
  Throughput: measured performance of a system
  E.g., number of bits/second of data that get through
Low delay
  Delay: time required to deliver a packet or message
  E.g., number of msec to deliver a packet
These two metrics are sometimes at odds
  E.g., suppose you drive a link as hard as possible
  … then, throughput will be high, but delay will be, too because of buffering along the way

## Slide 19: Framework
Connectionless flows
  sequence of packets sent between source/destination pair
  maintain soft state at the routers
Taxonomy
  router-centric versus host-centric
  reservation-based versus feedback-based
  window-based versus rate-based

## Slide 20: Load, Delay, and Power
Average
Packet delay
Load
Typical behavior of queuing
systems with random arrivals:
Power
Load
A simple metric of how well
the network is performing:
Power = throughput / delay
“optimal
load”
Goal: maximize power

## Slide 21: Queueing & Fairness

## Slide 22: Simple Resource Allocation
Simplest approach: FIFO queue and drop-tail
Link bandwidth: first-in first-out queue
  Packets transmitted in the order they arrive
Buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet

## Slide 23: Fairness
Effective utilization is not the only goal
  We also want to be fair to the various flows
  … but what the heck does that mean?
Simple definition: equal shares of the bandwidth
  N flows that each get 1/N of the bandwidth?
  But, what if the flows traverse different paths?

## Slide 24: FQ Algorithm
Suppose clock ticks each time a bit is transmitted
Let Pi denote the length of packet i
Let Si denote the time when start to transmit packet i
Let Fi denote the time when finish transmitting packet i
Fi = Si + Pi
When does router start transmitting packet i?
  if arrives before router finished packet i - 1 from this flow, then immediately after last bit of i - 1 (Fi-1)
  if no current packets for this flow, then start transmitting when arrives (call this Ai)
Thus: Fi = MAX (Fi - 1, Ai) + Pi

## Slide 25: FQ Algorithm (cont)
For multiple flows – The Problem
  calculate Fi for each packet that arrives on each flow
  treat all Fi’s as timestamps
  next packet to transmit is one with lowest timestamp
Not perfect: can’t preempt current packet
Example
Flow 1
Flow 2
(a)
(b)
Output
Output
F = 8
F = 10
F = 5
F = 10
F = 2
Flow 1
(arriving)
Flow 2
(transmitting)

## Slide 26: Approaches to TCP Congestion Control

## Slide 27: TCP Congestion Control
Idea
  assumes best-effort network (FIFO or FQ routers) each source determines network capacity for itself
  uses implicit feedback
  ACKs pace transmission (self-clocking)
Challenge
  determining the available capacity in the first place
  adjusting to changes in the available capacity
  When do we care about capacity?

## Slide 28: Idea of TCP Congestion Control
Each source determines the available capacity
  … so it knows how many packets to have in transit
Congestion window
  Maximum # of unacknowledged bytes to have in transit
  The congestion-control equivalent of receiver window
  MaxWindow = min{congestion window, receiver window}
  Send at the rate of the slowest component
Adapting the congestion window
  Decrease size upon losing a packet: backing off
  Increase upon success: optimistically exploring limits

## Slide 29: Additive Increase/Multiplicative Decrease
Objective: adjust to changes in the available capacity
New state variable per connection: CongestionWindow
  limits how much data source has in transit
  MaxWin = MIN(CongestionWindow, AdvertisedWindow)
  EffWin = MaxWin - (LastByteSent - LastByteAcked)
Idea:
  increase CongestionWindow when congestion goes down
  decrease CongestionWindow when congestion goes up

## Slide 30: AIMD (cont)
Question: how does the source determine whether or not the network is congested?
Answer: a timeout occurs
  timeout signals that a packet was lost
  packets are seldom lost due to transmission error (true?)
  lost packet implies congestion (Does Wireless change this?)

## Slide 31: AIMD (cont)
In practice: increment a little for each ACK
Increment = (MSS * MSS)/CongestionWindow
CongestionWindow += Increment
Algorithm
  increment CongestionWindow by one packet per RTT (linear increase)
  divide CongestionWindow by two whenever a timeout occurs (multiplicative decrease)
Source
Destination

## Slide 32: Additive Increase/Multiplicative Decrease
How much to increase and decrease?
  Increase linearly, decrease multiplicatively
  A necessary condition for stability of TCP
  Consequences of over-sized window are much worse than having an under-sized window
    Over-sized window: packets dropped and retransmitted
    Under-sized window: somewhat lower throughput
Multiplicative decrease
  On loss of packet, divide congestion window in half
Additive increase
  On success for last window of data, increase linearly

## Slide 33: AIMD (cont)
Trace: sawtooth behavior
Start with small Congestion Window to avoid overloading nextwork
Note, the ½ of the Window

## Slide 34: TCP Congestion Control: details
sender limits transmission:
cwnd is dynamic, function of perceived network congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
LastByteSent-
LastByteAcked
<
cwnd
sender sequence number space
rate
~
~
cwnd
RTT
bytes/sec

## Slide 35: Slow Start

## Slide 36: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is MSS/RTT
That could be pretty wasteful
  Might be much less than the actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (really “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases the rate exponentially
  … until the first loss event

## Slide 37: Slow Start
Objective: determine the available capacity.
Idea:
  begin with CongestionWindow = 1 packet
  double CongestionWindow each RTT (increment by 1 packet for each ACK)
Summary: initial rate is slow but ramps up exponentially fast
Source
Destination

## Slide 38: Leads to the TCP “Sawtooth”
t
Window
halved
Loss

## Slide 39: Practical Details
Congestion window
  Represented in bytes, not in packets (Why?)
  Packets have MSS (Maximum Segment Size) bytes
Increasing the congestion window
  Increase by MSS on success for last window of data
  In practice, increase a fraction of MSS per received ACK
    # packets per window: CW / MSS
    Increment per ACK: MSS * (MSS / CW)
Decreasing the congestion window
  Never drop congestion window below 1 MSS

## Slide 40: Slow Start (cont)
Exponential growth, but slower than all at once
Used…
  when first starting connection
  when connection goes dead waiting for timeout
Trace
Problem: lose up to half a CongestionWindow’s worth of data

## Slide 41: Two Kinds of Loss in TCP
Triple duplicate ACK
  Packet n is lost, but packets n+1, n+2, etc. arrive
  Receiver sends duplicate acknowledgments
  … and the sender retransmits packet n quickly
  Do a multiplicative decrease and keep going
Timeout
  Packet n is lost and detected via a timeout
  E.g., because all packets in flight were lost
  After the timeout, blasting away for the entire CW
  … would trigger a very large burst in traffic
  So, better to start over with a low CW

## Slide 42: Repeating Slow Start After Timeout
t
Window
Slow-start restart: Go back to CW of 1, but take advantage of knowing the previous value of CW.
Slow start in operation until it reaches half of previous cwnd.
timeout

## Slide 43: Repeating Slow Start After Idle Period
Suppose a TCP connection goes idle for a while
  E.g., Telnet session where you don’t type for an hour
Eventually, the network conditions change
  Maybe many more flows are traversing the link
  E.g., maybe everybody has come back from lunch!
Dangerous to start transmitting at the old rate
  Previously-idle TCP sender might blast the network
  … causing excessive congestion and packet loss
So, some TCP implementations repeat slow start
  Slow-start restart after an idle period

## Slide 44: Fast Retransmit and Fast Recovery
Problem: coarse-grain TCP timeouts lead to idle periods
Fast retransmit: use duplicate ACKs to trigger retransmission

## Slide 45: Results
Fast recovery
  skip the slow start phase
  go directly to half the last successful CongestionWindow (ssthresh)

## Slide 46: Other TCP Mechanisms
Nagle’s Algorithm and Delayed ACK

## Slide 47: Motivation for Nagle’s Algorithm
Interactive applications
  Telnet and rlogin
  Generate many small packets (e.g., keystrokes)
Small packets are wasteful
  Mostly header (e.g., 40 bytes of header, 1 of data)
Appealing to reduce the number of packets
  Could force every packet to have some minimum size
  … but, what if the person doesn’t type more characters?
Need to balance competing trade-offs
  Send larger packets
  … but don’t introduce much delay by waiting

## Slide 48: Nagle’s Algorithm
Wait if the amount of data is small
  Smaller than Maximum Segment Size (MSS)
And some other packet is already in flight
  I.e., still awaiting the ACKs for previous packets
That is, send at most one small packet per RTT
  … by waiting until all outstanding ACKs have arrived
Influence on performance
  Interactive applications: enables batching of bytes
  Bulk transfer: transmits in MSS-sized packets anyway
vs.
ACK

## Slide 49: Motivation for Delayed ACK
TCP traffic is often bidirectional
  Data traveling in both directions
  ACKs traveling in both directions
ACK packets have high overhead
  40 bytes for the IP header and TCP header
  … and zero data traffic
Piggybacking is appealing
  Host B can send an ACK to host A
  … as part of a data packet from B to A

## Slide 50: TCP Header Allows Piggybacking
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK

## Slide 51: Example of Piggybacking
Data
Data+ACK
Data
A
B
ACK
Data
Data + ACK
B has data to send
A has data to send
B doesn’t have data to send

## Slide 52: Increasing Likelihood of Piggybacking
Increase piggybacking
  TCP allows the receiver to wait to send the ACK
  … in the hope that the host will have data to send
Example: rlogin or telnet
  Host A types characters at a UNIX prompt
  Host B receives the character and executes a command
  … and then data are generated
  Would be nice if B could send the ACK with the new data
Data
Data+ACK
Data
A
B
ACK
Data
Data + ACK

## Slide 53: Delayed ACK
Delay sending an ACK
  Upon receiving a packet, the host B sets a timer
    Typically, 200 msec or 500 msec
  If B’s application generates data, go ahead and send
    And piggyback the ACK bit
  If the timer expires, send a (non-piggybacked) ACK
Limiting the wait
  Timer of 200 msec or 500 msec
  ACK every other full-sized packet

## Slide 54: Other Mechanisms
Random Early Detection (RED)
TCP Vegas

## Slide 55: Congestion Avoidance
TCP’s strategy
  control congestion once it happens
  repeatedly increase load in an effort to find the point at which congestion occurs, and then back off
Alternative strategy
  predict when congestion is about to happen
  reduce rate before packets start being discarded
  call this congestion avoidance, instead of congestion control
Two possibilities
  router-centric: DECbit and RED Gateways
  host-centric: TCP Vegas

## Slide 56: Bursty Loss From Drop-Tail Queuing
TCP depends on packet loss
  Packet loss is the indication of congestion
  In fact, TCP drives the network into packet loss
  … by continuing to increase the sending rate
Drop-tail queuing leads to bursty loss
  When a link becomes congested…
  … many arriving packets encounter a full queue
  And, as a result, many flows divide sending rate in half
  … and, many individual flows lose multiple packets

## Slide 57: Slow Feedback from Drop Tail
Feedback comes when buffer is completely full
  … even though the buffer has been filling for a while
Plus, the filling buffer is increasing RTT
  … and the variance in the RTT
Might be better to give early feedback
  Get one or two flows to slow down, not all of them
  Get these flows to slow down before it is too late

## Slide 58: Random Early Detection (RED)
Basic idea of RED
  Router notices that the queue is getting backlogged
  … and randomly drops packets to signal congestion
Packet drop probability
  Drop probability increases as queue length increases
  If buffer is below some level, don’t drop anything
  … otherwise, set drop probability as function of queue
Average Queue Length
Probability

## Slide 59: Properties of RED
Drops packets before queue is full
  In the hope of reducing the rates of some flows
Drops packet in proportion to each flow’s rate
  High-rate flows have more packets
  … and, hence, a higher chance of being selected
Drops are spaced out in time
  Which should help desynchronize the TCP senders
Tolerant of burstiness in the traffic
  By basing the decisions on average queue length
Notification is implicit

## Slide 60: RED Details
Compute average queue length
  AvgLen = (1 - Weight) * AvgLen +
  Weight * SampleLen
    0 < Weight < 1 (usually 0.002)
    SampleLen is queue length each time a packet arrives

## Slide 61: RED Details (cont)
Two queue length thresholds
  if AvgLen <= MinThreshold then
  enqueue the packet
  if MinThreshold < AvgLen < MaxThreshold then
  calculate probability P
  drop arriving packet with probability P
  if ManThreshold <= AvgLen then
  drop arriving packet

## Slide 62: RED Details (cont)
Computing probability P
    TempP = MaxP * (AvgLen - MinThreshold)/ (MaxThreshold - MinThreshold)
    P = TempP/(1 - count * TempP)
Drop Probability Curve

## Slide 63: Tuning RED
Probability of dropping a particular flow’s packet(s) is roughly proportional to the share of the bandwidth that flow is currently getting
MaxP is typically set to 0.02, meaning that when the average queue size is halfway between the two thresholds, the gateway drops roughly one out of 50 packets.
If traffic id bursty, then MinThreshold should be sufficiently large to allow link utilization to be maintained at an acceptably high level
Difference between two thresholds should be larger than the typical increase in the calculated average queue length in one RTT; setting MaxThreshold to twice MinThreshold is reasonable for traffic on today’s Internet
Penalty Box for Offenders

## Slide 64: Problems With RED
Hard to get the tunable parameters just right
  How early to start dropping packets?
  What slope for the increase in drop probability?
  What time scale for averaging the queue length?
Sometimes RED helps but sometimes not
  If the parameters aren’t set right, RED doesn’t help
  And it is hard to know how to set the parameters
RED is implemented in practice
  But, often not used due to the challenges of tuning right
Many variations
  With cute names like “Blue” and “FRED”… 
  What is the change in Philosophy?

## Slide 65: TCP Vegas
Idea: source watches for some sign that router’s queue is building up and congestion will happen too; e.g.,
  RTT growth indicates congestion…
  sending rate flattens
Congestion Window
Observed Throughput
Why no increase?
No bandwidth
Router Buffer Space

## Slide 66: Algorithm
Let BaseRTT be the minimum of all measured RTTs (commonly the RTT of the first packet)
If not overflowing the connection, then
ExpectRate = CongestionWindow/BaseRTT
as RTT increases, ExpectRate, descreases
Source calculates sending rate (ActualRate) once per RTT – More Work
Source compares ActualRate with ExpectRate
Diff = ExpectedRate – ActualRate (Always Positive)
if Diff < a -- Set to 1 buffer
increase CongestionWindow linearly
else if Diff > b -- Set to 3 buffer
decrease CongestionWindow linearly
else
leave CongestionWindow unchanged

## Slide 67: Algorithm (cont)
Parameters
  a = 1 packet
  b = 3 packets
  Congestion
  Window
Expected = color
Actual = black
Band = a, b
Even faster retransmit
  keep fine-grained timestamps for each packet
  check for timeout on first duplicate ACK

## Slide 68: Conclusions
Congestion is inevitable
  Internet does not reserve resources in advance
  TCP actively tries to push the envelope
Congestion can be handled
  Additive increase, multiplicative decrease
  Slow start, and slow-start restart
Active Queue Management can help
  Random Early Detection (RED)
  Explicit Congestion Notification (ECN)
Hosts can manage

## Slide 69: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!