## Slide 1: Routers Routing Forwarding
Reading: KR Chapter 5
Overview: Books on Routing, BGP is a life/career
Note to Students:
The course slides are a combination of slides from:
Peterson & Davie
Kurose & Ross
My previous lectures
I claim no copyright for any of the material and would recommend either book for a detailed treatment of the material

## Slide 2: Goals of Lecture
Routers
Forwarding
Routing
  Path selection
  Minimum-hop and shortest-path routing
Routing protocols
  Link state: OSPF, Open Shortest Path First
  Distance vector: RIP, Routing Information Protocol
Metrics
SDN

## Slide 3: IP Suite In Action: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 4: IP Suite In Action: Where We Are!!
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
Ethernet
interface
SONET
interface
host
host
router
Network
IP, ICMP,
Routing
Application
SNMP, DNS
Transport
IP packet
IP packet
Media
Ethernet,TRDHCP, ARP

## Slide 5: What is Routing?
A famous quotation from RFC 791
  “A name indicates what we seek. An address indicates where it is. A route indicates how we get there.” -- Jon Postel
Routing – Determining the Path

## Slide 6: IP Routing
Routing - operational aspects of Internet (NANOG)
Routing - process of choosing/creating a path
Router - network node making the choice on packet path
IP Routing Factors
  Network load
  Datagram length
  Requested service
  Physical network characteristics
SDN
Metrics
Truth - shortest paths usually based on hop counts???
  Net neutrality

## Slide 7: Routers architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 8: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 9: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 10: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
forwarding table

## Slide 11: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 12: Longest prefix matching
CIDRwhy longest prefix matching is used
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM

## Slide 13: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 14: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 15: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 16: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 17: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 18: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 19: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 20: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 21: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis – NN
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 22: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 23: Scheduling policies: still more
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available)
real world example?
1
2
3
4
5
5
5
2
3
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 24: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle – how are weights determined?
real-world example?

## Slide 25: Forwarding vs. Routing
Forwarding: data plane –moving packet
  Directing a data packet to an outgoing link
  Individual router using a forwarding table
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table

## Slide 26: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 27: Router Tasks Packet Forwarding Pack Dropping Rewrite Header Recompute Checksum Fragments Build the Forwarding Table

## Slide 28: At The Highest Level: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps destination addresses…
  … to outgoing interfaces
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats
  And the packet travels along the path to the destination

## Slide 29: Datagram Forwarding - Algorithm
Extract destination IP address, Id from datagram
Compute IP address of destination network In (Net Mask)
If In matches any directly connected network, send datagram to that network
Else If Id appears as a host-specific route, route datagram as specified in table;
Else If In appears in routing table, route datagram as specified in the table;
Else if a default route available, route datagram to default gateway; - Your Workstation
Else, routing error.

## Slide 30: Datagram Forwarding
Strategy
  every datagram contains destination’s address
  if connected to destination network, then forward to host
  if not directly connected, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Table Example Network Number Next Hop
1 R3
2 R1
3 interface 1
4 interface 0

## Slide 31: Stupidity of Separate Table Entries Per LAN Address
If a router had a forwarding entry per IP address
  Match destination address of incoming packet
  … to the forwarding-table entry
  … to determine the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 32: Separate Entry Per 24-bit Prefix, if only….
If the router had an entry per 24-bit prefix
  Look only at the top 24 bits of the destination address
  Index into the table to determine the next-hop interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 33: History: Separate Entry per Classful Address, limited future…
If the router had an entry per classful prefix
  Mixture of Class A, B, and C addresses
  Depends on the first couple of bits of the destination
Identify the mask automatically from the address
  First bit of 0: class A address (/8)
  First two bits of 10: class B address (/16)
  First three bits of 110: class C address (/24)
Then, look in the forwarding table for the match
  E.g., 1.2.3.4 maps to 1.2.3.0/24
  Then, look up the entry for 1.2.3.0/24
  … to identify the outgoing interface

## Slide 34: CIDR Makes Packet Forwarding Harder, but supports much larger Internet
There’s no such thing as a free lunch
  CIDR allows efficient use of the limited address space
  But, CIDR makes packet forwarding much harder
Forwarding table may have many matches
  E.g., table entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 35: Longest Prefix Match Forwarding
Forwarding tables in IP routers
  Maps each IP prefix to next-hop link(s)
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link

## Slide 36: Simplest Algorithm is Too Slow
Scan the forwarding table one entry at a time (even with indexing)
  See if the destination matches the entry
  If so, check the size of the mask for the prefix
  Keep track of the entry with longest-matching prefix
Worse Overhead is linear in size of the forwarding table
  Today, that means over 300,000 entries (in many cases)!
  And, the router may have just a few nanoseconds
  … before the next packet is arriving
Need greater efficiency to keep up with line rate
  Better algorithms
  Hardware implementations

## Slide 37: Patricia Tree
Store the prefixes as a tree
  One bit for each level of the tree
  Some nodes correspond to valid prefixes
  ... which have next-hop interfaces in a table
When a packet arrives
  Traverse the tree based on the destination address
  Stop upon reaching the longest matching prefix
0
1
00
10
11
100
101
00*
0*
11*

## Slide 38: Even Faster Lookups
Patricia tree is faster than linear scan
  Proportional to number of bits in the address
Patricia tree can be made faster
  Can make a k-ary tree
    E.g., 4-ary tree with four children (00, 01, 10, and 11)
  Faster lookup, though requires more space (memory is free)
Can use special hardware
  Content Addressable Memories (CAMs)
  Allows look-ups on a key rather than flat address
Huge innovations in the mid-to-late 1990s
  After CIDR was introduced (in 1994)
  … and longest-prefix match was a major bottleneck

## Slide 39: Where do Forwarding Tables Come From?
Routers have forwarding tables
  Map prefix to outgoing link(s)
Entries can be statically configured (yeah right…)
  E.g., “map 12.34.158.0/24 to Serial0/0.1”
But, this does not adapt to reality
  To failures
  To new equipment
  To the need to balance load
  …
That is where other technologies come in…
  Routing protocols, DHCP, and ARP

## Slide 40: What End Hosts Sending to Others Actually Do?
End host with single network interface
  PC with an Ethernet link
  Laptop with a wireless link
Don’t need to run a routing protocol
  Packets to the host itself (e.g., 1.2.3.4/32)
    Delivered locally
  Packets to other hosts on the LAN (e.g., 1.2.3.0/24)
    Sent out the interface
  Packets to external hosts (e.g., 0.0.0.0/0)
    Sent out interface to local gateway – how known?
How this information is learned
  Static setting of address, subnet mask, and gateway
  Dynamic Host Configuration Protocol (DHCP)

## Slide 41: What About Reaching the End Hosts?
How does the last router reach the destination?
Each interface has a persistent, global identifier
  MAC (Media Access Control) address – Link Address
  Burned in to the adaptors Read-Only Memory (ROM)
  Flat address structure (i.e., no hierarchy)
Constructing an address resolution table
  Mapping MAC address to/from IP address
  Address Resolution Protocol (ARP)
host
host
host
LAN
...
router
1.2.3.4
1.2.3.7
1.2.3.156

## Slide 42: IP Address Conclusions
IP address
  A 32-bit number still – someday it will expand everywhere
  Now Allocated in prefixes
  Non-uniform hierarchy for scalability and flexibility
Packet forwarding based on determining the Network
  Based on IP prefixes
  Longest-prefix-match forwarding
  Is there really a table size issue?

## Slide 43: Why Does Routing Matter?
End-to-end performance
  Quality of the path affects user performance
  Propagation delay, throughput, and packet loss
  Net Neutrality
Use of network resources
  Balance of the traffic over the routers and links, someone needs to pay…
  Avoiding congestion by directing traffic to lightly-loaded links – always an issue
Transient disruptions during changes
  Failures, maintenance, and load balancing
  Limiting packet loss and delay during changes

## Slide 44: Routing Overview
To build Forwarding Table Treat Network as a Graph
Problem: Find lowest cost path between two nodes
Factors
  Static: topology – really, at what level?
  Dynamic: load – definitely, time dependent
  Static: link speed – most likely
  Dynamic/Static: Weights and costs, effects defining ‘lowest cost’

## Slide 45: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested” or most “value”
routing: a “top-10” networking challenge!

## Slide 46
Per-router control plane: who is in my ‘graph’
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 47: Graph Theory: Start here: Shortest-Path Routing
Path-selection model
  Destination-based
  Load-insensitive (e.g., static link weights)
  Minimum hop count or sum of link weights
3
2
2
1
1
4
1
4
5
3

## Slide 48: Shortest-Path Problem
Given: network topology with link costs
  c(x,y): i.e., link cost from node x to node y
  Infinity if x and y are not direct neighbors
Compute: least-cost paths to all nodes
  From a given source U to all other nodes
  p(v): predecessor node along path from source to V
3
2
2
1
1
4
1
4
5
3
u
v
p(v)

## Slide 49: Dijkstra’s Shortest-Path Algorithm
Iterative algorithm
  After k iterations, know least-cost path to k nodes
S: nodes whose least-cost path definitively known
  Initially, S = {u} where u is the source node
  Add one node to S in each iteration
D(v): current cost of path from source to node v
  Initially, D(v) = c(u,v) for all nodes v adjacent to u
  … and D(v) = ∞ for all other nodes v
  Continually update D(v) as shorter paths are learned
How to learn paths? Note, each host different table

## Slide 50: Dijsktra’s Algorithm
1 Initialization:
2 S = {u}
3 for all nodes v
4 if v adjacent to u {
5 D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in S with the smallest D(w)
10 add w to S
11 update D(v) for all v adjacent to w and not in S:
D(v) = min{D(v), D(w) + c(w,v)}
/* new cost to v is either old cost to v or known shortest path cost to w plus cost from w to v */
13 until all nodes in S

## Slide 51: Shortest-Path Tree for Node u Built by Dijkstra’s Alg.
Shortest-path tree from u
Forwarding table at u
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)
Telling ‘u’ the next hop to reach any other node

## Slide 52: How to discover ‘my’ graph: nodes and weights?
Link-State Routing
Distance Vector Routing

## Slide 53: Link-State Routing
Each router keeps track of its incident links
  Whether the link is up or down
  The cost on the link
Each router broadcasts the link state
  To give every router a complete view of the graph
Each router runs Dijkstra’s algorithm
  To compute the shortest paths
  … and constructs its own forwarding table
Example protocols
  Open Shortest Path First (OSPF)
  Intermediate System – Intermediate System (IS-IS)

## Slide 54: Link State
Strategy
  send to all nodes (not just neighbors) information about directly connected links (not entire routing table)
  Routers can then build their own graph - map
Link State Packet (LSP)
  id of the node that created the LSP
  cost of link to each directly connected neighbor
  sequence number (SEQNO)
  time-to-live (TTL) for this packet

## Slide 55: Link State (cont)
Reliable flooding
  store most recent LSP from each node
  forward LSP to all nodes but one that sent it
  generate new (my) LSP periodically
    increment SEQNO
  start SEQNO at 0 when reboot
  decrement TTL of each stored LSP
    discard when TTL=0, aging

## Slide 56: Detecting Local Topology Changes
Beaconing
  Periodic “hello” messages in both directions
  Detect a failure after a few missed “hellos”, usually k of n
Performance trade-offs
  Detection speed
  Overhead on link bandwidth and CPU
  Likelihood of false detection
“hello”

## Slide 57: When to Initiate Flooding?
Topology change
  Link or node failure
  Link or node recovery
Configuration change
  Link cost change
Periodically
  Refresh the link-state information
  Typically (say) 30 minutes
  Corrects for possible corruption of the data

## Slide 58: Broadcasting the Link State
Reliable flooding
  Ensure all nodes receive link-state information
  … and that they use the latest version
Challenges
  Packet loss
  Out-of-order arrival
Solutions
  Acknowledgments and retransmissions (in routing protocol)
  Sequence numbers
  Time-to-live for each packet

## Slide 59: Issue: Broadcasting the Link State
Flooding
  Node sends link-state information out its links
  And then the next node sends out all of its links
  … except the one where the information arrived
  note race and time stamp needed at node B
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 60: Convergence
Getting consistent routing information to all nodes
  E.g., all nodes having the same link-state database
Consistent forwarding after convergence
  All nodes have the same link-state database
  All nodes forward packets on shortest paths
  The next router on the path forwards to the next hop
3
2
2
1
1
4
1
4
5
3

## Slide 61: Convergence Delay
Sources of convergence delay
  Detection latency of failed links
    Forwarding incorrect info
    Inconsistent link-state database
  Flooding of link-state information
  Shortest-path computation
  Creating the forwarding table
Performance during convergence period
  Lost packets due to black holes and TTL expiring
  Looping packets consuming resources
  Out-of-order packets reaching the destination
Very bad for VoIP, online gaming, and video

## Slide 62: Reducing Convergence Delay
Faster detection
  Smaller hello timers
  Link-layer technologies that can detect failures
Faster flooding
  Flooding immediately
  Sending link-state packets with high-priority
Faster computation
  Faster processors on the routers
  Incremental Dijkstra algorithm (can rebuild for part of graph)
Faster forwarding-table update
  Data structures supporting incremental updates

## Slide 63: Another Approach to Routing Distance Vector
Each node maintains a set of triples
  (Destination, Cost, NextHop)
Directly connected neighbors exchange table updates
  periodically (on the order of several seconds)
  whenever table changes (called triggered update)
Each update is a list of pairs:
  (Destination, Cost)
Update local table if receive a “better” route
  smaller cost
  came from next-hop
Refresh existing routes; delete if they time out
Depend on neighbor for correct info
Update = what a neighbor knows

## Slide 64: Distance Vector Algorithm
c(x,v) = cost for direct link from x to v
  Node x maintains costs of direct links c(x,v)
Dx(y) = estimate of least cost from x to y
  Node x maintains distance vector Dx = [Dx(y): y є N ]
Node x maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Each node v periodically sends Dv to its neighbors
  And neighbors update their own distance vectors
  Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Over time, the distance vector Dx converges

## Slide 65: Distance Vector Algorithm
Iterative, asynchronous:
each local iteration caused by:
Local link cost change
Distance vector update message from neighbor
Distributed:
Each node notifies neighbors only when its DV changes
Neighbors then notify their neighbors if necessary
wait for (change in local link cost or message from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 66: Distance Vector Example: Step 0
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C |  | –
D | 3 | D
E |  | –
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A |  | –
B |  | –
C | 0 | C
D | 1 | D
E |  | –
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A |  | –
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F |  | –
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B |  | –
C |  | –
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 6 | A
B | 1 | B
C | 1 | C
D |  | –
E | 3 | E
F | 0 | F
Optimum 1-hop paths

## Slide 67: Distance Vector Example: Step 2
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 7 | F
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 7 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 2-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 68: Distance Vector Example: Step 3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 6 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E | 5 | C
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D | 5 | F
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 3-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 69: DV Link Failures: Set cost to infinity: & - Changes propagate
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 6 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E | 5 | C
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D | 5 | F
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | & | 
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 3-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3
What about
D’s table

## Slide 70: Distance Vector: Link Cost Changes, an Issue!!
Link cost changes:
Node detects local link cost change
Updates the distance table
If cost change in least cost path, notify neighbors

## Slide 71: Distance Vector: Link Cost Changes
Count to Infinity:
Link from A to E goes down
Next advertisements:
  A advertises infinity to E, but B and C advertise a distance of 2 to E
Depending on timing:
  B hearing that E can be reached in 2 hops via C, concludes it (B) can reach E in 3 hops, hearing this A concludes it can get to E in 4 hops via B, hearing this C concludes it can get to E in 5 hops, etc.

## Slide 72: Loop-Breaking Heuristics
Set infinity to 16
Split horizon - Don’t send routes back to source of update - need to keep that info in the table
Split horizon with poison reverse - send routes back to source, but set distance to infinity

## Slide 73: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) messages sent
DV: exchange between neighbors only
  Convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) messages
DV: convergence time varies
  May be routing loops
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  Each node’s table used by others (error propagates)

## Slide 74: Summary of LS and DV
Distance Vector -- each node talks to its directly connected neighbors. It tells them everything that it knows about connectivity
Link State - each node talks to all other nodes, but it tells them only what it knows for sure -- directly connected links. Nodes then build their own network graph.

## Slide 75: Conclusions
Routing is a distributed algorithm
  React to changes in the topology
  Compute the shortest paths
Two main shortest-path algorithms
  Dijkstra  link-state routing (e.g., OSPF and IS-IS)
  Bellman-Ford  distance vector routing (e.g., RIP)
Convergence process
  Changing from one topology to another
  Transient periods of inconsistency across routers

## Slide 76: Scaling Routing
Overhead routing
  Determining Router Graph
  Running Dijkstra’s shortest-path algorithm on each router
Introduce hierarchy through “areas”
Area 0
Area 1
Area 2
Area 3
Area 4
area
border
router

## Slide 77: Routing Worlds – Problem Decomposition
IGP – within a Domain
  AS – Autonomous System == Domain
  Interior Gateway protocols – within AS
  Intradomain Routing protocols
  Need to define ‘Domain’, e.g., Claremont Colleges ?
EGP – between Domains
  Exterior Gateway protocols
  Interdomain Routing protocols – Between ASs

## Slide 78: What Routers? Internet Structure
Recent Past
NSFNET backbone
Stanford
BARRNET
regional
Berkeley
PARC
NCAR
UA
UNM
Westnet
regional
UNL
KU
ISU
MidNet
regional
■ ■ ■

## Slide 79: What Routers: Internet Structure Now
Today
Backbone service provider
Peering
point
Peering
point
Large corporation
Large corporation
Small
corporation
“Consumer”
ISP
“Consumer”
ISP
“Consumer”
ISP