## Slide 1: Routing Protocols
Reading: KR Chapter 5
Overview: Books on Routing, BGP is a life/career
Note to Students:
The course slides are a combination of slides from:
Peterson & Davie
Kurose & Ross
My previous lectures
I claim no copyright for any of the material and would recommend either book for a detailed treatment of the material

## Slide 2: IP Suite In Action: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 3: How to Make Routing Scale
Without CIDR but Hierarchical Addresses
Inefficient use of Hierarchical Address Space
  class C with 2 hosts (2/255 = 0.78% efficient)
  class B with 256 hosts (256/65535 = 0.39% efficient)
With CIDR - Still Too Many Networks
  routing tables do not scale
  route propagation protocols do not scale

## Slide 4: Forwarding Algorithm
D = destination IP address
for each entry (SubnetNum, SubnetMask, NextHop)
D1 = SubnetMask & D
if D1 = SubnetNum
if NextHop is an interface
deliver datagram directly to D
else
deliver datagram to NextHop
Use a default router if nothing matches
Not necessary for all 1s in subnet mask to be contiguous: be liberal in what you accept, conservative in what you send
Can put multiple subnets on one physical network
Subnets not visible from the rest of the Internet

## Slide 5: Historical: Internet Structure
NSFNET backbone
Stanford
BARRNET
regional
Berkeley
PARC
NCAR
UA
UNM
Westnet
regional
UNL
KU
ISU
MidNet
regional
■ ■ ■

## Slide 6: Today: Internet Structure
Backbone service provider
Peering
point
Peering
point
Large corporation
Large corporation
Small
corporation
“Consumer”
ISP
“Consumer”
ISP
“Consumer”
ISP

## Slide 7: Route Propagation
Know a smarter router
  hosts know local router
  local routers know site routers
  site routers know core router
  core routers know everything
Area, Domain ==Autonomous System (AS)
  corresponds to an administrative domain
  examples: University, company, backbone network
  assign each AS a 16-bit number
Two-level routing protcols
  interior gateway protocol (each AS selects its own)
  exterior gateway protocol (Internet-wide standard)

## Slide 8: Internet approach to scalable routing
“autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 9: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 10: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 11: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 12: Reducing Problem: Reduced!
Participating Nodes = # of ASs
Interdomain Route = Path to AS Border Route, AS Router
Therefore Complexity of Interdomain routing == order of number of ASs
e.g. Claremont Colleges
Complexity of Intradomain routing = order of number of networks in an AS
e.g., HMC vs Pitzer, etc.
e.g., HMC cs vs math, etc

## Slide 13: Popular Interior Gateway Protocols
RIP: Route Information Protocol
  developed for XNS
  distributed with Unix
  distance-vector algorithm
  based on hop-count
OSPF: Open Shortest Path First
  recent Internet standard
  uses link-state algorithm
  supports load balancing
  supports authentication

## Slide 14: Example Routing Protocol Routing Information Protocol (RIP)
Distance Vector protocol
  Nodes send distance vectors every 30 seconds
  … or, when an update causes a change in routing
Link costs in RIP
  All links have cost 1 – Hop Count Why??
  Valid distances of 1 through 15
  … with 16 representing infinity
  Small “infinity”  smaller “counting to infinity” problem
RIP is limited to fairly small networks
  E.g., used in the Princeton campus network

## Slide 17: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link
IS-IS routing protocol: nearly identical to OSPF

## Slide 18: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 19: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 20: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 21: Inter-AS tasks
ASs not interconnected:
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 22: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 23: BGP-4: Border Gateway Protocol
AS Types
  stub AS: has a single connection to one other AS
    carries local traffic only (HMC)
  multihomed AS: has connections to more than one AS
    refuses to carry transit traffic (Boeing)
  transit AS: has connections to more than one AS
    carries both transit and local traffic (ISP)
Each AS has:
  one or more border routers
  one BGP speaker that advertises:
    local networks
    other reachable networks (transit AS only)
    gives path information – list of ASs
    Reachability over optimality
Internet = interconnected set of ASs

## Slide 24: BGP Example
Speaker for AS2 advertises reachability to P and Q
  network 128.96, 192.4.153, 192.4.32, and 192.4.3, can be reached directly from AS2
Speaker for backbone advertises
  networks 128.96, 192.4.153, 192.4.32, and 192.4.3 can be reached along the path (AS1, AS2).
Speaker can cancel previously advertised paths

## Slide 25
AS = Routing Domain
Interdomain
Routing
R2, R4 = Border Router
EGP and IGP ability
Interdomain routing

## Slide 26: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 27: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 28: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 29: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 30: Conclusions
Routing is a distributed algorithm
  React to changes in the topology
  Compute the shortest paths
Two main shortest-path algorithms
  Dijkstra  link-state routing (e.g., OSPF and IS-IS)
  Bellman-Ford  distance vector routing (e.g., RIP)
Convergence process
  Changing from one topology to another
  Transient periods of inconsistency across routers