## Slide 1: Transport Protocols
Readings: KR Chapter 3
UDP - User Datagram Protocol
  TCP - Transmission Control Protocol
Note to Students:
The course slides are a combination of slides from:
Peterson & Davie
Kurose & Ross
My previous lectures
I claim no copyright for any of the material and would recommend either book for a detailed treatment of the material

## Slide 2: Goals for Today’s Lecture
Principles underlying transport-layer services
  (De)multiplexing
  Detecting corruption
  Reliable delivery
  Flow control
(Primary) Transport-layer protocols in the Internet
  User Datagram Protocol (UDP)
  Transmission Control Protocol (TCP)

## Slide 3: Layer Encapsulation in
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B
Link hardware
Host-to-host
connectivity
App-to-app
channels
Application

## Slide 4: IP Suite In Action: Where We Are!!
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
Ethernet
interface
SONET
interface
host
host
router
Network
IP, ICMP
Application
SNMP, DNS
Transport
IP packet
IP packet
Media
Ethernet,TRDHCP, ARP

## Slide 5: IP Suite In Action: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment/data gram
IP packet
IP packet
IP packet

## Slide 6: End-to-End Protocols
Working our way up and down Protocol Stack
  Directly connected networks
  Switching, Routing and Forwarding
  Internetworking: IP, Bridges, End-to-End
    Move from host-to-host
    To Process-to-process
  Applications: SNMP, DNS (Top down)
Transport next layer

## Slide 7: Roles of Layers
Application layer
  Communication for specific applications
  E.g., HyperText Transfer Protocol (HTTP), File Transfer Protocol (FTP), Network News Transfer Protocol (NNTP), DNS, SNMP
Transport layer
  Communication between processes (e.g., socket)
  Relies on network layer and serves the application layer
  E.g., TCP and UDP
Network layer
  Logical communication between nodes
  Hides details of the link technology
  E.g., IP

## Slide 8: Transport Protocols
Provide logical communication between application processes running on different hosts
Run on end hosts
  Sender: breaks application messages into segments, and passes to network layer
  Receiver: reassembles segments into messages, passes to application layer
Multiple transport protocol available to applications
  Internet: TCP and UDP – best known
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 9: End-to-End Protocols
Underlying best-effort network (IP)
  Drops messages
  re-orders messages … different routes, costs
  delivers duplicate copies of a given message
  limits messages to some finite size - MTU
  delivers messages after an arbitrarily long delay
Common end-to-end services (desired by application)
  guarantee message delivery
  deliver messages in the same order they are sent
  deliver at most one copy of each message
  support arbitrarily large messages
  support synchronization
  allow the receiver to flow control the sender
  support multiple application processes on each host
  SECURITY

## Slide 10: Internet Transport Protocols
Datagram messaging service (UDP)
  No-frills extension of “best-effort” IP
Reliable, in-order delivery (TCP)
  Connection set-up
  Discarding of corrupted packets
  Retransmission of lost packets
  Flow control
  Congestion control (next lecture)
Other services not available
  Delay guarantees
  Bandwidth guarantees
  Security

## Slide 11: Multiplexing and Demultiplexing
Host receives IP datagrams
  Each datagram has source and destination IP address,
  Each datagram carries one transport-layer segment
  Each segment has source and destination port number
Host uses IP addresses and port numbers to direct the segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 12: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 13: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 14: UDP - Unreliable Message Delivery Service
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
User Datagram Protocol (UDP)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents

## Slide 15: Simple Demultiplexor (UDP)
Unreliable and unordered datagram service
No flow control, No Acks, No msg ordering, No feedback
Endpoints identified by ports
  servers have well-known ports
  see /etc/services on Unix
Header format
length in bytes
Optional checksum
  pseudo header (Source, Destination, Protocol) + UDP header + data
Application - accepts full responsibility for all other issues

## Slide 16: Why Would Anyone Use UDP?
Finer control over what data is sent and when
  As soon as an application process writes into the socket
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, parameters, sequence #s, etc.
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only eight-bytes long

## Slide 17: Popular Applications That Use UDP
Multimedia streaming
  Retransmitting lost/corrupted packets is not worthwhile ??
  By the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
Simple query protocols like Domain Name System
  Overhead of connection establishment is overkill
  Easier to have application retransmit if needed
“Address for www.cnn.com?”
“12.3.4.15”

## Slide 18: UDP PseudoHeader
Issue - Message Correctness
  Only have ports in the UDP header, yet the message is directed to an IP address
  UDP wants to make sure that the message is directed to this host and this port
PseudoHeader
  Used in calculation of the checksum
  Includes Source and Destination IP addresses (from IP header)
  Also the type field
  Without reading the RFC, not sure if it is prepended or appended
  Also some books say UDP length field is used twice in the pseudoheader – read RFC if want to know truth
  UDP checksum, optional in v4, required in v6

## Slide 19: Reliable Byte-Stream (TCP)
Outline
  Connection Establishment/Termination
  Sliding Window
  Flow Control
  Adaptive Timeout
  Extensions

## Slide 20: TCP Overview
Connection-oriented
Byte-stream
  app writes bytes
  TCP sends segments
  app reads bytes
Full duplex
Flow control: keep sender from overrunning receiver
Congestion control: keep sender from overrunning network
Application process
Write
bytes
TCP
Send buffer
Segment
Segment
Segment
Transmit segments
Application process
Read
bytes
TCP
Receive buffer
■ ■ ■
reliable
unreliable

## Slide 21: Challenges of Reliable Data Transfer
Over a perfectly reliable channel
  All of the data arrives in order, just as it was sent
  Simple: sender sends data, and receiver receives data
Over a channel with bit errors
  All of the data arrives in order, but some bits corrupted
  Receiver detects errors and says “please repeat that”
  Sender retransmits the data that were corrupted
Over a lossy channel with bit errors
  Some data are missing, and some bits are corrupted
  Receiver detects errors but cannot always detect loss
  Sender must wait for acknowledgment (“ACK” or “OK”)
  … and retransmit data after some time if no ACK arrives

## Slide 22: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes on an Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header is typically 20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 23: Segment Format

## Slide 24: TCP Support for Reliable Delivery
Checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
Sequence numbers
  Used to detect missing data
  ... and for putting the data back in order
Retransmission
  Sender retransmits lost or corrupted data
  Timeout based on estimates of round-trip time
  Fast retransmit algorithm for rapid retransmission

## Slide 25: TCP “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80

## Slide 26: …Emulated Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.

## Slide 27: Segment Format (cont)
Each connection identified with 4-tuple:
  (SrcPort, SrcIPAddr, DsrPort, DstIPAddr)
Sliding window + flow control
  acknowledgment, SequenceNum, AdvertisedWindow
Flags
  SYN, FIN, RESET, PUSH, URG, ACK
Checksum
  pseudo header + TCP header + data

## Slide 28: Segment Transmission
MSS - Maximum Segment Size, ~ MTU (-IP Hdrs)
Push - Sending application/process “pushes” segment, do not wait for full segment, e.g. telnet
Timer - periodically fires “keep alive”

## Slide 29: Sequence Numbers
Host A
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte

## Slide 30: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not a de facto ISN of 0?
Practical issue
  IP addresses and port #s uniquely identify a connection
  Eventually, though, these port #s do get used again
  … and there is a chance an old packet is still in flight
  … and might be associated with the new connection
So, TCP requires changing the ISN over time
  Set from a 32-bit clock that ticks every 4 microseconds
  … which only wraps around once every 4.55 hours!
But, this means the hosts need to exchange ISNs

## Slide 31: TCP Three-Way Handshake

## Slide 32: State Transition Diagram

## Slide 33: Connection Establishment and Termination
A: Active participant
(client)
B: Passive participant
(server)
SYN, SequenceNum =
x
ACK, Acknowledgment =y+1
Acknowledgment =x+1
SYN+ACK, SequenceNum=y,

## Slide 34: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK

## Slide 35: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
Acknowledgment
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants to open a connection…

## Slide 36: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
A’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data

## Slide 37: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants is okay to start sending
Sequence number
… upon receiving this packet, B can start sending data

## Slide 38: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or
  Server rejects the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and waits for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP Sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  Some TCPs use a default of 3 or 6 seconds - ATTACK

## Slide 39: SYN Loss and Web Downloads
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  The 3-6 seconds of delay may be very long
  The user may get impatient
  … and click the hyperlink again, or click “reload”
User triggers an “abort” of the “connect”
  Browser creates a new socket and does a “connect”
  Essentially, forces a faster send of a new SYN packet!
  Sometimes very effective, and the page comes fast

## Slide 40: TCP Sliding Window

## Slide 41: Motivation for Sliding Window
Stop-and-wait is inefficient
  Only one TCP segment is “in flight” at a time
  Especially bad when delay-bandwidth product is high
Numerical example
  1.5 Mbps link with a 45 msec round-trip time (RTT)
    Delay-bandwidth product is 67.5 Kbits (or 8 KBytes)
  But, sender can send at most one packet per RTT
    Assuming a segment size of 1 KB (8 Kbits)
    … leads to 8 Kbits/segment / 45 msec/segment  182 Kbps
    That’s just one-eighth of the 1.5 Mbps link capacity

## Slide 42: TCP Sliding Window Data Link Versus Transport
Potentially connects many different hosts
  need explicit connection establishment and termination
Potentially different RTT
  need adaptive timeout mechanism
Potentially long delay in network
  need to be prepared for arrival of very old packets
Potentially different capacity at destination
  need to accommodate different node capacity
Potentially different network capacity
  need to be prepared for network congestion

## Slide 43: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received

## Slide 44: Receiver Buffering
Window size
  Amount that can be sent without acknowledgment
  Receiver needs to be able to store this amount of data
Receiver advertises the window to the Sender
Receiver tells the Sender the amount of free space left
  … and the Sender agrees not to exceed this amount
Window Size
Outstanding
Un-ack’d data
Data OK
to send
Data not OK
to send yet
Data ACK’d

## Slide 45: TCP Header for Receiver Buffering
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK

## Slide 46: Sliding Window Revisited
Sending side
  LastByteAcked < = LastByteSent
  LastByteSent < = LastByteWritten
  buffer bytes between LastByteAcked and LastByteWritten
Receiving side
  LastByteRead < NextByteExpected
  NextByteExpected < = LastByteRcvd +1
  buffer bytes between LastByteRead and LastByteRcvd

## Slide 47: Flow Control
Send buffer size: MaxSendBuffer
Receive buffer size: MaxRcvBuffer
Receiving side
  LastByteRcvd - LastByteRead < = MaxRcvBuffer
  AdvertisedWindow = MaxRcvBuffer - (NextByteExpected - NextByteRead)
Sending side
  LastByteSent - LastByteAcked < = AdvertisedWindow
  EffectiveWindow = AdvertisedWindow - (LastByteSent - LastByteAcked)
  LastByteWritten - LastByteAcked < = MaxSendBuffer
  block sender if (LastByteWritten - LastByteAcked) + y > MaxSenderBuffer
Always send ACK in response to arriving data segment
Persist when AdvertisedWindow = 0

## Slide 48: Silly Window Syndrome
How aggressively does sender exploit open window?
Because Ack indicates message size, a short message continues to always be short, Ack tells sender there is that much space available.
Receiver-side solutions
  after advertising zero window, wait for space equal to a maximum segment size (MSS) otherwise many small packets
  delayed acknowledgements
Sender
Receiver

## Slide 49: Nagle’s Algorithm
How long does sender delay sending data?
  too long: hurts interactive applications
  too short: poor network utilization
  strategies: timer-based vs self-clocking
When application generates additional data
  if new data fills a max segment (and window open): send it
  Else //partially filled buffer
    if there is unack’ed data in transit: buffer it until ACK arrives
    else: send it

## Slide 50: Protection Against Wrap Around
32-bit SequenceNum
Bandwidth Time Until Wrap Around
T1 (1.5 Mbps) 6.4 hours
Ethernet (10 Mbps) 57 minutes
T3 (45 Mbps) 13 minutes
FDDI (100 Mbps) 6 minutes
STS-3 (155 Mbps) 4 minutes
STS-12 (622 Mbps) 55 seconds
STS-24 (1.2 Gbps) 28 seconds
OC48 (2.4Gbps) 14 seconds Solution?

## Slide 51: Keeping the Pipe Full
16-bit AdvertisedWindow
Bandwidth Delay x Bandwidth Product
T1 (1.5 Mbps) 18KB
Ethernet (10 Mbps) 122KB
T3 (45 Mbps) 549KB
FDDI (100 Mbps) 1.2MB
STS-3 (155 Mbps) 1.8MB
STS-12 (622 Mbps) 7.4MB
STS-24 (1.2 Gbps) 14.8MB
OC48 (2.4Gbps) 29.6MB
assuming 100ms RTT

## Slide 52: TCP Retransmissions

## Slide 53: Automatic Repeat reQuest (ARQ)
Time
Packet
ACK
Timeout
Automatic Repeat Request
  Receiver sends acknowledgment (ACK) when it receives packet
  Sender waits for ACK and timeouts if it does not arrive within some time period
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
Sender
Receiver

## Slide 54: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 55: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short: wasted retransmissions
  Too long: excessive delays when packet lost
TCP sets timeout as a function of the RTT (Dynamic)
  Expect ACK to arrive after an RTT
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Can estimate the RTT by watching the ACKs
  Smooth estimate: keep a running average of the RTT
    EstimatedRTT = a * EstimatedRTT + (1 –a ) * SampleRTT
  Compute timeout: TimeOut = 2 * EstimatedRTT

## Slide 56: Example RTT Estimation

## Slide 57: A Flaw in This Approach
An ACK doesn’t really acknowledge a transmission
  Rather, it acknowledges receipt of the data
Consider a retransmission of a lost packet
  If you assume the ACK goes with the 1st transmission
  … the SampleRTT comes out way too large
Consider a duplicate packet
  If you assume the ACK goes with the 2nd transmission
  … the Sample RTT comes out way too small
Simple solution in the Karn/Partridge algorithm
  Only collect samples for segments sent one single time

## Slide 58: Yet Another Limitation…
Does NOT consider variance in the RTT
  If variance is small, the EstimatedRTT is pretty accurate
  … but, if variance is large, the estimate is NOT good
Better to directly consider the variance
  Consider difference: SampleRTT – EstimatedRTT
  Boost the estimate based on the difference
Jacobson/Karels algorithm
  See Peterson/Davie book for details

## Slide 59: History:Adaptive Retransmission (Original Algorithm)
Measure SampleRTT for each segment / ACK pair
Compute weighted average of RTT
  EstRTT = a x EstRTT + b x SampleRTT
  where a + b = 1
  a between 0.8 and 0.9
  b between 0.1 and 0.2
Set timeout based on EstRTT
  TimeOut = 2 x EstRTT

## Slide 60: History: Karn/Partridge Algorithm
Do not sample RTT when retransmitting
Double timeout after each retransmission

## Slide 61: History: Jacobson/ Karels Algorithm
New Calculations for average RTT
Diff = SampleRTT - EstRTT
EstRTT = EstRTT + (d x Diff)
Dev = Dev + d( |Diff| - Dev)
  where d is a factor between 0 and 1
Consider variance when setting timeout value
TimeOut = m x EstRTT + f x Dev
  where m = 1 and f = 4
Notes
  algorithm only as good as granularity of clock (500ms on Unix)
  accurate timeout mechanism important to congestion control (later)

## Slide 62: TCP Extensions
Implemented as header options
Store timestamp in outgoing segments
Extend sequence space with 32-bit timestamp (PAWS)
Shift (scale) advertised window

## Slide 63: TCP Issues
Messages vs Byte Stream
Record Boundaries…Database Records
Solution
  UrgPtr -- Sending app/process can tell receiver that there is urgent data, I.e., record boundary
  Push -- app/process can tell TCP “send now”…TCP receiver must inform receiving app…force records

## Slide 64: TCP Issues
TCP is reliable byte stream…what about
  Reliable, Ordered, etc: Request/Reply protocol
  Unreliable byte stream: video
TCP - High overhead to setup/close connection
  Web experience
TCP - Window Based
  How about Rate based…
TCP - Byte based…not message based

## Slide 65: State Transition Diagram