## Slide 1
ICMPv6

## Slide 2: Outline
Purpose of ICMPv6 and the structure of all ICMPv6 messages
ICMPv6 error messages
ICMPv6 informational messages used for diagnostics
Common ICMPv4 messages and their ICMPv6 equivalents
IPv6 Path MTU discovery process

## Slide 3: Overview of ICMPv6
Updated and expanded version of the Internet Control Message Protocol (ICMP) for IPv6
Reports delivery or forwarding errors and a simple echo service for troubleshooting
Provides a framework for (later):
  Multicast Listener Discovery (MLD)
  Neighbor Discovery (ND) which is ?
  IPv6 mobility

## Slide 4: Types of ICMPv6 Messages
Error messages
  Sent for errors encountered in forwarding or delivery by the destination node or an intermediate router
  The high order bit of the Type field is set to 0
    Type field is in the range of 0 - 127
Informational messages
  Provide diagnostic functions and additional host functionality
  The high order bit of the Type field is set to 1
    Type field is in the range of 128 - 255

## Slide 5: Structure of ICMPv6 Messages
Type
Code
Checksum
Message body
. . .
Two level breakdown
What are each of these?

## Slide 6: ICMP
Completely Changed – note new header type
Now includes IGMP (Multicast Group Mgmt)
Types organized as follows
  1 – 4 Error messages
  128 – 129 Ping
  130 – 132 Group membership
  133 – 137 Neighbor discovery
General Format

## Slide 7: ICMP
Type | Description
1 | Destination Unreachable
2 | Packet Too Big
3 | Time Exceeded
4 | Parameter Problem
128 | Echo Request
129 | Echo Reply
130 | Group Membership Query
131 | Group Membership Report
132 | Group Membership Reduction
133 | Router Solicitation
134 | Router Advertisement
135 | Neighbor Solicitation
136 | Neighbor Advertisement
137 | Redirect
Notes: Bill Owens will elaborate on multicast

## Slide 8: ICMPv6 Error Messages
Destination Unreachable (Code expands error)
  Code 0 - No route to destination
  Code 1 - Can’t get to destination for admin reasons
  Code 2 - Not assigned
  Code 3 - Address unreachable
  Code 4 - Port Unreachable
Packet Too Big
  Code 0 - Parameter is set to MTU of next hop, I.e., can determine MTU
Time Exceeded
Parameter Problem
ICMPv6 Error messages are rate limited
  By timer
  By percentage of bandwidth

## Slide 9: Error: Structure of the Destination Unreachable Message
Type
Code
Checksum
Parameter
Portion of discarded packet
= 1
= 0 - 4
. . .
Source can tell what destination
was not reached

## Slide 10: Error: Structure of the Packet Too Big Message
Type
Code
Checksum
(needed) MTU
Portion of discarded packet
= 2
= 0
. . .

## Slide 11: Error: Structure of the Time Exceeded Message
Type
Code
Checksum
Unused
Portion of discarded packet
= 3
= 0 or 1
. . .

## Slide 12: Error: Structure of the Parameter Problem Message – Error in Packet Structure
Type
Code
Checksum
(where pkt went bad)Pointer
Portion of discarded packet
= 4
= 0 - 2
. . .

## Slide 13: ICMPv6 Informational Messages
Echo Request
Echo Reply
Additional informational messages for
  ND (Neighbor Discovery),
  MLD (Multicast Listener Discovery), and
  IPv6 mobility

## Slide 14: Info: Structure of the Echo Request Msg
Type
Code
Checksum
Identifier
Sequence Number
Data
= 128
= 0
. . .
Match
response

## Slide 15: Info: Structure of the Echo Reply Message
Type
Code
Checksum
Identifier
Sequence Number
Data
= 129
= 0
. . .
Just Turn the message around

## Slide 16: ICMPv4 Messages and their ICMPv6 Equivalents
Common ICMPv4 Message
Destination Unreachable- Network unreachable (Type 3, Code 0)
Destination Unreachable-Protocol unreachable (Type 3, Code 2)
Destination Unreachable-Port unreachable (Type 3, Code 3)
Destination Unreachable-Fragmentation needed and DF set (Type 3, Code 4)
Time Exceeded-TTL expired (Type 11, Code 0)
Parameter Problem (Type 12, Code 0)
Source Quench (Type 4, Code 0)
Redirect (Type 5, Code 0)
ICMPv6 Equivalent
Destination Unreachable-No route to destination (Type 1, Code 0)
Parameter Problem-Unrecognized Next Header field (Type 4, Code 1)
Destination Unreachable-Port unreachable (Type 1, Code 4)
Packet Too Big (Type 2, Code 0)
Time Exceeded-Hop Limit exceeded (Type 3, Code 0)
Parameter Problem (Type 4, Code 0 or 2)
This message is not present in IPv6.
Neighbor Discovery Redirect message (Type 137, Code 0).

## Slide 17: Path MTU Discovery
For a given flow, the source host assumes that the path MTU is the MTU of the first link
If a packet reaches a link with a smaller MTU, that router discards it and returns an ICMP error message along with that link’s MTU
This continues until the packet reaches the destination
The source host caches the smallest link MTU as the “Path MTU” for that flow
To me not a problem…Ethernet won. I know of no useful link technology that has packets smaller than Ethernet.

## Slide 18: Path MTU Discovery

## Slide 19: Path MTU Discovery

## Slide 20: Path MTU Discovery

## Slide 21: Path MTU Discovery

## Slide 22: Path MTU Discovery

## Slide 23: Path MTU Discovery

## Slide 24: Path MTU Discovery

## Slide 25: Changes in PMTU – Path MTU
Set PMTU to destination to link MTU.
Send packet at PMTU size.
ICMPv6 Packet
Too Big message
received?
Yes
No
Set PMTU to destination to the value of the MTU field in the Packet Too Big message.
Is PMTU to destination
less than the link MTU?
Yes
No
Has PMTU timer expired?
Yes
No
Advantage of Flowchart?

## Slide 26: Consequences of New Fragmentation Method
Improved router performance (since routers don’t fragment), but must handle ICMP error packet
No more “fragments of fragments”
Hosts that do not support Path MTU discovery must limit packet size to 576 bytes
All links must support a MTU of at least 576 bytes or do “local” fragmentation (a la ATM AAL5)
This makes dynamic route changes problematic, since the new path may include a smaller MTU
  QoS promises associated with flows cause the same problem
  Result: no dynamic path changes in IPv6, which means no longer best effort on a random path of routers

## Slide 27: IPv6 Fragment Extension Header
Fragment Offset - offset of data in this packet, from the start of the original packet (counted in 8-byte units)
M Flag - Set to 1 if more fragments coming, set to 0 if this is the last fragment
Identification - a value unique to the original packet and common to all fragments

## Slide 28: IPv4 Fragmentation-Related Fields

## Slide 29: IPv6 Fragmentation Example

## Slide 30: Summary
Structure of all ICMPv6 messages
ICMPv6 error messages
ICMPv6 informational messages used for diagnostics
Common ICMPv4 messages and their ICMPv6 equivalents
IPv6 Path MTU discovery process