## Slide 1
IPv6
sources:
RFCs
books
presentations

## Slide 2: Outline
Limitations of IPv4 and modern day Internet
Features of IPv6
Differences between IPv4 and IPv6
IPv6 terminology
Case for IPv6 deployment

## Slide 3: Quick Review of IPv4 vs IPv6
IPv4 has problems with address space, fragmentation overhead, Quality of Service, security, autoconfiguration, etc.
  4-byte addresses
  Default 20-byte header
IPv6 addresses those problems
  16-byte address, fixed 40 byte header
  Flow labels for QoS support
  No more fragmentation in routers or checksums
  IPv4 Options become IPv6 Extension Headers
  Checksum removed, no hop checksum processing

## Slide 4: Limitations of IPv4
Exponential growth of the Internet and the impending exhaustion of the IPv4 address space
Growth of the Internet and the ability of Internet backbone routers to maintain large routing tables
Mobile Computing
IPv4 Missing Features
  Need for simpler configuration - startup
  Requirement for security at the IP level
  Need for better support for real-time delivery of data—quality of service (QoS)

## Slide 5: Competition from NAT Boxes
One of the strongest perceived incentives for migration was the shortage of IPv4 addresses
Network Address Translators helped to solve this problem by translating “official” external IP addresses into “private” internal addresses (10.x.x.x, etc.)
Created a disincentive for migration

## Slide 6: Consequences of the Limited IPv4 Address Space: NATs Impact peer to peer Applications
Internet
192.168.0.10
131.107.47.119
157.60.13.9
NAT
Host
Web
server
Remove End-to-End Nature of Internet

## Slide 7: Features of IPv6
New header format – faster processing
Large address space – IP everywhere
Possible Efficient and Hierarchical addressing and routing infrastructure – faster routing
Stateless and stateful address config
Built-in security
Better support for QoS – use header fields
New protocol for neighboring node interaction – new nodes, moble nodes
Extensibility – Designed in

## Slide 8: Quick Summary of IPv6
IPv6 still is an unreliable connectionless datagram protocol
IPv6 Base Header contains address, flow label (a QoS feature)
Extension Headers handle fragmentation, security, etc. (referenced by Next Header field)
Fragmentation avoided by Path MTU discovery

## Slide 9: IPv6 Address Space
Number of possible 128-bit addresses = 340,282,366,920,938,463,463,374,607,431,768,211,456
(3.4 * 1038)
That’s about 4 x 1018 per square meter of the Earth’s surface
Nevertheless, we could run short again if addresses are NOT allocated efficiently, how would you guarantee efficient allocation?

## Slide 10: Differences Between IPv4 and IPv6
Feature IPv4 IPv6
Address length 32 bits 128 bits
IPSec support Optional Required
QoS support Some Better
Fragmentation Hosts and routers Hosts only
Packet size 576 bytes 1280 bytes - Ethernet
Checksum in header Yes No
Options in header Yes No
Link-layer address resolution ARP (broadcast) Multicast Neighbor Discovery Messages
Multicast membership IGMP Multicast Listener Discovery (MLD)
Router Discovery Optional Required
Uses broadcasts Yes No
Configuration Manual, DHCP Automatic, DHCP
DNS name queries Uses A records Uses AAAA records
DNS reverse queries Uses IN-ADDR.ARPA Uses IP6.INT

## Slide 11: IPv6 Terminology
Additional subnets
Router
Host
Neighbors
Host
Host
Intra-subnet
router
Switch/Hub
LAN segment
Link
Subnet
Network

## Slide 12: The Case For IPv6 Deployment
IPv6 solves the address depletion problem
IPv6 solves the international address allocation problem – assign chunks
IPv6 restores end-to-end communication
IPv6 uses scoped addresses and address selection
IPv6 has more efficient forwarding
IPv6 has built-in security and mobility
Probably reached ‘standardization’ without enough implementation and testing...
Solves == Provides A Solution

## Slide 13: Migration Issues
The “Flag Day” problem
  Cannot simply pull the plug on IPv4 at some prearranged date, Why?
IPv4 will be around indefinitely - Problem?
Need to provide for a phased transition, but even more need to develop a ‘need’ to work that hard... Why Change??

## Slide 14: IPv6 Products
Done deal
All major players have IPv6 implementations for their OS's and routers
  Cisco – Linux
  Nortel - Gone – Solaris - Gone
  Microsoft – HP-UX - Gone
  Novell - Gone? – Mac OS X
  BSD (KAME) – Now Merged into BSD
www.moonv6.org
Renault car with Cisco router and Mobile IPv6 implementation

## Slide 15: Useful Books
IPv6 Essentials by S. Hagen (O’Reilly) (Best introduction)
IPng, The New Internet Protocol by C. Huitema (Prentice Hall)
IPng, Internet Protocol Next Generation by S. Bradner & A. Mankin (Addison-Wesley)
Internetworking with TCP/IP Vol. I, 5th Ed. by D. Comer (Prentice Hall)
IPng and the TCP/IP Protocols by S. Thomas (Wiley)
IPv6 Theory, Protocol, and Practice by Pete Loshin