## Slide 1
Neighbor Discovery

## Slide 2: Outline
Neighbor Discovery functions
Neighbor Discovery options
Neighbor Discovery messages
Address resolution, neighbor unreachability detection, duplicate address detection, router discovery, and redirect processes
Host sending algorithm

## Slide 3: Neighbor Solicitation
This protocol solves a set of problems related to the interaction between nodes attached to the same link (usually the same switch or LAN). It defines mechanisms for solving each of the following problems...

## Slide 4: Problems Solved by Neighbor Solicitation
Router Discovery: How hosts locate routers that reside on an attached link.
Prefix Discovery: How hosts discover the set of address prefixes that define which destinations are on-link for an attached link. (Nodes use prefixes to distinguish destinations that reside on-link from those only reachable through a router.)
Parameter Discovery: How a node learns such link parameters as the link MTU or such Internet parameters as the hop limit value to place in outgoing packets.

## Slide 5: Problems Solved by Neighbor Solicitation
Address Auto-configuration: How nodes automatically configure an address for an interface.
Address resolution: How nodes determine the link-layer address of an on-link destination (e.g., a neighbor) given only the destination's IP address - ARP
Next-hop determination: The algorithm for mapping an IP destination address into the IP address of the neighbor to which traffic for the destination should be sent. The next hop can be a router or the destination itself.

## Slide 6: Problems Solved by Neighbor Solicitation
Neighbor Unreachability Detection: How nodes determine that a neighbor is no longer reachable. For neighbors used as routers, alternate default routers can be tried. For both routers and hosts, address resolution can be performed again.
Duplicate Address Detection: How a node determines that an address it wishes to use is not already in use by another node.
Redirect: How a router informs a host of a better first-hop node to reach a particular destination.

## Slide 7: Neighbor Discovery Processes
Router discovery
  Router Solicitation, Router Advertisement
Prefix discovery
  Distinguish on link vs off link nodes
Parameter discovery
  additional operational parameters
Address auto configuration
  DHCP
Address resolution
  Neighbor Solicitation, Neighbor Advertisement
Next-hop determination
Neighbor unreachability detection
Duplicate address detection
Redirect function
  Better next hop

## Slide 8: Neighbor Discovery Message Format
ICMPv6 message structure and ICMPv6 types 133 through 137
To ensure local link traffic, all ND messages are sent with a hop limit of 255...seems reasonable, but why?
IPv6 Header
Next Header = 58
(ICMPv6)
Neighbor Discovery Message Options
Neighbor Discovery Message
Header
Neighbor Discovery Message

## Slide 9: Neighbor Discovery Messages
Router Solicitation
Router Advertisement
Neighbor Solicitation
Neighbor Advertisement
Redirect
All are accomplished by ICMP messages, expanding ICMP functions…

## Slide 10: ICMP Packet Types
Router Solicitation: When an interface becomes enabled, hosts may send out Router Solicitations that request routers to generate Router Advertisements immediately rather than at their next scheduled time, Why?
Router Advertisement: Routers advertise their presence together with various link and Internet parameters either periodically, or in response to a Router Solicitation message. Router Advertisements contain prefixes that are used for on-link determination and/or address configuration, a suggested hop limit value, etc. (in the olden days, one might argue against so much admin traffic, but bandwidth is plentiful and timeouts can be set)

## Slide 11: Structure of the Router Solicitation Message
Type
Code
Checksum
Reserved
Options
= 133
= 0
. . .

## Slide 12: Structure of the Router Advertisement Message
Type
Code
Checksum
Current Hop Limit
Managed Address Configuration flag
Other Stateful Configuration flag
Home Agent flag
Default Router Preference
Reserved
Router Lifetime
Reachable Time
Retrans Timer
Options
= 134
= 0
. . .

## Slide 13: ICMP Packet Types
Neighbor Solicitation: Sent by a node to determine the link-layer address of a neighbor, or to verify that a neighbor is still reachable via a cached link-layer address. Neighbor Solicitations are also used for Duplicate Address Detection.
Neighbor Advertisement: A response to a Neighbor Solicitation message. A node may also send unsolicited Neighbor Advertisements to announce a link-layer address change.
Redirect: Used by routers to inform hosts of a better first hop for a destination.

## Slide 14: Summary of ND Messages and Options
ND Message ND Option(s)
Router Solicitation Source Link-Layer Address
Router Advertisement Source Link-Layer Address
Prefix Information
MTU
Advertisement Interval
Home Agent Information
Route Information
Neighbor Solicitation Source Link-Layer Address
Neighbor Advertisement Target Link-Layer Address
Redirect Redirected Header
Target Link-Layer Address

## Slide 15: Neighbor Discovery Processes
ND provides message exchanges for the following processes:
  Address resolution (including duplicate address detection)
  Router discovery (including prefix and parameter discovery)
  Neighbor unreachability detection
  Redirect function

## Slide 16: Conceptual Host Data Structures
Neighbor cache
  Stores the on-link IPv6 address of a neighbor, its corresponding link-layer address, and an indication of the neighbor’s reachability state
  Equivalent to the ARP cache in IPv4
Destination cache
  Stores information on the next-hop IPv6 addresses for destinations to which traffic has recently been sent
Prefix list
  Lists on-link prefixes
Default router list
  Lists addresses corresponding to on-link routers that advertise themselves as default routers

## Slide 17: RFC 2461 Conceptual Host Data Structures
Prefix List
Default Router List
Destination Cache
Destination
Next-Hop Address
PMTU
Neighbor Cache
Link Layer Address
Next-Hop Address
State

## Slide 18: Address Resolution Process
An exchange of Neighbor Solicitation and Neighbor Advertisement messages to resolve the link-layer address of the next-hop address
  Multicast Neighbor Solicitation message
  Unicast Neighbor Advertisement message
Both hosts update their neighbor caches
Unicast traffic can now be sent

## Slide 19: Multicast Neighbor Solicitation
Host B
Host A
 Send multicast Neighbor Solicitation
Neighbor Solicitation
Ethernet Header
Destination MAC is 33-33-FF-02-6E-A5
IPv6 Header
Source Address is FE80::210:5AFF:FEAA:20A2
Destination Address is FF02::1:FF02:6EA5
Hop limit is 255
Neighbor Solicitation Header
Target Address is FE80::260:97FF:FE02:6EA5
Neighbor Discovery Option
Source Link-Layer Address is 00-10-5A-AA-20-A2
MAC: 00-10-5A-AA-20-A2
IP: FE80::210:5AFF:FEAA:20A2
MAC: 00-60-97-02-6E-A5
IP: FE80::260:97FF:FE02:6EA5

## Slide 20: Unicast Neighbor Advertisement
Host B
Host A
‚ Send unicast Neighbor Advertisement
Neighbor Advertisement
Ethernet Header
Destination MAC is 00-10-5A-AA-20-A2
IPv6 Header
Source Address is FE80::260:97FF:FE02:6EA5
Destination Address is FE80::210:5AFF:FEAA:20A2
Hop limit is 255
Neighbor Advertisement Header
Target Address is FE80::260:97FF:FE02:6EA5
Neighbor Discovery Option
Target Link-Layer Address is 00-60-97-02-6E-A5
MAC: 00-10-5A-AA-20-A2
IP: FE80::210:5AFF:FEAA:20A2
MAC: 00-60-97-02-6E-A5
IP: FE80::260:97FF:FE02:6EA5

## Slide 21: Neighbor Unreachability Detection
A neighboring node is reachable if:
  There has been a recent confirmation that IPv6 packets sent were received and processed by the neighboring node
Detects whether the first hop to the destination is reachable
Reachability is determined by:
  Receipt of a Neighbor Advertisement message in response to a unicast Neighbor Solicitation message
  Upper layer protocol indicators

## Slide 22: Neighbor Unreachability States
Unicast Neighbor Solicitation retries exceeded
Delay time exceeded
PROBE
Reachable Time exceeded
or unsolicited Neighbor
Advertisement received
STALE
Multicast Neighbor Solicitation retries exceeded
Reachability confirmed
by sending unicast Neighbor
Solicitation and receiving solicited Neighbor Advertisement
Receive solicited
Neighbor Advertisement
REACHABLE
Send packet
DELAY
Send multicast Neighbor Solicitation
INCOMPLETE
NO ENTRY EXISTS
Reachability
confirmed by
upper layer protocol

## Slide 23: Duplicate Address Detection
Use of a neighbor solicitation to detect a duplicate unicast address
  Target Address field in the Neighbor Solicitation message is set to the IPv6 address for which duplication is being detected
  The Source Address is set to the unspecified address (::)
For a duplicate address, the defending node replies with a multicast Neighbor Advertisement
  The Destination Address is set to the link-local scope all-nodes multicast address (FF02::1)

## Slide 24: Multicast Neighbor Solicitation for Duplicate Address Detection
Host B
Host A
 Send multicast Neighbor Solicitation
Neighbor Solicitation
Tentative IP: FEC0::2:260:8FF:FE52:F9D8
MAC: 00-60-08-52-F9-D8
IP: FEC0::2:260:8FF:FE52:F9D8
Ethernet Header
Dest MAC is 33-33-FF-52-F9-D8
IPv6 Header
Source Address is ::
Destination Address is FF02::1:FF52:F9D8
Hop limit is 255
Neighbor Solicitation Header
Target Address is FEC0::2:260:8FF:FE52:F9D8

## Slide 25: Multicast Neighbor Advertisement for a Duplicate Address
Host B
Host A
Ethernet Header
Destination MAC is 33-33-00-00-00-01
IPv6 Header
Source Address is FEC0::2:260:8FF:FE52:F9D8
Destination Address is FF02::1
Hop limit is 255
Neighbor Advertisement Header
Target Address is FEC0::2:260:8FF:FE52:F9D8
Neighbor Discovery Option
Target Link-Layer Address is 00-60-08-52-F9-D8
Tentative IP: FEC0::2:260:8FF:FE52:F9D8
‚ Send multicast Neighbor Advertisement
Neighbor Advertisement
MAC: 00-60-08-52-F9-D8
IP: FEC0::2:260:8FF:FE52:F9D8

## Slide 26: Router Discovery
Nodes discover the set of routers on the local link
IPv6 router discovery also provides:
  Default value of Hop Limit field
  Use of stateful address protocol
  Reachability and retransmission timers
  Network prefixes for the link
  MTU of the local link
  IPv6 mobility information
  Routes

## Slide 27: Multicast Router Solicitation Message
Router
Host A
 Send multicast Router Solicitation
Router Solicitation
Ethernet Header
Destination MAC is 33-33-00-00-00-02
IPv6 Header
Source Address is ::
Destination Address is FF02::2
Hop limit is 255
Router Solicitation Header
MAC: 00-B0-D0-E9-41-43
IP: none
MAC: 00-10-FF-D6-58-C0
IP: FE80::210:FFFF:FED6:58C0

## Slide 28: Multicast Router Advertisement Message
Host A
Ethernet Header
Destination MAC is 33-33-00-00-00-01
IPv6 Header
Source Address is FE80::210:FFFF:FED6:58C0
Destination Address is FF02::1
Hop limit is 255
Router Advertisement Header
Current Hop Limit, Flags, Router Lifetime, Reachable and Retransmission Timers
Neighbor Discovery Options
Source Link-Layer Address is 00-10-FF-D6-58-C0
MTU is 1500
Prefix Information is for FEC0:0:0:F282::/64
MAC: 00-10-FF-D6-58-C0
IP: FE80::210:FFFF:FED6:58C0
Router
‚ Send multicast Router Advertisement
Router Advertisement
MAC: 00-B0-D0-E9-41-43
IP: none

## Slide 29: Redirect Function
Inform originating hosts of a better first-hop neighbor to which traffic should be forwarded for a specific destination
Two instances:
  1. A router informs an originating host of the IP address of a router available on the local link that is “closer” to the destination
  2. A router informs an originating host that the destination is a neighbor (it is on the same link as the originating host)
Redirect message contains best first-hop address information
Redirect messages are only sent by the first router in the path between the originating host and the destination

## Slide 30: Unicast Packet to the Router
Host A
Ethernet Header
Destination MAC is 00-AA-00-22-22-22
IPv6 Header
Source Address is FEC0::1:2AA:FF:FE11:1111
Destination Address is FEC0::2:2AA:FF:FE99:9999
MAC: 00-AA-00-22-22-22
IP: FEC0::1:2AA:FF:FE22:2222
FE80::2AA:FF:FE22:2222
Router 2
Router 3
Unicast Packet
 Send unicast packet
MAC: 00-AA-00-33-33-33
IP: FEC0::1:2AA:FF:FE33:3333
FE80::2AA:FF:FE33:3333
MAC: 00-AA-00-11-11-11
IP: FEC0::1:2AA:FF:FE11:1111
FE80::2AA:FF:FE11:1111

## Slide 31: Redirect Message Sent by the Router
Host A
‚ Send unicast Redirect
Redirect
Ethernet Header
Destination MAC is 00-AA-00-11-11-11
IPv6 Header
Source Address is FE80::2AA:FF:FE22:2222
Destination Address is FEC0::1:2AA:FF:FE11:1111
Hop limit is 255
Redirect Header
Target Address is FE80::2AA:FF:FE33:3333
Destination Address is FEC0::2:2AA:FF:FE99:9999
Neighbor Discovery Options
Target Link-Layer Address is 00-AA-00-33-33-33
Redirected Header
Router 2
Router 3
MAC: 00-AA-00-33-33-33
IP: FEC0::1:2AA:FF:FE33:3333
FE80::2AA:FF:FE33:3333
MAC: 00-AA-00-11-11-11
IP: FEC0::1:2AA:FF:FE11:1111
FE80::2AA:FF:FE11:1111
MAC: 00-AA-00-22-22-22
IP: FEC0::1:2AA:FF:FE22:2222
FE80::2AA:FF:FE22:2222

## Slide 32: Unicast Packet Forwarded by the Router
Host A
Ethernet Header
Destination MAC is 00-AA-00-33-33-33
IPv6 Header
Source Address is FEC0::1:2AA:FF:FE11:1111
Destination Address is FEC0::2:2AA:FF:FE99:9999
MAC: 00-AA-00-11-11-11
IP: FEC0::1:2AA:FF:FE11:1111
FE80::2AA:FF:FE11:1111
MAC: 00-AA-00-22-22-22
IP: FEC0::1:2AA:FF:FE22:2222
FE80::2AA:FF:FE22:2222
Router 2
Router 3
MAC: 00-AA-00-33-33-33
IP: FEC0::1:2AA:FF:FE33:3333
FE80::2AA:FF:FE33:3333
Unicast Packet
 Forward unicast packet

## Slide 33: Host Sending Algorithm
1. Determine the next-hop address for the destination
  Check the destination cache
  If the destination address matches a prefix in the prefix list, next-hop address is destination address
  If the destination address does not match a prefix in the prefix list, next-hop address is the default router address
2. Determine the link-layer address for the next-hop address
  Check the neighbor cache
  Use address resolution to obtain the link-layer address for the next-hop address
3. Send the packet using the link-layer address of the next-hop address

## Slide 34: Host Sending Algorithm
Check destination cache for an entry
matching the destination address.
Entry found
in destination cache?
Yes
No
Is next-hop
address entry in
neighbor cache?
Yes
No
Use address resolution process to
determine the link-layer address
of the next-hop address.
Was
address resolution
successful?
Yes
No
Indicate an error.
Does the
destination address
match a prefix in the
prefix list?
Yes
No
Check prefix list for a prefix that
matches the destination address.
Update neighbor cache.
Send packet using link-layer address
of neighbor cache entry.
Set the next-hop address to
the default router address.
Set the next-hop address to
the destination address.
Obtain next-hop address from
destination cache or care-of destination cache entry.
Is there a
default router?
No
Yes
Update destination cache.
Check neighbor cache for an entry
matching the next-hop address.

## Slide 35: IPv4 Neighbor Functions and IPv6 Equivalents
IPv4 Neighbor Function IPv6 Neighbor Function
ARP Request message Neighbor Solicitation message
ARP Reply message Neighbor Advertisement message
ARP cache Neighbor cache
Gratuitous ARP Duplicate address detection
Router Solicitation message (optional) Router Solicitation (required)
Router Advertisement message (optional) Router Advertisement (required)
Redirect message Redirect message

## Slide 36: Neighbor Discovery Overview
Set of messages and processes that determine relationships between neighboring nodes
  Replaces ARP, ICMPv4 Router Discovery, and ICMPv4 Redirect
ND is used by nodes:
  For address resolution
  To determine link-layer address changes
  To determine neighbor reachability
ND is used by hosts:
  To discover neighboring routers
  Autoconfigure addresses, address prefixes, and other configuration parameters
ND is used by routers:
  To advertise their presence, host configuration parameters, and on-link prefixes
  To inform hosts of a better next-hop address to forward packets for a specific destination

## Slide 37: Summary
Neighbor Discovery functions
Neighbor Discovery options
Neighbor Discovery messages
Address resolution, neighbor unreachability detection, duplicate address detection, router discovery, and Redirect processes
Host sending algorithm

## Slide 38: Neighbor Discovery Option Format
ND options are formatted in Type-Length-Value (TLV) format
Type
Length
Value
. . .

## Slide 39: Neighbor Discovery Options
Type 1: Source Link-Layer Address
Type 2: Target Link-Layer Address
Type 3: Prefix Information
Type 4: Redirected Header
Type 5: MTU
Type 7: Advertisement Interval
Type 8: Home Agent Information
Type 9: Route Information

## Slide 40: Structure of the Source and Target Link-Layer Address Options
Type 1: Source Link-Layer Address option
Type 2: Target Link-Layer Address option
Source and Target Link-Layer Address options for Ethernet
Type
Length
Link-Layer Address
. . .
Type
Length
Ethernet MAC Address
= 1

## Slide 41: Structure of the Prefix Information Option
Type
Length
Prefix Length
On-Link flag
Autonomous flag
Router Address flag
Site prefix flag
Reserved1
Valid Lifetime
Preferred Lifetime
Reserved2
Site Prefix Length
Prefix
= 3
= 4

## Slide 42: Structure of the Redirected Header Option
Type
Length
Reserved
Portion of redirected packet
. . .
= 4

## Slide 43: Mixed Media Configuration
Host A
Host B
FDDI
FDDI
Ethernet
Backbone
Ethernet Switch
Ethernet Switch

## Slide 44: Structure of the MTU Option
Type
Length
Reserved
MTU
= 5
= 1

## Slide 45: Structure of the Advertisement Interval Option
Type
Length
Reserved
Advertisement Interval
= 7
= 1

## Slide 46: Structure of the Home Agent Information Option
Type
Length
Reserved
Home Agent Preference
Home Agent Lifetime
= 8
= 1

## Slide 47: Structure of the Route Information Option
Type
Length
Prefix Length
Reserved 1
Preference
Reserved 2
Route Lifetime
Prefix
= 9

## Slide 48: Example Configuration for Route Information Option
Router 2
Router 1
Subnet 1
Subnet 2
Rest of IPv6 network

## Slide 49: Structure of the Neighbor Solicitation Message
Type
Code
Checksum
Reserved
Target Address
Options
= 135
= 0
. . .

## Slide 50: Structure of the Neighbor Advertisement Message
Type
Code
Checksum
Router flag
Solicited flag
Override flag
Reserved
Target Address
Options
= 136
= 0
. . .

## Slide 51: Structure of the Redirect Message
Type
Code
Checksum
Reserved
Target Address
Destination Address
Options
= 137
= 0
. . .