## Slide 1
power
ground
signal
CONSTRUCTING THE CIRCUIT
Using the IR Remote: setup

## Slide 2
CONSTRUCTING THE CIRCUIT: IR Receiver
As you build, refer to the completed circuit shown on page two as a guide! As you go, you can keep your power wires red and your ground wires black so that your circuit stays color-coded and organized!
Stick the IR Receiver into the breadboard; make sure you're not connecting the three pins together in a circuit. Face the spherical bump on the receiver towards you: the signal pin is on the left, the ground pin is in the middle, the power pin is on the right, as shown in the diagram.
Using a red wire, connect the 5V hole on the Arduino board to one of the holes by the red line at the top of your breadboard. The entire row of holes is now connected to the 5V power source, and any of them can be used to access the 5V of power!
Then, using a black wire, connect one of the GND holes on the board to one of the holes by the blue line at the top of your breadboard. This entire row of holes is now connected to ground.
Use a red wire to connect the IR Receiver power pin (on the right) to one of the 5V holes on the breadboard.
Use a black wire to connect the IR Receiver ground pin (middle) to one of the ground holes on the breadboard.
Use a yellow wire to connect the IR Receiver signal pin (left) to any one of the digital pin holes on the Arduino.

## Slide 3
CONSTRUCTING THE CIRCUIT: Test LED
Put an LED light into the breadboard; make sure you don't stick both ends (cathode and anode) into the same circuit!
Put one end of a resistor into the same column as the signal pin of the IR Receiver, and the other end into the same column as the cathode (short end) of the LED light.
Put one end of a red wire into the same column as the power pin of the IR Receiver, and the other end into the same column as the anode (long end) of the LED light.
Now, take your remote and press any button. If you constructed your circuit correctly, the test LED should flash whenever you press a button!

## Slide 4
Using the IR Remote
Starter code
www.cs.hmc.edu/bots/
top link for library
2nd link for code

## Slide 5
GETTING STARTED CODING
Go to the menu bar on your Arduino IDE and go to Software > import libraries and see if "IRremote" is listed under "Contributed". If it is, skip to the next page. If not, continue!
Get the IRremote.zip file from the first link at www.cs.hmc.edu/bots Unzip or extract the file; you should have a folder named IRremote with an examples folder, IRremote.h, and some other files in it.
Find your libraries folder. The default location is Documents > Arduino > libraries. Copy the IRremote folder here.
Open the Arduino software.
In the menu bar, click on Sketch > import libraries. Click on "Add Library" and find the IRremote folder. You should be able to find it in Documents > Arduino > libraries > IRremote. Do not open the folder, just click on the folder and click the "choose" button.
Check that you've successfully imported the library. Go to the menu bar again and go to Sketch > Import Libraries. You should see "IRremote" listed under "Contributed" at the bottom of the drop-down menu.

## Slide 6
Copy the ArduBlock program shown below, and click "Upload to Arduino"
In "Control", get the "program" block with an empty setup and loop, the "subroutine" block (rename it "remote"), and two "if/else" blocks. You can grab the orange comparison blocks from "Tests"
In "Variables/Constants", get the integer variable block and an integer number block. Name the integer variable name variable.
You can access the serial printing blocks in the "Communication" category.
GETTING STARTED CODING

## Slide 7
Get the irRemoteSetupLoop text file from the second link at www.cs.hmc.edu/bots and paste it in place of the code that's boxed in red.
Upload the code through your Arduino IDE (not ArduBlock!), open up the serial monitor, and see what happens when you press the power and forward buttons!
Code not working?
Check which pin your IR receiver is connected to, and make sure the variable RECV_PIN has the correct pin assigned to it.
Look at the top of the file to see what int variable was created; it should look something like _ABVAR_#_irValue. Make sure that the variable called in the loop has the same # in it as the one created at the top of the file!
GETTING STARTED CODING

## Slide 8
CHALLENGES
0. Add an "if/else" statement for each of the buttons on your IR remote.
When a button is pressed, the remote will send a pulse of infrared waves to the receiver. These signal pulses are translated into the following numbers:
Power -28189
Spot 5386
Clean 9274
Max 5385
Forward -161
Left -28235
Right -162
Neutral* -22643
Pause 9273
You can either type these numbers directly into the conditional statements to check for equality or you can create constants that refer to each of these values.
*Neutral is the value that the IR receiver will get when you release the Forward, Left, and Right buttons. If you do not specify an action for the "Neutral" case, your robot will continue doing the same action it did when the Forward, Right, or Left button was pressed. You can make the robot stop doing whatever it was doing when the IR receiver gets the Neutral signal. Then, the robot will only continue doing an action if you hold down the Forward, Left, and Right buttons. The Power, Spot, Clean, Max, and Pause buttons are not affected in either case.

## Slide 9
CHALLENGES
1.Have each button turn on a different LED
Remember to copy/paste the starter file in place of setup() and loop()!
2. Have one button turn on ALL the LEDs!
Hint: Use a loop…
3. Have one of the buttons play a song through the speakers
You can grab the irRemoteSpeakerServo file from the website to copy/paste in place of the setup() and loop(). Before you upload your file, hit control/command + F to replace all instances of "tone" with "freqout"!
Make sure the SPEAKER_PIN variable holds the correct value! Also double-check that _ABVAR_#_irValue has the correct number where the # sign is; sometimes the number can change as you add more variables to your code.
4. Have the remote turn on and off the motor
Make sure you're attaching the right servo pins in the setup() code!
5. Set up other actions using the remote-control!