## Slide 1
LEDs: Getting Started
One of the things you can do with your Arduino board is control LED lights.
You need to connect one end of your circuit to a power source and you need to ground the other end.
This is what a bread board looks like:
The connections in a breadboard run horizontally down the red and blue lines and vertically from A to E and F to J.
1

## Slide 2
LEDs: Getting Started
This is what an Arduino Board looks like:
Use the digital pins to connect the longer end of the LED to the Arduino.
Pins 0 and 1 have a specific purpose and may not work correctly. Try just using pins 2 through 13.
The GND pin grounds the circuit. Connect the shorter end of the LED to this pin.
Digital pins
2

## Slide 3
LEDs: Getting Started
If your LED starts to heat up or you smell anything strange you will want to add a resistor to your circuit before the power reaches the LED. Resistors look like this:
Below is a picture of a complete circuit. The blue wire connects the GND (ground) pin to the blue row on the bread board. The yellow wire connects pin 13 to the bread board. The LED goes from pin 13's connection across the breadboard gap. The longer LED arm is plugged in to pin 13's connection. A resistor then goes from the LED to ground. The shorter LED arm is closer to ground.
3

## Slide 4
LEDs: Getting Started
Now, you'll program that LED. Open Arduino. Go to tools, and then board and select the matching Arduino board. Also, choose the appropriate serial port. Then click on tools > ArduBlock and create the following program. See if you can determine how it works!
4

## Slide 5
LED Challenges Part 1
Challenges
11. Change the digital pin for the LED to pin #7
From unlucky (13) to lucky (7). Get it to work!!
The Arduino supports any pins labeled 2 through 13.
12. Get the LED to stay on forever.
13. Get the LED to blink much faster!
What has to change here? (Remember what delay does!)
[CHALLENGE]
How fast can it blink -- so that you still see the individual flashes?
5

## Slide 6
LED Challenges Part 1
Challenges
14. Add a second LED to pin 6.
Get it to work!!
You need a resistor and another wire.
But, you can share the ground wire with the other LED.
15. Get the two LEDs to alternate blinking.
6

## Slide 7
LED Challenges Part 1
Challenges
16. Now, set up at least 8 LEDs.
You can use pins 6 through 13.
You might want more – you can use up to 12 (pins 2 through 13)
Here's a picture of how to set up four:
You need a loop to handle all of these – see the next program!!
7

## Slide 8
More LEDs
Create a new copy of the program and type this:
Look at the two for loops here!
for loop
for loop
8

## Slide 9
LED Challenges Part 2
Challenges
17. Turn the lights on one at a time.
Hint: You can just add a delay(milliseconds)inside the "turn-on" for loop! Perhaps use 100 for the number of milliseconds.
18. Turn the lights on and off one at a time.
Hint: Similar to #17, but for the "turn-off" for loop
19. Have the lights turn on and off in reverse order!
Hint: You will have to reverse the "turn on" and "turn off" for loops –
see if you can do it!
9

## Slide 10
LED Challenges Part 2
Challenges
20. Turn on only every other LED light.
Hint: Look at where the loop variable increases:
(the “step of” section of the “repeat
Between” block)
Try changing the amount from 1 to 2…
21. Vegas Lights!
Have the lights alternate between turning all the even numbered pins on and turning all the odd numbered pins on.
10

## Slide 11
LED Challenges Part 2
Challenges
22. Create the hypnotizer:
Here, the lights go on from each end toward the middle, together:
23. Create your own pattern of blinking lights!
Be creative!
You can customize colors in your breadboard and
customize the pattern of lights with your code!
and then they turn off in reverse
11