## Slide 1
Motors: Getting Started
There are a lot of cool things you can do with an Arduino board. For now we’re going to focus on controlling a servo motor. In order to do this you need the following parts:
Arduino board
Servo motor
3 wires

## Slide 2
Motors: Getting Started
Now before you start programming the servo motor you need to properly connect it to the Arduino board.
There should be three wires coming out of the motor. One wire should be red, one should be black, and one should be white. Connect the red wire to the 5V pin on the Arduino board, connect the black wire to the GND pin on the Arduino board (GND stands for “ground”), and connect the white wire to one of the digital pins labeled 2 through 13 on the Arduino board.
We will use pin 13.
Your circuit should look similar to this:

## Slide 3
Motor Starter Code
Open the Generic Hardware menu, and create the following program:
Next, go to the challenges
This program makes the servo motor (attached to pin 13) rotate at full speed in one direction. Changing the angle to 180 sets it to full speed in the other direction.

## Slide 4
Challenges
1. Get the motor to turn counterclockwise
Hint: The command myservo.write(integer)tells the object myservo to spin at the speed indicated by the integer value passed in. This integer value can be between 0 and 180: both 0 and 180 are top speeds! (different directions).
2. Get the motor to turn clockwise.
3. Figure out the value that makes the motor turn as SLOWLY as possible.
Hint: It's close to 90, but not always exactly 90.
4. Have the motor spin at top speed in one direction, stop, and then spin at top speed in the other direction.
4. Have the motor start out stationary and then gradually increase the speed of the motor.
Hint: You definitely want to use a loop for this problem…
Grab a for loop from your other code and modify it!
5. Create a decoration to place on your motor. Then write a program to have your decoration spin around in some way.
Motors: Challenges

## Slide 5
Photosensors: getting started
Let's add a sensor! Here is a photosensor:
To hook this up to the Arduino, you need to have a yellow-violet-red resistor
and you will want to
(1) hook up the resistor to +5 V
(2) place the photosensor in the same row as the other side of the resistor
(3) hook the other side of the photosensor to ground
(4) place a wire in the same row where the resistor and photosensor meet
(5) hook that wire up to the analog inputs of the Arduino…
Here are a couple of pictures (bigger on the next page)

## Slide 8
Photosensor Starter Code
Type this starter program – and try it out!
int value = 0;
void setup()
{
Serial.begin(9600); // print to serial port
}
void loop()
{
delay(500);
value = analogRead(0);
Serial.println(value, DEC);
}
You will need to open the serial port to see the readings:
This is the button:

## Slide 9
Challenges
1. See what values the photosensor gives…
Hint: Ask yourself if more light leads to higher values or lower ones…
See how high or low you can make the readings.
2. Choose a darkness threshold. When it's dark, make an LED go on.
When it's light, make the LED go off.
Hint: You will need to combine your ideas from the LED circuit!
3. When it's dark, make a motor go on.
When it's light, make the motor turn off.
Hint: Use your ideas from the motor circuit.
4. [Light meter challenge]
If it's darker, have more LEDs turn on; as it gets lighter, fewer are on.
Hint: You can use the map function:
numleds = map(value,0,1023,0,8);
Photosensors: Challenges