## Slide 1
CS 101010 Today
Hmmm… What is this all about?
No office hours this week
Thursday (9/30): Class in Galileo Edwards
HW5 due Monday Oct 4, 11:59pm
Tools of the trade
Arithmetic, revisited

## Slide 2
Assembly Language
Computer Architecture
Digital circuit design
Loops in AL
Functions and recursion in AL
Machine Language
More concrete
More abstract
A translation of the 1s and 0s
into something human-readable
sequences of 1s and 0s that drive the
hardware to perform the necessary functions
collections of circuits that can perform
all the needed functions to manipulate data
how to turn functions into hardware
how to use AL to do stuff that's useful
to humans

## Slide 3
Assembly Language
Computer Architecture
Digital circuit design
Loops in AL
Functions and recursion in AL
Machine Language
More concrete
More abstract
Today + Tuesday
Tuesday + Thursday
Tues 10/4
Tues 10/4
Thurs 10/6

## Slide 4
Hmmm
CPU
RAM
central processing unit
random access memory
Von Neumann bottleneck
read r1
0
1
2
3
4
5
…
6
255
halt
255 memory locations of 16 bits
r0
…
16 registers,
each 16 bits
r15
they can hold values from -32768 upto 32767
r1
r2
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
The Harvey Mudd Miniature Machine
mul r2 r1 r1
add r2 r2 r1
write r2
0
register 0
is “hard-wired”
to store 0

## Slide 5
Hmmm
CPU
RAM
central processing unit
random access memory
Von Neumann bottleneck
read r1
0
1
2
3
4
5
…
6
255
halt
255 memory locations of 16 bits
r0
…
16 registers,
each 16 bits
r15
they can hold values from -32768 upto 32767
r1
r2
Program Counter
Instruction Register
Holds the current instruction
Holds address of the next instruction
The Harvey Mudd Miniature Machine
mul r2 r1 r1
add r2 r2 r1
write r2
0
register 0
is “hard-wired”
to store 0
NOTE:
The Hmmm "machine" is does not exist in hardware.
It exists in simulation only (in Python).
We'll see it in action NOW!
Notes: HMMM Demo here. Show how to run Python. How to change programs. etc.

## Slide 6
Resources
http://www.cs.hmc.edu/~cs5grad/cs5/hmmm/documentation/documentation.html

## Slide 7
00 loadn r1 21
01 loadn r2 2
02 mul r3 r1 r2
03 add r4 r3 r0
04 sub r5 r1 r2
05 jltz r5 7
06 addn r2 42
07 halt
When this code completes, what is in register r5?
40
-40
19
-19
7

## Slide 8
00 loadn r1 21
01 loadn r2 2
02 mul r3 r1 r2
03 add r4 r3 r0
04 sub r5 r1 r2
05 jltz r5 7
06 addn r2 42
07 halt
When this code completes, what is in register r1?
21
42
84
2
7

## Slide 9
00 loadn r1 21
01 loadn r2 2
02 mul r3 r1 r2
03 add r4 r3 r0
04 sub r5 r1 r2
05 jltz r5 7
06 addn r2 42
07 halt
When this code completes, what is in register r3?
21
42
84
2
7

## Slide 10
00 loadn r1 21
01 loadn r2 2
02 mul r3 r1 r2
03 add r4 r3 r0
04 sub r5 r1 r2
05 jltz r5 7
06 addn r2 42
07 halt
When this code completes, what is in register r4?
21
42
84
2
7

## Slide 11
00 loadn r1 21
01 loadn r2 2
02 mul r3 r1 r2
03 add r4 r3 r0
04 sub r5 r1 r2
05 jltz r5 7
06 addn r2 42
07 halt
When this code completes, what is in register r2?
2
42
84
44
7

## Slide 12
00 read r1
01 write r1
02 addn r1 1
03 jgtz r1 01
04 halt
What will the above code do?
Print a number entered by the user on the screen and then halt.
Print a sequence of numbers, counting up by one from the original number entered by the user, and never halt
Both A and B are correct.
None of the above is correct.
I have no idea

## Slide 13
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
r0
r1
r13
Input value: x
Final result - in progress
0
Step 1: Plan your registers
r0 is ALWAYS 0!
Holds N
Holds the answer

## Slide 14
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r13 will hold the return value
Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Check to see if N%2 is zero
If so, write and halt.
Otherwise, add 1 to r13 and go to step 3

## Slide 15
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Check to see if N%2 is zero
If so, write and halt.
Otherwise, add 1 to r13 and go to step 2
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13

## Slide 16
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Check to see if N%2 is zero
If so, write and halt.
Otherwise, add 1 to r13 and go to step 2
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
More than 1 hmmm instruction

## Slide 17
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r3 in r2
Jump to the end if r2 is 0
If so, write and halt.
Otherwise, add 1 to r13 and go to step 2
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13

## Slide 18
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r13 in r2
Jump to the end if r2 is 0
If so, write and halt.
Otherwise, add 1 to r13 and go to step 2
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
02 mod r2 r1 r13 # r2 = r1%r13
03 jeqz r2 ?? # Jump to the end if r1%r13 is 0 (we don't know where yet)

## Slide 19
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r13 in r2
Jump to the end if r2 is 0
If so, write and halt.
Otherwise, add 1 to r13 and go to step 2
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
02 mod r2 r1 r13 # r2 = r1%r13
03 jeqz r2 ?? # Jump to the end if r1%r13 is 0 (we don't know where yet)
Not quite ready for this…

## Slide 20
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r13 in r2
Jump to the end if r2 is 0
If not, add 1 to r13
Jump back to line 2 (i.e., address 02)
The end: write result (r13)
halt
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
02 mod r2 r1 r13 # r2 = r1%r13
03 jeqz r2 ?? # Jump to the end if r1%r13 is 0 (we don't know where yet)

## Slide 21
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r13 in r2
Jump to the end if r2 is 0
If not, add 1 to r13
Jump back to line 2 (i.e., address 02)
The end: write result (r13)
halt
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
02 mod r2 r1 r13 # r2 = r1%r13
03 jeqz r2 ?? # Jump to the end if r1%r13 is 0 (we don't know where yet)
04 addn r13 1 # Add 1 to r1
05 jump 02 # Repeat the loop
06 write r13 # if we get here we're done
07 halt

## Slide 22
More Examples
Smallest Factor
Write a Hmmm function that finds the smallest prime factor of a number
Step 2: Plan your function
# r0 is 0
# r1 will hold N
# r2 holds intermediate mod calculation
# r13 will hold the return value
0. Get a number from the user
Store 2 (the smallest prime) in the return register (r13)
Store r1 mod r13 in r2
Jump to the end if r2 is 0
If not, add 1 to r13
Jump back to line 2 (i.e., address 02)
The end: write result (r13)
halt
00 read r1 # Get a number from the user
01 loadn r13 2 # Store 2 (smallest prime) in r13
02 mod r2 r1 r13 # r2 = r1%r13
03 jeqz r2 06 # Jump to the end if r1%r13 is 0 (we don't know where yet)
04 addn r13 1 # Add 1 to r1
05 jump 02 # Repeat the loop
06 write r13 # if we get here we're done
07 halt

## Slide 23
Base 10
What is 42 ?
42
4 tens + 2 ones
123
1 hundred + 2 tens + 3 ones
ONEs column
TENs column
ONEs column
TENs column
HUNDREDs column

## Slide 24
--------
Base 2
Base 10
42
4 tens + 2 ones
101010
123
1 hundred + 2 tens + 3 ones
ONEs column
TENs column
ONEs column
TENs column
HUNDREDs column
each column represents another power of the base
ONEs column
TWOs column
FOURs column
EIGHTs column
SIXTEENs col.
THIRTYTWOs col.
ONEs column
TWOs column
FOURs column
EIGHTs column
SIXTEENs col.
THIRTYTWOs col.
SIXTYFOURs col
128s column
Write 123 in binary…

## Slide 25: Counting in base b
Try this…
Count from zero to six in each of the following bases:
Base 2:
Base 3:
What’s the “algorithm” for counting in a general base b?
Hey, who are you?

## Slide 26: Is There Such a Thing as Base 1?
Now we’re using
powers of 1 (Weird!)
13 12 11 10
Unary!
Are we going to use 0 as our only digit?
Notes: By convention, we use 1’s as our only digit, even though this is not consistent with our earlier convention. Unary is an exception.

## Slide 27: Comparing Representations in Different Bases
Consider the number 109 in base 1, 2, 3, 10, and 20:
Base 1: 11111111111111111111111111111111111111111111…
Base 2: 111011100110101100101000000000
Base 3: 2120200200021010001
Base 10: 1000000000
Base 20: FCA0000
At 10 “1’s” per inch, this will be 1578 miles long!
What’s the ratio between the lengths of a number in bases x and y?
Notes: Moral of the story: Unary is not viable! All bases other than unary are “OK” and are “more or less” the same in the length of the representation.

## Slide 28
Binary math
tables of basic facts
Decimal math
+
*
Addition
Multiplication

## Slide 29: Addition
102 101 100
Base 10 Addition
4 3
+ 8 9

## Slide 30: Addition
102 101 100
Base 10 Addition
4 3
+ 8 9
2
That’s a “10”
1

## Slide 31: Addition
102 101 100
Base 10 Addition
4 3
+ 8 9
2
Move the “1” to the ten’s place
1

## Slide 32: Addition
102 101 100
Base 10 Addition
4 3
+ 8 9
2
Done!
1
13

## Slide 33: Addition
102 101 100
Base 10 Addition
4 3
+ 8 9
2
1
13
22 21 20
Base 2 Addition
Try it in base 2!
1 0 1
0 1 1
+
Notes: After doing the addition in base 2, have them convert the summands and the sum to base 10 and verify solution.

## Slide 34: Multiplication
102 101 100
Base 10 Multiplication
3 4 1
1 0 2

Notes: What’s with the shifting?

## Slide 35: Multiplication
102 101 100
Base 10 Multiplication
3 4 1
1 0 2

6 8 2
0 0 0
3 4 1
+
Notes: What’s with the shifting?

## Slide 36: Multiplication
102 101 100
Base 10 Multiplication
3 4 1
1 0 2

6 8 2
0 0 0
3 4 1
+
3 4 7 8 2
Notes: What’s with the shifting?

## Slide 37: Multiplication
102 101 100
Base 10 Multiplication
3 4 1
1 0 2

6 8 2
0 0 0
3 4 1
+
3 4 7 8 2
Base 2 Multiplication
22 21 20
1 1
1 0 1

Notes: Base 10: What’s with the shifting?

## Slide 38
"Quiz"
There are 10 kinds of "people" in the universe: those who use binary, and those who do not!
Convert these two decimal numbers to binary:
Add these two binary numbers:
529
742
1271
1
Hint: Remember this algorithm? It's the same…
+
Convert these two binary numbers to decimal:
110011
10001000
1
2
16
32
4
8
101
28
101101
1110
+
WITHOUT converting to decimal !
Multiply these binary numbers:
101101
1110
*

## Slide 39
Convert these two binary numbers to decimal:
110011
10001000
1
2
16
32
4
8
51
42
15
102
I'm not sure

## Slide 40
Convert these two binary numbers to decimal:
110011
10001000
1
2
16
32
4
8
10001
136
16
128
I'm not sure

## Slide 41
Convert these two decimal numbers to binary:
101
28
10001
1010
10101
11100
I'm not sure

## Slide 42
Convert these two decimal numbers to binary:
101
28
1001001
01100101
110011
10000001
I'm not sure

## Slide 43
Add these two binary numbers WITHOUT converting to decimal !
Hint:
529
742
1271
1
Do you remember this algorithm? It's the same!
+
101101
1110
+
111011
101111
100011
1011011
I'm not sure

## Slide 44
MULTIPLY these two binary numbers WITHOUT converting to decimal !
Hint:
529
42
1058
Do you remember this algorithm? It's the same!
*
101101
1110
*
2116
22218

## Slide 45
How functions work…
How could we write this in Hmmm?
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Notes: vault 713?

## Slide 46
How functions work…
def f(x):
return 11*g(x) + g(x/2)
def demo(x):
return x + f(x)
def g(x):
return -1 * x
One idea…
Observe that the above code can be simplified to:
def demo(x):
return x + 11*g(x) + g(x/2)
And then simplified again to:
def demo(x):
return x + 11*-1*x + -1*x/2
Notes: vault 713?

## Slide 47
How functions work…
def f(x):
return 11*g(x) + g(x/2)
def demo(x):
return x + f(x)
def g(x):
return -1 * x
One idea…
Observe that the above code can be simplified to:
def demo(x):
return x + 11*g(x) + g(x/2)
And then simplified again to:
def demo(x):
return x + 11*-1*x + -1*x/2
read r1 # get the input
loadn r4 -1
mul r2 r1 r4 # calculate –x
loadn r5 2 # load 2 into r5
div r3 r2 2 # calculate –x/2
loadn r6 11 # load 11 into r6
mul r2 r2 r6 # calculate –x*11
add r13 r1 r2 # calculate -11x + x
add r13 r13 r3 # calculate -11x+x+1x/2
write r13 # output the result
halt
Notes: vault 713?

## Slide 48
How functions work…
def f(x):
return 11*g(x) + g(x/2)
def demo(x):
return x + f(x)
def g(x):
return -1 * x
One idea…
Observe that the above code can be simplified to:
def demo(x):
return x + 11*g(x) + g(x/2)
And then simplified again to:
def demo(x):
return x + 11*-1*x + -1*x/2
What's the problem here??
read r1 # get the input
loadn r4 -1
mul r2 r1 r4 # calculate –x
loadn r5 2 # load 2 into r5
div r3 r2 2 # calculate –x/2
loadn r6 11 # load 11 into r6
mul r2 r2 r6 # calculate –x*11
add r13 r1 r2 # calculate -11x + x
add r13 r13 r3 # calculate -11x+x+1x/2
write r13 # output the result
halt
Notes: vault 713?

## Slide 49
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 50
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 51
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 52
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 53
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 54
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 55
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 56
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 57
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 58
How functions work…
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
Another idea… register "agreement"
I want my input in r1, and I'll put my output in r2
I want my input in r3, and I'll put my output in r4
I want my input in r5, and I'll put my output in r6
r1-r6 are "taken"
00 read r1 # input to demo
01 add r3 r1 r0 # move r1 to r3 to "pass"
# input to f
02 add r5 r3 r0 # move r3 to r5 to "pass"
# input to g
03 loadn r7 -1 # load -1 into a "free" register
04 mul r6 r5 r7 # g multiplies its input
# by -1 and "returns" it in r6
05 loadn r8 11 # load 11 into a "free" register
06 mul r9 r6 r8 # multiply the result of g by 11
07 loadn r10 2 # load 2 into a "free" register
08 div r5 r3 r10 # divide x by 2 and "pass" it
# to g
09 mul r6 r5 r7 # g multiplies its input by -1
# and "returns" it in r6
10 add r4 r6 r9 # calculate -11*g(x) + g(x/2)
# and "return" it in r4
11 add r2 r1 r4 # in demo, calculate x + f(x)
# and "return" it in r2
12 write r2 # write the result
13 halt # halt
Notes: vault 713?

## Slide 59
Pros and Cons of "register agreement"?
Notes: vault 713?

## Slide 60
Pros and Cons of "register agreement"?
Pros
  Conventions make functions general
  Keeps functions from "Stepping on" each other
Cons
  How do functions agree on who uses each register?
  How do we get all the instructions in order (and note the repeated code for the two calls to g)
  What if there are too many functions and registers fill up??
Notes: vault 713?

## Slide 61
Remember function stacking?
What is demo(-4) ?
demo
x = -4
return -4 + f(-4)
f
g
x = -4
return 11* 4 + g(-4/2)
x = -2
return -1 * -2
2
"The stack"
Remembers separate functions' values for variables…
Remembers where to send results back to…
(define (g x)
(* -1 x))
(define (demo x)
(+ x (f x)))
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
Notes: vault 713?

## Slide 62
How functions REALLY work…
Register agreement + the STACK
r1,r2,…
r13
r14
r15
function inputs
return value
return address
stack pointer
OUR "agreements":
When a function calls another function it will…
Save all of its important data in the stack
Put the inputs in r1, r2, r3…
Call the function…
(automatically) storing its return address in r14
And expect the results in r13
Retrieve its data from the stack
(define (g x)
(* -1 x))
(define (demo x)
(+ x (f x)))
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
Notes: vault 713?

## Slide 63
Where is the stack?
r1
…
Hmmm RAM
Hmmm CPU
read r1
r15
0
1
2
3
4
5
…
42
43
…
read r2
mul r3 r2 r1
write r3
halt
The program
The STACK!

## Slide 64
Key Idea: What's in RAM
Hmmm RAM
read r1
0
1
2
3
4
5
…
42
43
…
read r2
mul r3 r2 r1
write r3
halt
The program
The STACK!
The program and the stack SHARE
the RAM
program = low RAM stack = high RAM

## Slide 65
store goes TO memory
r1
…
Hmmm RAM
Hmmm CPU
read r1
r15
0
1
2
3
4
5
…
42
read r2
.
loadn r15 42
storei r1 r15
43
…
42
storei r1 r15
42
aliens
.
direct store
indirect store
store r2 43
r2

## Slide 66
load comes FROM memory
r1
…
Hmmm RAM
Hmmm CPU
.
r15
0
1
2
3
4
5
…
6
7
8
42
.
.
.
.
43
…
42
storei r1 r15
42
aliens
42
loadi r1 r15
aliens
load r2 43
.
loadi r1 r15
.
direct load
indirect load
r2

## Slide 67
call
A function call in Racket:
Hmmm's call operation:
call r14 4
puts NEXT line # into r14,
then jumps to line 4
(define (main)
(let* ((r1 (read-line)))
(result (demo r1)))
(display result)))
(define (demo x)
(+ x (f x)))

## Slide 68
How functions REALLY work…
I want my input in r1, and I'll put my output in r13
I want my input in r1, and I'll put my output in r13
I want my input in r1, and I'll put my output in r13
00 read r1 # Get the user's input
01 loadn r15 SA # Store the top of the stack
02 call r14 DEMO # Call demo, starts at line ??
03 write r13 # Demo has returned,
# so just write and halt
04 halt
TBD
(define (main)
(let* ((r1 (read-line)))
(result (demo r1)))
(display result)))
(define (demo x)
(+ x (f x)))
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (g x)
(* -1 x))
Notes: vault 713?

## Slide 69
How functions REALLY work…
I want my input in r1, and I'll put my output in r13
I want my input in r1, and I'll put my output in r13
I want my input in r1, and I'll put my output in r13
00 read r1 # Get the user's input
01 loadn r15 SA # Store the top of the stack
02 call r14 DEMO # Call demo, starts at line ??
03 write r13 # Demo has returned,
# so just write and halt
04 halt
# ** demo begins here **
# First calculate f(x)
# Prepare: store data
05 storei r1 r15 # Store x on the stack
06 addn r15 1 # Increment stack pointer
07 storei r14 r15 # Store our return address
08 addn r15 1 # increment the stack pointer
# Prepare input: r1 already
# contains x
09 call r14 F # Call f(x)
10 addn r15 -1 # F has returned. decr sp
11 loadi r14 r15 # Get our return address
12 addn r15 -1 # decrement the stack pointer
13 loadi r1 r15 # Get x back
14 add r13 r13 r1 # r13 = f(x) + x
15 jumpi r14 # Demo is done so return
(define (main)
(let* ((r1 (read-line)))
(result (demo r1)))
(display result)))
(define (demo x)
(+ x (f x)))
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (g x)
(* -1 x))
Notes: vault 713?

## Slide 70
00 read r1 # Get the user's input
01 loadn r15 SA # Store the top of the stack
02 call r14 DEMO # Call demo, starts at line ??
03 write r13 # Demo has returned,
# so just write and halt
04 halt
# ** demo begins here **
# First calculate f(x)
# Prepare: store data
05 storei r1 r15 # Store x on the stack
06 addn r15 1 # Increment stack pointer
07 storei r14 r15 # Store our return address
08 addn r15 1 # increment the stack pointer
# Prepare input: r1 already
# contains x
09 call r14 F # Call f(x)
10 addn r15 -1 # F has returned. decr sp
11 loadi r14 r15 # Get our return address
12 addn r15 -1 # decrement the stack pointer
13 loadi r1 r15 # Get x back
14 add r13 r13 r1 # r13 = f(x) + x
15 jumpi r14 # Demo is done so return
… [MORE CODE HERE]
50
51
52
53
Let's say SA is 50…
(We can't really know until we know how much code we have)
Main memory (RAM)
r0
r1
r13
Input value: x
Final result - return value - in progress
0
r14
location / line to return TO
r15
Stack pointer
CPU (registers)
Notes: vault 713?

## Slide 71
00 read r1 # Get the user's input
01 loadn r15 50 # Store the top of the stack
02 call r14 5 # Call demo, starts at line 9
03 write r13 # Demo has returned,
# so just write and halt
04 halt
# ** demo begins here **
# First calculate f(x)
# Prepare: store data
05 storei r1 r15 # Store x on the stack
06 addn r15 1 # Increment stack pointer
07 storei r14 r15 # Store our return address
08 addn r15 1 # increment the stack pointer
# Prepare input: r1 already
# contains x
09 call r14 F # Call f(x)
10 addn r15 -1 # F has returned. decr sp
11 loadi r14 r15 # Get our return address
12 addn r15 -1 # decrement the stack pointer
13 loadi r1 r15 # Get x back
14 add r13 r13 r1 # r13 = f(x) + x
15 jumpi r14 # Demo is done so return
… [MORE CODE HERE]
50
51
52
53
Main memory (RAM)
r0
r1
r13
Input value: x
Final result - return value - in progress
0
r14
location / line to return TO
r15
Stack pointer
CPU (registers)
Notes: vault 713?

## Slide 72
00 read r1 # Get the user's input
01 loadn r15 50 # Store the top of the stack
02 call r14 5 # Call demo, starts at line 9
03 write r13 # Demo has returned,
# so just write and halt
04 halt
# ** demo begins here **
# First calculate f(x)
# Prepare: store data
05 storei r1 r15 # Store x on the stack
06 addn r15 1 # Increment stack pointer
07 storei r14 r15 # Store our return address
08 addn r15 1 # increment the stack pointer
# Prepare input: r1 already
# contains x
09 call r14 F # Call f(x)
10 addn r15 -1 # F has returned. decr sp
11 loadi r14 r15 # Get our return address
12 addn r15 -1 # decrement the stack pointer
13 loadi r1 r15 # Get x back
14 add r13 r13 r1 # r13 = f(x) + x
15 jumpi r14 # Demo is done so return
… [MORE CODE HERE]
50
51
52
53
Main memory (RAM)
CPU (registers)
Store data
Prepare data to pass
Call function
Restore data (in REVERSE order)
Notes: vault 713?

## Slide 73
00 read r1 # Get the user's input
01 loadn r15 50 # Store the top of the stack
02 call r14 9 # Call demo, starts at line ??
03 write r13 # Demo has returned,
# so just write and halt
04 halt
# ** demo begins here **
# First calculate f(x)
# Prepare: store data
05 storei r1 r15 # Store x on the stack
06 addn r15 1 # Increment stack pointer
07 storei r14 r15 # Store our return address
08 addn r15 1 # increment the stack pointer
# Prepare input: r1 already
# contains x
09 call r14 16 # Call f(x)
10 addn r15 -1 # F has returned. decr sp
11 loadi r14 r15 # Get our return address
12 addn r15 -1 # decrement the stack pointer
13 loadi r1 r15 # Get x back
14 add r13 r13 r1 # r13 = f(x) + x
15 jumpi r14 # Demo is done so return
(define (main)
(let* ((r1 (read-line)))
(result (demo r1)))
(display result)))
(define (demo x)
(+ x (f x)))
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (g x)
(* -1 x))
Notes: vault 713?

## Slide 74
(define (f x)
(+ (* 11 (g x))
(g (/ x 2))))
(define (demo x)
(+ x (f x)))
(define (g x)
(* -1 x))
(define (main)
(let* ((r1 (read-line)))
(result (demo r1)))
(display result)))
# ****f begins here
16 storei r1 r15 # store our x
17 addn r15 1 # increment the stack pointer
18 storei r14 r15 # store our return address
19 addn r15 1 # increment the stack pointer
# r1 already contains x
20 call r14 44 # Call g(x)
# g(x) has returned
21 addn r15 -1 # decrement the stack pointer
22 loadi r14 r15 # get our return address back
23 addn r15 -1 # decrement the stack pointer
24 loadi r1 r15 # get x back
25 loadn r5 11 # load 11 into r5
26 mul r5 r13 r5 # r5 = 11*g(x)
27 storei r1 r15 # store x, prep for g again
28 addn r15 1 # increment stack pointer
29 storei r5 r15 # store our intermediate calculation
30 addn r15 1 # increment stack pointer
31 storei r14 r15 # store our return address
32 addn r15 1 # increment stack pointer
33 loadn r6 2 # prepare input
34 div r1 r1 r6 # x = x / 2
35 call r14 44 # call g(x/2)
36 addn r15 -1 # g is back, decr sp
37 loadi r14 r15 # get the return address
38 addn r15 -1 # decrement sp
39 loadi r5 r15 # get our intermediate value
40 addn r15 -1 # decrement the stack
41 loadi r1 r15 # get x back
42 add r13 r13 r5 # return g(x/2) + 11*g(x) (r13 + r5)
43 jumpi r14 # F is done!
# *** g starts here ***
44 loadn r5 -1 # prepare to multiply
45 mul r13 r1 r5 # return -1 * x
46 jumpi r14 # done, so return
Notes: vault 713?

## Slide 75
Implementing functions
(1) Before the function call,
non-destructively!
Store all valuable data to the stack
(2) Get r1, (r2), (r3), … ready as function "inputs."
The result, if any, will be in r13.
(3) Make the function call.
(0) Use r15 as the stack pointer.
loadn r15 42
or some other large-enough value
storei r1 r15
addn r15 1
store the return address r14 and the inputs: r1, (r2), (r3)
There may or may not be some lines of code necessary to do this.
(4) After the function call,
Load valuable data back from the stack
addn r15 -1
loadi r1 r15
call r14 #
line # of the function
for each item stored