## Slide 1
Task 1: Follow that !
We put a ! on the Create to
  help discern location
  help discern orientation
Image processing approach:
  (1) threshold image to find dark regions and contours
  (2) circle? compare region with min. enclosing circle
  (3) rectangle? compare region with min. enclosing rect.
  (4) filter noise, find centers, and construct heading line

## Slide 2
! finding
original
wall segmentation
contours

## Slide 3: GCER!

## Slide 4
GCER cooperation demo
2x

## Slide 5
Lessons learned
  The ! was far from a perfect landmark
  We wanted to use something more robust that could give us more accurate pose estimation
  We decided to explore April Tags...

## Slide 6
APRIL tags
Autonomy, Perception, Robotics, Interfaces, and Learning
Java-based landmark library from U. Michigan
We integrated it into ROS using Python's os.system call...
an example tag in the center...
provides full 6 DOF pose and scale

## Slide 7
APRIL tags' scale range
an example tag in the center...
provides full 6 DOF pose and scale
... when it's visible

## Slide 8
Task 2: The Hula-hoop hop
Getting from A to B
A
B

## Slide 9
getting from point A to point B
Task 2: The Hula-hoop hop

## Slide 10
Hula-hop's state machine
all transitions can also be made by the keyboard

## Slide 11
Hula-hop demo
sliding-scale autonomy is crucial
2x

## Slide 12
Hula-hop challenges
Drone challenges:
  drift ~ not easily positionable
  connection ~ video freezes
  artifacts ~ image stream noise
APRIL tag challenges:
  too narrow a field of view: height/scale tradeoffs
  call to APRIL library is slow (.5 second/image)
  unmodifiable environments?
Could we do without tags?
example encoding (?) artifact

## Slide 13
Localization without tags?
SURF features
  locally unique image patches
  fast libraries for extraction
  each SURF feature is described with a 64-dimensional vector that encodes size and local edge orientations
  in general, similar descriptor vectors are likely to be similar (or identical) image features

## Slide 14
Localization plan
Mapping (by hand)
  collect images and positions
  extract & store SURF features
Localization
  take a new image
  extract SURF features
  match them against the map
  estimate a pose distribution
new image
map images + matches

## Slide 15
Image-based map...
Locations with stored images == nodes in a graph
four locations in the NW corner of Sprague

## Slide 16
Image-based map...
beside the kitchen, facing roughly W

## Slide 17
Image-based map...
beside the boardgames, facing roughly N

## Slide 18
Live localization
top three matches and their likelihood distribution plotted on the map

## Slide 19
Demo...

## Slide 20
Results
Simply counting the # of matches did not yield good localization results:
< 25% of correct locations
< 10% of correct orientations
matches m
S
simple image-match score
1

## Slide 21
Other scoring systems...
matches m
S
distance-scaled score
1
e + dist(m)
... and filters
bidirectional matches only
strong ratio-matches only
weights features inversely proportional to their SURF distance
omits features whose 2nd nearest neighbor is about as good a match as its 1st nearest neighbor
omits features whose best match is not unique in both directions

## Slide 22
Without bidirectional filtering
many different features can have the same best match

## Slide 23
With bidirectional filtering
only mutually unique best matches are considered

## Slide 24
Comparative results

## Slide 25
The AR Drone is a capable platform
-- as long as precise positioning is not required
Options:
    research to improve localization
    tasks that do not require precision
The ROS software scaffolding is excellent
-- if not always thoroughly documented
The project's AR Drone drivers and supporting software generated interest at AAAI and will be released into the community's (Willow Garage's) repository.
Verdicts?

## Slide 26
Postscript
Room/hallway flying with forward camera