## Slide 1
Interdimensional Robot Cooperation
Kristina Ming, Chris Eriksen, Graham Montgomery,
Jerry Hsiung, Cyrus Huang, Zakkai Davidson, and Zach Dodds

## Slide 2
Now…
3d representations are a new standard for robot spatial reasoning, …
… yet 2d image sensing is still common – and will certainly continue to be for a long time.
… vs. Then

## Slide 3
Cooperating?!
Our goal: to investigate robot platforms, software, and algorithms for using 2d sensors amid 3d models of the world.
3d models
2d sensors

## Slide 4
Two concrete challenges…
more robust navigation
more general "lab escape"
bridging 2d sensors with 3d spatial representations

## Slide 5
Jerry, Cyrus, Zakkai

## Slide 6
New platform: Neato
Objective: to get this robot running and reasoning
Initial tasks
learn ASCII API
write device drivers
interpret sensor data
follow corridors
detect intersections
pt-to-pt navigating
localize and navigate
minimize ambiguity
navigate predictively
build 2d and 3d maps
AI Tasks

## Slide 7
New platform: Neato
laser-scan data, estimated walls, "aligning" wall
Initial tasks
learn ASCII API
write device drivers
interpret sensor data
follow corridors
detect intersections

## Slide 8
New platform: Neato
Initial tasks
learn ASCII API
write device drivers
interpret sensor data
follow corridors
detect intersections
wall-placement determines intersection type
This scan shows a "TL" intersection

## Slide 9
Neato navigation
navigating the Libra complex, with the start node given
robot_navigation_known_start
Notes: goal node has to be given, too – though there's no avoiding that…!

## Slide 10
Localization
What if the robot doesn't know its starting pose?
Don't worry about the goal.
Instead, make default motions…
Suppose the robot moves and sees
a "TL"
Which nodes remain?
Which are culled?
?

## Slide 11
Localization
What if the robot doesn't know its starting pose?
Don't worry about the goal.
Instead, make default motions…
With each observation, we
cull the robot's possible poses.
TL
TL

## Slide 12
Localization
previous distribution of poses
TL
TL
… cull again
Keep going…

## Slide 13
Localization
previous distribution of poses
TL
TL
… cull again
When it knows its location, head to the goal!

## Slide 14
Markov localization
navigating to a goal without the start node given
loc_short.mp4

## Slide 15
Can we be more deliberate?
Each intersection offers a choice:
Which turn to make, even if the robot isn't sure where it is?

## Slide 16
Can we be more deliberate?
Each intersection offers a choice:
Which turn to make, even if the robot isn't sure where it is?
Which way should we go?
We're at a TL…

## Slide 17
Can we be more deliberate?
Suppose the robot goes left…
2 LR
2 LL
5 DE
1 TL
This is the distribution of possible next corners it could see.

## Slide 18
Can we be more deliberate?
2 LR
2 LL
5 DE
1 TL
Suppose the robot goes left…

## Slide 19
Can we be more deliberate?
2 LR
2 LL
5 DE
1 TL
Suppose the robot goes left…

## Slide 20
Can we be more deliberate?
2 LR
2 LL
5 DE
1 TL
Suppose the robot goes left…

## Slide 21
Can we be more deliberate?
2 LR
2 LL
5 DE
1 TL
Suppose the robot goes left…

## Slide 22
Can we be more deliberate?
2
2
Suppose the robot goes straight…
1 LR
2 LL
1 TR
6 TL
the possibilities

## Slide 23
Which possibilities are better?
1 LR
2 LL
1 TR
6 TL
Which of these two possible actions (and their results) should we prefer?
straight
left
2 LR
2 LL
5 DE
1 TL

## Slide 24
Entropy
2 A
2 B
2 C
2 D
8 possibilities will remain!
4 A
4 B
0 C
0 D
8 A
0 B
0 C
0 D
Suppose there were 8 possibilities to begin with…
4 possibilities will remain!
2 possibilities will remain!
Flatter is better

## Slide 25
Entropy
2 A
2 B
2 C
2 D
Entropy ~ expected information.
2.00 bits
4 A
4 B
0 C
0 D
1.00 bit
8 A
0 B
0 C
0 D
0.0 bits
Entropy is the amount of uncertainty you expect to resolve by sampling a distribution.
Suppose there were 8 possibilities to begin with…

## Slide 26
Entropy
2 LR
2 LL
5 DE
1 TL
1.76 bits
Flatter is better
2 A
2 B
2 C
2 D
2.00 bits
4 A
4 B
0 C
0 D
1.00 bit
8 A
0 B
0 C
0 D
0.0 bits

## Slide 27
Go left!
1 LR
2 LL
1 TR
6 TL
straight
left
2 LR
2 LL
5 DE
1 TL
1.57 bits
1.76 bits
Flatter is better

## Slide 28
Entropy-based localization
entro_short.mp4

## Slide 29
Map-building
Ideally, mapping would be automated, as well…
Snapshot of Zakkai's brain while map-building…

## Slide 30
Autonomous Mapping
overlaying wall-lines using odometry
Notes: Graham start

## Slide 31
Mapping
slipping around the Olin Basement loop…

## Slide 32
Graham + Jerry

## Slide 33
gmapping
an algorithm for autonomous laser-based mapping
(1) adjust each scan's pose to best-fit previous scans
(2) search for distant-past similarities to "close loops"
straightens corridors
corrects slippage?
Olin basement loop
Beckman hallway

## Slide 34
gmapping
… can miss "obvious" loops
Laser scans aren't very distinctive
Better landmarks?
… probably texture in 3d
Beckman CS loop
Jacobs hallway

## Slide 35
2½-d mapping
Laser-scan of a corner
Assume wall-world: surfaces are vertical planes.
Create that "3d" representation
Texture it with the pixel colors ~ landmarks.
Idea:
Now, as vertical planes

## Slide 36
Painting the walls…
+
image of wall
laser scan of wall
Laser-scan of a wall
Image of the wall
textured model

## Slide 37
Painting the walls…
We can apply any geometry we like ~ here, a cylindrical panorama

## Slide 38
Where are the walls?
Raw laser scans lead to artifacts ~ walls vs. ribbons
linked to raw_corner_cropped.m4v

## Slide 39
Finding the walls
Extracting straight lines from laser scans yields too many of them
via the Hough transform
~24 lines extracted

## Slide 40
Selecting the best walls…
Use the Hough transform to find an initial set of wall segments
do
  Compute the slope and position of each segment
  Find a "close" pair of segments; remove them from set
  Merge the pair into a single segment and add to set
until no more "close" pairs exist.
~12 Hough lines
with all but 2 merged

## Slide 41
Better!
First, simplify the 3d structures, then paint them …
linked to hough_corner_3d_cropped.m4v

## Slide 42
Building the map…
Delegated to 2014: painting these walls in real time…
2p5d_mapped_hallway_cropped.m4v
the robot's final position…
… after creating its 2½-d map

## Slide 43
Chris + Kristina

## Slide 44
Or, use the Kinect: 3d mapping
Demonstration of RGBD-SLAM
SLAM ~ simultaneous localization and mapping

## Slide 45
The hot-air lab's map
Example of lab and hallway map created by RGBD-SLAM

## Slide 46
Two concrete challenges…
more robust navigation
more general "lab escape"
bridging 2d sensors with 3d spatial representations

## Slide 47
Escape the lab!
Localization-based loop:
(1) the drone grabs a 2d image
(2) the system matches that image into the 3d map to locate the drone
(3) once located, the drone computes its desired velocity and applies it
(4) after two seconds, stop and goto (1)
(given a known goal)

## Slide 48
Image matching
Our approach (well, really Kristina's):
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
new image (live)
many original images (stored)

## Slide 49
1st-best match
10th-best match
Image matching
for now, a linear search taking ~10 seconds for the hot-air map's 42 images
new image (live)
many original images (stored)

## Slide 50
One of the drone's escapes ~ 150 sec.
Results

## Slide 51
9 "landmarks"
0
1
2
3
4
5
6
7
8
live, novel images

## Slide 52
Their matches
0
1
2
3
4
5
6
7
8
live, novel images
map matches

## Slide 53
Map-based localization of those 9 estimated positions
Model

## Slide 54
Other runs
Why not localize once and just go!?
A view from the back of the lab

## Slide 55
don't use linear search!
do use multi-resolution search!!
use lack of features somehow
Verdicts & insights
Skeleton of next summer's robotics agenda…
What about next summer's robots?
slowness?
2d matching?
3d overall?
Yes!
surprisingly good!
not perfect
not fast… yet
more geometry to exploit
accuracy?
use 3d model to get "exact" location
opportunities!

## Slide 56
New platforms…
Microdrone
"The Sofa"
Thoughts? Questions?
LeapMotion

## Slide 57
(1) [anytime] Take our NSF research-finale survey!
(2) [afternoon] Create a slideshow of best summer images
-- it's great to have all of the images, but it's equally or more useful to have a slideshow of the highlights
(3) Let's show @ 4:30…
(4) [starting ~ 3:30] Save/archive your work
(5) Shutdown the HMC-owned computers
** Except in the games cubicle:
(6) Create lines of monitors, mice, cables, surge
protectors, computers, etc. along the back walls
(7) Clean/wipe off the workspace tabletops
(8) For kitchen, remove trash + clean surfaces/dishes
This afternoon…
www.cs.hmc.edu/~cs5grad/survey/

## Slide 58
Contributions…

## Slide 64
Accessing these 3d maps
saves each rgb image
and each depth image
Getting the data: by splicing into the code to extract the input images
our splicer

## Slide 65
Neato reasoning
Initial tasks
learn ASCII API
write device drivers
interpret sensor data
follow corridors
detect intersections
pt-to-pt navigating
localize and navigate
minimize ambiguity
navigate predictively
build 2d and 3d maps
AI Tasks
wall placement determines each intersection type

## Slide 66
Hough transform
Consider one point of a laser scan
These are all of the lines through it
Point space
Line space
x = 6
y = 8
r
q
y
x

## Slide 67
Hough transform
vertical line ~ q = 0
The dot is the line r = 6, q = 0
r
q
r = 6
q = 0
Point space
Line space
y
x

## Slide 68
Hough transform
y
x
angled line ~ q = 32°
The dot is the line r = 9.1, q = 32°
r = 9.1
r
q
Point space
Line space

## Slide 69
Hough transform
y
x
angled line ~ q = 90°
The dot is the line r = 8, q = 90°
r = 8
r
q
Point space
Line space

## Slide 70
Hough transform
three points of a laser scan
all the lines through all three
(dots ~ the shown horizontal lines)
(horizontal lines are shown)
y
x
r
q
Point space
Line space

## Slide 71
Hough transform
yield lines with substantial support in the original data
peaks here in line space
y
x
r
q
Point space
Line space

## Slide 72
Image matching?
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
new image
many original images

## Slide 73
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Extract features
matching?

## Slide 74
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Nearest-neighbor matching

## Slide 75
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep only two-way best matches

## Slide 76
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep geometrically realistic matches

## Slide 77
1st-best match
10th-best match
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Visual “closeness”

## Slide 78
1st-best match
10th-best match
Average feature distance ~ 40 px
Average feature distance ~ 270 px
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Pixel “closeness”

## Slide 79
Map-based navigation…

## Slide 80
Next: localization

## Slide 81
Accessing these models
3d lab model ~ with a surface added
the rendered view from that green cone

## Slide 82
Accessing these models
Cloud Compare is a visualizer that can include our own “annotations” …

## Slide 83
Zooming vs. Moving
zooming in to the balloon…
… vs. moving towards/past it
CloudCompare
MeshLab

## Slide 84
Using these models
How might a robot with an ordinary camera, i.e., only 2d sensing, use these 3d models?
Ideally, a 2d sensing system could localize – and reason – within a 3d model
2d – 2d matching
3d – 3d matching

## Slide 85
2d – 2d matching
with a new image from a robot (or other device)
vs. original images
vs. rendered images
These are the images used to create the 3d model in the first place: fewer, higher-fidelity.
Images yielded by the 3d model: arbitrarily many, but lower-quality.
we could compare

## Slide 86
2d – 2d matching
with a new image from a robot (or other device)
vs. original images
vs. rendered images
These are the images used to create the 3d model in the first place: fewer, higher-fidelity.
Images yielded by the 3d model: arbitrarily many, but lower-quality.
we could compare

## Slide 87
Matching?
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
new image
many original images

## Slide 88
Features
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances

## Slide 89
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Nearest-neighbor matching

## Slide 90
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep only two-way best matches

## Slide 91
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep geometrically realistic matches

## Slide 92
1st-best match
10th-best match
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Visual “closeness”

## Slide 93
1st-best match
10th-best match
Average feature distance ~ 40 px
Average feature distance ~ 270 px
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Pixel “closeness”

## Slide 94
PCL: Point Cloud Library
3D-Reasoning
Easy point cloud access
Screenshot

## Slide 95
NARFs!
3d features: Normal Aligned Radial Features
picture of NARFS
picture of pt cloud
NARF features are purely based on the range image of a point cloud: its geometry, not its looks (SIFT)
They are based on the normals of the point cloud’s surfaces
They are places distinguishable from multiple perspectives.

## Slide 96
3d matching
picture of pt cloud w/NARFS
picture of pt cloud w/NARFS
Take two point clouds
Find NARFs
Match features and find transform
Make transform and combine
naive merging

## Slide 97
3d SLAM
Simultaneous Localization And Mapping
Take two point clouds
Find NARFs
Match features and find transform
Make transform and combine

## Slide 98
3d SLAM
Simultaneous Localization And Mapping
Take two point clouds
Find NARFs
Match features and find transform (ICP)
Make transform and combine

## Slide 99
3d SLAM
Final point cloud map
Questions?
Future: using Neato to create 2.5d maps

## Slide 101
Kinect
The Kinect estimates distance-to-camera by projecting a “star field” on the world.
Z.D. video

## Slide 102
Now vs. Then

## Slide 103
Title

## Slide 104
Accessing these models
allows us to define the depth at each pixel
plane
other (sphere, cylinder, wavy,…)
K.M.

## Slide 105
Ideally, a camera-only system could localize – and reason – within the 3d model
Ideally, a camera-only system could localize – and reason – within the 3d model

## Slide 106
Intersection recognition
still image
Check for Front, Left, and Right obstacles
The number of obstacles determines the intersection type 3:D 2:L 1:T 0:+
Open space determines final label, e.g., TL
After 15 recognitions in a row, the robot checks the map (by broadcasting a message)
The robot does not broadcast again until it resets in a hallway: ST.
TL
TR
TD
+
LR
LL
ST
D
For each scan:
Front
Right
Left

## Slide 107
Accessing 3d models
splicing into the code…
RGB
Depth

## Slide 108
Hough transform
Consider one point of a laser scan
These are all of the lines through it
r
q
http://gmarty.github.io/hough-transform-js/
http://liquify.eu/flash/HoughTransform

## Slide 109
Can we be more deliberate?
map of current knowledge…
Each intersection offers a choice:
Which turn to make, even if the robot isn't sure where it is?
Consider all of the possible distributions of results…
Possible results if the robot heads straight
Possible results if the robot turns the corner
Possible results if the robot reverses course

## Slide 110
Entropy
in general
example 1 bit
example of 2 bits
example of 1.05 bits
~ the expected amount of information available from a distribution of possibilities.

## Slide 111
Entropy-based localization
map of current knowledge…
Possible results if the robot heads straight
Possible results if the robot turns the corner
Possible results if the robot reverses course
Each intersection offers a choice:
Which turn to make, even if the robot isn't sure where it is?
We choose the action with the greatest expected information.
bits
bits
bits

## Slide 112
Entropy-based localization
entro_short.mp4

## Slide 113
Could we be bolder?
… perhaps if robots felt more contemplative.
Leap before you look.
~ W. H. Auden .
Just do it.
~ Nike .

## Slide 114
Predictive path planning
map of current knowledge…
Given the same choice: Which turn to make?
We could opt for the turn most likely to make progress toward the goal.

## Slide 115
Predictive path planning
more robust navigation ~ but all with a hand-built map
pre_short.mp4

## Slide 116
Localization
What if the robot doesn't know its starting pose?
map with all nodes large and the goal node in red
Don't worry about the goal.
Instead, make default motions…
With each observation,
cull the robot's possible poses.
map with fewer nodes large and the goal node in red
move to the…?

## Slide 117
Localization
What if the robot doesn't know its starting pose?
Don't worry about the goal.
Instead, make default motions…
With each observation,
cull the robot's possible poses.
map with fewer nodes large and the goal node in red
~ sees a TL ~ a T intersection open to the left

## Slide 118
Too many walls…
crazy image from uninitilized scans
Uninitialized images ~ aargh!
"point fog" instead of "point cloud"
More of a "point fog" than a point cloud