## Slide 1
Interdimensional Robot Cooperation
Kristina Ming, Chris Eriksen, Graham Montgomery,
Jerry Hsiung, Cyrus Huang, Zakkai Davidson, and Zach Dodds

## Slide 2
Now vs. Then

## Slide 3
Now…
3d representations are a new standard for robot spatial reasoning
yet 2d image sensing is certainly still common – and will continue to be for a long time…
… vs. Then

## Slide 4
Cooperating?!
Our goal: to investigate robot platforms, software, and algorithms for using 2d sensors amid 3d models of the world.
3d models
2d sensors

## Slide 5
New platform: Neato
Objective: to get this robot working well
Promise…
360° laser scanner
bump sensor
forward
Unrealized…
beautiful 2d sensing
inexpensive ($250)
serial interface
existing drivers slow
only runs tethered
no navigation routines

## Slide 6
Neato drivers
Built: Robot Operating System (ROS) drivers w/full control
Hurdles overcome:
driver crashes
  - different Neatos!
unorganized data
multiple threads

## Slide 7
Visualizing
Objective: Find walls and navigate safely among them
OpenCV interface
beautiful data!
how to navigate smoothly?

## Slide 8
Hough transform
Consider one point of a laser scan
These are all of the lines through it
Point space
Line space
x = 6
y = 8
r
q
y
x

## Slide 9
Hough transform
vertical line ~ q = 0
The dot is the line r = 6, q = 0
r
q
r = 6
q = 0
Point space
Line space
y
x

## Slide 10
Hough transform
y
x
angled line ~ q = 32°
The dot is the line r = 9.1, q = 32°
r = 9.1
r
q
Point space
Line space

## Slide 11
Hough transform
y
x
angled line ~ q = 90°
The dot is the line r = 8, q = 90°
r = 8
r
q
Point space
Line space

## Slide 12
Hough transform
three points of a laser scan
all the lines through all three
(dots ~ the shown horizontal lines)
(horizontal lines are shown)
y
x
r
q
Point space
Line space

## Slide 13
Hough transform
yield lines with substantial support in the original data
peaks here in line space
y
x
r
q
Point space
Line space

## Slide 14
Hough in action
now… wall sensing

## Slide 15
Low-level navigation
idea: follow the most-vertical wall

## Slide 16
Intersection recognition
still image
Check for Front, Left, and Right obstacles
The number of obstacles determines the intersection type 3:D 2:L 1:T 0:+
Open space determines final label, e.g., TL
After 15 recognitions in a row, the robot checks the map (by broadcasting a message)
The robot does not broadcast again until it resets in a hallway: ST.
TL
TR
TD
+
LR
LL
ST
D
For each scan:
Front
Right
Left

## Slide 17
Recognition problems

## Slide 18
Recognition problems
Not really a +

## Slide 19
Recognition problems

## Slide 20
Recognition problems
Not really a hallway!

## Slide 21
Map-building
Intersections and hallways make up the nodes and edges of our map

## Slide 22
Map-based navigation…

## Slide 23
Next: localization

## Slide 24
Next: 2d mapping
We plan to “borrow” Alistair’s efforts for this…
from alistair import *
Pasting Hough lines together using odometry
Recognize this place?

## Slide 25
Now: 3d mapping
Demonstration of RGBD-SLAM

## Slide 26
Accessing these 3d maps
saves each rgb image
and each depth image
Getting the data: by splicing into the code to extract the input images
our splicer

## Slide 27
Accessing these models
3d lab model ~ with a surface added
the rendered view from that green cone

## Slide 28
Accessing these models
Cloud Compare is a visualizer that can include our own “annotations” …

## Slide 29
Zooming vs. Moving
zooming in to the balloon…
… vs. moving towards/past it
CloudCompare
MeshLab

## Slide 30
Goal: Escape from the lab!

## Slide 31
Using these models
How might a robot with an ordinary camera, i.e., only 2d sensing, use these 3d models?
Ideally, a 2d sensing system could localize – and reason – within a 3d model
2d – 2d matching
3d – 3d matching

## Slide 32
2d – 2d matching
with a new image from a robot (or other device)
vs. original images
vs. rendered images
These are the images used to create the 3d model in the first place: fewer, higher-fidelity.
Images yielded by the 3d model: arbitrarily many, but lower-quality.
we could compare

## Slide 33
2d – 2d matching
with a new image from a robot (or other device)
vs. original images
vs. rendered images
These are the images used to create the 3d model in the first place: fewer, higher-fidelity.
Images yielded by the 3d model: arbitrarily many, but lower-quality.
we could compare

## Slide 34
Matching?
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
new image
many original images

## Slide 35
Features
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances

## Slide 36
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Nearest-neighbor matching

## Slide 37
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep only two-way best matches

## Slide 38
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Keep geometrically realistic matches

## Slide 39
1st-best match
10th-best match
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Visual “closeness”

## Slide 40
1st-best match
10th-best match
Average feature distance ~ 40 px
Average feature distance ~ 270 px
Our approach:
Find features in each (SIFT)
Consider all matches (FLANN)
Ensure bidirectional constraints
Consistency filtering (via homography)
Best-matching by visual similarity metric
Tiebreaking by pixel distances
Pixel “closeness”

## Slide 41
PCL: Point Cloud Library
3D-Reasoning
Easy point cloud access
Screenshot

## Slide 42
NARFs!
3d features: Normal Aligned Radial Features
picture of NARFS
picture of pt cloud
NARF features are purely based on the range image of a point cloud: its geometry, not its looks (SIFT)
They are based on the normals of the point cloud’s surfaces
They are places distinguishable from multiple perspectives.

## Slide 43
3d matching
picture of pt cloud w/NARFS
picture of pt cloud w/NARFS
Take two point clouds
Find NARFs
Match features and find transform
Make transform and combine
naive merging

## Slide 44
3d SLAM
Simultaneous Localization And Mapping
Take two point clouds
Find NARFs
Match features and find transform
Make transform and combine

## Slide 45
3d SLAM
Simultaneous Localization And Mapping
Take two point clouds
Find NARFs
Match features and find transform (ICP)
Make transform and combine

## Slide 46
3d SLAM
Final point cloud map
Questions?
Future: using Neato to create 2.5d maps

## Slide 48
Kinect
The Kinect estimates distance-to-camera by projecting a “star field” on the world.
Z.D. video

## Slide 49
Now vs. Then

## Slide 50
Title

## Slide 51
Accessing these models
allows us to define the depth at each pixel
plane
other (sphere, cylinder, wavy,…)
K.M.

## Slide 52
Ideally, a camera-only system could localize – and reason – within the 3d model
Ideally, a camera-only system could localize – and reason – within the 3d model

## Slide 53
Accessing 3d models
splicing into the code…
RGB
Depth

## Slide 54
Hough transform
Consider one point of a laser scan
These are all of the lines through it
r
q
http://gmarty.github.io/hough-transform-js/
http://liquify.eu/flash/HoughTransform