## Slide 1: Localization Using Interactive C and a Standard LEGO Mindstorms Hardware Suite
Gary R. Mayer, Dr. Jerry Weinberg, Dr. Xudong Yu
malekith@alum.wpi.edu, jweinbe@siue.edu, xyu@siue.edu
Southern Illinois University at Edwardsville
Department of Computer Science
22 March 2004
American Association for Artificial Intelligence
Spring Symposium 2004
Session on
Accessible Hands-On Artificial Intelligence and Robotics Education:
Laboratory Exercises 1

## Slide 2: Localization
Discussed with students after
  Deliberative robotic paradigm.
  World models
  Knowledge representation.
  STM and LTM.
Discuss both deductive reckoning and landmarking.
  LEGO sensors limit landmarking ability.
  Using ded reckoning for deliberative exercises.

## Slide 3: Deductive Reckoning
Shaft Encoder
  Rotation sensor.
    16 ticks / rotation (22.5 degrees / tick).
      Typically accurate between 50 and 300 rpm.
        Standard 9V motor turns at 250 rpm under typical load.
  Can emulate with light sensor or touch sensor.
    Can’t determine direction of rotation.
IC4
  Require UI to input start location and orientation.
  Reference encoders by port number.
    enable_encoder(#) versus enable_bidir_encoder(#)
    reset_encoder(#)
    read_encoder(#)

## Slide 4: Overcoming Problems Facing Deductive Reckoning
LEGO Sensors Provide Poor Granularity.
  22.5 degrees is about 6 mm of possible error on a 30.4 mm diameter wheel.
    Most noticeable when turning; error propagates to next linear motion.
  Place sensor on same shaft as motor and gear down to wheel shaft.
    Less rotation / tick, lower speed, greater torque.
Physical Design Causes Immeasurable Errors.
  Supported axles (“bowing”)
  Balance load (“skateboard effect”)
  Centrally-mounted turning axle (“shopping cart effect”)
  Account for gear slop.

## Slide 5: Dual-Differential Design
Wheel shaft on one differential.
  Preferably centrally located
One motor geared to each differential shell.
Consistent power to both wheels is ensured if second motor is braked or on.
  Best way to ensure straight-line motion without PID.
  Given gearing between shells, each applies power to the other’s shafts in equal but opposite directions.
Allows numerous types of motion with single configuration.
  linear motion (drive shell > 0, turn shell = 0)
  0-radius turn (drive shell = 0, turn shell > 0)
  turns about a wheel (drive shell > 0, turn shell = ± drive shell)
  varying radial turns (drive shell > 0, turn shell < > drive shell)
Drive shell
shaft 2
shaft 1
Turn shell
For class instruction, use a model!

## Slide 6: Sample IC4 Code
#define DRIVE_ENCODER 1
#define DRIVE_MOTOR 1
#define TURN_MOTOR 2
#define MOVE_TICKS 30
void main()
{
enable_bidir_encoder(DRIVE_ENCODER);
reset_encoder(DRIVE_ENCODER);
brake(TURN_MOTOR);
motor(DRIVE_MOTOR, 100);
while ( read_encoder(DRIVE_ENCODER) < MOVE_TICKS );
brake(DRIVE_MOTOR);
motor(DRIVE_MOTOR, -100);
while ( read_encoder(DRIVE_ENCODER) > 0 );
brake(DRIVE_MOTOR);
return;
}

## Slide 7: Application
Many students taking an introductory robotics course are programmers and know little of mechanics.
Students designed and built the robots for the labs.
Along with instruction on steering, radius of turns, and differentials, the localization lecture can be used to ground the code to the realities of the physical world brought on by student designs.
  Ratios impacting code variables.
    Distance to travel : wheel circumference : ticks per wheel turn
    Motor : rotation sensor : wheel axle gear trains
  Steering approach.
  Sensor calibration.
  Error compensation.
    Bonus points for less nudges.

## Slide 8: Demonstration
Student lab objective was to build a deliberative paradigm architecture that planned and traveled a path from start location to known goal location, avoiding obstacles (known and unknown) on the way.

## Slide 9: Landmarking
Light sensor is main ranged sensor.
  Limited range makes placing color codes on floor better option than beacons.
  Inconsistent values between different light sensors.
  Color accuracy may allow for 3 distinct shades (black, white, green)
  Light sensor array (mux on same port) is possible but very non-deterministic.
IR port can also be used as a sensor.
  “Marco-Polo” approach using another RCX as a beacon.
Touch sensor could align by impacting known obstacles.
  Impacts may knock robot, causing errors.
  Use light sensor if consistent reading is gotten at X distance?
IC4
  Raw values give better granularity than fitted range.
  High values = darker; low values = lighter

## Slide 10: Diane’s Localization
Using ded reckoning supported by a balanced design, dual-differentials, and correction for gear slop; Diane was able to navigate to the goals on a basic course and through an S-curve with little trouble. However, for the S-curve, the return trip required some nudges to ensure she stayed on course.
This was consistent for most long runs. Thus, it is recommended that student labs be designed to focus on a one-way trip.

## Slide 11: Reference
Ferrari, Mario, and Giulio Ferrari. Building Robots with LEGO Mindstorms: The Ultimate Tool for Mindstorms Maniacs!. Ed. Ralph Hempel. Rockland: Syngress Publishing, Inc., 2002.