## Slide 1: Teaching Deliberative Navigation Using the LEGO RCX and Standard LEGO Components
Gary R. Mayer, Dr. Jerry Weinberg, Dr. Xudong Yu
malekith@alum.wpi.edu, jweinbe@siue.edu, xyu@siue.edu
Southern Illinois University at Edwardsville
Department of Computer Science
23 March 2004
American Association for Artificial Intelligence
Spring Symposium 2004
Session on
Accessible Hands-On Artificial Intelligence and Robotics Education:
Laboratory Exercises 2

## Slide 2: Deliberative Navigation Exercise
Students should have knowledge of
  World Representation Models
  Localization (using ded reckoning)
  Path Planning (using wavefront algorithm)
  Deliberative Robotic Paradigm
  Mechanics of Movement
    Gears, steering, building balanced LEGO constructs
  LEGO Sensor Abilities and Limitations

## Slide 3: World Representation
Grid-based format
  4 x 6 usable graph of 10” squares.
    6 x 8 in memory, counting border.
  Robot only traveled horizontally and vertically.
    Used dual-differential and centrally mounted wheel axel to turn in place.
  Vertex representation
    Space is either an obstacle, a goal, or open.
Requires firmware replacement that frees memory resources for programs; such as Interactive C.
  Bitwise encoding possible but may detract from lesson.

## Slide 4: A Priori Data
Constant objects, like the border obstacles, are hard coded.
User inputs known obstacles, known goals, start position, and start heading.
  Using a programming language like IC4, the RCX buttons can be reprogrammed for a user interface.
More utility if map, goals and obstacles are separate data structures.
  Easy maintenance of goals and obstacles.
  Allows multiple goal searches with wavefront planning.

## Slide 5: Wavefront Path Planning
Two nested loops traverse entire grid; a change flag notes if a vertex is updated.
  Repeat until no changes.
  Ensures shortest path, not just first path to goal.
For multiple goals, plan to one goal at a time.
  Set other goals to spaces. If there is goal priority, use obstacles.
Typically takes < 10 sec to determine nearest goal and plan a path to it on a 4 x 6 usable grid with 2 goals.
  Generates path to each goal to determine shortest path; then re-plans to closest and saves path.
Try to minimize turns when constructing path.
  Greedy approach at each step may work best.

## Slide 6: Plan Success and Failure
Two concurrent processes are run - Goal Retrieval and Plan Failure Monitor.
If the robot detects a new obstacle, detects a new goal, or determines that a goal isn’t present, then the robot stops, backs to the last known empty space, updates the respective data structure and re-calculates closest goal and path from the current position.
Once robot has reached target, it can update the goal locations and plan a path to the next goal.
  If the robot is to return to start position, it can follow the path backward. However, if the plan failed along the way, this may no longer be the shortest path.

## Slide 7: Alternatives
Terrain difficulty can be modeled in wavefront.
  Instead of simply assigning a value 1 greater than the current node, a value of 1 + some difficulty value can be used.
A more complex approach may be used where nodes are positions with either goals, the robot, or empty. Obstacles are represented by the edge values between nodes.
  Each node would require additional memory to store information about each edge leading from it.
  Using this approach, one-way paths could be created.

## Slide 8: Student Laboratory
Students required to design, build, and program LEGO robots.
Robot required to travel shortest path from start position to goal using a deliberative architecture.
  Goal, obstacle, and start positions unknown to students before demonstration.
Robot required to recover from plan failure by giving auditory cue if another goal was found or stopping and re-planning if an unknown obstacle was found.
Return to start position was not required as it was felt that it provided little educational benefit but greatly increased the chance of localization failure.
Physical obstacles also removed; impacts tend to decay localization.
  Black colored tape outlined obstacle grid spaces.
To reduce complexity of hardware design, robot was not required to trap a physical object.
  Removed complexity of accuracy between target and trap design.
  Goals represented by green colored tape spanning grid space edges.

## Slide 9: Demonstration
Diane….
Student run for completion of deliberative lab assignment.

## Slide 10: Results
Student Feedback
  Mostly positive; worthwhile and educational.
  Few were annoyed with sensor limitations.
  Built two robots for two labs; too time consuming.
    Did reactive architecture first; had to rebuilt to more stringent requirements for deliberative architecture.
Possible Approach as Hybrid Lab in Two Parts.
  Deliberative
  Reactive
  Physical architecture built to more demanding deliberative requirements; reactive incorporated into existing deliberative architecture.

## Slide 11: Diane’s Run
…Back