## Slide 1
Energy
fires!
A possible summary of E11 so far...

## Slide 2
Energy
Hardware
fires!
wires!!

## Slide 3
Energy
Hardware
Software
fires!
wires!!
vampires!!!

## Slide 4
Problem Set #1: Programming your Mudduino
just like the Arduino!
"the best way to get your own hardware to talk to your computer."

## Slide 5
Problem #1
Problem Set #1
Problem #2
Problem #3
Problem #4
Harris numbers (Arithmetic and printing)
Lightin' it up... (LEDs and serial input)
That's random? (delay and random)
React! (range sensing and timing)
filename: ps1_1.pde
filename: ps1_2.pde
filename: ps1_3.pde
filename: ps1_4.pde
Submit these to www.cs.hmc.edu/~submissions/submissions/home.py

## Slide 6
Take-home message
This site is the secret to all Mudduino programming happiness and/or vampiric secrets...

## Slide 7
Hello, World!
"Computational Model?"
Language: C
actually, it's Arduino's version of C called, not surprisingly, Arduino
setup
loop
MUST have these two functions!

## Slide 8
Hello, World!
"Computational Model?"
Language: C
actually, it's Arduino's version of C called, not surprisingly, Arduino
setup
loop
MUST have these two functions!
print in loop
delay and random
// ps10
// David_Harris@hmc.edu
// Test the serial port
void setup()
{
Serial.begin(9600);
Serial.println("Hello world!");
}
void loop()
{
}

## Slide 9
Math?
Syntax!?!
C must stand for Crazy!
// ps11: math
// name
// Shows off some arithmetic!
int num = 0;
void setup()
{
Serial.begin(9600);
Serial.println("Hello world!");
}
void loop()
{
Serial.print("num is ");
Serial.println( num );
if (num % 2 == 0)
{
num = num + 1;
}
else
{
num = num + 3;
}
}

## Slide 10
if
else
C has only half of Python's punctuation !
{ } ;
variable declaration!
int num = 0;
I'm here!
Math?
Syntax!?!
powers of two... ouch!
swap two values
// ps11: math
// name
// Shows off some arithmetic!
int num = 0;
void setup()
{
Serial.begin(9600);
Serial.println("Hello world!");
}
void loop()
{
Serial.print("num is ");
Serial.println( num );
if (num % 2 == 0)
{
num = num + 1;
}
else
{
num = num + 3;
}
}

## Slide 11
Types!
int
32 bit floating-point value
long
unsigned int
unsigned long
float
other stuff…
from 0 to 4,294,967,295
from -2,147,483,648 to 2,147,483,647
32 bits
16 bits
from 0 to 65,535
from -32,768 to 32,767
see Arduino webpage
byte
8 bits
from 0 to 255
32 bits
Deliberate design vs. encouraging experimentation
You MUST declare your variables beforehand!

## Slide 12
"Quiz"
There are 14 errors here... can you find them?!
Note added by Professor Lape: the intended behavior of this code is self-evidently correct.
# quiz challenge!
int harris = 1000000;
void setup()
{
serial.begin(9600);
serial.println("Hello world!);
}
void Loop()
{
lape = harris + 1;
if harris > lape
{
Serial.println("Impossible!")
}
else
{
Serial.println("Of course.")
}

## Slide 13
int light = 5;
void setup()
{
pinMode(5, OUTPUT); // 5 is red
pinMode(6, OUTPUT); // 6 is yellow
pinMode(7, OUTPUT); // 7 is green
Serial.begin(9600);
Serial.println("\nHola, mundo!");
}
void loop()
{
Serial.print("Light is ");
Serial.println(light);
digitalWrite( light, HIGH );
delay(500);
digitalWrite( light, LOW );
if (Serial.available())
{
light = Serial.read() - 48; // What??
}
}
Input and physical Output!
What's this stuff?
digitalWrite
Set the mode of your pins!
What will this do?
and how to improve it?

## Slide 14
ASCII
In my eyes, that should be spelled ASCIII

## Slide 15
int DIST_PIN = 0; // the range sensor's pin
int SPEAKER_PIN = 4; // the speaker pin
int raw_distance = 0;
void setup()
{
pinMode(DIST_PIN, INPUT);
pinMode(SPEAKER_PIN, OUTPUT);
Serial.begin(9600);
Serial.println("Hello, world!");
}
void loop()
{
raw_distance = analogRead(DIST_PIN);
Serial.print("I read ");
Serial.println(raw_distance);
//tone( SPEAKER_PIN, 440 /* raw_distance*2 */ ); // 440hz
delay(100); // 100ms
//noTone( SPEAKER_PIN );
}
Input and physical Output!
What's new here?

## Slide 16
Reaction-time game
See if you can determine the algorithm here...

## Slide 17
Reaction-time game
Wait until the user places her hand in the range beam
The algorithm…
Wait a random number of ms (maybe between 500 and 1500)
Start playing a tone
Start playing a different tone
Measure the "starting" time
Wait until the range sensor changes enough
Measure the "ending" time
Report the results!
see next slide...

## Slide 18
start_time = millis();
while (analogRead(DIST_PIN) > END_THRESH)
{
;
}
end_time = millis();
Reaction-time game: hints
More loops next time!
unsigned long start_time;
unsigned long end_time;

## Slide 19
Help?
Arduino tutors available...
Sarah
Beryl
Phil (with shirt!)
Saturdays 1-3pm in the LAC lab
Work in pairs!

## Slide 20
Why C?
C
http://www.tiobe.com/index.php/content/paperinfo/tpci/index.html
Python
based on the number of skilled engineers world-wide, courses and third party vendors

## Slide 21
int DIST_PIN = 0; // the range sensor's pin
int SPEAKER_PIN = 4; // the speaker pin
int raw_distance = 0;
void setup()
{
pinMode(DIST_PIN, INPUT);
pinMode(SPEAKER_PIN, OUTPUT);
Serial.begin(9600);
Serial.println("Hello, world!");
}
void loop()
{
raw_distance = analogRead(DIST_PIN);
Serial.print("I read ");
Serial.println(raw_distance);
//tone( SPEAKER_PIN, 440 /* raw_distance*2 */ ); // 440hz
delay(100); // 100ms
//noTone( SPEAKER_PIN );
}
Class Challenge
start here and make a range/traffic light!

## Slide 22
Introductions...
elevator video
Robotics, Spring 2010