## Slide 1
The dream…
Sebastian Thrun
Google's driverless vehicle(s)

## Slide 2
"…only possible because of our maps."
Untold hours of computation, additional data collection, and hand-checking…
obstacle permanence
road-lane location
3d point cloud of obstacles
road surface texture

## Slide 3
"…only possible because of our maps."
Collect current snapshot of the world, and align it to the most likely position in the map.
Map-matching: 10cm accuracy
GPS: 12-15 foot accuracy
Local, sensor-based "maps"

## Slide 4
Our roads
Goal:
- to get around “normal” indoor environments, e.g. the Libra Complex
Subtasks:
- cooperation Convoys?
- navigation Where should I go?
- localization Where am I?
- mapping Where was I?

## Slide 5
Quadcopter: AR.Drone 2
MuddBot!
Our robots
Nerf Launcher
Application software
Driver software
Hardware

## Slide 6
The key: building and using maps effectively
Our maps
Sensor-based "maps" for convoying mutiple robots
Local data, immediate decision-making
Global data, longer-term planning
Vivian
Hand-built occupancy maps for navigation
Panoramic visual maps for localization
Experiments in autonomous mapping and other algorithms
Lena
Cecily
Alistair

## Slide 7
Sensory-based "maps"
Application: robot convoys
a first message-passing task, using HTTP
Duckling-inspired following…

## Slide 8
Other examples…
convoying at AAAI ~ a challenging environment

## Slide 9
Motivation…
snacks!

## Slide 10
Results: Snack Train
Starting at about 2:20…

## Slide 11
Mapping the Libra Complex!
Our map is an image drawn by OpenCV (red dot is the robot look closely!)
data collection (a lot!)
not only empty space, but labeled space
hallways, intersections, and their adjacencies are stored here, too

## Slide 12
Navigating from BkB111 to the Math lounge…
plan (map)
execution (guided by map)

## Slide 13
Using a map to replace the Kinect sensor…
Idea: navigate with an unseeing robot, using only the map?
Key: actively re-localize the robot as necessary

## Slide 14
Panorama Maps
Adding visual information in the world’s map, in the form of panoramas
A successful panorama built in 2nd floor Sprague
Each location would contribute a panorama.
Notes: basic idea ~ map with a panorama
use several panoramas to represent different locations
works even with no Kinect (copter or missile launcher)

## Slide 15
Panorama matching using keypoints
Match
keypoints
Extract good matches
Calculate location
Transform location
Find
keypoints
A successful match!
And a failed one...
Notes: example results
- insight into how it works
examples of it not working...

## Slide 16
New image
Target chosen
Navigation result
Panorama map, SURF matches, and best match
Panorama Targeting
Notes: ask how to do it!?!

## Slide 17
Panorama Targeting at AAAI
Notes: ask how to do it!?!

## Slide 18
Panorama Selection: the idea
Notes: example results
- insight into how it works
examples of it not working...

## Slide 19
Panorama Selection - success
Notes: example results
- insight into how it works
examples of it not working...

## Slide 20
Panorama Selection - failure
Notes: example results
- insight into how it works
examples of it not working...

## Slide 21
Using ROS: the Robot Operating System
In addition to building our own, we investigated ROS libraries for mapping, localization, and navigation.
To build incremental free-space maps the algorithms use
- many path hypotheses
- many location hypotheses
- maximum-likelihood matching
When large offsets are detected, corresponding corrections in position "jumps" are made.

## Slide 22
gmapping in action – where in the Libra Complex is this?
https://www.youtube.com/watch?feature=player_embedded&v=j05Wb5dpQ28
muddbot_mapping_4x
4x
2d mapping in Beckman

## Slide 23
2d localization (and navigation)
Light-blue hypotheses track possible robot positions.
The fitness of each hypothesis is bases on how close its anticipated sensor reading match the actual readings.
The "cloud" of hypotheses converges to the correct pose.

## Slide 24
amcl in action!
https://www.youtube.com/watch?feature=player_embedded&v=EG4ALhSM-C8
2x
muddbot_navigation_2x
2D localization and navigation

## Slide 25
final position
2D localization and navigation, one result
final position estimate
(collection of blue hypotheses)

## Slide 26
Muddbot's Libra Complex Map
N
Galileo Foyer
Big Beckman

## Slide 27
What's Next?
(1) 3d mapping
(2) Improved platforms and support
misaligned scans
demo: new AR.Drone and its drivers…

## Slide 28
What's Next?
(1) 3d mapping
(2) Improved platforms and support
David L.
Becca T.
misaligned scans
demo: new AR.Drone and its drivers…

## Slide 29
drone demo

## Slide 31
Getting (un)lost in the Libra Complex…
Vivian Wehner, Lena Reed, Cecily Hunt, Alistair Dobke, and Zach Dodds
everyone made it here
Our nemesis: complex seems a reasonable name…