## Slide 1
Last week's thoughts...
or worries, perhaps?

## Slide 2
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
A circuit for any function can be built from …
… just these three logic gates!
Hw#4: binary + Python
Jotto Corner
Natalya
alien: 2
queue: 0
lofty: 1
diner: 1
savvy: 1
flock: 2
thumb: ?
my guess
AM guess
apple: 1
route: 2
bands: 1
cigar: 1
diner: 1
savvy: 1
flock: 1
thumb: 1
my guess
HS guess
960
1249
956
1249
words remaining
Alex
Circuit design, part 1
This circuit was NOT, in fact, designed!
OK Recursing?
OKer than before?
Notes: jazzy!

## Slide 3
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
What's in that green box?
(3) read output voltages
(1) set input voltages
(2) perform computation
Richard Feynman: "Computation is just a physics experiment that always works!"
The big picture...

## Slide 4
Part 1: Represent your f'n as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
This one is named the sum function
That's some function, all right!
three bits in...
...one bit out

## Slide 5
Part 1: Represent your f'n as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
0
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
1
1
our f'n!
fun!
three bits in...
...one bit out

## Slide 6
All computations…
…are simply f'ns of bits
00
00
00
01
00
10
00
11
01
00
01
01
01
10
01
11
10
00
10
01
10
10
10
11
11
00
11
01
11
10
11
11
000
001
010
011
001
010
011
100
010
011
101
100
100
011
101
110
A
B
binary inputs A and B
output, A+B
bitwise
addition function
You'll build this f'n in Logisim this week… !
You built this in Python last week as addB
add
Each of these columns uses the sum function!
four bits in...
...three bits out

## Slide 7
Part 2: Arrange logic gates to do the work…
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
not just theoretical models!

## Slide 8
Our building blocks: logic gates
AND outputs 1 only if ALL inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
AND
OR
NOT
These circuits are physical functions of bits…
… and all mathematical functions can be built from them!
not just theoretical models

## Slide 9
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
drill sergeant metaphor?
Strict! Everything input must be True to output a True

## Slide 10
AND
AND's function:
inputs
output
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
output
"Truth table"
Strict! Everything input must be True to output a True

## Slide 11
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
How many different input combinations yield an output of 0 here?
Strict! Everything input must be True to output a True

## Slide 12
AND
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
one 1
AND's function:
Strict! Everything input must be True to output a True
fifteen 0s

## Slide 13
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
OR
camp counselor metaphor?
easy-going: if anything is OK, everything's OK

## Slide 14
OR
inputs
output
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
output
OR's function:
OR
easy-going: if anything is True, the output is True

## Slide 15
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
How many different 4-input combinations yield an output of 1?
OR
easy-going: if anything is OK, everything's OK

## Slide 16
OR
inputs
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
0
1
1
1
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
1
one 0
OR's function:
easy-going: if anything is OK, everything's OK
fifteen 1s

## Slide 17
NOT
inputs
output
NOT
"NOT bubble" (optional – or the only thing needed!)
x
x
0
1
NOT(x)
1
0
input
output
one 1
one 0
NOT's function:

## Slide 18
Our building blocks: logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT

## Slide 19
Claim !?
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 iff ALL its inputs are 1
OR outputs 1 iff ANY input is 1
NOT reverses its input

## Slide 20
Logisim
A circuit…
c
What inputs make this circuit output 0?
What inputs make this circuit output 1?
What are ALL its outputs?

## Slide 21
Rails
There is NO difference between these two circuits!
How?
Any advantages of this "rails" approach?
using rails for not x, not y, not c
Any disadvantages?

## Slide 22
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
This circuit is prime!

## Slide 23
Fill in the function values for this circuit (the truth table)
A
B
C
D
Quiz
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
1
circuit
Try this on the back page first…
(3) For each possible input, write the circuit output in the truth table above.
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
0
0
1
1
1
0
1
0
A
B
C
D
This circuit is prime!
4
1
3
YES!

## Slide 24
Real! logic gates...
Hex NOT gate
Notes: these quotes are important to yahoo… !

## Slide 25
Real? logic gates
1:11
:41
"It's not real unless it can be done in Minecraft."
https://www.youtube.com/watch?v=P7E4K5D834g "Minecraft Logi Gates"
https://www.youtube.com/watch?v=r7N3K8ulEEM "Minecraft Logic Gates Water"
Notes: these quotes are important to yahoo… !

## Slide 26
The claim…
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input

## Slide 27
The proof… !
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using the minterm expansion principle.

## Slide 28
Specify a truth table defining any function you want
A constructive proof… !
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
Hey! This is a 3-i'ed proof!

## Slide 29
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
The ZERO rows ALREADY work – with no connections at all !
x
y
x
y
We ensure this OR outputs zero by default.
0

## Slide 30
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
Does this wire turn on for the red input row?
Does this wire turn on for any other input rows?

## Slide 31
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?

## Slide 32
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!

## Slide 33
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!
but ALL functions are just functions of bits !

## Slide 34
What input "activates" each of these minterms?
Minterm?
A minterm is an AND gate connected to all input bits - either directly or inverted
Minterm Expansion Principle
we did this before!

## Slide 35
Each minterm selects one input:
a minterm is an AND gate that "selects" a single input row
111
the ONLY input to make this minterm output 1
110
x y c
x y c
the ONLY input to make this minterm output 1
010
x y c
the ONLY input to make this minterm output 1
Minterm Expansion Principle
Looks a little wiry to me!

## Slide 36
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
c
SUM
CarryOut
OR
(Extra #2) How could you replace the OR with only ANDs and NOTs – so ORs aren't needed !?
(Extra #3) How do the two circuits on this page implement addition of any two binary #s!?
1011
1111
11010
1
1
1
+
x
y
(Extra #1) Any gates you can optimize away here?

## Slide 37
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(Extra #2) How could you replace the OR with only ANDs and NOTs – so ORs aren't needed !?
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #3) How do the two circuits on this page implement addition of any two binary #s!?
c
0
1
1
0
0
0
1
1
A
B
C
D
1011
1111
11010
1
1
1
+
x
y
A
B
C
D
(Extra #1) Any gates you can optimize away here?
SUM
CarryOut
Can combine D and ...
OR

## Slide 38
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 38

## Slide 39
A full adder sums three input bits to create a 2-bit binary output
3 bits of input
2 bits of output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
x
y
0 1
1 0
1 0
1 1
Lab5: adders!
these columns look familiar!
the full adder
FA
x
y
cin
sum
cout
Full Adder (FA)
(considered individually)
(considered a binary #)
Full Adder (FA)

## Slide 40
A full adder sums three input bits to create a 2-bit binary output
3 individual bits of input
Lab5: adders!
connect these directly…
2 bits of output: a two-bit binary #
for this bottom-half circuit, you'll add the wires you designed a couple of minutes - and a couple of slides - ago…
Use this in lab this week!
sum
carryout
the full adder
x
y
cin
FA
x
y
cin
sum
cout
Full Adder (FA)
OR

## Slide 41
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how you might use four Full Adders here?
X
Y
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 42
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Y
X
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
We've used four full adders here… .
carries…

## Slide 43
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how to use our Full Adders here?
Y
X
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 44
It looks pretty wiry to me!
A zombie-themed ripple-carry adder
an "official" adder…

## Slide 45
relative scale…

## Slide 46
Many adders!
These aren't Easter Eggs, they're adder eggs!

## Slide 47
Ridin' the Rails !
chugging right along…

## Slide 48
What to do with all that extra silicon?

## Slide 49
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 50
Homestate pride…

## Slide 51
Marriage proposals?

## Slide 52
and secret? messages…

## Slide 53
and secret? messages…
VAX c. 1977

## Slide 54
and secret? messages!
VAX...
When you care enough to steal the very best

## Slide 55
Composing circuits ~ hw5
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider
12 nGbits of memory (RAM)
extra credit

## Slide 56
Composing circuits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
let's abstract these details away…

## Slide 57
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder

## Slide 58: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could THREE 4-bit ripple-carry adders help here?
(Q2) What bit would be correct for the starred spot ?
(Q3) What circuits could you use to create the four "partial products" ??
0

## Slide 59: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three (3) ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0

## Slide 60
CS 5 lab: where the circuits, not the zombies, will be multiplying!
Join us for Lab!

## Slide 62
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:

## Slide 63
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(Extra #1) Could you replace the OR gate with ANDs and NOTs – so ORs aren't needed at all?!
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #2) How could the two circuits on this page be used to implement any binary addition at all !?
c
… extras …
(SUM)
(CarryOut)

## Slide 64: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three (3) ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0

## Slide 65
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 65

## Slide 66
Celebrataing humanness…

## Slide 67
Past zombie run-ins… Not sure about the tie?!

## Slide 68
Celebrataing humanness…
CS 5 lab ~ a no-zombie zone!

## Slide 69
CS 5 lab: where the circuits, not the zombies, will be multiplying!
Stay safe! Join us for Lab!

## Slide 70
relative scale…

## Slide 71
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how to use our Full Adders here?

## Slide 72
0 1 1 1
1 1 0 1
Compose!
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
We've used four full adders here… .
This may be less clear than before!
(A 3-bit adder is a full adder)
(A 2-bit adder is a half adder)

## Slide 73
0 1 1 1
1 1 0 1
Compose!
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
We've used four full adders here… .
This may be less clear than before!
(A 3-bit adder is a full adder)
(A 2-bit adder is a half adder)

## Slide 74
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(Extra #1) Could you replace the OR gate with ANDs and NOTs – so ORs aren't needed at all?!
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #2) How could these two circuits can implement any binary addition at all !?
c

## Slide 75
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 75

## Slide 76
MacGyver, back for 2016…
Thirty years ago, Angus MacGyver was the most iconic engineer hero on TV. In 2015, we’re looking for new engineering heroes.
The USC Viterbi School of Engineering and the National Academy of Engineering are partnering with Lee Zlotoff, creator of the MacGyver series to identify and develop the first great TV show featuring women engineers.
Five winners receive $5,000 each and be given the rare opportunity to be paired with top Hollywood mentors [to develop the show]. Please submit your ideas to www.thenextmacgyver.com
We’re looking for ideas only at this stage. No completed scripts necessary. All genres welcome.
We’re not looking to re-make MacGyver. We’re looking for that next show in the spirit of MacGyver, with a female protagonist who uses engineering to solve problems.
Who can submit: Anyone worldwide over 18. Screenwriters, engineers, students, non-students and essentially anyone who has a good idea and cares deeply about exciting young people to STEM fields.
Submission deadline: April 17

## Slide 77
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 77

## Slide 78: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield the four "partial products" ??
0

## Slide 79
What inputs make this circuit output 1?
Logisim
What inputs make this circuit output 0?
A circuit…

## Slide 80
Building a Full Adder
A separate circuit for each output bit
input
output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
0 1
1 0
1 0
1 1
x
y
"Carry-out" Circuit
You'll build both of these in Lab!
x
y
cin
Full Adder
3 input bits
sum output bit
cout output bit
2 output bits
"Rails" of each bit and its inverse

## Slide 81
(2) Which truth-table line does each AND gate - i.e., each minterm A, B, C, and D - implement?
(1) Fill in the function values (the truth table) for this circuit…
Quiz
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
1
1
0
1
0
0
1

## Slide 82
GHC!
… as these folks (and 40 other HMCers) did!
Needed: pictures from the 2014 GHC bus!

## Slide 83
(3) Draw the upstream wires that will implement this function as a circuit.
(2) Which line does each AND gate (each minterm) A, B, C, D - implement?
A
B
C
D
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
Name(s)
(1) Fill in the function values (the truth table) for this circuit…
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) The second circuit has four ANDs (minterms). Could it use fewer ANDs?
(EC) Do you see how these two circuits can implement all binary additions !?
Let's go over these… in a moment

## Slide 84
Specify a truth table defining any function you want
Another example
x
y
0
0
0
1
1
0
1
1
fn(x,y)
1
0
0
1
1
2
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together
2 ANDs
1 OR
input
output
x
y
x
y

## Slide 85
def decipher( S ):
Creativity with Caesar...

## Slide 86
0 1 1 1
1 1 0 1
Composing circuits
+
two 4-bit inputs
How many output bits?
Could we use pieces we already have?
FA
x
y
cin
sum
cout
4-bit Ripple-carry Adder

## Slide 87: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield those four "partial products" ??
0

## Slide 88
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 88

## Slide 89
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 89

## Slide 90
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 90

## Slide 91
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 91

## Slide 92
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 92

## Slide 93
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 93

## Slide 94
"Rails"
What are the differences between these two circuits?
Any advantages of the "rails" approach?
using rails for Not X and Not Y

## Slide 95
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:

## Slide 96
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
input (0 or 1)
+5 v power
Ground
SIGNAL
POWER
Transistors are current switches:
output
input
NOT

## Slide 97
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto: Word == ?????
am guess
bagel: 2
first: 0
hound: 2
bendy: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: 2
pm guess
alien: 0
slope: 2
truck: 2
shock: 1
my guess
diner: 2
sassy: 0
thumb: 1
cruel: 2
Madi M.
Lani C.
booed?
sigma?

## Slide 98
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 99
Here's the truth table defining a function
Quiz
y
c
0
0
0
1
1
0
1
1
odd(x,y,c)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with an OR.
Create NOT "rails" ... if you want to...
x
y
Name(s):
3
Using multiplication for AND and addition for OR, what formula represents this circuit?
0
0
0
1
1
0
1
1
0
1
1
0
x
0
0
0
0
1
1
1
1
c
ExCr
Can you get rid of the ANDs by using only NOTs and ORs?
Notes: 99

## Slide 100
Getting rid of ANDs ?
Can you get rid of the ANDs by using only NOTs and ORs?
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
xy
Notes: 100

## Slide 101
Jotto !
morning class's
our guesses
938 words remaining
630 words remaining
2749 words remaining
2047 words remaining
tower 1
trump 1
462 words remaining
285 words remaining
afternoon class's
our guesses
784 words remaining
303 words remaining
1361 words remaining
1844 words remaining
339 words remaining
206 words remaining
smile 2
bacon 1
happy 1
shyly 2
hairy 2
wasps 2
plane 1
credo 2
gumbo 1
thumb 0
front 1
154 words remaining
deify 1
bunch 1

## Slide 102
The LogiSketch circuit simulator
http://www.cs.hmc.edu/~alvarado/research/sketch/release/LogiSketchFun2011.m4v

## Slide 103
One sort of creativity…

## Slide 104
Cookies!

## Slide 105
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
using the singularity as a problem-solving strategy
Hw#5: Circuit design in Logisim
on Th.: guest talk by Don Chamberlin HMC '66
Comparing types of programming languages
recursion seems OK?
or more so than before?
A circuit for any binary function can be built from
only these three logic gates
Also:
Sheldon-approved!

## Slide 106
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
R
input
NOR's Truth Table

## Slide 107
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
feedback loop

## Slide 108
NOR
S
Q
input
output
feedback loop
Take a look at this circuit.
If S is 1, what will Q be?
NOR's Truth Table
What happens if S becomes 0?
Reminders
NOR outputs 1 only if both inputs are 0
NOR outputs 0 if either inputs is 1

## Slide 109
Is it currently stable or oscillating?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
Follow how the signals will change…
Which signals will change?
How could we change this circuit so that it takes 1 bit of DATA as input?
What will happen if input R is then set to 1?
how do R and S affect Q in general?
The SR latch
NOR
NOR
S
R
0
1
0
input
input
1
0
0
Q
output
NOR's Truth Table
SET
RESET

## Slide 110
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
only one of S or R is high
How could we change this circuit so that it takes 1 bit of DATA as input?
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 111
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
tells when to remember the data!
mutually exclusive ANDs
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 112
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
S sets Q to 1.
R resets Q to 0.
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
The data can be ready any time (or NOT!) But nothing will happen until the strobe says so!
"flip-flop"

## Slide 113
NOR
NOR
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the circuit element
The SR latch

## Slide 114
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 115
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 116
def decipher( S ):
""" This works sometimes
"""
return encipher( S, 3 )
Creativity with Caesar...
and the docstring is 100% correct!
MacGyver'ed!
solving with whatever resources are at hand

## Slide 117
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 118
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 119
See you in Lab…

## Slide 120
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 121
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
Central Processing Unit
Memorable media…
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
"640K ought to be enough for anybody"
- not Bill Gates!
~ 1 billion bits +
< 10,000 bits
~1 trillion bits (or more)
120 gigabyte drive

## Slide 122
Memorable media…
Not Bill Gates, Logic Gates!
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
~1 trillion bits (or more)
120 gigabyte drive
Central Processing Unit
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 1 billion bits +
< 10,000 bits
"Leaky Bucket" capacitors
remagnetizing surfaces
strategies for storage

## Slide 123
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
Price
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 124
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 125
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
If “cycle”
were 1 min
1 min
1.5 hours
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
?
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 126
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1.5 hours
19 YEARS
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
If “cycle”
were 1 min
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 127
See you in Lab!

## Slide 128
Optimization hinders Evolution
- A Perlis

## Slide 129
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm
Integrated Circuits

## Slide 130
The enemy ...
Keeping particles out of the fabrication process is paramount!
Nature still impresses...
Pollen on a memory chip
A ruthless invader...
Ouch!

## Slide 131
It’s totally FAB
How are all of these gates actually realized?
Layering
silicon wafer
silicon dioxide
photoresist
mask w/ circuit (or sailboat)
conductor
Lithography
Etching
Cleaning
x 200 or so
http://www.techfak.uni-kiel.de/matwis/amat/elmat_en/makeindex.html

## Slide 132
CS 101 Today
Minterm Expansion Principle
Hw #5:
Any circuit for any binary function can be built from three components:
x
x
"not x"
x
"w or x or y or z"
w+x+y+z
y
wxyz
"w and x and y and z"
AND
OR
NOT
due 10/11 @ 11:59 pm
Circuit design in Logisim
Extra credit: memory design
to all Grace Hopper-ers
Welcome Back!
Too many inputs !?
start it in lab (perhaps finish!)
w
z
x
y
w
z
Gallery

## Slide 133
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
AND
OR
NOT

## Slide 134
Universal set
output
input
Any function of bits can be built from these three gates:
“Hex NOT gate"
AND
OR
NOT
Notes: these quotes are important to yahoo… !

## Slide 135
Minterm Expansion
… is a proof that AND, OR, and NOT suffice to construct any function!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Build circuits of NOTs and AND that computes each "1" row.
OR them together.
Process
Notes: 135

## Slide 136
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row!
Notes: 136

## Slide 137
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
AND
These are not bubbles, they’re NOT bubbles
KEY
This circuit always outputs 0 - except for the third row!
Notes: 137

## Slide 138
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
Notes: 138

## Slide 139
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
Or you can start here…
3
"the formula"
xy + xy
Notes: 139

## Slide 140
Specify the Truth Table defining the function
"Rails"
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
AND
AND
OR
x
x
y
y
This wire ("rail") carries x's value.
This wire ("rail") carries y's value.
Notes: 140

## Slide 141
The XOR circuit in Logisim
The Logisim circuit simulator
It's no coincidence that the "high-power" lines are lime green!
http://ozark.hendrix.edu/~burch/logisim/
Rails for circuit cleanliness!

## Slide 142
Specify the Truth Table defining the function
x
y
0
0
0
1
1
1
1
<=(x,y)
1
0
1
1
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
How many ANDs will there be?
The "less than or equal to" function…
3
What is the "formula" for this boolean function?
Use these "rails" to help draw your circuit
x
x
y
y
0
Notes: 142

## Slide 143
I'm chomping at the bit to find out…
4
Minterm expansion proves that you need only AND, OR, and NOT gates in order to construct any boolean function.
Can we do without some of the 3? Which?
5
How could we create functions with two bits, or N bits, of output?

## Slide 144
or maybe not so safe…