## Slide 1
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
A circuit for any function can be built from …
… just these three logic gates!
Hw#4: binary + Python
Circuit design, part 1
This circuit was NOT, in fact, designed!
OK Recursing?
OKer than before?
Jotto Corner
my guess
AM guess
my guess
HS guess
words remaining
?
?
?
?
Jeff
party: 3
pears: 3
lucid: 1
?????: ?
diner: 1
savvy: 1
flock: 0
thumb: ?
alien: 2
ghost: 1
today: 1
?????: ?
diner: 2
savvy: 1
flock: 0
thumb: ?
Santiago
Notes: jazzy!

## Slide 2
Last week's solutions
too compressed, admittedly!

## Slide 3
Reading responses
Emily F.
are we in a simulation?

## Slide 4
Reading responses
Meyya M

## Slide 5
Reading responses
Kate L.

## Slide 6
a wonderfully docstring'ed decipher…
Grading!
and...

## Slide 7
def decipher( S ):
""" TESIJHYDW - je tusyfxuh
jxyi tesijhydw, zkij hkd
tusyfxuh ed yj. """
… code here …
Creativity with Caesar...

## Slide 8
def decipher( S ):
""" DOCSTRING - to decipher
this docstring, just run
decipher on it. """
… code here …
Creativity with Caesar...
my favorite not-fully-working decipher…

## Slide 9
def decipher( S ):
""" This works sometimes
"""
return encipher( S, 3 )
Creativity with Caesar...
and the docstring is 100% correct!

## Slide 10
Designing physical devices that work all the time!
def decipher( S ):
""" This works sometimes
"""
return encipher( S, 3 )
Circuits!
This week

## Slide 11
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
What's in that green box?
(3) read output voltages
(1) set input voltages
(2) perform computation
Richard Feynman: "Computation is just a physics experiment that always works!"
The big picture...

## Slide 12
All computations…
… are functions of bits
00
00
00
01
00
10
00
11
01
00
01
01
01
10
01
11
10
00
10
01
10
10
10
11
11
00
11
01
11
10
11
11
000
001
010
011
001
010
011
100
010
011
101
100
100
011
101
110
A
B
binary inputs A and B
output, A+B
bitwise
addition function
You'll build this add function in Logisim Evolution this week… !
You built this in Python last week as addB
add
four bits in...
...three bits out

## Slide 13
1
0
1
Motivation: A function we want...
3 bits of input
10
+
2 bits of output
All 5 of these bits have names... !
What! Why do these bits get individual names?!

## Slide 14
1
0
1
Truth table
3 bits of input
10
Which output bit is this truth table ?!?
+
x
y
0
0
0
0
0
1
0
1
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
circuit output
sum bit
carry bit
x
y
c

## Slide 15
1
0
1
Truth table
3 bits of input
10
Which output bit is this truth table ?!?
+
x
y
0
0
0
0
0
1
0
1
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
circuit output
"sum" bit
"sum" bit
sum bit
carry bit

## Slide 16
Part 1: Represent your f'n as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
This one is named the sum function
That's some function, all right!
three bits in...
...one bit out
c
y
x
+
sum bit
carry bit

## Slide 17
c
x
y
Truth table
3 bits of input
??
What truth table for the "carry" bit?
+
x
y
0
0
0
0
0
1
0
1
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
circuit output
"carry" bit
sum bit
carry bit

## Slide 18
Part 1: Represent your f'n as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
0
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
0
0
1
1
another f'n!
fun!
three bits in...
...one bit out
Use a truth table!

## Slide 19
Part 2: Arrange logic gates to do the work…
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
not just theoretical models!

## Slide 20
Our building blocks: logic gates
AND outputs 1 only if ALL inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
AND
OR
NOT
These circuits are physical functions of bits…
… and all mathematical functions can be built from them!
not just theoretical models

## Slide 21
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
drill sergeant metaphor?
Strict! Everything input must be True to output a True

## Slide 22
AND
AND's function:
inputs
output
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
output
"Truth table"
Strict! Everything input must be True to output a True

## Slide 23
AND
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
z
y
x
AND's function:
Strict! Everything input must be True to output a True
How many of the 16 rows here will output a 1?

## Slide 24
AND
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
one 1
AND's function:
Strict! Everything input must be True to output a True
fifteen 0s

## Slide 25
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
OR
camp counselor metaphor?
easy-going: if anything is OK, everything's OK

## Slide 26
OR
inputs
output
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
output
OR's function:
OR
easy-going: if anything is True, the output is True

## Slide 27
OR
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
OR's function:
easy-going: if anything is OK, everything's OK
How many of the 16 rows here will output a 1?
inputs

## Slide 28
OR
inputs
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
0
1
1
1
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
1
one 0
OR's function:
easy-going: if anything is OK, everything's OK
fifteen 1s

## Slide 29
NOT
inputs
output
NOT
"NOT bubble" (optional – or the only thing needed!)
x
x
0
1
NOT(x)
1
0
input
output
one 1
one 0
NOT's function:

## Slide 30
Our building blocks: logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
ALL
ANY

## Slide 31
Claim !?
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 iff ALL its inputs are 1
OR outputs 1 iff ANY input is 1
NOT reverses its input

## Slide 32
Logisim Evolution
A circuit…
c
What inputs make this circuit output 0?
What inputs make this circuit output 1?
What are ALL its outputs?

## Slide 33
Rails
There is NO difference between these two circuits!
How?
Any advantages ?
Any disadvantages of this "rails" approach?
using rails for not x, not y, not c

## Slide 34
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
y
c
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow upstream from A. What x,y,c bits make A output 1 ? (and why is that all we need to know for A?)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
This circuit is prime!
together
Gate?
A
c

## Slide 35
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
y
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
(2) Follow upstream from A. What x,y,c bits make A output 1 ? (and why is that all we need to know for A?)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
This circuit is prime!
together
Gate?
Try this on the back page first…
A
B
C
D
1
0
0
1
1
1
0
1
0
c
c
4
1
3
010
it's zero otherwise
see above!
two can be combined!

## Slide 36
Real! logic gates...
Hex NOT gate
Notes: these quotes are important to yahoo… !

## Slide 37
Real? logic gates
1:11
:41
"It's not real unless it can be done in Minecraft."
https://www.youtube.com/watch?v=P7E4K5D834g "Minecraft Logi Gates"
https://www.youtube.com/watch?v=r7N3K8ulEEM "Minecraft Logic Gates Water"
Notes: these quotes are important to yahoo… !

## Slide 38
The claim…
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input

## Slide 39
The proof… !
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using the minterm expansion principle.

## Slide 40
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
Hey! This is a 3-i'ed proof!

## Slide 41
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
The ZERO rows ALREADY work – with no connections at all !
x
y
x
y
We ensure this OR outputs zero by default.
0

## Slide 42
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
This wire DOES turn on for the red input row?
Does this wire turn on for any other input rows?
A
A

## Slide 43
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
NOT
AND
blue row?
other rows?
AND
A
B
B
A

## Slide 44
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
NOT
AND
blue row?
other rows?
AND
A
B
B
A
MINTERM expansion princple
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!

## Slide 45
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
NOT
AND
blue row?
other rows?
AND
A
B
B
A
MINTERM expansion princple
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!
but ALL functions are just functions of bits !

## Slide 46
What input "activates" each of these minterms?
Minterm Expansion Principle
we did this before!
A minterm is an AND gate connected to all input bits - either directly or inverted
For each 1 in the truth table, use one AND gate, called a minterm.

## Slide 47
Each minterm selects one input:
a minterm is an AND gate that "selects" a single input row
111
the ONLY input to make this minterm output 1
110
x y c
x y c
the ONLY input to make this minterm output 1
010
x y c
the ONLY input to make this minterm output 1
Minterm Expansion Principle
Looks a little wiry to me!

## Slide 48
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(1) Fill in all 8 rows of the function values (truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Take 2…
c
SUM
A
B
C
D
CarryOut
OR
c
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
A
B
C
D
(Extra #2) How could you replace the OR with only ANDs and NOTs? ORs aren't needed!
(Extra #3) How do the two circuits on this page implement addition of any two binary #s!?
1011
1111
11010
1
1
1
+
x
y
(Extra #1) Any gates you can optimize away here?

## Slide 49
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(1) Fill in all 8 rows of the function values (truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Take 2…
c
SUM
0
1
1
0
0
0
1
1
A
B
C
D
A
B
C
D
CarryOut
OR
c
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
A
B
C
D
(Extra #2) How could you replace the OR with only ANDs and NOTs? ORs aren't needed!
(Extra #3) How do the two circuits on this page implement addition of any two binary #s!?
1011
1111
11010
1
1
1
+
x
y
(Extra #1) Any gates you can optimize away here?

## Slide 50
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 50

## Slide 51
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 51

## Slide 52
A full adder sums three input bits to create a 2-bit binary output
3 bits of input
2 bits of output
carryout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
x
y
0 1
1 0
1 0
1 1
Lab5: adders!
these columns look familiar!
the full adder
FA
x
y
cin
sum
carryout
Full Adder (FA)
(considered individually)
(considered a binary #)
Full Adder (FA)

## Slide 53
A full adder sums three input bits to create a 2-bit binary output
3 individual bits of input
Lab5: adders!
connect these directly…
2 bits of output: a two-bit binary #
for this bottom-half circuit, you'll add the wires you designed a couple of minutes - and a couple of slides - ago…
Use this in lab this week!
sum
carryout
x
y
cin
OR
the full adder
FA
x
y
cin
sum
carryout
Full Adder (FA)

## Slide 54
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how you might use four Full Adders here?
X
Y
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 55
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how you might use four Full Adders here?
X
Y
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 56
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how you might use four Full Adders here?
X
Y
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 57
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Y
X
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
We've used four full adders here… .
carries…

## Slide 58
It looks just as wiry!
A zombie-themed ripple-carry adder
an "official" adder…

## Slide 59
relative scale…

## Slide 60
Many adders!
These aren't Easter Eggs, they're adder eggs!

## Slide 61
Ridin' the Rails !
chugging right along…

## Slide 62
What to do with all that extra silicon?

## Slide 63
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 64
Homestate pride…

## Slide 65
Marriage proposals?

## Slide 66
and secret? messages…

## Slide 67
and secret? messages…
VAX c. 1977

## Slide 68
and secret? messages…

## Slide 69
and secret? messages!
VAX...
When you care enough to steal the very best

## Slide 70
Composing circuits ~ hw5
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider
12 nGbits of memory (RAM)
extra credit

## Slide 71
Composing circuits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
let's abstract these details away…
8 input bits
5 output bits
carries…

## Slide 72
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder

## Slide 73: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could THREE 4-bit ripple-carry adders help here?
(Q2) What bit would be correct for the starred spot ?
(Q3) What circuits could you use to create the four "partial products" ??
0

## Slide 74: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three (3) ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0

## Slide 75
Logisim layout…
6 x 7… what else?
the 4-bit ripple-carry adder
one factor horizontal…
one factor vertical…
use labels!
the output
4-bit multiplier
demo...

## Slide 76
Logisim layout…
6 x 7… what else?
the 4-bit ripple-carry adder
one factor horizontal…
one factor vertical…
use labels!
the output
4-bit multiplier
demo...
CS 5 lab: go forth + multiply!
Join us for Circuits Lab!

## Slide 78
house: 1
alien: 2
?????: ?
?????: ?
diner: 0
savvy: 0
flock: ?
?????: ?
ZD guess
1:15 guess
apple: 1
?????: ?
diner: 1
savvy: ?
GK guess
2:45 guess
house: 1
alien: 2
?????: ?
?????: ?
diner: 0
savvy: 0
flock: ?
thumb: ?
my guess
1:15 guess
388
307
words remaining

## Slide 79
CS 5 lab: where the circuits, not the zombies, will be multiplying!
Join us for Lab!

## Slide 80
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how to use our Full Adders here?
Y
X
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…

## Slide 81
Grading...
dinner

## Slide 82
Last week's thoughts...
or worries... !

## Slide 83
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:

## Slide 84
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(Extra #1) Could you replace the OR gate with ANDs and NOTs – so ORs aren't needed at all?!
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #2) How could the two circuits on this page be used to implement any binary addition at all !?
c
… extras …
(SUM)
(CarryOut)

## Slide 85: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three (3) ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0

## Slide 86
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 86

## Slide 87
Celebrataing humanness…

## Slide 88
Past zombie run-ins… Not sure about the tie?!

## Slide 89
Celebrataing humanness…
CS 5 lab ~ a no-zombie zone!

## Slide 90
CS 5 lab: where the circuits, not the zombies, will be multiplying!
Stay safe! Join us for Lab!

## Slide 91
relative scale…

## Slide 92
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how to use our Full Adders here?

## Slide 93
0 1 1 1
1 1 0 1
Compose!
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
We've used four full adders here… .
This may be less clear than before!
(A 3-bit adder is a full adder)
(A 2-bit adder is a half adder)

## Slide 94
0 1 1 1
1 1 0 1
Compose!
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
We've used four full adders here… .
This may be less clear than before!
(A 3-bit adder is a full adder)
(A 2-bit adder is a half adder)

## Slide 95
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate – each minterm -- to True
A
B
C
D
(Extra #1) Could you replace the OR gate with ANDs and NOTs – so ORs aren't needed at all?!
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #2) How could these two circuits can implement any binary addition at all !?
c

## Slide 96
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 96

## Slide 97
MacGyver, back for 2016…
Thirty years ago, Angus MacGyver was the most iconic engineer hero on TV. In 2015, we’re looking for new engineering heroes.
The USC Viterbi School of Engineering and the National Academy of Engineering are partnering with Lee Zlotoff, creator of the MacGyver series to identify and develop the first great TV show featuring women engineers.
Five winners receive $5,000 each and be given the rare opportunity to be paired with top Hollywood mentors [to develop the show]. Please submit your ideas to www.thenextmacgyver.com
We’re looking for ideas only at this stage. No completed scripts necessary. All genres welcome.
We’re not looking to re-make MacGyver. We’re looking for that next show in the spirit of MacGyver, with a female protagonist who uses engineering to solve problems.
Who can submit: Anyone worldwide over 18. Screenwriters, engineers, students, non-students and essentially anyone who has a good idea and cares deeply about exciting young people to STEM fields.
Submission deadline: April 17

## Slide 98
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 98

## Slide 99: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield the four "partial products" ??
0

## Slide 100
What inputs make this circuit output 1?
Logisim
What inputs make this circuit output 0?
A circuit…

## Slide 101
Building a Full Adder
A separate circuit for each output bit
input
output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
0 1
1 0
1 0
1 1
x
y
"Carry-out" Circuit
You'll build both of these in Lab!
x
y
cin
Full Adder
3 input bits
sum output bit
cout output bit
2 output bits
"Rails" of each bit and its inverse

## Slide 102
(2) Which truth-table line does each AND gate - i.e., each minterm A, B, C, and D - implement?
(1) Fill in the function values (the truth table) for this circuit…
Quiz
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
1
1
0
1
0
0
1

## Slide 103
GHC!
… as these folks (and 40 other HMCers) did!
Needed: pictures from the 2014 GHC bus!

## Slide 104
(3) Draw the upstream wires that will implement this function as a circuit.
(2) Which line does each AND gate (each minterm) A, B, C, D - implement?
A
B
C
D
(5) Could you replace the OR gate with ANDs and NOTs -- so ORs aren't needed at all?!
Name(s)
(1) Fill in the function values (the truth table) for this circuit…
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Quiz
(4) The second circuit has four ANDs (minterms). Could it use fewer ANDs?
(EC) Do you see how these two circuits can implement all binary additions !?
Let's go over these… in a moment

## Slide 105
Specify a truth table defining any function you want
Another example
x
y
0
0
0
1
1
0
1
1
fn(x,y)
1
0
0
1
1
2
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together
2 ANDs
1 OR
input
output
x
y
x
y

## Slide 106
def decipher( S ):
Creativity with Caesar...

## Slide 107
0 1 1 1
1 1 0 1
Composing circuits
+
two 4-bit inputs
How many output bits?
Could we use pieces we already have?
FA
x
y
cin
sum
cout
4-bit Ripple-carry Adder

## Slide 108: hw5pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could you use 4-bit ripple-carry adders above?
(Q2) How many of them do you need? Where?
(Q3) What circuits can you use to yield those four "partial products" ??
0

## Slide 109
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 109

## Slide 110
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 110

## Slide 111
x
y
c
Here are the truth table and circuit defining the odd parity f'n:
Quiz
y
c
0
0
0
1
1
0
1
1
oddpar
0
1
1
0
x
y
Name(s):
0
0
0
1
1
0
1
1
1
0
0
1
x
0
0
0
0
1
1
1
1
c
input
output
not
not
not
x
y
c
outputs 1 when xyc ==
001
outputs 1 when xyc ==
outputs 1 when xyc ==
AND
AND
AND
AND
OR
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
(1) Label the AND gates with the 3 input bits and row # that make it output 1. (They're not in order.)
(2) Which row does the unwired AND gate need to be? Draw the correct upstream wires for that one.
(3) When the input is from rows 0, 3, 5, or 6, what are the outputs of all the AND gates?
Row 1
Notes: 111

## Slide 112
Here's the truth table defining an "mj" function
Quiz, part 2
0
0
0
1
1
0
1
1
0
0
0
1
Sketch a circuit for this function using ANDs and NOTs, then combined with an OR.
2
1
0
0
0
1
1
0
1
1
0
1
1
1
0
0
0
0
1
1
1
1
(5) Wow! How could the the odd parity and mj circuits be replicated and combined in order to build a circuit that adds any two binary numbers at all!?!
x
y
c
x
y
c
not
not
not
x
y
c
y
c
mj
x
input
output
(4) Hmmm… Could this circuit be built without an OR gate at all by using only ANDs and NOTs? This is a thought experiment – not something to do on the circuit above…. .
Notes: 112

## Slide 113
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 113

## Slide 114
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
OR
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
x OR y
Notes: 114

## Slide 115
"Rails"
What are the differences between these two circuits?
Any advantages of the "rails" approach?
using rails for Not X and Not Y

## Slide 116
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Transistors are current switches:

## Slide 117
Transistors, computationally
A low voltage here
A high voltage here
allows current here
allows current here
Building a NOT gate from transistors…
input (0 or 1)
+5 v power
Ground
SIGNAL
POWER
Transistors are current switches:
output
input
NOT

## Slide 118
words remaining: 433
761 words remaining
2320 words remaining
words remaining: 1771
words remaining: 138
369 words remaining
words remaining: 240
667 words remaining
1917 words remaining
words remaining: 650
words remaining: 72
310 words remaining
Jotto: Word == ?????
am guess
bagel: 2
first: 0
hound: 2
bendy: 2
my guess
diner: 1
ghost: 2
plumb: 1
omega: 2
pm guess
alien: 0
slope: 2
truck: 2
shock: 1
my guess
diner: 2
sassy: 0
thumb: 1
cruel: 2
Madi M.
Lani C.
booed?
sigma?

## Slide 119
Transistors: a disruptive technology
1947: Bell Labs
seeking cheaper amplifiers for phone lines
team of scientists: Walter Brattain, William Shockley, and John Bardeen
1948: junction transistor
1956: Shockley semiconductor corp.
1957: Fairchild semiconductor corp.
much more robust design
the "traitorous eight" - ICs
point contact transistor
the start of Silicon Valley…

## Slide 120
Here's the truth table defining a function
Quiz
y
c
0
0
0
1
1
0
1
1
odd(x,y,c)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with an OR.
Create NOT "rails" ... if you want to...
x
y
Name(s):
3
Using multiplication for AND and addition for OR, what formula represents this circuit?
0
0
0
1
1
0
1
1
0
1
1
0
x
0
0
0
0
1
1
1
1
c
ExCr
Can you get rid of the ANDs by using only NOTs and ORs?
Notes: 120

## Slide 121
Getting rid of ANDs ?
Can you get rid of the ANDs by using only NOTs and ORs?
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
xy
Notes: 121

## Slide 122
Jotto !
morning class's
our guesses
938 words remaining
630 words remaining
2749 words remaining
2047 words remaining
tower 1
trump 1
462 words remaining
285 words remaining
afternoon class's
our guesses
784 words remaining
303 words remaining
1361 words remaining
1844 words remaining
339 words remaining
206 words remaining
smile 2
bacon 1
happy 1
shyly 2
hairy 2
wasps 2
plane 1
credo 2
gumbo 1
thumb 0
front 1
154 words remaining
deify 1
bunch 1

## Slide 123
The LogiSketch circuit simulator
http://www.cs.hmc.edu/~alvarado/research/sketch/release/LogiSketchFun2011.m4v

## Slide 124
One sort of creativity…

## Slide 125
Cookies!

## Slide 126
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
using the singularity as a problem-solving strategy
Hw#5: Circuit design in Logisim
on Th.: guest talk by Don Chamberlin HMC '66
Comparing types of programming languages
recursion seems OK?
or more so than before?
A circuit for any binary function can be built from
only these three logic gates
Also:
Sheldon-approved!

## Slide 127
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
R
input
NOR's Truth Table

## Slide 128
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
S
Q
input
output
feedback loop

## Slide 129
NOR
S
Q
input
output
feedback loop
Take a look at this circuit.
If S is 1, what will Q be?
NOR's Truth Table
What happens if S becomes 0?
Reminders
NOR outputs 1 only if both inputs are 0
NOR outputs 0 if either inputs is 1

## Slide 130
Is it currently stable or oscillating?
What will happen if input S is set to 1?
What will happen if input S is then set back to 0?
Follow how the signals will change…
Which signals will change?
How could we change this circuit so that it takes 1 bit of DATA as input?
What will happen if input R is then set to 1?
how do R and S affect Q in general?
The SR latch
NOR
NOR
S
R
0
1
0
input
input
1
0
0
Q
output
NOR's Truth Table
SET
RESET

## Slide 131
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
only one of S or R is high
How could we change this circuit so that it takes 1 bit of DATA as input?
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 132
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
tells when to remember the data!
mutually exclusive ANDs
We might want to deliberately trigger the memory of our 1 bit of data.
S sets Q to 1.
R resets Q to 0.

## Slide 133
1 bit of memory!
The SR latch
NOR
NOR
S
R
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
S sets Q to 1.
R resets Q to 0.
These ANDs ensure
if D == 1, S is 1
if D == 0, R is 1
The data can be ready any time (or NOT!) But nothing will happen until the strobe says so!
"flip-flop"

## Slide 134
NOR
NOR
Q
0
1
0
inputs
output
1
0
0
The D latch
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
"flip-flop"
the circuit element
The SR latch

## Slide 135
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 136
Random Access Memory
We can use data latches to create a 12 nG bit RAM !
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
"on-chip"

## Slide 137
def decipher( S ):
""" This works sometimes
"""
return encipher( S, 3 )
Creativity with Caesar...
and the docstring is 100% correct!
MacGyver'ed!
solving with whatever resources are at hand

## Slide 138
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
5 into memory location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
4. How do the * AND gates help?
*
*
"QUIZ"
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
3. How does it all work?

## Slide 139
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
data from mem. location #1
3 data input bits
write enable line
read enable line
IN: data address, in binary
0
1
Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates ensure data from memory location #1 is read?
"QUIZ"
4. Which gates ensure data from memory location #0 is not read?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high

## Slide 140
See you in Lab…

## Slide 141
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 142
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
Central Processing Unit
Memorable media…
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
"640K ought to be enough for anybody"
- not Bill Gates!
~ 1 billion bits +
< 10,000 bits
~1 trillion bits (or more)
120 gigabyte drive

## Slide 143
Memorable media…
Not Bill Gates, Logic Gates!
CPU = "on-chip"
Main Memory
(replaceable RAM)
50 Registers of 8-64 bits each
Disk Drive
magnetic storage
~1 trillion bits (or more)
120 gigabyte drive
Central Processing Unit
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
~ 1 billion bits +
< 10,000 bits
"Leaky Bucket" capacitors
remagnetizing surfaces
strategies for storage

## Slide 144
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
Price
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 145
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 146
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
If “cycle”
were 1 min
1 min
1.5 hours
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
?
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 147
8 billion bits
800 billion bits (or more)
1 billion bytes
~$100
100 billion bytes (or more)
~$100
~$100
A Memorable Aside…
1.5 hours
19 YEARS
Price
Time
~50 Registers of 8-32 bits each
s
D
Q
An 8-bit register: 8 flip-flops
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
s
D
Q
If “cycle”
were 1 min
1 min
1 clock cycle
100 cycles
107 cycles
10-9 sec
10-7 sec
10-2 sec
CPU = "on-chip"
Main Memory
("real" RAM)
Disk Drive
magnetic storage
Central Processing Unit

## Slide 148
See you in Lab!

## Slide 149
Optimization hinders Evolution
- A Perlis

## Slide 150
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm
Integrated Circuits

## Slide 151
The enemy ...
Keeping particles out of the fabrication process is paramount!
Nature still impresses...
Pollen on a memory chip
A ruthless invader...
Ouch!

## Slide 152
It’s totally FAB
How are all of these gates actually realized?
Layering
silicon wafer
silicon dioxide
photoresist
mask w/ circuit (or sailboat)
conductor
Lithography
Etching
Cleaning
x 200 or so
http://www.techfak.uni-kiel.de/matwis/amat/elmat_en/makeindex.html

## Slide 153
CS 101 Today
Minterm Expansion Principle
Hw #5:
Any circuit for any binary function can be built from three components:
x
x
"not x"
x
"w or x or y or z"
w+x+y+z
y
wxyz
"w and x and y and z"
AND
OR
NOT
due 10/11 @ 11:59 pm
Circuit design in Logisim
Extra credit: memory design
to all Grace Hopper-ers
Welcome Back!
Too many inputs !?
start it in lab (perhaps finish!)
w
z
x
y
w
z
Gallery

## Slide 154
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
AND
OR
NOT

## Slide 155
Universal set
output
input
Any function of bits can be built from these three gates:
“Hex NOT gate"
AND
OR
NOT
Notes: these quotes are important to yahoo… !

## Slide 156
Minterm Expansion
… is a proof that AND, OR, and NOT suffice to construct any function!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Build circuits of NOTs and AND that computes each "1" row.
OR them together.
Process
Notes: 156

## Slide 157
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row!
Notes: 157

## Slide 158
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
AND
These are not bubbles, they’re NOT bubbles
KEY
This circuit always outputs 0 - except for the third row!
Notes: 158

## Slide 159
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
Notes: 159

## Slide 160
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
Or you can start here…
3
"the formula"
xy + xy
Notes: 160

## Slide 161
Specify the Truth Table defining the function
"Rails"
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
AND
AND
OR
x
x
y
y
This wire ("rail") carries x's value.
This wire ("rail") carries y's value.
Notes: 161

## Slide 162
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 162

## Slide 163
The XOR circuit in Logisim
The Logisim circuit simulator
It's no coincidence that the "high-power" lines are lime green!
http://ozark.hendrix.edu/~burch/logisim/
Rails for circuit cleanliness!

## Slide 164
Specify the Truth Table defining the function
x
y
0
0
0
1
1
1
1
<=(x,y)
1
0
1
1
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
How many ANDs will there be?
The "less than or equal to" function…
3
What is the "formula" for this boolean function?
Use these "rails" to help draw your circuit
x
x
y
y
0
Notes: 164

## Slide 165
I'm chomping at the bit to find out…
4
Minterm expansion proves that you need only AND, OR, and NOT gates in order to construct any boolean function.
Can we do without some of the 3? Which?
5
How could we create functions with two bits, or N bits, of output?

## Slide 166
or maybe not so safe…