## Slide 1
Below binary: physical circuits
More bits of CS
Too many bits? Compress!
Hw #4 due Mon. 10/5
Lots of tutoring hrs - join in... !
pr1 (lab) binary ~ decimal
pr2 conversion + compression
extra image processing...
pr0 (reading) A bug and a crash!
Jotto Corner
I'd call this a KNOT gate…
Circuit design, part 1
This circuit was NOT, in fact, designed!
Natalya
alien: 2
queue: 0
?????: .
diner: 1
savvy: 1
flock: ?
my guess
AM guess
apple: 1
route: 2
?????: .
diner: 1
savvy: 1
flock: ?
my guess
HS guess
960
1249
956
1249
words remaining
P/F
T/F
vs
web extra Stylin' with CSS
Alex
Visual Art ~ Audio Art

## Slide 2
Below binary: physical circuits
More bits of CS
Too many bits? Compress!
Hw #4 due Mon. 10/5
Lots of tutoring hrs - join in... !
pr1 (lab) binary ~ decimal
pr2 conversion + compression
extra image processing...
pr0 (reading) A bug and a crash!
Jotto Corner
I'd call this a KNOT gate…
Circuit design, part 1
This circuit was NOT, in fact, designed!
Natalya
alien: 2
queue: 0
?????: .
diner: 1
savvy: 1
flock: ?
my guess
AM guess
apple: 1
route: 2
?????: .
diner: 1
savvy: 1
flock: ?
my guess
HS guess
960
1249
956
1249
words remaining
P/F
T/F
vs
web extra Stylin' with CSS
Alex
Visual Art ~ Audio Art

## Slide 3
Below binary: physical circuits
More bits of CS
Too many bits? Compress!
Hw #4 due Mon. 10/5
Lots of tutoring hrs - join in... !
pr1 (lab) binary ~ decimal
pr2 conversion + compression
extra image processing...
pr0 (reading) A bug and a crash!
Jotto Corner
I'd call this a KNOT gate…
Circuit design, part 1
This circuit was NOT, in fact, designed!
Natalya
alien: 2
queue: 0
?????: .
diner: 1
savvy: 1
flock: ?
my guess
AM guess
apple: 1
route: 2
?????: .
diner: 1
savvy: 1
flock: ?
my guess
HS guess
960
1249
956
1249
words remaining
P/F
T/F
vs
web extra Stylin' with CSS
Alex

## Slide 4
Below binary: physical circuits
More bits of CS
Too many bits? Compress!
Hw #4 due Mon. 10/5
Lots of tutoring hrs - join in... !
pr1 (lab) binary ~ decimal
pr2 conversion + compression
extra image processing...
pr0 (reading) A bug and a crash!
Jotto Corner
I'd call this a KNOT gate…
Circuit design, part 1
This circuit was NOT, in fact, designed!
Natalya
alien: 2
queue: 0
?????: .
diner: 1
savvy: 1
flock: ?
my guess
AM guess
apple: 1
route: 2
?????: .
diner: 1
savvy: 1
flock: ?
my guess
HS guess
960
1249
956
1249
words remaining
P/F
T/F
vs
web extra Stylin' with CSS
Alex

## Slide 5
Bits' big idea
Bitwise reason
left-shifting by 1 doubles a value
Python
Do I halve to remember this?
42 << 1
84
'101010'
'1010100'
'101010'
'10101'
Concept
right-shifting by 1 halves a value
42 >> 1
21
in binary, columns double in value leftward
in binary, columns halve in value rightward
No - it falls out!
purely mechanical
Aha! This can be implemented just with wiring!
42
84
21
42
I hope I don't have to remember L vs R!
Take-home

## Slide 6
Lab Debriefing & hw4pr2.py
def numToBin( N ):
""" converts a decimal int to a binary string
"""
if N==0: return ''
elif N%2==0: return numToBin( N//2 ) + '0'
elif N%2==1: return numToBin( N//2 ) + '1'
ntb( 42 )
ntb( 21 ) + '0'
'101010'
ntb( 10 ) + '1'
ntb( 5 ) + '0'
ntb( 2 ) + '1'
ntb( 1 ) + '0'
ntb( 0 ) + '1'
''
42
in
out

## Slide 7
Lab Debriefing & hw4pr2.py
def numToBin( N ):
""" converts a decimal int to a binary string
"""
if N==0: return ''
elif N%2==0: return numToBin( N//2 ) + '0'
elif N%2==1: return numToBin( N//2 ) + '1'
ntb( 42 )
ntb( 21 ) + '0'
'101010'
ntb( 10 ) + '1'
ntb( 5 ) + '0'
ntb( 2 ) + '1'
ntb( 1 ) + '0'
ntb( 0 ) + '1'
''
42
in
out
these are awfully similar…

## Slide 8
Lab Debriefing & hw4pr2.py
ntb( 42 )
ntb( 21 ) + '0'
'101010'
ntb( 10 ) + '1'
ntb( 5 ) + '0'
ntb( 2 ) + '1'
ntb( 1 ) + '0'
ntb( 0 ) + '1'
''
42
in
out
def numToBin( N ):
""" converts a decimal int to a binary string
"""
if N==0: return ''
else: return numToBin( N//2 ) + str(N%2)
fleek-ified!
What if you wanted base-3 output?! base-B output?
make sure your notes have TWO forward slashes!

## Slide 9
btn('101010')
def binToNum( S ):
""" converts a binary string to a decimal int
"""
if S=='': return 0
elif S[-1]=='0': return 2*binToNum(S[:-1]) + 0
elif S[-1]=='1': return 2*binToNum(S[:-1]) + 1
'101010'
2*btn('10101') + 0
2*btn('1010') + 1
2*btn('101') + 0
2*btn('10') + 1
2*btn('1') + 0
2*btn('') + 1
0
Lab Debriefing & hw4pr2.py
2*1
2*2*2*1
2*2*2*2*2*1
42
in
out
again, awfully similar…

## Slide 10
btn('101010')
def binToNum( S ):
""" converts a binary string to a decimal int
"""
if S=='': return 0
else: return 2*binToNum(S[:-1]) + int( S[-1] )
saves the need for another if
'101010'
2*btn('10101') + 0
2*btn('1010') + 1
2*btn('101') + 0
2*btn('10') + 1
2*btn('1') + 0
2*btn('') + 1
0
Lab Debriefing & hw4pr2.py
2*1
2*2*2*1
2*2*2*2*2*1
42
in
out
What if you wanted base-3 input?! base-B input?
fleek-ified!

## Slide 11
Ariane 5
TypeError
IndexError
HumanError
This week's reading: bits can be vital
version 5
version 4
64 bits
16 bits

## Slide 12
1 bit
How high can we count…?
with
2 bits
3 bits
4 bits
8 bits
N bits
31 bits
7 bits
1
11
111
1111
I can see some patterns here –even with one eye closed!
11111111
1111111
3
1
7
15
127
255

## Slide 13
Other overflow errors...
Less worrisome, perhaps...
The "sign bit" has flipped to one. Thus, the number has become negative... !

## Slide 14
Ariane 5
TypeError
IndexError
HumanError
This week's reading: bits can be vital
version 5
version 4
64 bits
16 bits
Is everything bits?

## Slide 15
Insight: Ancient Egyptian Multiplication
Is everything bits?
No, but surprisingly much is ...
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 16
Write the factors in two columns.
Repeatedly halve the LEFT and double the RIGHT. (toss remainders…)
Pull out the RIGHT values where the LEFT values are odd.
Sum those values for the answer!
Buddy, can you spare an eye?
Why does this work?
AEM/RPM algorithm
Insight Ancient Egyptian Multiplication
a.k.a. Russian Peasants' Multiplication
21  6
halver
dbler
(ans. should be 126)
21
6
halver
dbler
Example
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 17
21  6
Write the factors in two columns.
Repeatedly halve the LEFT and double the RIGHT. (toss remainders…)
Pull out the RIGHT values where the LEFT values are odd.
Sum those values for the answer!
11  15
Extra: Why does this always work? Hint: it's binary!
AEM algorithm
Try it!
Quiz
halver
dbler
halver
dbler
Ancient Egyptian Multiplication!
Name(s) _______________________
10
5
2
1
21
12
24
48
96
6
24
96
6
126
+
(ans. should be 126)
Example
(ans. ~ 165)
12  20
halver
dbler
(ans. ~ 240)
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 18
21  6
Write the factors in two columns.
Repeatedly halve the LEFT and double the RIGHT. (toss remainders…)
Pull out the RIGHT values where the LEFT values are odd.
Sum those values for the answer!
11  15
Extra: Why does this always work? Hint: it's binary!
AEM algorithm
Try it!
Quiz
halver
dbler
halver
dbler
Ancient Egyptian Multiplication!
Name(s) _______________________
10
5
2
1
21
12
24
48
96
6
24
96
6
126
+
(ans. should be 126)
Example
(ans. ~ 165)
12  20
halver
dbler
(ans. ~ 240)
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 19
6
24
96
110
0000
11000
000000
1100000
Decimal
Insight AEM algorithm
Binary
110
10101
+
x
21 6
10 12
5 24
2 48
1 96
1111110
126
+
6
12
24
48
96
126
6
21
21
6
Notes: To see why it works, let’s convert the numbers in both columns to binary.

## Slide 20
11
15
15
30
120
1111
11110
000000
1111000
1111
1011
+
x
11 15
5 30
2 60
1 120
10100101
165
+
15
30
60
120
165
15
11
Decimal
Binary
Insight Egyptian + Russian Multiplication
Notes: To see why it works, let’s convert the numbers in both columns to binary.

## Slide 21
12
20
80
160
00000
000000
1010000
10100000
10100
1100
+
x
12 20
6 40
3 80
1 160
11110000
240
+
20
40
80
160
240
20
12
Decimal
Binary
Insight Egyptian + Russian Multiplication
Notes: To see why it works, let’s convert the numbers in both columns to binary.

## Slide 22
hw4pr3 (extra)
how many bits represent each color channel?
Hw4: images are just bits, too!
old pixel at 42,42 has
red = 1 (out of 255)
green = 36 (out of 255)
blue = 117 (out of 255)
new pixel at 42,42 has
guesses as to what this transformation was?

## Slide 23
hw4pr3 (extra)
how many bits represent each color channel?
Hw4: images are just bits, too!
old pixel at 42,42 has
red = 1 (out of 255)
green = 36 (out of 255)
blue = 117 (out of 255)
new pixel at 42,42 has
red = 254 (out of 255)
green = 219 (out of 255)
blue = 138 (out of 255)

## Slide 24
Binary Image
Encoding as raw bits
one big string of 64 characters
10101010
01010101
10101010
01010101
10101010
01010101
10101010
01010101
"1010101001010101101010100101010110101010010101011010101001010101"
especially binary images
Hw4: images are just bits, too!

## Slide 25
likelier binary image...
home!
and a reasonable candidate for compression

## Slide 26
image compression is everywhere!
How is it possible to throw away 98% of the image data!?
Too many pixels... too little time + space!

## Slide 27
One solution!
How is it possible to throw away 98% of the image data!?
We throw away 98% of the image area!
Looks like the right 2% to keep!

## Slide 28
compressed to 40kb
original: 2.3mb
More often... what's done?

## Slide 29
compressed to 40kb
original: 2.3mb

## Slide 30
compressed
original

## Slide 31
compressed
original

## Slide 32
Binary Image
00000000
00000000
11111111
11111111
00000000
00000000
00000000
00001111
Encoding as raw bits
one big string of 64 characters
"0000000000000000111111111111111100000000000000000000000000001111"
If our images tend to have long streaks of unchanging data, how might we represent it more efficiently, but still in binary?
Hw4: lossless binary image compression
same-data streaks
compress
uncompress

## Slide 33
One possible algorithm:
bit #repeats
Any problems with this?
0100001100000111001100
0 is the first digit
There are 16 of them.
1 is the next digit
Again, there are 16 of them.
00000000
00000000
11111111
11111111
00000000
00000000
00000000
00001111
0 is the next digit
There are 28
1 is the final digit
There are 4
Hw4: lossless image compression
0100001100000111001100

## Slide 34
0100001100000111001100
0100001100000111001100
0 is the first digit
and there are 1,098,188 of them.
00000000
00000000
00000000
00000000
00000000
00000000
00000000
000000…
Hw4: lossless image compression
It's ambiguous! this could just be a huge number of 0 pixels!
1,098,188 zeros!
our algorithm:
bit #repeats
could be misinterpreted!

## Slide 35
fixed-width compression
00010000100100000001110010000100
0 is the first digit
There are 16 of them.
1 is the next digit
Again, there are 16 of them.
7 bits: # of repeats
and so on…
7 bits: # of repeats
8-bit data block
8-bit data block
8-bit data block
8-bit data block
28 zeros
4 ones
00000000
00000000
11111111
11111111
00000000
00000000
00000000
00001111
We need fixed-width blocks:
bit #repeats
8-bits total
00010000100100000001110010000100
1 bit fill
7 bits for the # of repeats

## Slide 36
If you use 7 bits to hold the # of consecutive repeats, what is the largest number of bits that one block can represent?
B bits?
00010000
7 bits: # of repeats
8-bit total data block
7 bits?
1 bit: the initial pixel
What if you need a larger # of repeats?

## Slide 37
hw4 pr2
def compress( I ):
""" returns the RLE of the
input binary image, I """
def uncompress( CI ):
""" returns the binary image I
from the run-length-encoded,
"compressed" input, CI """

## Slide 38
hw4 pr2
def compress( I ):
""" returns the RLE of the
input binary image, I """
def uncompress( CI ):
""" returns the binary image I
from the run-length-encoded,
"compressed" input, CI """
"0000000000000000111111111111111100000000000000000000000000001111"
"00010000100100000001110010000100"
a binary image
the "compressed" image:
"0000000000000000111111111111111100000000000000000000000000001111"
back to the original binary image
16 zeros
16 ones
28 zeros
4 ones
16
16
28
4
16 zeros
16 ones
28 zeros
4 ones

## Slide 39
hw4 pr2
def compress( I ):
""" returns the RLE of the
input binary image, I """
def uncompress( CI ):
""" returns the binary image I
from the run-length-encoded,
"compressed" input, CI """
"0000000000000000111111111111111100000000000000000000000000001111"
"00010000100100000001110010000100"
a binary image
the "compressed" image:
"0000000000000000111111111111111100000000000000000000000000001111"
back to the original binary image
16 zeros
16 ones
28 zeros
4 ones
16
16
28
4
16 zeros
16 ones
28 zeros
4 ones
what helper function might be useful here?

## Slide 40
Try it!
Try writing the recursive function, frontNum(S)
>>> frontNum('1111010')
4
>>> frontNum('00110010')
2
Examples…
def frontNum(S):
if
return
elif
return
else:
return
What are the BEST / WORST compression results you can get for an 8x8 input image (64 bits)?
shortest
EXTRA! How can you change our algorithm so that compressed images are always smaller than the originals?
longest
len(S)<=1:
S[0] ==
len(S)== 0:
len(S)== 1:
or 2 base cases:
1 base case:
:
frontNum(S) should return the # of times the first element of the input S appears consecutively at the start of S:

## Slide 41
What are the BEST and the WORST compression results you can get for an 8x8 image input (64 bits)?
shortest compressed representation
longest compressed representation
How could we improve this compression algorithm so that all images compress to smaller than the originals? That is, how can we make compression always work ?
?
?
?
BEST
WORST

## Slide 42
What are the BEST and the WORST compression results you can get for an 8x8 image input (64 bits)?
shortest compressed representation
longest compressed representation
How could we improve this compression algorithm so that all images compress to smaller than the originals? That is, how can we make compression always work ?
?
Anyone see why this is NOT QUITE the worst-compressable image?
only 8 bits total!
aargh! 512 bits!

## Slide 43
What are the BEST and the WORST compression results you can get for an 8x8 image input (64 bits)?
shortest compressed representation
longest compressed representation
How could we improve this compression algorithm so that all images compress to smaller than the originals? That is, how can we make compression always work ?
!
columns!!
This is provably IMpossible!

## Slide 44
Original Image
T = 78/255
T = 120/255
Adaptive T
Binary images in practice...
T = 120/255
Adaptive Threshold
No magic!
(unfortunately!)

## Slide 45
Portrait vs. landscape?

## Slide 46
This landscape image is determined to contain a portrait document.
Intensity profiles
Portrait vs. landscape?
Right-side up?
Lots of peaks == lots of text lines
few peaks == few text lines

## Slide 47
This landscape image is determined to contain a portrait document.
Intensity profiles
Portrait vs. landscape?
Right-side up?
Lots of peaks == lots of text lines
few peaks == few text lines

## Slide 48
It's all bits!
'forty*two'
011001100110111101110010011101000111100100101010011101000111011101101111
9*8 == 72 bits total
All computation boils down to manipulating bits!
even the string 'forty*two' is represented as a sequence of bits…
9 ASCII characters
8 bits each
images, text, sounds, data, …

## Slide 49
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
Computation is simply the deliberate combination of those voltages!
But what's this green thing?
(1) set input voltages

## Slide 50
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
Computation is simply the deliberate combination of those voltages!
(1) set input voltages
(2) perform computation
But what's this green thing?

## Slide 51
42
101010
In a computer, each bit is represented as a voltage (1 is +5v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
Richard Feynman: "Computation is just a physics experiment that always works!"
(3) read output voltages
(1) set input voltages
(2) perform computation
But what's this green thing?

## Slide 52
All computation
is simply functions of bits
00
00
00
01
00
10
00
11
01
00
01
01
01
10
01
11
10
00
10
01
10
10
10
11
11
00
11
01
11
10
11
11
000
001
010
011
001
010
011
100
010
011
101
100
100
011
101
110
A
B
binary inputs A and B
output, A+B
bitwise
addition function
This week: you'll build this in Python.
Next week: you'll design this with wires.
addB

## Slide 53
Adding strings?
def add10(S,T):
""" adds the *strings* S and T
as decimal numbers
"""
if len(S) == 0: return T
if len(T) == 0: return S
eS = S[-1]
eT = T[-1]
if eS == '0' and eT == '1': return add10(S[:-1],T[:-1]) + '1'
if eS == '1' and eT == '1': return add10(S[:-1],T[:-1]) + '2'
if eS == '2' and eT == '1': return add10(S[:-1],T[:-1]) + '3'
if eS == '3' and eT == '1': return add10(S[:-1],T[:-1]) + '4'
# Lots more rules - how many in all?
eS ~ the "end of S"
eT ~ the "end of T"
is circuit addition!
'11'
'31'
is syntactic addition!
S
T
Notice that this code doesn't "understand" addition at all!
'31'
'11'
S
T

## Slide 54
Carrying on…
def add10(S,T):
""" adds the *strings* S and T
as decimal numbers
"""
if len(S) == 0: return T
if len(T) == 0: return S
eS = S[-1]
eT = T[-1]
if eS == '0' and eT == '1': return add10(S[:-1],T[:-1]) + '1'
if eS == '1' and eT == '1': return add10(S[:-1],T[:-1]) + '2'
if eS == '2' and eT == '1': return add10(S[:-1],T[:-1]) + '3'
if eS == '3' and eT == '1': return add10(S[:-1],T[:-1]) + '4'
# what if we have to carry to the next column?
if eS == '3' and eT == '9':
return
'19'
'23'
S
T
hw4: addB
'23'
'19'
eS ~ the "end of S"
eT ~ the "end of T"
S
T
Notice that this code doesn't "understand" addition at all!

## Slide 55
Carrying on…
def add10(S,T):
""" adds the *strings* S and T
as decimal numbers
"""
if len(S) == 0: return T
if len(T) == 0: return S
eS = S[-1]
eT = T[-1]
if eS == '0' and eT == '1': return add10(S[:-1],T[:-1]) + '1'
if eS == '1' and eT == '1': return add10(S[:-1],T[:-1]) + '2'
if eS == '2' and eT == '1': return add10(S[:-1],T[:-1]) + '3'
if eS == '3' and eT == '1': return add10(S[:-1],T[:-1]) + '4'
# what if we have to carry to the next column?
if eS == '3' and eT == '9':
return
'19'
'23'
S
T
hw4: addB
'23'
'19'
eS ~ the "end of S"
eT ~ the "end of T"
S
T
Notice that this code doesn't "understand" addition at all!

## Slide 56
Adding strings?
is circuit addition!
is syntactic addition!
Multiplying by machine:
is circuit multiplying!
is syntactic multiplying!
Doing anything by machine…
is circuit interaction!
is syntactic interaction!
means it can be done purely via surface syntax, which means it can be done without thinking…
syntactic ~ meaning-free
Notes: meaning-free vs meaningless

## Slide 57
Our building blocks: logic gates
AND outputs 1 only if ALL inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
AND
OR
NOT
These circuits are physical functions of bits…
… and all mathematical functions can be built from them!

## Slide 58
Have an outst ing and f tuitous week(end)!
Why ?!
next 2 weeks
from circuit design…
…to a full computer!

## Slide 60
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
drill sergeant metaphor?
straight-backed; everything must be True

## Slide 61
AND
AND's function:
inputs
output
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
output
"Truth table"
straight-backed; everything must be True to output True

## Slide 62
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
How many different input combinations yield an output of 0 here?
straight-backed; everything must be True to output True

## Slide 63
AND
is a physical function of bits!
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
fifteen 0s
one 1
AND's function:

## Slide 64
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
OR
camp counselor metaphor?
easy-going: if anything is OK, everything's OK

## Slide 65
OR
inputs
output
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
output
OR's function:
OR
easy-going: if anything is True, the output is True

## Slide 66
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
How many different 4-input combinations yield an output of 1?
OR
easy-going: if anything is OK, everything's OK

## Slide 67
OR
inputs
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
0
1
1
1
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
1
fifteen 1s
one 0
OR's function:
easy-going: if anything is OK, everything's OK

## Slide 68
NOT
inputs
output
NOT
"NOT bubble" (optional – or the only thing needed!)
x
x
0
1
NOT(x)
1
0
input
output
one 1
one 0
NOT's function:

## Slide 69
Our building blocks: logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT

## Slide 70
Claim !?
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 iff ALL its inputs are 1
OR outputs 1 iff ANY input is 1
NOT reverses its input

## Slide 71
From gates to circuits...
What inputs make this circuit output 1?
Logisim
What inputs make this circuit output 0?

## Slide 72
Fill in the function values for this circuit (the truth table)
(3) For each of the 8 possible inputs, write the circuit output in the truth table. What f'n is it?
A
B
C
D
(4) This circuit uses 9 logic gates – could it use fewer? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
Each input x, y, and z can independently be 0 or 1, for 8 total input possibilities:
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 9 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit

## Slide 73
Fill in the function values for this circuit (the truth table)
(3) For each of the 8 possible inputs, write the circuit output in the truth table. What f'n is it?
A
B
C
D
(4) This circuit uses 9 logic gates – could it use fewer? If so, how?! If not, how do you know?!
Quiz
Try this on the back page first…
Each input x, y, and z can independently be 0 or 1, for 8 total input possibilities:
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 9 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit

## Slide 76
Any more recent stories of bit-overflow?

## Slide 77
binary image ~ ready for compression

## Slide 78
Bit-matching Quiz!
Suppose that a '1' represents a black pixel and a '0' represents a white pixel
B/W images:
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 79
Thinking about bits...
Is everything bits?
Matching Quiz
No, but everything represented on a computer is!
Notes: This algorithm for multiplying two numbers was evidently widely used by peasants in Russia into the 19th century and is evidently still used in some parts of Russia!
The algorithm goes like this: Write down the two numbers side-by-side. In this case, 21 and 6. Then divide 21 by 2 (rounding down) and multiply 6 by 2. Repeat this process until the number in the left column becomes 1. Then, highlight those rows in which the first number is odd. In those rows, collect all the number in the second column and add them up. That’s the desired product!

## Slide 80
1 bit
How high can we count…?
with
2 bits
3 bits
4 bits
8 bits
32 bits
31 bits
7 bits
1
11
111
1111
I can see some patterns here –with one eye closed!
11111111
1111111

## Slide 81
Yes! More recent bit-overcounting?

## Slide 82
More recent bit-overcounting?

## Slide 83
More recent bit-overcounting?

## Slide 84
Yes! More recent bit-overcounting?

## Slide 85
Yes! More recent bit-overcounting?
only briefly, of course...

## Slide 86
Carrying on…
def add10(S,T):
""" adds the *strings* S and T
as decimal numbers
"""
if len(S) == 0: return T
if len(T) == 0: return S
eS = S[-1]
eT = T[-1]
if eS == '0' and eT == '1': return add10(S[:-1],T[:-1]) + '1'
if eS == '1' and eT == '1': return add10(S[:-1],T[:-1]) + '2'
if eS == '2' and eT == '1': return add10(S[:-1],T[:-1]) + '3'
if eS == '3' and eT == '1': return add10(S[:-1],T[:-1]) + '4'
# what if we have to carry to the next column?
if eS == '3' and eT == '9':
return
eS ~ the "end of S"
eT ~ the "end of T"
'19'
'23'
S
T
hw4: addB

## Slide 87
One possible idea:
bit #repeats
See any problems with this?
0100001100000111001100
0 is the first digit
There are 16 of them.
1 is the next digit
Again, there are 16 of them.
00000000
00000000
11111111
11111111
00000000
00000000
00000000
00001111
0 is the next digit
There are 28
1 is the final digit
There are 4
Hw4: lossless image compression
0100001100000111001100

## Slide 88
Try it!
Write a recursive function, frontNum(S)
It should return the # of times the first element of the input S appears consecutively at the start of S:
>>> frontNum('1111010')
4
>>> frontNum('00111000010')
2
Name(s) _________________________________
Examples…
def frontNum(S):
if
return
elif
return
else:
return
What are the BEST / WORST compression results you can get for an 8x8 input image (64 bits)?
shortest
EXTRA! How can you change the algorithm so that compressed images are always smaller than the originals?
longest
len(S)<=1:
S[0] …
Don't hand this in…

## Slide 89
What are the BEST and the WORST compression results you can get for an 8x8 image input (64 bits)?
shortest compressed representation
longest compressed representation
How could we improve this compression algorithm so that all compressed images are smaller than their originals ? That is, how can we make compression always work ?
??

## Slide 90
Quiz
Find the outputs for these circuits
x
y
0
0
0
1
1
0
1
1
inputs
output
(1) Which gate runs line (A) of the truth table?
(2) Which gate runs line (D) of the truth table?
(D)
(C)
(B)
(A)
top
AND
lower
AND
OR
truth table
x
y
0
0
0
1
1
0
1
1
inputs
output
top
AND
middle
AND
bottom AND
OR
(These gates have been rearranged relative to the truth-table rows they control.)
Name(s) ___________________________________
truth table

## Slide 91
Fill in the function values (truth table) for this circuit…
(3) What property of integers (up to 7) does this circuit compute?
(1) Which truth table lines do the AND gates A, B, C, and D implement?
A
B
C
D
(2) This circuit uses 9 logic gates – could it use fewer?
Three bits ?
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output

## Slide 92
Draw the upstream wires to build a circuit for the truth table at left…
A
B
C
D
(*) Given a truth table, could you now design the circuit for it?
DIY !
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
1
1
0
1
0
0
1

## Slide 93
Specify a truth table defining any function you want
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
This is a three i'ed proof!
Constructive Proof !

## Slide 94
Specify a truth table defining any function you want
Constructive Proof !
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
x
y
NOT
AND
Does this work for the red row?
Does this work for any other rows?
x
y

## Slide 95
Specify a truth table defining any function you want
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
NOT
AND
NOT
AND
OR
How did we handle the rows outputting zero?
x
y
x
y
Constructive Proof !

## Slide 96
Specify a truth table defining any function you want
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
NOT
AND
NOT
AND
OR
How did we handle the rows outputting zero?
x
y
x
y
This is a constructive proof that AND, OR, and NOT suffice to build any (boolean) function!
Constructive Proof !

## Slide 97
Specify a truth table defining any function you want
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
NOT
AND
NOT
AND
OR
How did we handle the rows outputting zero?
x
y
x
y
This is a constructive proof that AND, OR, and NOT suffice to build any (boolean) function!
But... ALL functions are just boolean functions: because everything is in binary!
Constructive Proof !

## Slide 98
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Given the truth table on the right, draw the circuit that implements it!
(3) How many AND gates will be needed "upstream" of the OR gate? Which of the AND gates' inputs will need NOT gates?
(1) Use the previous examples as a guide…
(2) Use a single OR gate beside the output…
Try it!
0
1
1
0
1
0
0
1
output

## Slide 99
Try it!
Fill in the output values for this circuit…
x
y
0
0
0
1
1
0
1
1
input
output
(1) Which gate implements line (A) of the truth table?
(2) Which gate implements line (D) of the truth table?
(3) Which gates implement the other lines of the truth table?
(D)
(C)
(B)
(A)
(4) How would the table change if the top NOT gate were removed?
top
AND
lower
AND
OR
Rails and NAND! This one – hand in…
(truth table)

## Slide 100
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Fill in the function values (truth table) for this circuit…
(3) If the inputs are considered the bits of a three-bit integer, xyz, what property of integers does this circuit compute?
(1) Which truth table lines do the AND gates A,B,C,D implement?
A
B
C
D
(2) This circuit uses 9 logic gates – could it use fewer?
Try it!
Rails and prime and oddparity !

## Slide 101
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Given the truth table on the right, draw the circuit that implements it!
(3) How many AND gates will be needed "upstream" of that OR gate? Which of the AND gates' inputs will need NOT gates?
(1) Use the previous examples as a guide…
(2) Use a single OR gate beside the output…
Try it!
0
1
1
0
1
0
0
1
output

## Slide 103
OK, so binary > decimal
but why not balanced ternary ?
>

## Slide 104
Balanced ternary computers…
I feel unbalanced…
50 of these Setun ternary machines were made at Moscow U. ~1958
This project was discontinued in 1970… though not because of the ternary design!
This wasn't even the first!
+5v
0v
-5v

## Slide 105
Thomas Fowler's Ternary Computer – from the 1830's!
T. Fowler 1777-1843, Treasurer of the Poor Law Union
ternary representation
the 2005 reconstruction
the 3:1 carry mechanism
balanced ternary calculations from Fowler's papers
Notes: http://www.mortati.com/glusker/fowler/fowlerbio.htm
"In the 1830’s, Fowler was Treasurer of the Poor Law Union. This job required a considerable number of repetitive monetary calculations, made more complex by the pre-decimal British currency."

## Slide 106
Fowler's machine was rebuilt from two sources:
a picture of it as a stained-glass window in Fowler's church: St. Michael's of Great Torrington, North Devon, U.K.!
a two-page description (but no images!) by mathematician A. DeMorgan
http://www.mortati.com/glusker/fowler/index.htm

## Slide 107
Fowler's machine was rebuilt from two sources:
a picture of it as a stained-glass window in Fowler's church: St. Michael's of Great Torrington, North Devon, U.K.!
a two-page description (but no images!) by mathematician A. DeMorgan
http://www.mortati.com/glusker/fowler/index.htm
In honor of Fowler, this week's HW may be submitted in stained glass …

## Slide 108
Each line is divided into thirds…
Top and bottom “thirds” are compared for text density
The higher-density direction is presumed to be ascenders ~ up!
Up vs. down?

## Slide 109
Use it or lose it!

## Slide 110
Use it or lose it!
def exact_change( t, L ):
if t == 0: return True
if t < 0 or L == []: return False
USEIT = exact_change( t-L[0], L[1:] )
LOSEIT = exact_change( t, L[1:] )
return USEIT or LOSEIT
exact_change( 12, [ 1,5,1,1,1,5 ] )
True
exact_change( 12, [ 10,5,1,5,5 ] )
False
Can you make the target value t with the coins in L ?
t
t
L
L

## Slide 111
Use it or lose it - or lose-it!
def LCS( S, T ):
if S == '' or T == '': return ''
if S[0] == T[0]: # USEIT!
return S[0] + LCS( S[1:], T[1:] )
LI_S = LCS( S[1:], T ) # LOSEIT from S
LI_T = LCS( S, T[1:] ) # LOSEIT from T
if len( LI_S ) > len( LI_T ): return LI_S
else: return LI_T
LCS('richard','kristin')
'ri'
LCS('gattaca','tacgaacta')
'gaaca'
What's the longest common subsequence of S and T ?
S
T
S
T

## Slide 112
likelier images to compress

## Slide 113
Ray Kurzweil

## Slide 114
LA County Fair…
What Ray can't eat, at least if he wants to live forever…

## Slide 115
Different underlying assumptions…

## Slide 116
Specify a truth table defining any function you want
Try it...
x
y
0
0
0
1
1
0
1
1
fn(x,y)
1
0
0
1
input
output
1
2
How did we handle the rows outputting zero?
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together
x
y
x
y

## Slide 117
Try it!
Fill in the function values (truth table) for this circuit…
x
y
0
0
0
1
1
0
1
1
input
output
(1) Which gate implements line (A) of the truth table?
(2) Which gate implements line (D) of the truth table?
(3) Which gates implement the other lines of the truth table?
(D)
(C)
(B)
(A)
(4) How would the table change if the top NOT gate were removed?

## Slide 118
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Fill in the function values (truth table) for this circuit…
(3) If the inputs are considered the bits of a three-bit integer, xyz, what property of integers does this circuit compute?
(1) Which truth table lines do the AND gates A,B,C,D implement?
A
B
C
D
(2) This circuit uses 9 logic gates – could it use fewer?
Try it!

## Slide 119
Try it!
Fill in the function values (truth tables) for these two circuits!
x
y
0
0
0
1
1
0
1
1
input
output
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output

## Slide 120
Try it!
Design circuits that implement the functions (truth tables) shown below.
x
y
0
0
0
1
1
0
1
1
input
output
y
z
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output

## Slide 121
x
y
0
0
0
0
0
1
0
1
fn(x,y,z)
0
1
1
0
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
This looks like fn !
DIY: design-it-yourself…

## Slide 122
Circuits
are physical functions of bits!
inputs
output
AND
AND's function:
x
y
0
0
0
0
1
1
1
1
AND(x,y)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
fifteen 0s
one 1

## Slide 123
AND
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
OR
NOT

## Slide 124
All computation
… consists of functions of bits, or boolean values
Boolean inputs x,y,… can only be 0 or 1.
Boolean functions can output only 0 or 1.
Truth table
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
inputs
output
This seems fn !

## Slide 125
Lots of bits!
Truth table
x
y
0
0
0
0
0
1
0
1
fn(x,y,z)
0
1
1
0
inputs
output
z
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
Even more fn !

## Slide 126
Physical Logic Gates...
6 NOT gates:
Notes: these quotes are important to yahoo… !

## Slide 127
Claim!
Three – of course!
We need only three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 iff ALL its inputs are 1
OR outputs 1 iff ANY input is 1
NOT reverses its input

## Slide 128
"Quiz"
Write a recursive function frontNum(s) It. should return the # of times the first element of the input s appears consecutively AT THE FRONT of that string:
>>> frontNum('1111010')
4
>>> frontNum('00111000010')
2
Name(s):
Examples…
def frontNum(s):
What are the BEST and the WORST compression results you can get for an 8x8 input image (64 bits)?
shortest compressed representation
longest compressed representation
How can you change fixed-length compression so that all compressed images are smaller than their originals ? That is, how can we make compression always "work" ?
EXTRA

## Slide 129
Write a recursive function frontNum(s) It. should return the # of times the first element of the input s appears consecutively AT THE FRONT of that string:
>>> frontNum('00111000010')
2
>>> frontNum('1111010')
4
Examples…
def frontNum(s):

## Slide 130
What are the BEST and the WORST compression results you can get for an 8x8 image input (64 bits)?
shortest compressed representation
longest compressed representation
How can you change this compression algorithm so that all compressed images are smaller than their originals ? That is, how can we make compression always work ?
EXTRA

## Slide 131
Minterm Expansion
… is a proof that AND, OR, and NOT suffice to construct any function!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Build circuits of NOTs and AND that computes each "1" row.
OR them together.
Process
Notes: 131

## Slide 132
Bit functions are truth tables!
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
Any function can be represented as a table of inputs and outputs.
If we create a circuit that always outputs 0, how much does it already do correctly !?
What more do we need?
Notes: 132

## Slide 133
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Truth Table
What is a circuit that outputs 1 ONLY WHEN x is 0 and y is 1 ?
x
y
output
Notes: 133

## Slide 134
Plot of total intensity across each row of pixels
What's in the image?
Why is it important to have binarized first?
What do these peaks mean?

## Slide 135
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row, when x is 0 and y is 1
This is not a bubble, it's a NOT bubble!
What about the third row?
Notes: 135

## Slide 136
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
AND
KEY
This circuit always outputs 0 - except for the third row!
Notes: 136

## Slide 137
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
Notes: 137

## Slide 138
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
output
input x
input y
AND
AND
OR
Or you can start here…
3
"the formula"
xy + xy
Notes: 138

## Slide 139
Specify the Truth Table defining the function
"Rails"
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
AND
AND
OR
x
x
y
y
This wire ("rail") carries x's value.
This wire ("rail") carries y's value.
Notes: 139

## Slide 140
Representing Sound
continuous plot of air pressure vs. time
samples taken every ~ 1/22050nd of a second
Each sample is measured on a pressure scale from -32,767 to 32,767. (This fits into 2 bytes.)
Raw audio data - such as what is written to the surface of a CD - is simply a list of these values.
sampling
quantization
storage
physics
Ex. Cr.
pulse code modulation
Time
Pressure
plus formatting information
uncompressed sound data

## Slide 141
Specify a truth table defining any function you want
Constructive Proof !
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
x
y
NOT
AND
NOT
AND
OR

## Slide 142
Sound: frequency
Ex. Cr.
Any sound data is simply a sum of sine and cosine waves
How can we tell what frequencies make up a particular sound?
We can create "pure" tones with a sine or cosine wave.
We can add "pure" tones to create chords or other effects
A list of frequencies + their strength represents any sound!
sin(2x)
sin(8x)
sin(2x) + sin(8x)
multiply by the frequency you want to test, and then add!

## Slide 143
A bit of intuition…
Sometimes the bits are almost visible:
21 >> 1
21 << 1
5 & 6
5 | 6
5 ^ 6
42
10
?
?
?

## Slide 144
More bits of Python
Which results will Python produce here?
5 & 6
5 | 6
0
1
A
B
C
D
E
1
0
2
3
3
5
4
7

## Slide 145
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
Build separate circuits for each output-1 row using ANDs and NOTs
2
1
Combine them with OR.
input x
input y
AND
KEY
This circuit always outputs 0 - except for the second row, when x is 0 and y is 1
This is not a bubble, it's a NOT bubble!
What about the third row?
Notes: 145

## Slide 146
Specify a truth table defining any function you want
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
fn(x,y)
0
1
1
0
input
output
1
output
input x
input y
AND
AND
OR
2
How did we handle the rows outputting zero?
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
3
OR them all together

## Slide 147
Specify the Truth Table defining the function
Claim: All computation
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
1
1.5
Formula !
SELECT EACH ROW whose output is 1.
2
then combine…
I need proof!
Requires only 3 gates: AND, OR, and NOT

## Slide 148
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
1
1.5
Formula !
SELECT EACH ROW whose output is 1.
2
then combine…

## Slide 149
Specify the Truth Table defining the function
Minterm Expansion
x
y
0
0
0
1
1
0
1
1
XOR(x,y)
0
1
1
0
input
output
SELECT EACH ROW whose output is 1.
2
1
1.5
then combine…
Formula !
output
input x
input y
AND
AND
OR
These are not bubbles, they’re NOT bubbles
xy + xy
This is a constructive proof that AND, OR, and NOT suffice to construct any (boolean) function!
Notes: 149

## Slide 150
Designing a circuit
We usually know what we want to do…
We just have to determine how to build it!
"English"
f(x,y) should output 1 when x != y otherwise, output 0
Truth Table
Formula
Circuit
the not equal circuit (!=)
What is the general way to get a formula?
x
y
input bits
output bit
x != y
0
0
0
1
1
0
1
1

## Slide 151
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
AND
OR
NOT

## Slide 152
A bit of intuition…
Sometimes the bits are almost visible:
21 >> 1
21 << 1
5 & 6
5 | 6
5 ^ 6
10101
~0
This is NOT legal Python! Is it?
10101
101
110
101
110
101
110
000

## Slide 153
Which way is up?
This landscape image is determined to contain a portrait document.
Intensity profiles
Right-side up?

## Slide 154
Binary Data
All data is binary…
But some data is naturally binary!
I consider myself naturally ternary
Original Image
Histogram of intensities
BINARY image

## Slide 155
hw4pr4 (extra)
IM will be a Python list.
What structure will IM have ?
import cs5png
IM = cs5png.getRGB( 'olin.png' )
A
B
C
D
E
just a list
a list of lists
a list of lists of lists
a list of lists of lists of lists!
a list of lists of lists of lists of lists!!
cs5png.saveRGB( IM, 'out.png' )

## Slide 156
camera ~ scanner
HMC clinic …

## Slide 157
>>> .1
Beyond binary … to bits themselves
Hw #4: due 10/7 @ 11:59 pm
>>> .01*10 == .01/.1
CS 101 Today
King of ANDs
Queen of ORs
Jack of NOTs
Too many bits? Compress!
0.10000000000001
What is python thinking?!?
diner 2
diner 1
Hw #5: due 10/14 @ 11:59 pm
Exam 1:
Mon., 10/15 in-class
Tue., 10/16 in-class
"Quiz"-type problems (+ reading)
may bring 1 page of notes
False
Jessica's word
In 2009 Chris did the floating pt. stuff in the previous lecture

## Slide 158
>>> .1
Beyond binary … to bits themselves
Hw #4: due 10/7 @ 11:59 pm
>>> .01*10 == .01/.1
CS 101 Today
King of ANDs
Queen of ORs
Jack of NOTs
Binary - is it ever used by people?
0.10000000000001
What is python thinking?!?
diner 1
diner 1
Hw #5: due 10/14 @ 11:59 pm
Exam 1:
Mon., 10/15 in-class
Tue., 10/16 in-class
"Quiz"-type problems (+ reading)
may bring 1 page of notes
False
Matt's word

## Slide 159
IEEE* floats
*Institute of Electrical and Electronics Engineers
Python uses double precision floats
64 bits == 8 bytes each

## Slide 160
sinking with floats
0.0000
0.0001
0.0010
0.0011
0.1111
0.0100
0.0101
4 bits
In reality, 23 bits or 52 bits will be used to represent the fractional part of a floating-point number
0.1110
0.1101
0.1100
…
0.0000
exact decimal equivalents
0.0625
0.1250
0.1875
0.2500
0.3125
0.7500
0.8125
0.8750
0.9375
…
Imagine we had only 4 bits …
.125
.5
.25
.0625
lots of gaps in here…

## Slide 161
sinking with floats !
0.0000
0.0001
0.0010
0.0011
0.1111
0.0100
0.0101
4 bits
0.1110
0.1101
0.1100
…
0.0000
0.0625
0.1250
0.1875
0.2500
0.3125
0.7500
0.8125
0.8750
0.9375
…
We type the decimal value 0.1
The computer represents it as the closest available float:
This float's decimal value is 0.1250
So, it acts like you typed 0.1250 !
The "error" is
  necessarily limited binary precision
  our own high expectations!
  not fundamentally a rounding issue
.125
.5
.25
.0625

## Slide 162
Low-level AI?
"Actuation"
"Sensing"

## Slide 163
sinking with floats !
0.0000
0.0001
0.0010
0.0011
0.1111
0.0100
0.0101
4 bits
0.1110
0.1101
0.1100
…
0.0000
0.0625
0.1250
0.1875
0.2500
0.3125
0.7500
0.8125
0.8750
0.9375
…
We type the decimal value 0.1
The computer represents it as the closest available float:
This float's decimal value is 0.1250
So, it acts like you typed 0.1250 !
The "error" is
  necessarily limited binary precision
  our own high expectations!
  not fundamentally a rounding issue
.125
.5
.25
.0625
Additional work can be done to compute with the decimal digits themselves - and thus avoid these issues.
str vs. int
from decimal import *

## Slide 164
Designing a circuit
We usually know what we want to do…
We just have to determine how to build it!
"English"
f(x,y) should output 1 when x = y otherwise, output 0
Truth Table
Formula
Circuit
the equals to circuit (==)
What is the general way to get a formula?
x
y
input bits
output bit
x == y
0
0
0
1
1
0
1
1

## Slide 165
"Quiz"
Write a recursive function startCount(s) It. should return the # of times the first element of the input s appears consecutively AT THE START of that string:
>>> startCount('1111010')
4
>>> startCount('00111000010')
2
Name(s):
Examples…
def startCount(s):
What are the BEST and the WORST compression results you can get for an 8x8 square input?
shortest compressed representation
longest compressed representation
How can you change this compression algorithm so that all compressed images are smaller than their originals? That is, how can we make compression always work?
EXTRA

## Slide 166
Building in Binary
Underneath the strings, floats, and ints are simply bits…
'forty-two'
how many bits are used to represent this data?
I thought that binary came already built-in

## Slide 167
Building in Binary
Underneath the strings, floats, and ints are simply bits…
'forty-two'
how many bits are used to represent this data?
I thought that binary came already built-in
11001101101111111001011101001111001101101111010011101111101111
9*8 bits == 72 bits
8 bits each for 9 ASCII characters

## Slide 168
Building in Binary
Underneath the strings, floats, and ints are simply bits…
42
101010
Each bit is represented as a voltage (1 is +5v or 0 is 0v)
9
001001
+
adder
input
input
output
110011
51
which is
in decimal
It might be stored in memory
Or carried along wires to interact with other information

## Slide 169
All computation…
reduces to functions of boolean values
bit values
binary values
other aliases
Boolean variables x,y,… can only be 0 or 1.
Boolean functions can output only 0 or 1.
Truth tables describe boolean functions:
or True/False
Everything is finite (no real numbers!)
x
y
f(x,y)
input
output

## Slide 170
All computation
reduces to functions of boolean values
bit values
binary values
Boolean variables x,y,… can only be 0 or 1.
Boolean functions can output only 0 or 1.
Truth tables describe boolean functions:
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
0
0
1
There are 4 possible input combinations for x and y :
input
output
What is this f?
It's a lousy, two-bit function, if you ask me!

## Slide 171
Basic Boolean functions
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if BOTH inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if EITHER input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
It must mean something that there are three of these functions…

## Slide 172
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
output
input
Not a bubble, a not bubble… !

## Slide 173
Logic Gates
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
Any function of bits can be built from these three gates:
and that means?
AND
OR
NOT

## Slide 174
Logic Gates
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
Any function of bits can be built from these three gates:
and that means?
AND
OR
NOT
"Quad and gate"
these quotes are important to google… !

## Slide 175
Sound: frequency
Ex. Cr.
Any sound data is simply a sum of sine and cosine waves
How can we tell what frequencies make up a particular sound?
We can create "pure" tones with a sine or cosine wave.
We can add "pure" tones to create chords or other effects
A list of frequencies + their strength represents any sound!
sin(2x)
sin(8x)
sin(2x) + sin(8x)
multiply by the frequency you want to test, and then add!

## Slide 176
Building in Binary
Underneath the strings, floats, and ints are simply bits…
'forty-two'
how many bits are used to represent this data?
I thought that binary came already built-in
11001101101111111001011101001111001101101111010011101111101111
9*8 bits == 72 bits
8 bits each for 9 ASCII characters

## Slide 177
Building in Binary
Underneath the strings, floats, and ints are simply bits…
42
101010
Each bit is represented as a voltage (1 is +5v or 0 is 0v)
9
001001
+
adder
input
input
output
110011
51
which is
in decimal
It might be stored in memory
Or carried along wires to interact with other information

## Slide 178
All computation
reduces to functions of boolean values
bit values
binary values
Boolean variables x,y,… can only be 0 or 1.
Boolean functions can output only 0 or 1.
Truth tables describe boolean functions:
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
0
0
1
There are 4 possible input combinations for x and y :
input
output
What is this f?
It's a lousy, two-bit function, if you ask me!

## Slide 179
Basic Boolean functions
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if BOTH inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if EITHER input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
It must mean something that there are three of these functions…

## Slide 180
Logic Gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
output
input
Not a bubble, a not bubble… !

## Slide 181
Logic Gates
x
x
"not x"
x
"x or y"
x
y
x + y
y
xy
"x and y"
output
input
Any function of bits can be built from these three gates:
and that means?
AND
OR
NOT
"Quad and gate"
these quotes are important to yahoo… !

## Slide 182
Designing a circuit
We usually know what we want to do…
We just have to determine how to build it!
"English"
f(x,y) should output 1 when x != y otherwise, output 0
Truth Table
Formula
Circuit
the not equal circuit (!=)
What is the general way to get a formula?
x
y
input bits
output bit
x != y
0
0
0
1
1
0
1
1

## Slide 183
Try it!
We usually know what we want to do…
We just have to determine how to build it!
"English"
f(x,y) should output 1 when x <= y otherwise, output 0
Truth Table
Formula
Circuit
the less than or equal circuit (<=)
What is the general way to get a formula?
x
y
input bits
output bit
x != y
0
0
0
1
1
0
1
1
I think we'll need a bit more (or several)

## Slide 184
Good luck with Hw 4!

## Slide 185
Designing a circuit
We usually know what we want to do…
We just have to determine how to build it!
"English"
f(x,y) should output 1 when x = y otherwise, output 0
Truth Table
Formula
Circuit
the equals to circuit (==)
What is the general way to get a formula?
x
y
input bits
output bit
x == y
0
0
0
1
1
0
1
1

## Slide 186
"Quiz"
Write a recursive function startCount(s) It. should return the # of times the first element of the input s appears consecutively AT THE START of that string:
>>> startCount('1111010')
4
>>> startCount('00111000010')
2
Name(s):
Examples…
def startCount(s):
What are the BEST and the WORST compression results you can get for an 8x8 square input?
shortest compressed representation
longest compressed representation
How can you change this compression algorithm so that all compressed images are smaller than their originals? That is, how can we make compression always work?
EXTRA

## Slide 187
Constructing a circuit
x + y
For example, start with the formula
In English…
The Truth Table
The circuit
x
y
input
output
x + y

## Slide 188
Constructing a circuit
More often we know what we want from f
But we have to figure out how to build it!
In English…
f(x,y) should output 1 when x != y
Truth Table
Formula
Circuit
the not equal test
Is there a general way to get a formula?

## Slide 189
"Quiz"
(1) Create a truth table
(3) Design a circuit for it…
Name(s):
Design a "less than or equal to" circuit for 2 bits:
x <= y
Circuit-building
(2) Create a formula
x
y
input
output
x <= y
0
0
0
1
1
0
1
1
Ex. Cr.: how many different boolean functions with 2 inputs are there?
How about with N inputs?

## Slide 190
(1) Create a truth table
Design a "less than or equal to" circuit for 2 bits:
x <= y
x
y
input
output
x <= y
0
0
0
1
1
0
1
1

## Slide 191
(1) Create a truth table
Design a "less than or equal to" circuit for 2 bits:
x <= y
x
y
input
output
x <= y
0
0
0
1
1
0
1
1
(3) Design a circuit for it…
(2) Create a formula
2-bits? N-bits?
1
1
0
1
Friday: more bits!

## Slide 192
See you Friday!

## Slide 193
"Easy"
Subtleties in tasks we take for granted…
You think you know when you can learn, are more sure when you can write, even more when you can teach, but certain when you can program.

## Slide 194
Shifting, adding, and subtracting are faster than multiplying and dividing.
Knowing this, what is a "faster" strategy for multiplying a number N by 7 ?
What are these shifts?
5 << 4
100 >> 3
One strategy for these:
Convert the 5 and 100 to binary
Shift left or right
Convert back to decimal
1
2
16
32
4
8
64
128
1
2
16
32
4
8
64
128

## Slide 195
Write a recursive function startCount(s) It. should return the # of times the first element of the input s appears consecutively AT THE START of that string:
>>> startCount('00111000010')
2
>>> startCount('1111010')
4
Examples…
def SC(s):

## Slide 196
Write a recursive function startCount(s) It. should return the # of times the first element of the input s appears consecutively AT THE START of that string:
>>> startCount('00111000010')
2
>>> startCount('1111010')
4
Examples…
def SC(s
default arguments!

## Slide 197
See you in Lab!

## Slide 198
"Quiz"
Shifting, adding, and subtracting are faster than multiplying and dividing.
Write a recursive function startCount(s) It. should return the # of times the first element of the input s appears consecutively AT THE START of that string:
>>> startCount('00111000010')
2
>>> startCount('1111010')
4
Name(s):
Knowing this, what is a "faster" strategy for multiplying a number N by 7 ?
Examples…
Shiftiness with Python
What will be the results of these shifts ?
5 << 4
100 >> 3
Shiftiness with Python
Shiftiness with Python
One strategy for these:
Convert the 5 and 100 to binary
Shift left or right
Convert back to decimal
def startCount(s):

## Slide 199
50 of these Setun ternary machines were made at Moscow University ~1958
http://museum.e-ukraine.org/PHOTOS/Setun-1.html
They were deployed all over the CCCP.
A redesign was underway until 1970…
http://sovietcomputing.com/node/47
Notes: in 1970 - he was moved to an attic room in a student dormatory at MSU! The new univ. rector felt that computer design was not a real science and sought to get rid of Nikolai Brusentsov - also, there had been inquiries from foreign interests, but those were never filled…
He continued working at MSU until very recently (how recently?)