## Slide 1: The CS 5 Times
Professor Loses Drinking
Contest in Local Bar
Pomona (Penguin Press): A little-known professor
from a local college was found under the table here
after coming in second in a game that required him
to consume twice as many mugs of liquid as his opponent.
“His mistake was to agree to compete on the basis of mug count,” explained the winner. “He left the choice of mugs up to me.”
In other news, a second professor’s dog was found soaking wet and yelping in a neighbor’s back yard. “The odor was overpowering,” said the neighbor. “We had to hose the animal down before we could approach it.” Police are investigating a rumor that the canine had been attacked by a tuxedo-wearing street gang.
Penguin celebrates win over professor.
Notes: Setup: have logisim ready to go.
Worksheet options: the full adder, the first step of “Sending a message to Prof. Ben” (preferred), or analyzing a D latch.

## Slide 2: More on Circuits!
Last time…
1. String representation
2. From Boolean functions to digital circuits
Today…
1. A circuit for adding
2. A circuit simulator
3. How logic gates really work
4. Universality of logic gates
5. Memory

## Slide 3: A Circuit for Adding!
Base 2 Addition
0
sum
carry out
0 1 0 1
1 0 0 1
+
FA
Notes: This slide has an animation that causes the FA to pop up.
FA = "Full Adder", so called because it is possible to build it from two identical "Half Adders". We won't do half adders; it's easier to create a full adder directly.
If you have a FA for one bit position, you can wire up a multi-bit adder…see the next slide.

## Slide 4: A Circuit for Adding!
Base 2 Addition
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
Cool, but how do we build a FA?
Notes: If you have a working full adder, you can treat it as a black box that takes three inputs and produces TWO outputs. Then wire a “carry” of zero to the right-most FA, and wire each other FA’s carry to the next higher one. What happens to the final carry?

## Slide 5: A Circuit for Adding!
Base 2 Addition
0 1 0 1
1 0 0 1
+
FA
FA
FA
FA
0
FA
x
y
carryin
sum
carryout
x y carryin sum carryout
0 0 0 0 0 0 0 1 1 0
Notes: Note that a FA has three inputs and TWO outputs. The easy way to build it is to write a separate truth table for each output, and then build a circuit for each. Then just wire the “global” input x to the x input for each sub-circuit, and do the same for y and carry!
Notice that one of the columns in the truth table is the odd-parity circuit we built earlier. The other column we could build using the minterm expansion principle again.
This is a problem on this week’s homework/lab.

## Slide 6: Logisim: A Digital Logic Simulator
Notes: Demo Logisim. Explain drawing, deleting, labeling, projects, objects, reusing objects to build larger objects, and simulation. This will likely take 15 minutes.

## Slide 7: Implementing Gates with Relays
NOT Gate
Figures courtesy of HowStuffWorks.com
A
Q = A
6v power

## Slide 8: And AND…
Figure courtesy of HowStuffWorks.com
A
B
AB
6v power
Notes: How about an OR gate?

## Slide 9: Integrated Circuits
http://www.helicon.co.uk
http://personalpages.manchester.ac.uk/staff/p.dudek/projects/scamp
3mm

## Slide 10: AND, OR, NOT Is a “Universal Set”
Are there other universal sets of gates?
De Morgan’s Laws:
x y = x + y
x+y = x y
By Sophia Elizabeth De Morgan - Memoir of Augustus De Morgan, Public Domain
https://commons.wikimedia.org/w/index.php?curid=4722207
Augustus De Morgan
1806-1871
Notes: Augustus De Morgan: British mathematician, born in India, died in London.
Explain and justify universality.
How do you prove De Morgan’s Laws? Truth tables!
Now show that AND and NOT suffice. OR and NOT too. Define NAND and show that it’s universal.

## Slide 11: The Alien’s Life Advice
Get your eyes off the ground (and your phone)!
Your poor sore nose will appreciate it...and so will the people you look at.

## Slide 12: Sending a Message to Prof. Ben
Worksheet!
Notes: This will probably take 15 minutes.
Bring up a blank Logisim, explaining that you’d like to send Ben a message (1 or 0). This works, but you have to lean on the button. So how can we modify this circuit so that if I push the button, it remembers the 1 so I can let go and Ben will still see the 1? That’s the worksheet problem; they should come up with adding a feedback OR gate.
Having solved that problem by inserting an OR gate, now we can’t reset the message to 0 later. Lead them (not with worksheet) to inserting an AND gate (facing west) that can force the feedback loop back to 0. For now, the input to the AND is normally 1, and needs to be set to 0 if you want to reset the feedback loop. Show how when the AND input is 0, the output follows the button; when it’s 1 it’s “sticky”.
It’s unpleasant to require a constant 1 to let the OR gate be “normal”. Insert a NOT gate on the reset line to cure that. First insert a physical NOT gate. Then remove it and show how Logisim can just put a NOT circle on one of the inputs.
Now comes a tricky part: it’s going to turn out to be ugly to have a NOT on only one of the AND gate’s inputs. So invert the other input, and change the OR gate to a NOR gate to compensate. Note that this makes the output inverted; we’ll fix that in a minute. Demonstrate the circuit.
The next step is DeMorgan’s laws: the AND with inverted inputs is also a NOR gate. Remove the AND, insert a NOR in its place, and demonstrate that the circuit works in the same way. Note that now we have two NOR gates.
Finally, neatness counts. Turn the reset NOR gate back to facing east, and cross-connect it. Label S, R, and ~Q. Then connect the output of the reset NOR to an output pin, label it Q, and show how it is in fact Q.
Given time, also talk about what happens when both S and R are 1.

## Slide 13: A 1-Bit Memory
This stuff is truly unforgettable!
OR + NOT = NOR
Notes: Next slides have animations to explain how this works.

## Slide 14: A 1-Bit Memory

## Slide 15: Setting a 1-Bit Memory

## Slide 16: Initializing a 1-Bit Memory
Notes: This circuit is the simplest type of "latch" or a "flip-flop". It is called an "S-R latch" or sometimes an "R-S" one.

## Slide 17: From S-R Latches to D-Latches
>
Notes: WORKSHEET PROBLEM: What does this circuit do when "Strobe" is high? What about when it is low?
Strobes are often called clocks, and may be represented by greater-than signs or triangles. In Logisim, S-R flip-flops have clocks. Clocks can be active-low, active-high, or edge-triggered on either the rising or the falling edge. In Logisim, flip-flops clock on the rising edge.

## Slide 18
A Random-Access Memory (RAM)
A 512K x 8 RAM
(About 4.2 million bits)
Notes: If you Google for HM628512 you can learn all about this chip. Some RAM is x1, some x4, and some x8. SIMMs and DIMMs aggregate RAM chips to make x32 and x64.

## Slide 19
A Random-Access Memory (RAM)
0 1 0
1 1 1
0 0 0
0 0 1
small!
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)

## Slide 20: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q

## Slide 21: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder
Notes: Explain what a decoder does. Building one is a homework problem this week!

## Slide 22: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 23: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 24: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 25: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 26: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 27: A Random-Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder
Notes: Note that a real modern RAM would have literally hundreds of millions of “rows” of memory, each of which might be 8 bits (columns) wide or wider! Actually, since the chip surface is 2-dimensional, the bits are arranged in rows and columns, with a more complicated selection scheme.
Connecting the latches to the output is left as an exercise.