## Slide 1
CS Today
Minterm Expansion Principle
That's minterm, NOT midterm
A circuit for any function can be built from…
…just these three logic gates!
Hw#5: binary + Python
Circuit design, part 1
This circuit was NOT, in fact, designed!
OK Recurring?
OKer than before?
Professor Disappears!
Claremont (AP) —An obscure computer science professor failed to show up for classes last week. Some sources suggest that he was present but invisible, but others alleged that he had decamped to Oakland, California. Still others felt that it was unlikely that anybody would voluntarily visit Oakland, and were convinced that he had been abducted by three-eyed aliens who probed him (continued on p. 42)
Notes: INHANDOUT
Class 11 logic
We’ll take a break from Python starting today, for a couple of weeks.
Setup: have Logisim running with lec11_demos.circ.

## Slide 2
42
101010
In a computer, each bit is represented as a voltage (1 is +3v and 0 is 0v)
9
001001
ADDER circuit
110011
51
Computation is simply the deliberate combination of those voltages!
What's in that green box?
(3) read output voltages
(1) set input voltages
(2) perform computation
Richard Feynman: "Computation is just a physics experiment that always works!"
The big picture...
Notes: INHANDOUT

## Slide 3
Part 1: Represent your function as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
1
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
1
0
0
1
This one is named the sum function
That's some function, all right!
three bits in...
...one bit out
Notes: INHANDOUT
There are three steps. Here’s the big picture of them.
Draw decimal values of the inputs.

## Slide 4
Part 1: Represent your function as bits…
Any function can be represented using only bits…
x
y
0
0
0
0
0
1
0
1
circuit output
0
0
1
0
IN
OUT
c
0
1
0
1
1
0
1
0
1
1
1
1
0
1
0
1
0
0
1
1
our function!
fun!
three bits in...
...one bit out
Notes: Very short: just that this is another three-argument function.

## Slide 5
All computations…
…are simply functions of bits
00
00
00
01
00
10
00
11
01
00
01
01
01
10
01
11
10
00
10
01
10
10
10
11
11
00
11
01
11
10
11
11
000
001
010
011
001
010
011
100
010
011
101
100
100
011
101
110
A
B
binary inputs A and B
output, A+B
bitwise
addition function
You'll build this function in Logisim this week!
You built this in Python last week as addB
add
Each of these columns uses the sum function!
four bits in...
...three bits out
Notes: Highlight that the green rows represent the sums 1+1=2 and 2+3=5.

## Slide 6
Part 2: Arrange logic gates to do the work…
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
not just theoretical models!
Notes: These are also Boolean functions in Python—same thing!

## Slide 7
Our building blocks: logic gates
AND outputs 1 only if ALL inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
AND
OR
NOT
These circuits are physical functions of bits…
…and all mathematical functions can be built from them!
not just theoretical models

## Slide 8
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
drill sergeant metaphor?
Strict! Everything input must be True to output a True
Notes: Straight line: drill sergeants don’t bend.

## Slide 9
AND
AND's function:
inputs
output
AND
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
input
output
x
y
output
"Truth table"
Strict! Everything input must be True to output a True

## Slide 10
AND
AND outputs 1 when ALL inputs are 1
otherwise it outputs 0
inputs
output
AND
How many different input combinations yield an output of 0 here?
Strict! Everything input must be True to output a True

## Slide 11
AND
inputs
output
AND
x
y
0
0
0
0
1
1
1
1
AND(xyzw)
0
0
0
1
z
0
0
1
1
w
0
1
0
1
w
output
input
output
…12 more rows not shown…
0
z
y
x
one 1
AND's function:
Strict! Everything input must be True to output a True
fifteen 0s

## Slide 12
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
OR
camp counselor metaphor?
easy-going: if anything is OK, everything's OK
Notes: Arms open: it embraces you.

## Slide 13
OR
inputs
output
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x
y
output
OR's function:
OR
easy-going: if anything is True, the output is True

## Slide 14
OR
OR outputs 1 when ANY input is 1
It outputs 0 only if all inputs are 0.
inputs
output
How many different 4-input combinations yield an output of 1?
OR
easy-going: if anything is OK, everything's OK

## Slide 15
OR
inputs
output
OR
w
output
z
y
x
x
y
0
0
0
0
1
1
1
1
OR(xyzw)
0
1
1
1
z
0
0
1
1
w
0
1
0
1
input
output
…12 more rows not shown…
1
one 0
OR's function:
easy-going: if anything is OK, everything's OK
fifteen 1s

## Slide 16
NOT
inputs
output
NOT
"NOT bubble" (or the only thing needed!)
x
x
0
1
NOT(x)
1
0
input
output
one 1
one 0
NOT's function:

## Slide 17
Our building blocks: logic gates
x
y
0
0
0
1
1
0
1
1
AND(x,y)
0
0
0
1
AND outputs 1 only if ALL inputs are 1
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
OR outputs 1 if ANY input is 1
NOT reverses its input
input
output
x
0
1
NOT(x)
1
0
input
output
input
output
AND
OR
NOT
Notes: INHANDOUT
Orange is where the outputs are 1.

## Slide 18
Claim!?
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 iff ALL its inputs are 1
OR outputs 1 iff ANY input is 1
NOT reverses its input

## Slide 19
Logisim
A circuit…
c
What inputs make this circuit output 0?
What inputs make this circuit output 1?
What are ALL its outputs?
Notes: INHANDOUT
Demo Logisim here
COME TO LAB to get help installing Logisim (it can be troublesome!)
To understand a circuit, “swim upstream”.
Demo all three combinations – this is the whole truth table.
Demo adding an AND gate to handle 011.

## Slide 20
Rails
There is NO difference between these two circuits!
How?
Any advantages of this "rails" approach?
using rails for not x, not y, not c
Any disadvantages?
Notes: INHANDOUT
Disadvantage: appearance is more complex. Advantages: minimum NOTs and easier wiring.

## Slide 21
Fill in the function values for this circuit (the truth table)
(3) For each possible input, write the circuit output in the truth table above.
A
B
C
D
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
Quiz
Name(s) ___________________________________
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
1
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
circuit
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
This circuit is prime!
Notes: QUIZSLIDE
This is 2+3+5+7, or ~xy~z + ~xyz + x~yz + xyz = ~xy + xz, i.e. prime numbers.

## Slide 22
Fill in the function values for this circuit (the truth table)
A
B
C
D
Quiz
y
z
0
0
0
1
1
0
1
1
inputs
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
Each output is 0 or 1
1
circuit
Try this on the back page first…
(3) For each possible input, write the circuit output in the truth table above.
(4) Could this circuit use fewer logic gates? If so, how?! If not, how do you know?!
(1) This circuit uses 8 logic gates – how many of each? AND ___ OR ___ NOT ___
(2) Follow the inputs of x=1, y=1, z=1 and see why the overall output is 1 ... (already labeled)
Each input x, y, and z can independently be 0 or 1, for eight total possible inputs:
0
0
1
1
1
0
1
0
A
B
C
D
This circuit is prime!
4
1
3
YES!

## Slide 23
Real! logic gates...
Hex NOT gate
Notes: These are Schottky inverters, which are faster and lower-power but more expensive than non-Shottky. You can get them for about a dime (or free from the Engineering stockroom).
If you put 0 on I0, where does the 5V for O0 come from?

## Slide 24
Real? logic gates
1:11
:41
"It's not real unless it can be done in Minecraft."
https://www.youtube.com/watch?v=P7E4K5D834g "Minecraft Logi Gates"
https://www.youtube.com/watch?v=r7N3K8ulEEM "Minecraft Logic Gates Water"

## Slide 25
The claim…
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input

## Slide 26
The proof… !
I need proof!
We need only these three building blocks to compute anything at all
AND
OR
NOT
AND outputs 1 only if ALL its inputs are 1
OR outputs 1 if ANY input is 1
NOT reverses its input
We prove this constructively using the minterm expansion principle.

## Slide 27
Specify a truth table defining any function you want
A constructive proof… !
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
Hey! This is a 3-i'ed proof!

## Slide 28
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
The ZERO rows ALREADY work – with no connections at all !
x
y
x
y
We ensure this OR outputs zero by default.
0

## Slide 29
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
Does this wire turn on for the red input row?
Does this wire turn on for any other input rows?

## Slide 30
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
Notes: INHANDOUT

## Slide 31
Specify a truth table defining any function you want
A constructive proof…
x
y
0
0
0
1
1
0
1
1
f(x,y)
0
1
1
0
input
output
i
ii
For each input row whose output needs to be 1, build an AND circuit that outputs 1 only for that specific input!
iii
OR them all together
OR
x
y
x
y
NOT
AND
NOT
AND
blue row?
other rows?
This is a constructive proof that AND, OR, NOT suffice to build any function of bits!
but ALL functions are just functions of bits !

## Slide 32
What input "activates" each of these minterms?
Minterm?
A minterm is an AND gate connected to all input bits - either directly or inverted
Minterm Expansion Principle
we did this before!
Notes: Minterm == Minimum term, i.e. something that matches a minimum set of inputs: exactly 1.
Expansion because we use the OR gate to expand a bunch of minterms into a function.

## Slide 33
Each minterm selects one input:
a minterm is an AND gate that "selects" a single input row
111
the ONLY input to make this minterm output 1
110
x y c
x y c
the ONLY input to make this minterm output 1
010
x y c
the ONLY input to make this minterm output 1
Minterm Expansion Principle
Looks a little wiry to me!
Notes: INHANDOUT

## Slide 34
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate—each minterm—to True
A
B
C
D
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
c
SUM
CarryOut
OR
(Extra #2) How could you replace the OR with only ANDs and NOTs – so ORs aren't needed !?
(Extra #3) How do the two circuits on this page implement addition of any two binary #s?
1011
1111
11010
1
1
1
+
x
y
(Extra #1) Any gates you can optimize away here?
Notes: INHANDOUTFULL
Do one example for them (gate A).
Solutions are in the notes.

## Slide 35
(2) Draw the upstream wires that will implement this function as a circuit.
Hint: Determine the input that turns each AND gate—each minterm—to True
A
B
C
D
(Extra #2) How could you replace the OR with only ANDs and NOTs – so ORs aren't needed !?
(1) Fill in the function values (the truth table) for this circuit…
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
A
B
C
D
y
c
0
0
0
1
1
0
1
1
input
0
0
0
1
1
0
1
1
x
0
0
0
0
1
1
1
1
output
0
0
0
1
0
1
1
1
Take 2…
(Extra #3) How do the two circuits on this page implement addition of any two binary #s!?
c
0
1
1
0
0
0
1
1
A
B
C
D
1011
1111
11010
1
1
1
+
x
y
A
B
C
D
(Extra #1) Any gates you can optimize away here?
SUM
CarryOut
Can combine D and ...
OR
Notes: INHANDOUT
Bring this page to lab!

## Slide 36
OR else ?!
Can you get rid of ORs by using only NOTs and ANDs?
x
y
0
0
0
1
1
0
1
1
OR(x,y)
0
1
1
1
input
output
x OR y
OR
x
y
Notes: 36
INHANDOUT
Draw the DeMorgan answer inside the giant OR

## Slide 37
A full adder sums three input bits to create a 2-bit binary output
3 bits of input
2 bits of output
cout sum
0 0 0
cin
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0
0 1
0 1
1 0
x
y
0 1
1 0
1 0
1 1
Lab 6: adders!
these columns look familiar!
the full adder
FA
x
y
cin
sum
cout
Full Adder (FA)
(considered individually)
(considered a binary number)
Full Adder (FA)
Notes: Show that the output is a binary number. Then explain why we call the third input and the first output “c”.
Show that the columns can be separated into two circuits.
You’ll build this in lab.
Logisim lets you make the circuit into a building block—demo that fact.
Demo FA as building block in Logisim.
Then demo that RCA works (8 + 3, no carries, then 15 + 5)

## Slide 38
A full adder sums three input bits to create a 2-bit binary output
3 individual bits of input
Lab 6: adders!
connect these directly…
2 bits of output: a two-bit binary #
for this bottom-half circuit, you'll add the wires you designed a couple of minutes—and a couple of slides—ago…
Use this in lab this week!
sum
carryout
the full adder
x
y
cin
FA
x
y
cin
sum
cout
Full Adder (FA)
OR
Notes: INHANDOUT

## Slide 39
0 1 1 1
1 1 0 1
Compose!
+
Any binary addition at all?
8 bits in
5 bits out
Do you see how you might use four Full Adders here?
X
Y
Y0
X0
Y1
X1
Y2
X2
Y3
X3
Carry
carries…
Notes: Ask class: how have we used 4 FA’s?
Draw the RH FA.
Show how you can reuse circuits in Logisim by just dragging.

## Slide 40
It looks pretty wiry to me!
A zombie-themed ripple-carry adder
an "official" adder…

## Slide 41
relative scale…
Notes: Zooming in a bit…see next slide

## Slide 42
Many adders!
These aren't Easter Eggs, they're adder eggs!

## Slide 43
Ridin' the Rails !
chugging right along…

## Slide 44
What to do with all that extra silicon?

## Slide 45
What to do with all that extra silicon?
The "silicon zoo": micro.magnet.fsu.edu/creatures/index.html

## Slide 46
Homestate pride…

## Slide 47
Marriage announcements?
Notes: This is from

## Slide 48
and secret? messages…
Notes: This is on a chip built for the VAX 11/780, which was introduced in 1977 (during the Cold War). The designers know the Russians would reverse-engineer it…

## Slide 49
and secret? messages…
VAX c. 1977

## Slide 50
and secret? messages!
VAX...
When you care enough to steal the very best

## Slide 51
Composing circuits ~ hw6
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider
12 nGbits of memory (RAM)
extra credit
Notes: The lab is about building a ripple-carry adder.

## Slide 52
Composing circuits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
let's abstract these details away…

## Slide 53
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
Notes: It looks like a school bus.

## Slide 54: hw6pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q1) How could THREE 4-bit ripple-carry adders help here?
(Q2) What bit would be correct for the starred spot ?
(Q3) What circuits could you use to create the four "partial products" ??
0
Notes: The * represents a carry.

## Slide 55: hw6pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A2) Use a 4x1-bit helper circuit to find the four partial products…
(A1) You need three ripple-carry adders to finish: see above…
(A3) Remember that the AND gate is single-bit multiplication.
0
Notes: INHANDOUT