## Slide 1: The CS 5 Times
Dormitory Destroyed
Claremont (PP): A Harvey Mudd College dormitory
was left in shambles Tuesday after an unexpected
low-frequency resonance caused it to self-destruct.
“I didn’t mean any harm,” reported a shaken
student. “I was doing my CS lab, and I thought it
would be cool to share my sounds with the other Westies, so I hooked my computer up to the dorm speakers. Who knew that 42 Hertz was a special frequency?”
Rescuers worked frantically to recover the student’s hard drive, which reportedly contained notes for an upcoming physics exam. At press time, the drive remained buried under tons of rubble, and hope for a positive outcome was fading. “I’d give anything for a copy of the Lorentz velocity transformation equations,” wailed the distraught student.
Upon hearing of this offer, North dorm residents reportedly got together and, after much difficulty, reconstructed the equation and offered it in return for West’s best speakers.
“West” dormitory after unfortunate incident.
Notes: This is a good day to do evals (the break comes early).
No worksheet.

## Slide 2: True Story: Alan Turing
Alan Turing 1912-1954
1938 Princeton Ph.D.
thesis on uncomputability
Notes: Talented runner; sometimes ran 40 miles to London for meetings. Tried out for 1948 Olympics (marathon), ran 2:46 despite an injury.

## Slide 3: Alan Turing
Allied Tanker hit by U-Boat Torpedo
German WWII U-Boat
Enigma
Bletchley Park
Notes: Enigma machine was crucial both to early German successes and later Allied win. Some of Turing’s cryptography papers weren’t released until April 2012.

## Slide 4: A 1-Bit Memory
This stuff is truly unforgettable!
OR + NOT = NOR
Notes: Next slides have animations to explain how this works.

## Slide 5: A 1-Bit Memory

## Slide 6: Setting a 1-Bit Memory

## Slide 7: Initializing a 1-Bit Memory
Notes: This circuit is the simplest type of "latch" or a "flip-flop". It is called an "S-R latch" or sometimes an "R-S" one.

## Slide 8: From S-R Latches to D-Latches
>
Worksheet!
Notes: WORKSHEET PROBLEM: What does this circuit do when "Strobe" is high? What about when it is low?
Strobes are often called clocks, and may be represented by greater-than signs or triangles. In Logisim, S-R flip-flops have clocks. Clocks can be active-low, active-high, or edge-triggered on either the rising or the falling edge. In Logisim, flip-flops clock on the rising edge.

## Slide 9: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
3 data
bits (out)
Read
Write
00
01
10
11
1
0
1
1
0
1

## Slide 10: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
3 data
bits (out)
Read
Write
1
1
0
00
01
10
11

## Slide 11: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
3 data
bits (out)
Read
Write
1
1
0
1
0
1
1
1
0

## Slide 12: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q

## Slide 13: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 14: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 15: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 16: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 17: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 18: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder

## Slide 19: A Random Access Memory (RAM)
2 address
bits
3 data
bits (in)
Read
Write
3 data
bits (out)
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
D
Latch
D
Strobe
Q
Decoder
Notes: Note that a real modern RAM would have literally hundreds of millions of “rows” of memory, each of which might be 8 bits (columns) wide or wider!

## Slide 20
A Random Access Memory (RAM)
A 512K RAM
(About 4.2 million bits)

## Slide 21: Small Memory, “Big” Memory…
2 address
bits
3 data
bits (in)
3 data
bits (out)
Read
Write
8 address
bits
X data
bits (in)
X data
bits (out)
Read
Write
X

## Slide 22: DROP! COVER! HOLD ON!

## Slide 23: The Alien’s Life Advice
Shower!
You only think you don’t smell bad.
And wash your clothes!

## Slide 24
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Load 5 into Register 0
0
0
0
0
Register 3

## Slide 25
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Load 5 into Register 0
5
0
0
0
Register 3

## Slide 26
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register1
5
0
0
0
Register 3

## Slide 27
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register1
5
0
5
0
Register 3

## Slide 28
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
5
0
Register 3

## Slide 29
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
0
Register 3

## Slide 30
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000

## Slide 31
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide

## Slide 32
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000
00______
00 add
01 subtract
10 multiply
11 divide

## Slide 33
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000
0010____
00 add
01 subtract
10 multiply
11 divide

## Slide 34
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000
001000__
00 add
01 subtract
10 multiply
11 divide

## Slide 35
A “Calculator”
Instruction Register
Register 0
Register 1
Register 2
Register2=Register0+Register2
5
0
10
00000101
00000000
00001010
0
Register 3
00000000
00100010
00 add
01 subtract
10 multiply
11 divide

## Slide 36
A Computer!
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00000000

## Slide 37
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00000000
A Computer!

## Slide 38
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00000000
A Computer!

## Slide 39
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00110010
A Computer!

## Slide 40
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000000
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00110010
Register3=Register0+Register2
A Computer!

## Slide 41
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000000
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00110010
Register3=Register0+Register2
A Computer!

## Slide 42
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000001
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00110010
Program Counter Incremented
A Computer!

## Slide 43
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000001
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00110010
A Computer!

## Slide 44
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000001
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
What is this command saying?

## Slide 45
Instruction Register
Register 0
Register 1
Register 2
00000010
00000000
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000001
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
Register1=Register2+Register2
A Computer!

## Slide 46
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000001
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
Register1=Register2+Register2
A Computer!

## Slide 47
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
Program Counter Incremented
A Computer!
Notes: What happens next?

## Slide 48
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
Notes: What happens next?

## Slide 49
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
1
Notes: What happens next?

## Slide 50
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
1
Notes: What happens next?

## Slide 51
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
1
10001100
Notes: What happens next?

## Slide 52
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
00011010
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
10001100
Notes: What happens next?

## Slide 53
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
10001100
Notes: What happens next?

## Slide 54
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
10001100
Notes: There are more decoders - one for each of the four instructions!
WHAT HAPPENS NEXT???

## Slide 55
Instruction Register
Register 0
Register 1
Register 2
00000010
00000010
00000001
Register 3
00000011
00 add
01 subtract
10 multiply
11 divide
00110010
Central Processing Unit (CPU)
00000010
Program Counter
Memory
00000000 0
00000001 1
00000010 2
00000011 3
00000100 4
11111111 255
Memory Location
Binary Base 10
00011010
10001100
A Computer!
8 bit
address
8 bit
data in
Read
Write
8 bit data out
10001100
1
Notes: There are more decoders - one for each of the four instructions!
WHAT HAPPENS NEXT???

## Slide 56: The von Neumann “Architecture”
CPU
RAM
central processing unit
random access memory
r0
…
r15
r1
r2
Program Counter
A few fast
registers
Large but
slow memory
Instruction Register
Ripple-carry adder
Multiplier,
Registers, etc.
Lots of latches!
00110010
00011010
10001100
John von Neumann

## Slide 57
2006
Intel Core 2 Duo
3 GHz clock
64-bit processor
291 million transistors
65 nm wires
It doesn’t look all that fast to me!

## Slide 58: A Short Aside…
CPU
Main Memory
(RAM)
Disk Drive
1 cycle
200 cycles
? cycles
16 Registers (“Bytes”)
109 “Bytes” of
memory
1012 “Bytes” of
memory
107 cycles
Actual
time:
<10-9 sec
<10-7 sec
<10-2 sec
If “cycle”
= 1 sec
1 sec
3-5 minutes
???
4.5 MONTHS!

## Slide 59: A Short Aside…
CPU
Main Memory
(RAM)
Disk Drive
1 cycle
200 cycles
? cycles
16 Registers (“Bytes”)
109 “Bytes” of
memory
1012 “Bytes” of
memory
Actual
time:
<10-9 sec
<10-7 sec
<10-2 sec
If “cycle”
= 1 sec
1 sec