## Slide 1
Any function's circuit can be built from …
… just three logic gates!
CS Today
Minterm Expansion Principle
Notes: Class 12 gates
Logisim is flaky; reset the simulation or save and restart
Have lec12_demos.circ ready. Editing Logisim files in emacs can be a quick way to do things that Logisim itself doesn’t support, such as renaming, sorting, combining files. You should be ready to show rsff, maybe development of rsff from a wire (in rsff_develop), maybe RCA, multiplier, divider, memory (not necessarily in that order).
Be sure you know how to develop an RSFF from a wire.

## Slide 2
Things seem to get messy around here…
An example of a happy RCA solution...
taking
Logisim's "canvas" literally
…
CS 5
logic gates
switches: transistors
bitwise functions
arithmetic
1-bit memory: flip-flops
main memory
computer
Hmmm...
registers
Python
A
B
S
T
R
A
C
T
I
O
N
OUR
CS5
PATH
Notes: Class 12 gates
INHANDOUT
RCA = Ripple-Carry Adder
We’re going to go all the way down to transistors today.

## Slide 3
Composing circuits ~ hw6
4-bit "Ripple-Carry" Adder
4-bit Multiplier
3x2-bit Divider
12 nGbits of memory (RAM)
extra credit

## Slide 4
Composing circuits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
8 bits in
5 bits out
let's abstract these details away…
Notes: The RCA here (without the smiley) will work for building a multiplier.

## Slide 5
Composing circuits
8 input bits
Now let's make lots of them!!
1 0 1 0 0
5 output bits
0 1 1 1
1 1 0 1
+
4-bit Ripple-Carry Adder
Notes: INHANDOUT
Looking at the RCA as a school bus, it’s a building block for a multiplier.

## Slide 6: hw6pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(Q3) How could THREE 4-bit ripple-carry adders help here?
(Q2) What bit would be correct for the starred spot ?
(Q1) What circuits could you use to create the four "partial products" ??
0
Notes: On the next slide we show the school buses.

## Slide 7: hw6pr2: A 4-bit multiplier
1 1 0 1 Multiplicand
x 0 1 1 0 Multiplier
0 0 0 0 4 partial products
1 1 0 1
1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1 0 Final answer…
(A1) Use a 4x1-bit helper circuit to find the four partial products…
(A3) You need three (3) ripple-carry adders to finish: see above…
(A1) The AND gate is single-bit multiplication.
0
(A2) == 0
Notes: INHANDOUT
Show how first partial-product bit just goes down to output without going through RCA.
Circle bus “wheels”. Talk about how leftmost bit of bus top comes from a zero.
Use Logisim to show 4x4 multiplication: 7x6, 6x7, 15x15

## Slide 8
The "canvas"
These are circuit-based compositions!

## Slide 9
Division? hw6pr3
Ideas?
Notes: INHANDOUT
Ask for ideas, then turn to logisim covered_divider to show divide by 1 = duplicate, by 0 = error, by 2 = RH bit lost, by 3 is complex

## Slide 10
Division! hw6pr3
Notes: This circuit doesn’t work.

## Slide 11
bit
principled design
Minterm Division
(0) All computation can be expressed as bits...
(1) Any function of bits can be made a truth table
INPUTS
Y2 Y1 Y0 X1 X0
OUTPUT
Z2 Z1 Z0 E
0 0
anything
0 0 0
0 1
0 0 1
0 1
0 1 0
0 1
0 1 1
0 1
1 0 0
0 1
1 0 1
0 1
1 1 0
0 1
1 1 1
0 1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 1
1 1
1 1
1 1
1 1
1 1
1 1
1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 1 0 0
1 0 1 0
1 1 1 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 1 1 0
0 1 0 0
0 1 1 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 1 0
0 0 1 0
0 1 0 0
0 0 1 0
0 1 0 0
(2) Consider the output, one bit at a time...
(5) Else, use an AND gate to select each input for which the output should be 1 (a minterm!)
(3) The circuit will output 0 by default!
(6) OR the outputs from step (5) together.
anything
(7) optimize your circuit later -- or never
To implement the red 1, how many inputs will its AND gate have?
What division is it?
How many negated?
dividend
divisor
quotient
error
(4) Are there subcircuit patterns to notice?
Notes: INHANDOUT
Every AND would need 5 inputs; there are tons of ANDs.
Show how divide-by-3 is sensible to do with minterm expansion (circle the 1’s)
Is there a way to reduce it further?

## Slide 12
Circuit Optimization?
Perhaps artistically optimized!
Optimize for what?!
16 gates
7 gates
using a genetic algorithm
try E85 !
Notes: INHANDOUT
Be vague. E85 covers this.
What are you optimizing for? (Next slide)

## Slide 13
Time-optimized circuits: Carry lookahead adders
The following circuit is called a carry lookahead adder.
By adding more hardware, we reduced the number of levels in the circuit and sped things up.
We can "cascade" carry lookahead adders, just like ripple carry adders.
We'd have to do carry lookahead between the adders too.
How much faster is this?
  For a 4-bit adder, not much. There are 4 gates in the longest path of a carry lookahead adder, versus 9 gates for a ripple carry adder.
  But if we do the cascading properly, a 16-bit carry lookahead adder could have only 8 gates in the longest path, as opposed to 33 for a ripple carry adder.
  Newer CPUs these days use 64-bit adders. That's 12 vs. 129 gates or 10x speedup!
The delay of a carry lookahead adder grows logarithmically with the size of the adder, while a ripple carry adder's delay grows linearly.
The thing to remember about this is the trade-off between complexity and performance. Ripple carry adders are simpler, but slower. Carry lookahead adders are faster but more complex.
Notes: INHANDOUT

## Slide 14
A 4-bit carry-lookahead adder circuit
A 4-bit ripple-carry adder circuit
speed vs. complexity tradeoffs ~ cs facets of engineering
What information is needed? Where? How?
Notes: RCA flows information through 2 gates per column.

## Slide 15
“carry-out”, not “c-zero”
A 4-bit carry-lookahead adder circuit
Sum bits
Carry bits
carry-in
xor
xor
xor
xor
xor
xor
xor
xor
Details!

## Slide 16
What's inside gates?
What's the other half of computation?
Notes: Now we’re going to go one layer deeper.

## Slide 17
Today's gates?
https://www.youtube.com/watch?v=Fxv3JoS1uY8

## Slide 18
Silicon-based switches (transisors)
a single etched transistor labeled with base (b), emitter (e), and collector (c)

## Slide 19
Transistors
switch-on-type transistor
single-electron tunneling, or SET transistor
20 nm
+3v voltage here
allows current here
Radio Shack transistors
0v
switch-off-type (pmos)
0v “connects" this wire
Transistors are current switches:
3v "cuts" this wire
3v
switch-on-type (nmos)
0v
0v "cuts" this wire
3v “connects" this wire
3v
Notes: Think of it as like a drawbridge

## Slide 20
Building a NOT gate
Building a NOT gate from transistors…
output
input
NOT
(0 or 1)
+3 v
Ground = 0v
INPUT
POWER
OUTPUT
(1 or 0)
0v
switch-off-type (pmos)
0v “connects" this wire
Transistors are current switches:
3v "cuts" this wire
3v
switch-on-type (nmos)
0v
0v "cuts" this wire
3v “connects" this wire
3v
Notes: INHANDOUT
Show how 1 input connects output to ground, 0 does the reverse.

## Slide 21
NOT gate
(0 or 1)
+3 v
Ground = 0v
INPUT
POWER
OUTPUT
(1 or 0)
0v
switch-off-type (pmos)
0v “connects" this wire
Transistors are current switches:
3v "cuts" this wire
3v
switch-on-type (nmos)
0v
0v "cuts" this wire
3v “connects" this wire
3v

## Slide 22
(2) the above circuit is one of these gates – which one?
each is 0 or 1 independently
Ground, 0 or 0v
Inputs: X, Y
Output: Z
X
Y
X
Y
NAND
"not and"
OR
NOR
XOR
"not or"
Z
(3) Extra! How could you alter the transistor-level design to make an AND?
Power, 1 or +3v
"exclusive or"
Name(s) __________________________________________
Quiz
(1) Find the circuit's truth table
X
Y
Z
0
0
0
1
1
0
1
1
Notes: QUIZSLIDE
Remind them that they built XOR in lab. NAND and NOR are inverses of AND and OR.
Demonstrate how to analyze the 1/1 input case.

## Slide 23
Reading this week: H2O computing !
Notes: Take note that it’s this week’s reading

## Slide 24
NOT gate
Signal Input, A
Signal Output
Q
Spring
Electromechanical "gates" (relays)
1940's computers
External Power (6v)
Electro-magnet
metal plate

## Slide 25
Which gate is this?
Input, A
Signal Output
Q
External Power (6v)
AND
NAND
OR
NOR
XOR
Input, B

## Slide 26
The Mark 1
ran at 0.00001 MHz
5 tons
530 miles of wiring
765,299 distinct parts!
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html
Grace Hopper + Howard Aiken, Harvard ~ 1944
an early, relay-based computer
Notes: 10Hz clock
All those parts => always broken

## Slide 27
The Mark 1
ran at 0.00001 MHz
5 tons
530 miles of wiring
765,299 distinct parts!
Addition: 0.6 seconds
Multiplication: 5.7 seconds
Division: 15.3 seconds
http://www-03.ibm.com/ibm/history/exhibits/markI/markI_reference.html
Grace Hopper + Howard Aiken, Harvard ~ 1944
an early, relay-based computer
a "modern" relay-based computer
Notes: Zach has a video showing how loud this is.

## Slide 28
Transistors as disruptive technology
1947: Bell Labs
seeking amplifiers for phone lines
team of physicists: Walter Brattain, William Shockley, and John Bardeen
1948: Junction transistor
1956: Shockley Semiconductor Co.
1957: Fairchild Semiconductor Co.
much more robust design
the "traitorous eight" – left - ICs
point contact transistor
in hometown of Palo Alto...
... and the valley had begun silicon-izing
Notes: Shockley was a horrible person. Everybody hated him (abrasive, domineering, paranoid).
He had a visiting position at CalTech, was kicked out after only 4 months.
Nobody from Bell Labs would join Shockley Semi so he had to scour the nation for people who didn’t know him.
The self-described “tratorious 8” left after one year.

## Slide 29
Half a computer: the CPU
transistors
6 x 7… !
arithmetic
gates
Notes: INHANDOUT

## Slide 30
What's inside gates?
What's the other half of computation?

## Slide 31
Make no mistake: computers process numbers—not symbols.
We can only automate what we can arithmetize.
- Alan Perlis
True! But it misses 99% of what computers do! What?
Store + Retrieve
incl. communication

## Slide 32
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
input
output
- also Alan Perlis
Notes: INHANDOUT
Here, draw a feedback edge through a NOR gate. Show how this just oscillates until X becomes 1.

## Slide 33
For systems, a face-lift is to add an edge that creates a cycle, not just an additional node.
NOR
X
NOR
inputs
output
Y
NOR's Truth Table
X
Y
Z
Z
0
0
0
1
1
0
1
1
1
0
0
0
Let's engineer this into 1 bit of memory!
- also Alan Perlis
Notes: INHANDOUT

## Slide 34
The circuit starts with R being 0 + S being 0
The internal wires may be undefined, to start (this is ok) ...
NOR
NOR
S
R
?
?
0
"Set"
"Reset"
?
0
?
Q
Q is the output
What happens if R is set to 1? (and S stays 0)
What happens if R is set back to 0? (and S stays 0)
What if, then, S is set to 1? (and R stays 0)
Thought experiment
What happens if, then, S is set back to 0? (and R stays 0)
Why does "S" stand for "Set" and R for "Reset" ?
Notes: INHANDOUT

## Slide 35
Q still stays (!) at 0
Q is then set to 1
Q still stays (!) at 1
Q is then set to 0
What happens if S stays 0 and R is set back to 0?
What happens if R is 0 and S is set to 1?
Memory!
Take a look at this circuit:
The D (data) line holds a single bit we want to store (either a 0 or a 1).
How does the strobe bit help store the bit D into Q?
Why does "S" stand for "Set" and R for "Reset" ?
What happens if S is 0 and R is set back to 0?
Hint: What happens when the "strobe" is 1?
NOR
NOR
S
R
1
0
0
"Set"
"Reset"
1
Q
Q is 1 bit of storage
The circuit starts with R being 0 + S being 0
What if S stays 0 and R is set to 1?
S "sets" Q to 1; R "resets" it back to 0.
"we are ready to handle the data"
Notes: The D circuit is on the next slide in the handout.

## Slide 36
NOR
NOR
inputs
The flip-flop
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
the flip-flop's diagram
Demo!
Q
Q is 1 bit of storage
"we are ready to handle the data"
Notes: INHANDOUT

## Slide 37
NOR
NOR
inputs
The flip-flop
D
data
"strobe"
AND
AND
strobe
D
Q
1 bit of memory!
the flip-flop's diagram
Demo!
Q
Q is 1 bit of storage
But there's a LOT more than 1 bit of memory… !

## Slide 38
Random Access Memory
Extra this week: Design 12nGbits of RAM
3 data output bits
Inputs
3 data input bits
Simplified
Prototype for
Accessing
Memory
Outputs
write enable line
read enable line
2 data address bits
3 bits stored at location 00
3 bits stored at location 01
3 bits stored at location 10
3 bits stored at location 11
12 bits of RAM
Demo!
Notes: INHANDOUT
Demo RAM in Logisim.

## Slide 39
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
STORE
the value 5 into mem. loc. #1
3 data input bits
write enable line
read enable line
0
1
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Make data input bits 101
3. How do the * AND gates make sure that the value does go into memory location #1?
*
*
Extra Credit
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Write Enable" high
Binary Address Decoder
4. How do the * AND gates make sure that the value does NOT go into memory location #0?
0
1
data address, in binary
A0
A1
Notes: INHANDOUT

## Slide 40
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
strobe
D
Q
LOAD
take data from mem. location #1
3 data input bits
write enable line
read enable line
data address, in binary
0
1
Binary Address Decoder
two other memory lines and their flip-flops are not drawn
3 data output bits
2
3
OR
OR
OR
0. Suppose 101 is in Location #1
3. Which gates will ensure bits from memory location #1 are read out?
4. Which gates will ensure bits from memory location #0 are not read out?
memory location
1. Give 01 to the decoder (the 1 goes on)
2. Make the "Read Enable" high
5. Draw where the "Read Enable" wire should go!
0
1
A0
A1
Notes: INHANDOUT