## Slide 1: Machine-Level Programming I:
Topics
  Assembly Programmer’s Execution Model
  Accessing Information
    Registers
    Memory
  Arithmetic operations
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: Intel x86 (IA32/64) Processors
Totally Dominate Computer Market
Evolutionary Design
  Starting in 1978 with 8086 (really 1971 with 4004)
  Added more features as time went on
  Still support old features, although obsolete
Complex Instruction Set Computer (CISC)
  Many different instructions with many different formats
    But only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But Intel has done just that!
    Well…in terms of speed; less so for low power

## Slide 3: X86 Evolution: Milestones
Name Date Transistors Frequency
4004 1971 2.3K 108 KHz
  4-bit processor. First 1-chip microprocessor
  Didn’t even have interrupts!
8008 1972 3.3K 200-800 KHz
  Like 4004, but with 8-bit ALU
8080 1974 6K 2 MHz
  Compatible at source level with 8008
  Processor in first “kit” computers
  Pricing caused it to beat similar processors with better programming models
    Motorola 6800
    MOS Technologies (MOSTEK) 6502

## Slide 4: X86 Evolution: Milestones
Name Date Transistors Frequency
8086 1978 29K 5-10 MHz
  16-bit processor. Basis for IBM PC & DOS
  Limited to 1MB address space. DOS only gives you 640K
80286 1982 134K 4-12 MHz
  Added elaborate, but not very useful, addressing scheme
  Basis for IBM PC-AT and Windows
386 1985 275K 16-33 MHz
  Extended to 32 bits. Added “flat addressing”
  Capable of running Unix
  By default, Linux/gcc compiling for 32-bit x86 machines use no instructions introduced in later models

## Slide 5: X86 Evolution: Milestones
Name Date Transistors Frequency
486 1989 1.9M 16-150 MHz
Pentium P5 1993 3.1M 60-66 MHz
Pentium 4E 2004 125M 2.8-3.8 GHz
  First 64-bit Intel x86 processor
Core 2 2006 291M 1.0-3.5 GHz
  First multi-core Intel processor
Core i7 2008 731M 1.7-3.9 GHz
Ivy Bridge 2012 0.6-4.3B 3.2-4.0 GHz
  Transistor counts are going crazy here…
  …but max GHz has been stuck since 2004

## Slide 6: X86 Evolution: Clones
Advanced Micro Devices (AMD)
  Historically
    AMD has followed just behind Intel
    A little bit slower, a lot cheaper
  Late 1990s
    Recruited top circuit designers from Digital Equipment Corp.
    Exploited fact that Intel distracted by Itanium
    Became close competitors to Intel
  Developed own extension to 64 bits (called x86_64)
  Intel adopted in early 2000’s after Itanium bombed
    Has recovered lead in semiconductor technology
    AMD has fallen behind again

## Slide 7: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand or write assembly/machine code.
  Examples: instruction set specification, registers.
Microarchitecture: Implementation of the architecture.
  Examples: cache sizes and core frequency.
Code Forms:
  Machine Code: The byte-level programs that a processor executes
  Assembly Code: A text representation of machine code
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones

## Slide 8: Assembly Programmer’s View
Programmer-Visible State
  RIP (Program Counter)
    Address of next instruction
  Register File
    Heavily used program data
  Condition Codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
R
I
P
Registers
CPU
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes
  Memory
    Byte-addressable array
    Code, user data, (most) OS data
    Includes stack used to support procedures

## Slide 9: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Wall -Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc -Wall -Og p1.c p2.c -o p
    Use basic optimizations (-Og) (new to recent versions of gcc)
    Put resulting binary in file p

## Slide 10: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on Wilkes) with command
  gcc –Og –S sum.c
Produces file sum.s
(Note: we’re removed a bunch of irrelevant pseudo-ops intended for the assembler)
Warning: May get very different results on other machines (Knuth, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 11: Assembly Characteristics
Minimal data types
  Integer data of 1, 2, 4, or 8 bytes
    Data values
    Addresses (untyped pointers)
  Floating-point data of 4, 8, or 10 bytes
  No aggregate types such as arrays or structures
    Just contiguously allocated bytes in memory
  Code is also just byte sequences encoding instructions
Primitive operations
  Perform arithmetic function on register or memory data
  Transfer data between memory and register
    Load data from memory into register
    Store register data into memory
  Transfer control
    Unconditional jumps to/from procedures
    Conditional branches

## Slide 12: Object Code
Sample code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 13: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 14: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 15: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  gdb sum
  disassemble sumstore
  Disassembles procedure named sumstore
  x/14xb sumstore
  Examines the 14 hex bytes starting at sumstore
  x/6i sumstore
  Disassembles 6 insructions starting at sumstore
Object
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 16: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 17: x86-64 Integer Registers
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%ax
%bx
%cx
%dx
%si
%di
%sp
%bp
%r8w
%r9w
%r10w
%r11w
%r12w
%r13w
%r14w
%r15w
%dx
%si
%di
%sp
%bp
%r8w
%r9w
%r10w
%r11w
%r12w
ah
al
bh
bl
ch
cl
dh
dl
sil
dil
spl
bpl
r8b
r9b
r10b
r11b
r12b
r13b
r14b
r15b
Oh.
My.
God.

## Slide 18: x86-64 Integer Registers
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d

## Slide 19: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, 4, or 8 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 20: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 21: Simple Addressing Modes
Direct A Mem[A]
  Memory address A is directly specified
  Mostly used for static and global variables
  movl 0x804acb8,%eax
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C
  movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset
  movq 8(%rbp),%rdx

## Slide 22: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 23: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 24: Understanding Swap()
123
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 25: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 26: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 27: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 28: Simple Addressing Modes
Direct A Mem[A]
  Memory address A is directly specified
  Mostly used for static and global variables
  movl 0x804acb8,%eax
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C
  movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset
  movq 8(%rbp),%rdx

## Slide 29: Complete Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes (but not 8)
    Can be small (offset) or large (address)
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
D Mem[D]
(,Ri,S) Mem[S*Reg[Ri]]

## Slide 30: Address Computation Examples
%rdx
%rcx
0xf000
0x100
Expression | Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080

## Slide 31: Address Computation Instruction
leaq Src,Dest
  Src is address mode expression
  Set Dest to address denoted by expression
Uses
  Computing address without doing memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8.
LEARN THIS INSTRUCTION!!!
  Used heavily by compiler
  Appears regularly on exams & quizzes

## Slide 32: leaq vs. movq
Assume dest is %rax:
%rdi = 0xF000
%rsi = 0x8
Memory at 0xF000 = 0x12345
Memory at 0xF008 = 0x6789A
Memory at 0xF010 = 0xBCDEF
Src leaq movq
(%rdi) 0xF000 0x12345
8(%rdi) 0xF008 0x6789A
(%rdi,%rsi) 0xF008 0x6789A
(%rdi,%rsi,2) 0xF010 0xBCDEF
%rdi Illegal! 0xF000

## Slide 33: Some Arithmetic Operations
Carnegie Mellon
Two-Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)
Note: immediate source limited to 4 bytes (sigh)

## Slide 34: Some Arithmetic Operations
Carnegie Mellon
One-Operand Instructions
    incq Dest = Dest + 1
    decq Dest = Dest  1
    negq Dest =  Dest
    notq Dest = ~Dest
See textbook for more instructions

## Slide 35: Arithmetic Expression Example
Carnegie Mellon
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But only used once!
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 36: Understanding Arithmetic Expression Example
Carnegie Mellon
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5