## Slide 1: Floating Point
Topics
  IEEE Floating-Point Standard
  Rounding
  Floating-Point Operations
  Mathematical Properties
CS 105 “Tour of the Black Holes of Computing!”

## Slide 2: Floating-Point Puzzles
  For each of the following C expressions, either:
    Argue that it is true for all argument values
    Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (float) d
f == -(-f)
2/3 == 2/3.0
d < 0.0  ((d*2) < 0.0)
d > f  -f > -d
d * d >= 0.0
(d+f)-d == f
int x = foo();
float f = bar();
double d = baz();
Assume neither
d nor f is NaN
Assume a 32-bit
machine

## Slide 3: Fractional binary numbers
Carnegie Mellon
What is 1011.1012?

## Slide 4: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
Carnegie Mellon
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 5: Fractional Binary Numbers: Examples
Carnegie Mellon
Value Representation
5 3/4 101.112
2 7/8 010.1112
1 7/16 001.01112
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 6: Representable Numbers
Carnegie Mellon
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 7: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating-point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make go fast
    Numerical analysts predominated over hardware types in defining standard

## Slide 8: Floating-Point Representation
Numerical Form
  –1s M 2E
    Sign bit s determines whether number is negative or positive
    Significand M normally a fractional value in range [1.0,2.0).
    Exponent E weights value by a power of two
Encoding
  MSB is sign bit
  exp field encodes E (emphasis on “encodes”)
  frac field encodes M (likewise)
s
exp
frac

## Slide 9: Precision Options (Not to Scale)
Carnegie Mellon
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8 bits | 23 bits
s | exp | frac
1 | 11 bits | 52 bits
s | exp | frac
1 | 15 bits | 63 or 64 bits

## Slide 10: “Normalized” Values
Carnegie Mellon
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 – 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 11: Normalized Encoding Example
Value
  Float F = 15213.0;
  1521310 = 111011011011012 = 1.11011011011012 X 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Floating-Point Representation (Class 02):
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
140: 100 0110 0
15213: 1110 1101 1011 01

## Slide 12: Denormalized Values
Carnegie Mellon
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
v = (–1)s M 2E
E = 1 – Bias

## Slide 13: Special Values
Carnegie Mellon
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 14: Visualization: Floating-Point Encodings
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0

## Slide 15: Tiny Floating-Point Example
8-bit floating-point representation
  The sign bit is in the most significant bit.
  The next four bits are the exponent, with a bias of 7.
  The last three bits are the frac
Same general form as IEEE format
  Normalized, denormalized
  Representation of 0, NaN, infinity
s
exp
frac
0
2
3
6
7

## Slide 16: Values Related to the Exponent
Exp exp E 2E
0 0000 -6 1/64 (denorms)
1 0001 -6 1/64
2 0010 -5 1/32
3 0011 -4 1/16
4 0100 -3 1/8
5 0101 -2 1/4
6 0110 -1 1/2
7 0111 0 1
8 1000 +1 2
9 1001 +2 4
10 1010 +3 8
11 1011 +4 16
12 1100 +5 32
13 1101 +6 64
14 1110 +7 128
15 1111 n/a (inf, NaN)

## Slide 17: Dynamic Range
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 18: Distribution of Values
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 19: Distribution of Values (close-up view)
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3

## Slide 20: Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} X 2– {126,1022}
  Single (float)  1.4 X 10–45
  Double  4.9 X 10–324
Largest Denormalized 00…00 11…11 (1.0 – ) X 2– {126,1022}
  Single (float)  1.18 X 10–38
  Double  2.2 X 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 X 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ) X 2{127,1023}
  Single (float)  3.4 X 1038
  Double  1.8 X 10308

## Slide 21: Special Properties of Encoding
FP zero same as integer zero
  All bits = 0
Can (almost) use unsigned integer comparison
  Must first compare sign bits
  Must consider -0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denormalized vs. normalized
    Normalized vs. infinity

## Slide 22: Floating Point Operations: Basic Idea
Carnegie Mellon
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 23: Rounding
Carnegie Mellon
Rounding Modes (illustrated with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 24: Closer Look at Round-To-Even
Default rounding mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
    Need randomness
Applying to other decimal places / bit positions
  When exactly halfway between two possible values:
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    1.2349999 1.23 (Less than half way)
    1.2350001 1.24 (Greater than half way)
    1.2350000 1.24 (Half way—round up)
    1.2450000 1.24 (Half way—round down)

## Slide 25: Rounding Binary Numbers
Binary fractional numbers
  “Even” when least significant bit is 0
  Halfway when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 (1/2—up) 3
  2 5/8 10.101002 10.102 (1/2—down) 2 1/2

## Slide 26: FP Multiplication
Operands
  (–1)s1 M1 2E1 * (–1)s2 M2 2E2
Exact Result
  (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 * M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 27: FP Addition
Operands
  (–1)s1 M1 2E1
  (–1)s2 M2 2E2
  Assume E1 > E2
Exact Result
  (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
  (–1)s1 M1
  (–1)s2 M2
E1–E2
+
  (–1)s M

## Slide 28: Mathematical Properties of FP Add
Carnegie Mellon
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost

## Slide 29: Mathematical Properties of FP Mult
Carnegie Mellon
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 30: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions
  Casting between int, float, and double changes numeric values
  Double or float to int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range
      Generally saturates to TMin or TMax
  int to double
    Exact conversion, as long as int has ≤ 53-bit word size
  int to float
    Will round according to rounding mode

## Slide 31: Answers to Floating-Point Puzzles
          No: 24 bit significand
          Yes: 53 bit significand
              Yes: increases precision
        No: loses precision
Yes: Just change sign bit
        No: 2/3 == 0
              Yes!
          Yes!
        Yes!
        No: Not associative
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (float) d
f == -(-f)
2/3 == 2/3.0
d < 0.0 ((d*2) < 0.0)
d > f -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NAN

## Slide 32: Ariane 5
  Exploded 37 seconds after liftoff
  Cargo worth $500 million
Why
  Computed horizontal velocity as floating-point number
  Converted to 16-bit integer
  Worked OK for Ariane 4
  Overflowed for Ariane 5
    Used same software

## Slide 33: Summary
IEEE floating point has clear mathematical properties
  Represents numbers of form M X 2E
  Can reason about operations independent of implementation
    As if computed with perfect precision and then rounded
  Not the same as real arithmetic
    Violates associativity/distributivity
    Makes life difficult for compilers & serious numerical applications programmers