## Slide 1: Cache Memories
Topics
  Generic cache-memory organization
  Direct-mapped caches
  Set-associative caches
  Impact of caches on performance
CS 105 Tour of the Black Holes of Computing

## Slide 2: Locality
Principle of Locality: Programs tend to use data and instructions with addresses equal or near to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 3: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 4: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 5: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 6: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}

## Slide 7: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Faster storage technologies cost more per byte and have less capacity
  Gap between CPU and main-memory speed is widening
  Well-written programs tend to exhibit good locality
These fundamental properties complement each other beautifully
They suggest an approach for organizing memory and storage systems known as a memory hierarchy

## Slide 8: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk
blocks retrieved from local
disks
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 9: Caches
Cache: Smaller, faster storage device that acts as staging area for subset of data in a larger, slower device
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as cache for larger, slower device at level k+1
Why do memory hierarchies work?
  Programs tend to access data at level k more often than they access data at level k+1
  Thus, storage at level k+1 can be slower, and thus larger and cheaper per bit
Big Idea: Large pool of memory that costs as little as the cheap storage near the bottom, but serves data to programs at ≈ rate of the fast storage near the top

## Slide 10: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache, then in main memory
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 11: Typical Speeds
Registers: 1 clock (= 400 ps on 2.5 GHz processor) to get 8 bytes
Level-1 (L1) cache: 3–5 clocks for 32–64 bytes
L2 cache: 10–20 clocks, 32–64 bytes
L3 cache: 20–100 clocks (multiple cores make things slower), 32–64 bytes
DRAM: 100–300 clocks, 32–64 bytes
SSD: 75,000 clocks and up (high variance), 4096 bytes
Hard drive: 5,000,000–25,000,000 clocks, 4096 bytes
  Ouch!

## Slide 12: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 13: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 14: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 15: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k
    E.g. Block i at level k+1 must go in block (i mod 4) at level k
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time
Capacity miss
  Occurs when set of active cache blocks (working set) is larger than the cache

## Slide 16: General Cache Organization (S, E, B)
E lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit
Not always power of 2!
Set # ≡ hash code
Tag ≡ hash key

## Slide 17: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 18: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Find set

## Slide 19: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
Match: both yes = hit
Valid? +
Block offset
tag

## Slide 20: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
Match: both yes = hit
Valid? +
int (4 Bytes) is here
Block offset
If tag doesn’t match: old line is evicted and replaced

## Slide 21: Direct-Mapped Cache Simulation
M=16 bytes (4-bit addresses), B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 22: E-way Set-Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Find set

## Slide 23: E-way Set-Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Compare both
Valid? +
Match: both yes = hit
Block offset
tag

## Slide 24: E-way Set-Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Compare both
Valid? +
Match: both yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 25: 2-Way Set-Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 26: What About Writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a “dirty” bit (line different from memory or not)
What to do on a write miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 27: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 28: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    Can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    Includes time to determine whether line is in the cache
  Typical numbers:
    4 clock cycles for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    Typically 50-200 cycles for main memory

## Slide 29: Let’s Think About Those Numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: Cache hit time of 1 cycle Miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 30: Writing Cache-Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified by our understanding of cache memories

## Slide 31: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 32: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array “data” with stride of "stride", using
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 33: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching

## Slide 34: Matrix-Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    But may be able to keep in register
/* ijk */
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
sum = 0.0;
for (k = 0; k < N; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 35: Miss-Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 36: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  Each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  Accesses successive elements
  If block size (B) > sizeof(aij) bytes, exploit spatial locality
    Miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  Accesses distant elements
  No spatial locality!
    Miss rate = 1 (i.e. 100%)

## Slide 37: Matrix Multiplication (ijk)
/* ijk */
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++) {
sum = 0.0;
for (k = 0; k < n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Inner loop:
A
C
(i,*)
(*,j)
(i,j)
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c
B

## Slide 38: Matrix Multiplication (jik)
/* jik */
for (j = 0; j < n; j++) {
for (i = 0; i < n; i++) {
sum = 0.0;
for (k = 0; k < n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Inner loop:
A
C
(i,*)
(*,j)
(i,j)
Column-
wise
Row-wise
Fixed
B

## Slide 39: Matrix Multiplication (kij)
/* kij */
for (k = 0; k < n; k++) {
for (i = 0; i < n; i++) {
r = a[i][k];
for (j = 0; j < n; j++)
c[i][j] += r * b[k][j];
}
}
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c
Inner loop:
A
C
(k,*)
(*,j)
(i,k)
Row-wise
Fixed
Row-wise
B
(i,*)

## Slide 40: Matrix Multiplication (ikj)
/* ikj */
for (i = 0; i < n; i++) {
for (k = 0; k < n; k++) {
r = a[i][k];
for (j = 0; j < n; j++)
c[i][j] += r * b[k][j];
}
}
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c
Inner loop:
A
C
(k,*)
(*,j)
(i,k)
Row-wise
Fixed
Row-wise
B
(i,*)

## Slide 41: Matrix Multiplication (jki)
/* jki */
for (j = 0; j < n; j++) {
for (k = 0; k < n; k++) {
r = b[k][j];
for (i = 0; i < n; i++)
c[i][j] += a[i][k] * r;
}
}
matmult/mm.c
Inner loop:
A
C
(k,j)
(*,k)
Fixed
Column-wise
Column-wise
B
(*,j)
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 42: Matrix Multiplication (kji)
/* kji */
for (k = 0; k < n; k++) {
for (j = 0; j < n; j++) {
r = b[k][j];
for (i = 0; i < n; i++)
c[i][j] += a[i][k] * r;
}
}
Inner loop:
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
A
C
(k,j)
(*,k)
Fixed
Column-wise
B
(*,j)
Column-wise

## Slide 43: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  Misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  Misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  Misses/iter = 2.0
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++) {
sum = 0.0;
for (k = 0; k < n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k = 0; k < n; k++) {
for (i = 0; i < n; i++) {
r = a[i][k];
for (j = 0; j < n; j++)
c[i][j] += r * b[k][j];
}
}
for (j = 0; j < n; j++) {
for (k = 0; k < n; k++) {
r = b[k][j];
for (i = 0; i < n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 44: Better Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 45: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 46: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 47: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i += B)
for (j = 0; j < n; j += B)
for (k = 0; k < n; k += B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n + j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B
matmult/bmm.c

## Slide 48: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 49: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 50: Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
(plus n2/8 misses for C)
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array element used O(n) times!
  But program has to be written properly

## Slide 51: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects with sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.