## Slide 1: Networking
Topics
  Network model
  Client-server programming model
  Sockets interface
  Writing clients and servers
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: Computer Networks
A network is a hierarchical system of boxes and “wires” organized by geographical proximity
  LAN (local area network) spans building or campus
    Ethernet
    802.11 (wireless)
  WAN (wide-area network) spans country or world
    Different, usually faster technology
An internetwork (internet) is an interconnected set of networks
  Global IP Internet (uppercase “I”) is most famous example of an internet (lowercase “i”)

## Slide 3: Lowest Level: Ethernet Segment
Ethernet segment consists of collection of hosts connected by wires (twisted pairs) to a switch
All or part of a building
Operation
  Each Ethernet adapter has unique 48-bit address
  Hosts send bits to any other host in chunks called frames
  Switch copies bits to proper destination port
    Dynamically learns which port has which host address
host
host
host
hub
100 Mb/s
100 Mb/s
ports

## Slide 4: Next Level: Bridged Ethernet Seg
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port. How? Frames have source and destination addresses….
host
host
host
host
host
switch
switch
bridge
100 Mb/s
100 Mb/s
host
host
switch
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
switch
A
B
C
X
Y

## Slide 5: Conceptual View of LANs
For simplicity, switches, bridges, and wires are often shown as collection of hosts attached to a single wire:
host
host
host
...
Key: any host can easily talk to any other host on the “wire”

## Slide 6: Next Level: internets
Multiple incompatible LANs can be physically connected by specialized computers called routers
The connected networks are called an internet
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible LANs (e.g., Ethernet and ATM)

## Slide 7: Notion of an internet Protocol
How is it possible to send bits across incompatible LANs and WANs?
Solution: protocol software running on each host and router smooths out differences between different networks
Implements an internet protocol (i.e., set of rules) that governs how hosts and routers should cooperate when they transfer data from network to network
  TCP/IP is protocol (family) for global IP Internet

## Slide 8: What Does an internet Protocol Do?
1. Provides naming scheme
  Defines uniform format for host addresses
  Each host (and router) is assigned at least one internet address that uniquely identifies it
2. Provides delivery mechanism
  An internet protocol defines a standard transfer unit (packet)
  Packet consists of header and payload
    Header: contains info such as packet size, source and destination addresses
    Payload: contains data bits sent from source host
  Encapsulation—key to network messages

## Slide 9: Other Issues
We are glossing over several important questions:
  What if different networks have different maximum frame sizes? (segmentation)
  How do routers know where to forward frames?
  How do routers learn when the network topology changes?
  What if packets get lost?
These (and other) questions are addressed by the area of systems known as computer networking: CS 125

## Slide 10: Global IP Internet
Most famous example of an internet
Based on TCP/IP protocol family
  IP (Internet protocol) :
    Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host to host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable datagram delivery from process to process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable byte streams from process to process over connections
  …and several more
Accessed via mix of Unix file I/O and functions from the sockets interface

## Slide 11: Hardware and Software Organization of an Internet Application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 12: Programmer’s View of Internet
1. Hosts are mapped to a set of 32-bit IP(v4) addresses or 128-bit IP(v6) addresses
  134.173.42.100 is Knuth (IPv6: 2620:102:2001:902:f069:3ff:fe3e:8a5c or 2620:102:2001:902::100)
2. IP addresses are mapped to set of identifiers called Internet domain names
  134.173.42.2 is mapped to www.cs.hmc.edu
  128.2.203.164 is mapped to www.cs.cmu.edu
  Mapping is many-to-many
3. Process on one Internet host can communicate with process on another via a connection—IP Address, Port Number

## Slide 13: Transferring Data via a Network
protocol
software
client
LAN1
adapter
Host A
data
data
PH
FH1
data
PH
data
PH
FH2
LAN1
LAN2
data
data
PH
data
PH
FH2
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
internet packet
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Routers
FH1
data
PH
protocol
software
server
LAN2
adapter
Host B
Frame

## Slide 14: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
As of 2020, vast majority of Internet traffic still carried by IPv4
  Only 30% of users access Google services using IPv6
  Growth appears linear since 2015
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.

## Slide 15: 1. IP (v4) Addresses
32-bit IP addresses are stored in IP address struct
  Always stored in memory in network byte order (big-endian)
  True in general for any integer transferred in packet header from one machine to another.
    E.g., port number used to identify Internet connection
/* Internet address structure */
struct in_addr {
unsigned int s_addr; /* network byte order (big-endian) */
};
Handy network byte-order conversion functions (no-ops on some machines):
  htonl: convert int from host to network byte order
  htons: convert short int from host to network byte order
  ntohl: convert int from network to host byte order
  ntohs: convert short int from network to host byte order

## Slide 16: Dotted-Decimal Notation
By convention, each byte in 32-bit IP address is represented by its decimal value and separated by period
    IP address 0x8002C2F2 = 128.2.194.242
    IPv6 addresses uglier: 2001:1878:301:902:218:8bff:fef9:a407
Functions for converting between binary IP addresses and dotted decimal strings:
  inet_pton: converts dotted-decimal string to IP address in network byte order
  inet_ntop: converts IP address in network byte order to its corresponding dotted-decimal string
  “n” denotes network representation; “p” denotes printable representation

## Slide 17: 2. Internet Domain Names
mil
edu
gov
com
hmc
berkeley
mit
cs
math
wilkes
134.173.42.167
unnamed root
Knuth
134.173.42.100
amazon
www
208.216.181.15
Top-level domain names
Second-level domain names
Third-level domain names

## Slide 18: Domain Naming System (DNS)
Internet tracks mapping between IP addresses and domain names in worldwide many-to-many distributed database called DNS.
  Conceptually, programmers can view DNS database as collection of millions of address information structures:
Functions for retrieving host entries from DNS:
  getaddrinfo: query key is DNS domain name
  getnameinfo: query key is IP address (V4 or V6)
/* Address information structure (DNS only has + entries) */
struct addrinfo {
int ai_flags; /* Various options */
int ai_family; /* + AF_INET or AF_INET6 */
int ai_socktype; /* Preferred socket type */
int ai_protocol; /* Preferred protocol */
size_t ai_addrlen; /* Length of address */
struct sockaddr *ai_addr; /* + Encoded IP address */
char *ai_canonname; /* + Canonical host name */
struct addrinfo *ai_next; /* Link to next answer */
};

## Slide 19: Properties of DNS Host Entries
Each host entry is equivalence class of domain names and IP addresses
Each host has a locally defined domain name localhost, which always maps to loopback address 127.0.0.1
Different kinds of mappings are possible:
  Simple case: 1-1 mapping between domain name and IP addr:
    www.cs.hmc.edu maps to 134.173.42.2
  Multiple domain names mapped to the same IP address:
    cs.hmc.edu and knuth.cs.hmc.edu both map to 134.173.42.100
  Multiple domain names mapped to multiple IP addresses:
    aol.com and www.aol.com map to multiple IP addresses
  Some valid domain names don’t map to any IP address:
    For example: research.cs.hmc.edu

## Slide 20: A Program That Queries DNS
int main(int argc, char **argv) { /* argv[1] is a domain name */
struct addrinfo hints, *host, *firsthost = NULL;
struct sockaddr_in *addr;
char buf[80];
memset(&hints, 0, sizeof hints);
hints.ai_flags = AI_CANONNAME;
hints.ai_family = AF_INET; /* Or AF_INET6 or AF_UNSPEC */
if (getaddrinfo(argv[1], NULL, &hints, &firsthost) != 0)
exit(1);
printf("official hostname: %s\n", firsthost->ai_canonname);
/* CHANGES NEEDED BELOW FOR AF_INET6 or AF_UNSPEC: see handout */
for (host = firsthost; host != NULL; host = host->ai_next) {
addr = (struct sockaddr_in *)host->ai_addr;
inet_ntop(addr->sin_family, &addr->sin_addr, buf, sizeof buf);
printf("address: %s\n", buf);
}
freeaddrinfo(firsthost);
exit(0);
}

## Slide 21: Querying DNS from the Command Line
Domain Information Groper (dig) provides scriptable command line interface to DNS.
linux> dig +short knuth.cs.hmc.edu
134.173.42.100
linux> dig +short -x 134.173.42.100
Knuth.cs.hmc.edu.
linux> dig +short aol.com
64.12.79.57
64.12.89.186
205.188.100.58
205.188.101.58
207.200.74.38
linux> dig +short -x 64.12.79.57
5minmedia.com.
mightyaol.com.
…

## Slide 22: 3. Internet Connections
Clients and servers communicate by sending streams of bytes over connections:
  Point-to-point, full-duplex (2-way communication), and reliable
Socket is application endpoint of connection
  Socket address is IPaddress:port pair
Port is 16-bit integer that identifies a process:
  Ephemeral port: Assigned automatically on client when client makes connection request
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)
Connection is uniquely identified by socket addresses of its endpoints (socket pair)
  (clientaddr:clientport, serveraddr:serverport)

## Slide 23: Well-known Ports and Service Names
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo server: 7/echo
  ssh servers: 22/ssh
  email server: 25/smtp
  Web servers: 80/http
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 24: Putting it all Together: Anatomy of an Internet Connection
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15

## Slide 25: Client-Server Transactions
(Almost) every network application is based on client-server model:
  Server process and one or more client processes
  Server manages some resource.
  Server provides service by manipulating resource for clients
Client
process
Server
process
1. Client sends request
2. Server
handles
request
3. Server sends response
4. Client
handles
response
Resource
Note: clients and servers are processes running on hosts
(can be the same or different hosts)

## Slide 26: 1. IP Addresses
Computers are identified by IP addresses
Two flavors: IPv4 (old) and IPv6 (new)
Both are stored in an IP address struct of appropriate type
  in_addr for IPv4
  in6_addr for IPv6
Details don’t matter; library functions usually hide them

## Slide 27: 2. Domain Naming System (DNS)
Internet maintains mapping between IP addresses and domain names in huge worldwide distributed database called DNS
  Conceptually, programmers can view DNS database as collection of millions of host entry structures:
Functions for retrieving host entries from DNS:
  getaddrinfo: query key is a DNS domain name
  getnameinfo: query key is an IP address
/* Address information structure (DNS only has + entries) */
struct addrinfo {
int ai_flags; /* Various options */
int ai_family; /* + AF_INET or AF_INET6 */
int ai_socktype; /* Preferred socket type */
int ai_protocol; /* Preferred protocol */
size_t ai_addrlen; /* Length of address */
struct sockaddr *ai_addr; /* + Encoded IP address */
char *ai_canonname; /* + Canonical host name */
struct addrinfo *ai_next; /* Link to next answer */
};

## Slide 28: 3. Internet Connections
Clients and servers communicate by sending streams of bytes over connections
Connections are point-to-point, full-duplex (2-way communication), and reliable
Connection socket pair
(128.2.194.242:51213, 134.173.42.2:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
134.173.42.2:80
Client host address
128.2.194.242
Server host address
134.173.42.2
Note: 51213 is an
ephemeral (temporary) port
allocated by the OS kernel
Note: 80 is a well-known port
associated with Web servers

## Slide 29: Clients
Examples of client programs
  Web browsers, telnet, ssh, games, WhatsApp, …
How does a client find the server?
  IP address in server socket address identifies host (more precisely, an adapter on the host)
  (Well-known) port in server socket address identifies service, and thus implicitly identifies server process that provides it
  Examples of well-known ports
    Port 7: Echo server
    Port 22: ssh server
    Port 25: Mail server
    Port 80: Web server

## Slide 30: Using Ports to Identify Services
Web server
(port 80)
Client host
Server host 134.173.42.2
Echo server
(port 7)
Service request for
134.173.42.2:80
(i.e., Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
134.173.42.2:7
(i.e., echo server)
Kernel
Kernel
Client
Client

## Slide 31: Servers
Servers are long-running processes (daemons).
  Created at boot time (typically) by init process (process 1)
  Run continuously until machine is turned off
  Or spawned by inetd in response to connection to port
Each server waits for requests to arrive on well-known port associated with that particular service
  Port 7: echo server
  Port 22: ssh server
  Port 25: mail server
  Port 80: HTTP server
Machine that runs a server process is also often referred to as a “server”

## Slide 32: Server Examples
Web server (port 80)
  Resource: files/compute cycles (CGI programs)
  Service: retrieves files and runs CGI programs on behalf of the client
FTP server (20, 21)
  Resource: files
  Service: stores and retrieve files
ssh server (22)
  Resource: terminal
  Service: proxies a terminal on the server machine
Mail server (25)
  Resource: email “spool” file
  Service: stores mail messages in spool file
See /etc/services for a comprehensive list of the services (potentially) available on a Linux machine.

## Slide 33: Sockets Interface
Set of system-level functions used in conjunction with Unix I/O to build network applications.
Created in the early 80’s as part of the original Berkeley distribution of Unix that contained an early version of the Internet protocols.
Available on all modern systems
  Unix variants, Windows, OS X, IOS, Android, ARM

## Slide 34: Sockets
What is a socket?
  To the kernel, a socket is an endpoint of communication
  To an application, a socket is a file descriptor that lets the application read from or write to the network
    Remember: All Unix I/O devices, including networks, are modeled as files
Clients and servers communicate with each other by reading from and writing to socket descriptors
Main distinction between regular file I/O and socket I/O is how the application “opens” the socket descriptors
Client
Server
clientfd
serverfd

## Slide 35: Overview of Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
getaddrinfo

## Slide 36: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 37: Socket Address Structures
Generic socket address:
  For address arguments to connect, bind, and accept
  Intended to be generic and future-proof
  Too small for IPv6! (Thus, union needed; see later)
struct sockaddr {
uint16_t sa_family; /* Protocol family */
char sa_data[14]; /* Address data. */
};
sa_family
Family-specific

## Slide 38: Socket Address Structures
IPv4-specific socket address:
0
0
0
0
0
0
0
0
sa_family
Family-specific
struct sockaddr_in {
uint16_t sin_family; /* Protocol family (always AF_INET) */
uint16_t sin_port; /* Port num in network byte order */
struct in_addr sin_addr; /* IP addr in network byte order */
unsigned char sin_zero[8]; /* Pad to sizeof(struct sockaddr) */
};
sin_port
AF_INET
sin_addr
sin_family

## Slide 39: Socket Address Structures
IPv6-specific socket address:
...
sa_family
Family-specific
struct sockaddr_in6 {
uint16_t sin6_family; /* Protocol family (always AF_INET6) */
uint16_t sin6_port; /* Port num in network byte order */
uint32_t sin6_flowinfo; /* IPv6 flow information */
struct in6_addr sin6_addr; /* IP addr in network byte order */
uint32_t sin6_scope_id; /* scope id (new in RFC2553) */
};
sin_port
AF_INET
sin6_flowinfo
sin6_family
sin6_addr
sin6_scope_id

## Slide 40: Truly Generic Socket Address Structure
Union that can handle IPv4 or IPv6
  For casting convenience, we adopt the Stevens convention: SA is declared as a generic type that can hold IPv4 or IPV6 socket address
  Must cast (struct sockaddr_in *) or (struct sockaddr_in6 *) to and from (SA *) for functions that take socket-address arguments.
typedef union {
struct sockaddr_in client4;
struct sockaddr_in6 client6;
} SA;

## Slide 41: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 42: Sockets Interface: socket
Clients and servers use the socket function to create a socket descriptor:
Example:
Protocol-specific! Best practice is to use getaddrinfo to generate parameters automatically, so that code is protocol-independent.
int socket(int domain, int type, int protocol)
int clientfd = Socket(AF_INET6, SOCK_STREAM, 0);
Indicates that we are using IPV6 addresses
Indicates that the socket will be the end point of a reliable connection

## Slide 43: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 44: Sockets Interface: connect
A client establishes a connection with a server by calling connect:
Attempts to establish a connection with server at socket address addr
  If successful, then clientfd is now ready for reading and writing.
  Resulting connection is characterized by socket pair
  (x:y, addr.sin_addr:addr.sin_port)
    x is client address
    y is ephemeral (temporary) port that uniquely identifies client process on client host
Best practice is to use getaddrinfo to supply arguments addr and addrlen.
int connect(int clientfd, SA *addr, socklen_t addrlen);

## Slide 45: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 46: Sockets Interface: bind
Server uses bind to ask kernel to associate the server’s socket address with a socket descriptor:
The process can read bytes that arrive on the connection whose endpoint is addr by reading from descriptor sockfd.
Similarly, writes to sockfd are transferred along connection whose endpoint is addr.
Again, best practice is to use getaddrinfo to supply arguments addr and addrlen.
int bind(int sockfd, SA *addr, socklen_t addrlen);

## Slide 47: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 48: Sockets Interface: listen
By default, kernel assumes that descriptor from socket function is an active socket that will be on the client end of a connection
A server calls listen to tell kernel that a descriptor will be used by a server rather than a client:
Converts sockfd from an active socket to a listening socket that can accept connection requests from clients
backlog is a hint about how many outstanding connection requests the kernel should queue up before starting to refuse requests.
int listen(int sockfd, int backlog);

## Slide 49: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 50: Sockets Interface: accept
Server waits for connection requests from clients by calling accept:
Waits for connection request to arrive on connection bound to listenfd, then fills in client’s socket address in addr and size of socket address in addrlen
Returns a connected descriptor that can be used to communicate with client via Unix I/O routines.
int accept(int listenfd, SA *addr, socklen_t *addrlen);

## Slide 51: accept Illustrated
listenfd(3)
Client
1. Server blocks in accept, waiting for connection request on listening descriptor listenfd
clientfd
Server
listenfd(3)
Client
clientfd
Server
2. Client makes connection request by calling and blocking in connect
Connection
request
listenfd(3)
Client
clientfd
Server
3. Server returns connfd from accept. Client returns from connect. Connection is now established between clientfd and connfd
connfd(4)

## Slide 52: Connected vs. Listening Descriptors
Listening descriptor
  End point for client connection requests
  Created once and exists for lifetime of the server
Connected descriptor
  End point of the connection between client and server
  A new descriptor is created each time the server accepts a connection request from a client
  Exists only as long as it takes to service client
Why the distinction?
  Allows concurrent servers that can communicate over many client connections simultaneously
    E.g., each time we receive a new request, we fork a child or spawn a thread to handle the request

## Slide 53: Sockets Interface
Client / Server
Session
Client
Server
socket
socket
bind
listen
accept
read
read
write
close
read
connect
write
close
Connection
request
EOF
Await connection
request from
next client
open_listenfd
open_clientfd
getaddrinfo
``
getaddrinfo
``

## Slide 54: Echo Client Main Routine
/* #include lots of stuff */
/* usage: ./echoclient host port */
int main(int argc, char **argv)
{
int clientfd;
size_t n;
char *host, *port, buf[MAXLINE];
host = argv[1];
port = argv[2];
if ((clientfd = open_clientfd(host, port)) == -1)
exit(1);
while (fgets(buf, sizeof buf - 1, stdin) != NULL) {
write(clientfd, buf, strlen(buf));
n = read(clientfd, buf, sizeof buf - 1);
if (n != -1) {
buf[n] = '\0';
fputs(buf, stdout);
}
}
close(clientfd);
exit(0);
}

## Slide 55: Echo Client: open_clientfd
int open_clientfd(char *hostname, char *port)
{
int clientfd;
struct addrinfo hints, *hostaddresses = NULL;
/* Find out the server's IP address and port */
memset(&hints, 0, sizeof hints);
hints.ai_flags = AI_ADDRCONFIG | AI_V4MAPPED;
hints.ai_family = AF_INET6;
hints.ai_socktype = SOCK_STREAM;
if (getaddrinfo(hostname, port, &hints, &hostaddresses) != 0)
return -1; /* Caller must generate error message */
}
/* We take advantage of the fact that AF_* and PF_* are identical */
clientfd = socket(hostaddresses->ai_family, hostaddresses->ai_socktype,
hostaddresses->ai_protocol);
if (clientfd == -1)
return -1; /* check errno for cause of error */
/* Establish a connection with the server */
if (connect(clientfd, hostaddresses->ai_addr, hostaddresses->ai_addrlen) == -1)
return -1; /* Caller must generate error message */
freeaddrinfo(hostaddresses);
return clientfd;
}
This function opens a connection from client to server at hostname:port
Details follow….
freeaddrinfo needed here too (lack of space on slide)

## Slide 56: Echo Client: open_clientfd (getaddrinfo)
hints.ai_flags = AI_ADDRCONFIG | AI_V4MAPPED;
hints.ai_family = AF_INET6;
hints.ai_socktype = SOCK_STREAM;
if (getaddrinfo(hostname, port, &hints, &hostaddresses) != 0)
... (more)
getaddrinfo finds out about an Internet host
  AI_ADDRCONFIG: only give IPv6 address if our machine can talk IPv6; likewise for IPv4
  AI_V4MAPPED: translate IPv6 to IPv4 when needed
  AF_INET6: prefer IPv6 to IPv4
  SOCK_STREAM: selects a reliable byte-stream connection

## Slide 57: Echo Client: open_clientfd (socket)
int clientfd; /* socket descriptor */
clientfd = socket(hostaddresses->ai_family, hostaddresses->ai_socktype,
hostaddresses->ai_protocol);
... (more)
socket creates socket descriptor on client
  All details provided by getaddrinfo
  Possibility of multiple addresses (serious code must loop & try all)

## Slide 58: Echo Client: open_clientfd (connect)
Finally, client creates connection with server
  Client process suspends (blocks) until connection is created
  After resuming, client is ready to begin exchanging messages with server via Unix I/O calls on descriptor sockfd
  hostaddresses is linked list, must be freed
    Including on error returns (not shown, for brevity)
int clientfd; /* socket descriptor */
...
/* Establish a connection with the server */
if (connect(clientfd, hostaddresses->ai_addr, hostaddresses->ai_addrlen) == -1) {
freeaddrinfo(hostaddresses);
return -1;
}
freeaddrinfo(hostaddresses);

## Slide 59: Echo Server: Main Routine
int main(int argc, char **argv) {
int listenfd, connfd, error;
socklen_t clientlen;
char * port;
SA clientaddr;
char hostname[NI_MAXHOST], hostaddr[NI_MAXHOST];
listenfd = open_listenfd(argv[1]);
if (listenfd < 0)
exit(1);
while (1) {
clientlen = sizeof clientaddr;
connfd = accept(listenfd, (struct sockaddr *)&clientaddr, &clientlen);
if (connfd == -1)
continue; /* Needs error message (omitted for space) */
error = getnameinfo((struct sockaddr*)&clientaddr, clientlen, hostname,
sizeof hostname, NULL, 0, 0);
if (error != 0)
continue; /* Needs error message (omitted for space) */
getnameinfo((struct sockaddr*)&clientaddr, clientlen, hostaddr, sizeof hostaddr,
NULL, 0, NI_NUMERICHOST);
printf("server connected to %s (%s)\n", hostname, hostaddr);
echo(connfd);
close(connfd);
}
}
This program repeatedly waits for connections, then calls echo(). Details will follow after we look at open_listenfd()…

## Slide 60: Echo Server: open_listenfd
int open_listenfd(char *port)
{
int listenfd, optval = 1, error;
struct addrinfo hints;
struct addrinfo *hostaddresses = NULL;
/* Find out the server's IP address and port */
memset(&hints, 0, sizeof hints);
hints.ai_flags = AI_ADDRCONFIG | AI_V4MAPPED | AI_PASSIVE;
hints.ai_family = AF_INET6;
hints.ai_socktype = SOCK_STREAM;
error = getaddrinfo(NULL, port, &hints, &hostaddresses);
if (error != 0)
return -1;
if ((listenfd = socket(hostaddresses->ai_family, hostaddresses->ai_socktype, hostaddresses->ai_protocol)) == -1)
return -1; /* Also needs freeaddrinfo but that won’t fit on this slide */
/* Eliminates "Address already in use" error from bind. */
if (setsockopt(listenfd, SOL_SOCKET, SO_REUSEADDR, (const void *)&optval , sizeof optval) == -1) {
freeaddrinfo(hostaddresses);
return -1;
}
/* Listenfd will be an endpoint for all requests to port */
if (bind(listenfd, hostaddresses->ai_addr, hostaddresses->ai_addrlen) == -1)
return -1; /* Also needs freeaddrinfo but that won’t fit on this slide */
/* Make it a listening socket ready to accept connection requests */
if (listen(listenfd, LISTEN_MAX) == -1)
return -1; /* Also needs freeaddrinfo but that won’t fit on this slide */
freeaddrinfo(hostaddresses);
return listenfd;
}
This function opens a file descriptor on which server can listen for incoming connections. Details follow…

## Slide 61: Echo Server: open_listenfd (getaddrinfo)
Here, getaddrinfo sets up to create generic “port”
  Most options same as for open_clientfd
  AI_PASSIVE: allow any host to connect to us (because we’re a server)
  First argument to getaddrinfo is NULL because we won’t be connecting to a specific host
memset(&hints, 0, sizeof hints);
hints.ai_flags = AI_ADDRCONFIG | AI_V4MAPPED | AI_PASSIVE;
hints.ai_family = AF_INET6;
hints.ai_socktype = SOCK_STREAM;
error = getaddrinfo(NULL, port, &hints, &hostaddresses);

## Slide 62: Echo Server: open_listenfd (socket)
socket creates socket descriptor on the server
  All important parameters provided by getaddrinfo
  Saves us from worrying about IPv4 vs. IPv6
int listenfd; /* listening socket descriptor */
/* Create a socket descriptor */
listenfd = socket(hostaddresses->ai_family,
hostaddresses->ai_socktype, hostaddresses->ai_protocol);
if (listenfd == -1)
return -1;

## Slide 63: Echo Server: open_listenfd (setsockopt)
The socket can be given some attributes
Handy trick that allows us to rerun the server immediately after we kill it
  Otherwise we would have to wait about 15 seconds
  Eliminates “Address already in use” error from bind()
Strongly suggest you do this for all your servers to simplify debugging
/* Eliminates "Address already in use" error from bind(). */
if (setsockopt(listenfd, SOL_SOCKET, SO_REUSEADDR,
(const void *)&optval, sizeof optval) == -1) {
freeaddrinfo(hostaddresses);
return -1;
}

## Slide 64: Echo Server: open_listenfd (bind)
bind associates socket with socket address we just created
Again, important parameters come from getaddrinfo
int listenfd; /* listening socket */
...
/* listenfd will be an endpoint for all requests to port
on any IP address for this host */
if (bind(listenfd, hostaddresses->ai_addr, hostaddresses->ai_addrlen) == -1) {
freeaddrinfo(hostaddresses);
return -1;
}

## Slide 65: Echo Server: open_listenfd (listen)
listen indicates that this socket will accept connection (connect) requests from clients
We’re finally ready to enter main server loop that accepts and processes client connection requests
int listenfd; /* listening socket */
...
/* Make it a listening socket ready to accept connection requests */
if (listen(listenfd, LISTEN_MAX) == -1) {
freeaddrinfo(hostaddresses);
return -1;
}
freeaddrinfo(hostaddresses);
return listenfd;
}

## Slide 66: Echo Server: Main Loop
Server loops endlessly, waiting for connection requests, then reading input from client and echoing it back to client
main() {
/* create and configure the listening socket */
while(1) {
/* accept(): wait for a connection request */
/* echo(): read and echo input lines from client til EOF */
/* close(): close the connection */
}
}

## Slide 67: Echo Server: accept
accept() blocks waiting for connection request
accept returns connected descriptor (connfd) with same properties as listening descriptor (listenfd)
  Returns when connection between client and server is created and ready for I/O transfers
  All I/O with client will be done via connected socket
accept also fills in client’s IP address
int listenfd; /* listening descriptor */
int connfd; /* connected descriptor */
SA clientaddr;
socklen_t clientlen;
clientlen = sizeof(clientaddr);
connfd = accept(listenfd, (struct sockaddr *)&clientaddr, &clientlen);
SA is union big enough to hold IPv6 addresses

## Slide 68: Echo Server: Identifying Client
Server can determine domain name and IP address of client
char hostname[NI_MAXHOST], hostaddr[NI_MAXHOST];
…
error = getnameinfo((struct sockaddr*)&clientaddr, clientlen,
hostname, sizeof hostname, NULL, 0, 0);
if (error != 0) {
close(connfd);
continue;
}
getnameinfo((struct sockaddr*)&clientaddr, clientlen,
hostaddr, sizeof hostaddr, NULL, 0, NI_NUMERICHOST);
printf("server connected to %s (%s)\n", hostname, hostaddr);

## Slide 69: Echo Server: echo
Server uses Unix I/O to read and echo text lines until EOF (end-of-file) is encountered
  EOF notification caused by client calling close(clientfd)
  IMPORTANT: EOF is a condition, not a particular data byte
void echo(int connfd)
{
size_t n;
char buf[MAXLINE];
while((n = read(connfd, buf, sizeof buf)) > 0) {
printf("server received %d bytes\n", n);
write(connfd, buf, n);
}
}

## Slide 70: Testing Servers Using telnet
The telnet program is invaluable for testing servers that transmit ASCII strings over Internet connections
  Our simple echo server
  Web servers
  Mail servers
Usage:
  unix> telnet host portnumber
  Creates connection with server running on host and listening on port portnumber

## Slide 71: Testing Echo Server With telnet
mallet> ./echoserver 5000
server connected to bow.cs.hmc.edu (::ffff:134.173.42.60)
server received 5 bytes
server received 8 bytes
bow> telnet mallet 5000
Trying 134.173.42.59...
Connected to mallet-.
Escape character is '^]'.
123
123
456789
456789
^]
telnet> quit
Connection closed.
bow>

## Slide 72: Running Echo Client and Server
mallet> echoserver 5000
server connected to bow.cs.hmc.edu (::ffff:134.173.42.60)
server received 4 bytes
server connected to bow.cs.hmc.edu (::ffff:134.173.42.60)
server received 7 bytes
...
bow> echoclient mallet 5000
123
123
Bow> echoclient mallet 5000
456789
456789
bow>

## Slide 73: One More Important Function
Real servers often want to handle multiple clients
Problem: you have 3 clients. Only B wants service. You can’t really write serve(A); serve(B); serve(C) because B must wait for A to ask for service
Solution A: One thread or subprocess per client
Solution B: select system call
  Accepts set of file descriptors you’re interested in
  Tells you which ones have input waiting or are ready for output
  Then you can read from or write to only the active ones
  For more info, see man 2 select and Section 12.2 in text

## Slide 74: For More Information
W. Richard Stevens, “Unix Network Programming: Networking APIs: Sockets and XTI”, Volume 1, Second Edition, Prentice Hall, 1998
  THE network programming bible
Complete versions of the echo client and server (for IPv4 only) are developed in the text
  Fully general IPv4/IPv6 versions (from these slides) are available from class web page