## Slide 1: Machine-Level Programming II: Control Flow
Topics
  Condition codes
  Conditional branches
  Loops
  Switch statements
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: Condition Codes (Implicit Setting)
Single-bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (signed)
Implicitly set (as side effect) by arithmetic operations
  addq Src,Dest
  C analog: dest += src;
  CF set if carry out from most significant bit
    Detects unsigned overflow; also used for multiprecision arithmetic
  ZF set if src+dest == 0
  SF set if src+dest < 0
  OF set if two’s complement overflow
    (src > 0 && dest > 0 && src + dest < 0) \
    || (src < 0 && dest < 0 && src + dest >= 0)
Not set by leaq instruction

## Slide 3: Condition Codes (Explicit Setting)
Explicit setting by Compare instruction
  cmpq Src2,Src1
  cmpq b,a like computing a-b without setting destination
    Note reversed operand order!
  CF set if carry out from most significant bit
    Used for unsigned comparisons
    Also good for multi-precision arithmetic (at assembly level)
  ZF set if a == b
  SF set if (a-b) < 0
  OF set if two’s complement overflow
    (a > 0 && b < 0 && (a - b) < 0) || (a < 0 && b > 0 && (a - b) > 0)

## Slide 4: Condition Codes (Explicit Setting)
Explicit setting by Test instruction
  testq Src1,Src2
  Sets condition codes based on value of Src1 & Src2
    Intel thought it useful to have one operand be a mask
    Compiler usually sets Src1 and Src2 the same
  testq a,b like computing a&b without setting destination
  ZF set when a&b == 0
  SF set when a&b < 0
  CF, OF unaffected (not cleared!)
  Most common usage: testq %rax,%rax
    Sets ZF if %rax == 0, SF if %rax < 0
    I.e., “Is %rax zero, negative, or positive?”
  Usually immediately precedes jump instruction (covered in a few minutes)
This is the one that matters!

## Slide 5: Reading Condition Codes
SetX instructions
  Set single byte based on combinations of condition codes
  Remaining 7 bytes unaltered!

## Slide 6: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 7: Reading Condition Codes (Cont.)
SetX instructions
  Set single byte based on combinations of condition codes
One of 8 addressable byte registers
  Does not alter remaining 7 bytes!
  Typically use movzbl to finish job
    “l” instructions also set upper 32 bits (of 64) to 0
int gt (long x, long y)
{
return x > y;
}
cmpq %rsi, %rdi # Compare x:y
setg %al # Set when x>y
movzbl %al, %eax # Zero rest of %rax
ret
Note inverted ordering!
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 8: Jumping
jX instructions
  Jump to different part of code depending on condition codes

## Slide 9: Conditional-Branch Example (Old Style)
long absdiff (long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  wilkes> gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 10: Expressing with Goto Code
long absdiff(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
long absdiff_j(long x, long y)
{
long result;
int ntest = x <= y;
if (ntest) goto Else;
result = x-y;
return result;
Else:
result = y-x;
return result;
}
Sinful!

## Slide 11: General Conditional Expression Translation (Using Branches)
Carnegie Mellon
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 12: Using Conditional Moves
Carnegie Mellon
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are disruptive to instruction flow through pipelines
  Branches can kill performance
  Conditional moves do not require control transfer

## Slide 13: Conditional Move Example
Carnegie Mellon
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 14: Bad Cases for Conditional Move
Carnegie Mellon
Expensive Computations
val = test(x) ? hard_1(x) : hard_2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x *= 7 : x += 3;
Both values get computed
Only makes sense when computations are very simple

## Slide 15: “Do-While” Loop Example
Carnegie Mellon
C Code
long pcount_do(unsigned long x)
{
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto(unsigned long x)
{
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount” or “bitcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 16: “Do-While” Loop Compilation
Carnegie Mellon
Goto Version
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
long pcount_goto(unsigned long x)
{
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 17: General “Do-While” Translation
Carnegie Mellon
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 18: General “While” Translation #1
Carnegie Mellon
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 19: While Loop Example #1
Carnegie Mellon
C Code
long pcount_while(unsigned long x)
{
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump-to-Middle Version
long pcount_goto_jtm(unsigned long x)
{
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if (x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 20: General “While” Translation #2
Carnegie Mellon
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1 and above
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 21: While Loop Example #2
Carnegie Mellon
C Code
long pcount_while(unsigned long x)
{
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw(unsigned long x)
{
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if (x) goto loop;
done:
return result;
}
Compare to do-while version of function
Initial conditional guards entrance to loop

## Slide 22: “For” Loop Form
Carnegie Mellon
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(long)
long pcount_for(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit = (x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit = (x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 23: “For” Loop  While Loop
Carnegie Mellon
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 24: For-While Conversion
Carnegie Mellon
long pcount_for_while(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
while (i < WSIZE)
{
unsigned bit = (x >> i) & 0x1;
result += bit;
i++;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit = (x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 25: “For” Loop Do-While Conversion
Carnegie Mellon
C Code
Initial test can often be optimized away
long pcount_for(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit = (x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit = (x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 26: Switch Statement Example
Carnegie Mellon
Multiple case labels
  Here: 5 & 6
Fall-through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg(long x, long y, long z)
{
long w = 1;
switch (x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
break;
}
return w;
}

## Slide 27: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
goto *Jtab[x];
Switch (x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 28: Switch Statement Example
Carnegie Mellon
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch (x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default option?
Note that w is not initialized here!
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 29: Switch Statement Example
Carnegie Mellon
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
long switch_eg(long x, long y, long z)
{
long w = 1;
switch (x) {
. . .
}
return w;
}

## Slide 30: Assembly Setup Explanation
Carnegie Mellon
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 31: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Carnegie Mellon
Jump table
switch (x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 32: Code Blocks (x == 1)
Carnegie Mellon
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch (x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 33: Handling Fall-Through
Carnegie Mellon
long w = 1;
. . .
switch (x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 34: Code Blocks (x == 2, x == 3)
Carnegie Mellon
.L5: # Case 2
movq %rsi, %rax
cqto
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch (x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 35: Code Blocks (x == 5, x == 6, default)
Carnegie Mellon
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch (x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 36: Sparse Switches
What if jump table is too large?
  Compiler uses if-then-else structure
  Ternary tree gives O(log n) performance