## Slide 1: Machine-Dependent Optimization
CS 105 “Tour of the Black Holes of Computing”
Notes: Print separate notes to see where animations are.

## Slide 2: Machine-Dependent Optimization
Need to understand the architecture
Not portable
Not often needed
…but critically important when it is
Also helps in understanding modern machines

## Slide 3: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 4: Superscalar Processor
Definition: A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction-level parallelism that most programs have
Most modern CPUs are superscalar.
Intel: since Pentium (1993)

## Slide 5: What Is a Pipeline?
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Result
Bucket

## Slide 6: Pipelined Functional Units
  Divide computation into stages (e.g., one per partial product in multiplication)
  Pass partial computations from stage to stage
  Stage i can start new computation once values passed to i+1
  Here, we complete 3 multiplications in 7 cycles, even though each requires 3 cycles
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2
Notes: This slide animates the two dependency arrows, one at a time.

## Slide 7: Haswell CPU
  11 functional units in total
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15

## Slide 8: x86-64 Compilation of Combine4
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 9: Combine4 = Serial Computation (OP = *)
Computation (length=8)
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
Sequential dependence
  Performance: determined by latency of OP
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7

## Slide 10: Loop Unrolling (2x1)
Perform 2x more useful work per iteration
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x OP d[i]) OP d[i+1];
}
/* Finish any remaining elements */
for ( ; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}

## Slide 11: Effect of Loop Unrolling
Helps integer add by reducing number of overhead instructions
  (Almost) achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 12: Loop Unrolling with Reassociation (2x1a)
Can this change result of computation?
Yes, for multiply and floating point. Why?
void unroll2aa_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x OP (d[i] OP d[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
x = (x OP d[i]) OP d[i+1];
Compare to before
Notes: An animation pops up the “Yes…why?”

## Slide 13: Effect of Reassociation
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  Why is that? (next slide)
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 functional units for FP *
2 functional units for load
4 functional units for int +
2 functional units for load
Notes: Animation pops up the “nearly 2x” box on the left

## Slide 14: Reassociated Computation
What changed:
  Operations in the next iteration can be started early (no dependency)
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);

## Slide 15: Loop Unrolling with Separate Accumulators (2x2)
Different form of reassociation
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}

## Slide 16: Effect of Separate Accumulators
Int + makes use of two load units
2x speedup (over unroll2) for Int *, FP +, FP *
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Unroll 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 17: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/operation
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?

## Slide 18: Unrolling & Accumulating
Idea
  Can unroll to any degree L
  Can accumulate K results in parallel
  L must be multiple of K
Limitations
  Diminishing returns
    Cannot go beyond throughput limitations of execution units
  May run out of registers for accumulators
  Large overhead for short lengths
    Finish off iterations sequentially

## Slide 19: Unrolling & Accumulating: Double *
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Number of
Accumulators

## Slide 20: Unrolling & Accumulating: Int +
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 1.00
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Number of
Accumulators

## Slide 21: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, unoptimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best | 0.54 | 1.01 | 1.01 | 0.52
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 22: What About Branches?
Challenge
  Instruction Control Unit must work well ahead of Execution Unit to generate enough operations to keep EU busy
  When encounters conditional branch, cannot reliably determine where to continue fetching
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
Executing
How to continue?

## Slide 23: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates
Notes: The circle around “Prediction OK?” is animated.

## Slide 24: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
Branch Taken
Branch Not-Taken
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 25: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data
Predict Taken
Begin
Execution
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 26: Branch Prediction Through Loop
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Read invalid location
Executed
Fetched

## Slide 27: Branch Misprediction Invalidation
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Invalidate

## Slide 28: Branch Misprediction Recovery
Performance Cost
  Multiple clock cycles on modern processor
  Can be a major performance limiter
  Current CPUs (2019+) speculate 150 or more instructions ahead!
  One of the motivations for introducing conditional move (cmov) instructions
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401036: jmp 401040
. . .
401040: vmovsd %xmm0,(%r12)
i = 99
Definitely not taken
Reload
Pipeline

## Slide 29: Visualizing Operations
Operations
  Vertical position denotes time at which executed
    Cannot begin operation until operands available
  Height denotes latency
Operands
  Arcs shown only for operands that are passed within execution unit
cc.1
t.1
load
%ecx.1
incl
cmpl
jl
%rdx.0
%rdx.1
%ecx.0
imull
load (%rax,%rdx.0,4) t.1
imull t.1, %ecx.0  %ecx.1
incl %rdx.0  %rdx.1
cmpl %rsi, %rdx.1  cc.1
jl-taken cc.1
Time

## Slide 30: 3 Iterations of Combining Product
Unlimited-Resource Analysis
  Assume operation can start as soon as operands available
  Operations for multiple iterations overlap in time
Performance
  Limiting factor becomes latency of integer multiplier
  Gives CPE of 4.0
load
imull
load
load
imull
incl
incl
incl
cmpl
jll
cmpl
jll
cmpl
jll
%rax.0
%rax.1
%rax.2
%rax.3
%rcx.1
%rcx.2
%rcx.3
t.1
cc.1
t.2
t.3
cc.2
cc.3
Iteration 1
Iteration 2
Iteration 3
Cycle
i=0
i=1
i=2
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
imull
%rcx.0

## Slide 31: 4 Iterations of Combining Sum
Unlimited-Resource Analysis
Performance
  Can begin a new iteration on each clock cycle
  Should give CPE of 1.0
  Would require executing 4 integer operations in parallel
4 integer ops

## Slide 32: Combining Sum: Resource Constraints
  Suppose only have two integer functional units
  Some operations delayed even though operands available
  Set priority based on program order
Performance
  Sustains CPE of 2.0

## Slide 33: Visualizing Parallel Loop
  Two multiplies within loop no longer have data dependency
  Allows them to pipeline
load (%eax,%edx.0,4)  t.1a
imull t.1a, %ecx.0  %ecx.1
load 4(%eax,%edx.0,4)  t.1b
imull t.1b, %ebx.0  %ebx.1
iaddl $2,%edx.0  %edx.1
cmpl %esi, %edx.1  cc.1
jl-taken cc.1
Time
%edx.1
%ecx.0
%ebx.0
cc.1
t.1a
imull
%ecx.1
addl
cmpl
jl
%edx.0
imull
%ebx.1
t.1b
load
load

## Slide 34: Executing with Parallel Loop
Note: actually delayed 1 clock from what diagram shows. (Why?)
  Predicted Performance
    Can keep 4-cycle multiplier busy performing two simultaneous multiplications
    Gives CPE of 2.0
Notes: The note about the delayed addl is animated.

## Slide 35: Getting High Performance
Use a good compiler and appropriate flags
Don’t do anything stupid
  Watch out for hidden algorithmic inefficiencies
  Write compiler-friendly code
    Watch out for optimization blockers: procedure calls & memory references
  Look carefully at innermost loops (where most work is done)
Tune code for machine
  Exploit instruction-level parallelism
  Avoid unpredictable branches
  Make code cache-friendly
But DON’T OPTIMIZE UNTIL IT’S DEBUGGED!!!

## Slide 36: Meltdown and Spectre
Consider a few things
  Access to cached things is much faster than to non-cached ones
  Programs have access to detailed timing information
    Intel offers free-running cycle counter to all programs
    Thus, can tell whether something was cached
  OS has access to everything
    Carefully checks whether you have access before giving stuff to you
  CPU speculates many instructions ahead
    Must guess about branch directions
  User programs can either flush cache (clflush instruction) or clobber with loop

## Slide 37: Meltdown and Spectre
Trick OS into doing these steps:
  Check whether you have access to arbitrary location x (you don’t)
  Mispredict that branch
  Read location x and use its contents as follows:
    Extract bit b
    Multiply (shift left) bit b by, e.g., 1024
    Access array y[b*1024] that you do have access to
  Hardware will eventually discover mispredicted branch and cancel all those instructions
    …but cache now contains y[b*1024]
Scan cache to see whether y[0] or y[1024] is fast (i.e., in cache)
  You now know bit b of location x
  Lather, rinse, repeat until you know all bits of x
  Lather, rinse, repeat for all locations you want to read

## Slide 38: So What?
Can read arbitrary memory at about 2K bits/second
  No biggie on your laptop
  Huge issue in the cloud
    Physical machines often shared
    Supposedly isolated by virtual-machine technology
  Grab people’s encryption keys, passwords, all sorts of stuff
  Next stop: Putin
What to do?
  Disabling speculation kills performance
  Only certain branches are vulnerable
    Can do special things for those branches
    But hard to find (millions of lines in kernel)
  Compiler can try to identify risky branches
    But will be conservative  OS will slow down