## Slide 1: Exceptional Control Flow
Topics
  Exceptions
  Signals
  Shells
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: Join the ACM for Free!
World’s most important society for computer scientists
Publishes cutting-edge research
Many, many benefits
Just visit https://www.acm.org/studentjoin
It’s easy…and free!

## Slide 3: Dealing With I/O
Problem: I/O devices are slow
Solution 1: wait for I/O
  CPU stops executing instructions until device gives answer
Solution 2: polling
  Keep computing something else while I/O is happening
  Every so often, check to see whether I/O is done
Solution 3: interrupts
  Keep computing something else while I/O is happening
  Device eventually interrupts CPU to tell it I/O is done

## Slide 4: Dealing With Errors
How to handle bad mistakes like divide by 0?
Solution 1: ignore completely
Solution 2: set a flag and let program check
  Used for minor errors like integer overflow
  Nuisance to check after every important operation (e.g., division)
Solution 3: interrupts
  Let CPU notify program in a special way when bad things happen
  Mechanism can be (nearly) identical to that used for I/O

## Slide 5: Control Flow
Computers do only one thing
  From startup to shutdown, a CPU core simply reads and executes (interprets) a sequence of instructions, one at a time
  This sequence is the system’s physical control flow (or flow of control)
<startup>
inst1
inst2
inst3
…
instn
<shutdown>
Physical control flow
Time

## Slide 6: Altering the Control Flow
Up to now: two mechanisms for changing control flow:
  Jumps and branches—react to changes in program state
  Call and return using stack discipline—react to program state
Insufficient for a useful system
  Difficult for the CPU to react to other unexpected changes in system state
    Data arrives from a disk or a network adapter
    Instruction divides by zero
    User hits control-C at the keyboard
    System timer expires
System needs mechanisms for “exceptional control flow”

## Slide 7: Exceptional Control Flow
  Exists at all levels of a computer system
Low-Level Mechanism
  Exceptions
    Change in control flow in response to a system event (i.e., change in system state)
  Combination of hardware and OS software
Higher-Level Mechanisms
  Process context switch (done by OS software and hardware timer)
  Signals (done by OS software)
  Nonlocal jumps (throw/catch)—ignored in this course

## Slide 8: Exceptions
An exception is a transfer of control to OS kernel in response to some event (i.e., change in processor state)
Exceptions interrupt the normal control flow
User Process
OS
Exception
Exception processing
by exception handler
Return to current
Return to next
Abort & never return
Switch to a new process
event
current
next
Think of it as a hardware-initiated function call
Notes: “Hardware-initiated function call” is a popup.

## Slide 9: Exception Tables (Interrupt Vectors)
0
1
2
n-1
...
  Each type of event has a unique exception number k
  k = index into exception table (a.k.a., interrupt vector)
  Jump table entry k points to a function (exception handler).
  Handler k is called each time exception k occurs.
interrupt
vector
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers

## Slide 10: Asynchronous Exceptions (Interrupts)
Caused by events external to processor
  Indicated by putting voltage on the processor’s interrupt pin(s)
  Handler returns to “next” instruction.
Examples:
  Timer interrupt
    Every few milliseconds, triggered by external timer chip
    Used by kernel to take control back from user programs
  I/O interrupts
    Hitting control-C (or any key) at the keyboard
    Arrival of packet from network
    Finishing writing data to disk

## Slide 11: Synchronous Exceptions
Caused by events that occur as result of executing an instruction:
  Traps
    Intentional
    Examples: system calls, breakpoint traps, special instructions
    Returns control to “next” instruction
  Faults
    Unintentional but possibly recoverable
    Examples: page faults (recoverable), protection faults (unrecoverable)
    Either re-executes faulting (“current”) instruction or aborts
  Aborts
    Unintentional and unrecoverable
    Examples: memory error; machine fails ongoing self-tests
    Aborts current program or entire OS

## Slide 12: Examples of x86-64 Exceptions
Exception Number | Description | Exception Class
0 | Divide by zero | Fault
13 | General protection fault | Fault
14 | Page fault | Fault
18 | Machine check | Abort
32-255 | OS-defined exceptions | Interrupt or trap

## Slide 13: System Calls
Number | Name | Description
0 | read | Read file
1 | write | Write file
2 | open | Open file
3 | close | Close file
4 | stat | Get info about file
57 | fork | Create process
59 | execve | Execute a program
60 | _exit | Terminate process
62 | kill | Send signal to process
Each x86-64 system call has a unique ID number
Examples:

## Slide 14: System Call Example
User calls: open(filename, options)
Calls __open function, which invokes system call instruction syscall
00000000000e5d70 <__open>:
...
e5d79: b8 02 00 00 00 mov $0x2,%eax # open is syscall #2
e5d7e: 0f 05 syscall # Return value in %rax
e5d80: 48 3d 01 f0 ff ff cmp $0xfffffffffffff001,%rax
... ...
e5dfa: c3 retq
User code
Kernel code
Exception
Open file
Returns
syscall
cmp
%rax contains syscall number
Other arguments in %rdi, %rsi, %rdx, %r10 (weird!), %r8, %r9
Return value in %rax
Negative value is an error corresponding to negative errno
Notes: The control flow is animated in four popups.

## Slide 15: Fault Example: Page Fault
Memory Reference
  User writes to memory location
  That portion (page) of user’s memory is currently on disk
  Page handler must load page into physical memory
  Returns to faulting instruction
  Successful on second try
User Process
OS kernel
page fault
Create page and load into memory
return
event
movl
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10

## Slide 16: Fault Example: Invalid Memory
Memory Reference
  User writes to memory location
  Address is not valid
  Virtual memory system detects invalid address, causes fault
  OS sends SIGSEGV signal to user process (discussed in a few minutes)
  User process exits with “segmentation fault”
User Process
OS
page fault
Detect invalid address
event
movl
int a[1000];
main ()
{
a[5000] = 13;
}
80483b7: c7 05 60 e3 04 08 0d movl $0xd,0x804e360
Signal process

## Slide 17: ECF Exists at All Levels of a System
Exceptions
  Hardware and operating system kernel software
Concurrent processes
  Hardware timer and kernel software
Signals
  Kernel software
Non-local jumps (ignored in this class)
  Application code
  Unsupported in C (except for horrible setjmp hack)
  C++/Java throw/catch
  Python try/except

## Slide 18: Killing a Process
Problem: runaway process (e.g., unintentional infinite loop)
  Solution: kernel has superpowers, can kill it off
Problem: cleaning up after killing process
  Kernel can close open files, release memory, etc.
  Kernel can’t know whether to delete temporary files or send “bye-bye” message across network
Solution: let processes intercept attempt to kill
  Assumption is that they will clean up and exit gracefully
  No direct enforcement of that assumption!

## Slide 19: Signals
A signal is a small “message” that notifies a process that an event of some type has occurred in the system
  OS abstraction for exceptions and interrupts
  Sent from OS kernel (sometimes at request of another process) to a process
  Different signals are identified by small integer IDs
  Only information in a signal is its ID and fact of arrival
  Represented internally by one bit in kernel
ID | Name | Default Action | Corresponding Event
2 | SIGINT | Terminate | Interrupt from keyboard (ctl-c)
9 | SIGKILL | Terminate | Kill program (cannot override or ignore)
11 | SIGSEGV | Terminate & Dump | Segmentation violation
14 | SIGALRM | Terminate | Timer signal
17 | SIGCHLD | Ignore | Child stopped or terminated

## Slide 20: Signal Concepts: Sending
Kernel sends (delivers) a signal to a destination process by updating some state in the context of the destination process
Kernel sends a signal for one of the following reasons:
  Kernel has detected a system event such as divide by zero (SIGFPE) or termination of a child process (SIGCHLD)
  Another process has invoked the kill system call to explicitly request that the kernel send a signal to the destination process

## Slide 21: Signal Concepts: Receiving
A destination process receives a signal when it is forced by kernel to react in some way to delivery of the signal
Five possible ways to react:
  Ignore the signal (do nothing)
  Terminate the process
  Temporarily stop the process from running
  Continue a stopped process (let it run again)
  Catch the signal by executing a user-level function called a signal handler
    OS-initiated function call
    Akin to hardware exception handler being called in response to asynchronous interrupt
    Like interrupts, signal handler might or might not return
Notes: Don’t demo control-Z here.

## Slide 22: Signal Concepts: Pending & Blocked Signals
A signal is pending if it has been sent but not yet received
  There can be at most one pending signal of any particular type
  Important: signals are not queued
    If a process has pending signal of type k, then subsequent signals of type k for that process are discarded
Process can block receipt of certain signals
  Blocked signals can be delivered, but won’t be received until signal is unblocked
Pending signal is received at most once

## Slide 23: Signal Concepts: Bit Masks
Kernel maintains pending and blocked bit vectors in the context of each process.
  pending – represents set of pending signals
    Kernel sets bit k in pending whenever signal of type k is delivered
    Kernel clears bit k in pending whenever signal of type k is received
  blocked – represents set of blocked signals
    Can be set and cleared by application using sigprocmask
    Also referred to as the signal mask

## Slide 24: Receiving Signals
Suppose kernel is returning from an exception handler and is ready to pass control to process p
Process A
Process B
user code
kernel code
user code
kernel code
user code
context switch
context switch
Time
Important: All context switches are initiated by calling some exception handler, e.g. timer.

## Slide 25: Receiving Signals
Suppose kernel is returning from exception handler and is ready to pass control to process p
Kernel computes pnb = pending & ~blocked
  The set of pending nonblocked signals for process p
If (pnb == 0)
  Pass control to next instruction in logical flow for p
Else
  Choose lowest-numbered signal k in pnb, clear corresponding pending bit, and force process p to receive signal k
  Receipt of signal triggers some action by p
  Repeat for all nonzero k in pnb
  Pass control to next instruction in logical flow for p

## Slide 26: Process Groups
Every process belongs to exactly one process group
Fore-
ground
job
Back-
ground
job #1
Back-
ground
job #2
Shell
Child
Child
pid=10
pgid=10
Foreground
process group 20
Background
process group 32
Background
process group 40
pid=20
pgid=20
pid=32
pgid=32
pid=40
pgid=40
pid=21
pgid=20
pid=22
pgid=20
getpgrp() – Return process group of current process
setpgid() – Change process group of a process

## Slide 27: Sending Signals with kill
kill sends arbitrary signal to a process
Examples
  kill –KILL 24818
    Send SIGKILL to process 24818
    SIGKILL can’t be caught
  kill –9 24818
    Same, for lazy typists
linux> ./forks 16
linux> Child1: pid=24818
Child2: pid=24819
linux> ps
PID TTY TIME CMD
24788 pts/2 00:00:00 zsh
24818 pts/2 00:00:02 forks
24819 pts/2 00:00:02 forks
24820 pts/2 00:00:00 ps
linux> kill -9 24818
linux> ps
PID TTY TIME CMD
24788 pts/2 00:00:00 zsh
24819 pts/2 00:00:03 forks
24823 pts/2 00:00:00 ps
linux>

## Slide 28: Sending Signals with kill
kill sends arbitrary signal to a process or process group
Examples
  kill –KILL 24818
    Send SIGKILL to process 24818
  kill –9 –24817
    Send SIGKILL to every process in process group 24817
linux> ./forks 16
linux> Child1: pid=24818 pgrp=24817
Child2: pid=24819 pgrp=24817
linux> ps
PID TTY TIME CMD
24788 pts/2 00:00:00 zsh
24818 pts/2 00:00:02 forks
24819 pts/2 00:00:02 forks
24820 pts/2 00:00:00 ps
linux> kill -9 -24817
linux> ps
PID TTY TIME CMD
24788 pts/2 00:00:00 zsh
24823 pts/2 00:00:00 ps
linux>
Notes: Should we eliminate the process-group example completely?

## Slide 29: Sending Signals From the Keyboard
Typing ctrl-c (ctrl-z) sends a SIGINT (SIGTSTP) the “foreground” process
  SIGINT – default action is to terminate process
  SIGTSTP – default action is to stop (suspend) process
Fore-
ground
job
Back-
ground
job #1
Back-
ground
job #2
Shell
pid=10
pid=20
pid=32
pid=40
Notes: Unset LESS.
stty –tostop, then demonstrate control-Z. First do it with less on some file; then do it with gdb.
Show how less correctly restores screen & prompts bur gdb doesn’t.
Show how gdb remembers breakpoints, etc.
Stop gdb, start & stop less, show “jobs” and “jobs –l”, then “fg %n”.
Finally start up a background shell loop: “i=0; while sleep 1; do echo $i; (( i++ )); done &” and show how to kill –STOP %1, pick it up as foreground, and put it into the background again.

## Slide 30: Sending Signals From the Keyboard
Typing ctrl-c (ctrl-z) sends a SIGINT (SIGTSTP) to every job in the foreground process group.
  SIGINT – default action is to terminate each process
  SIGTSTP – default action is to stop (suspend) each process
Fore-
ground
job
Back-
ground
job #1
Back-
ground
job #2
Shell
Child
Child
pid=10
pgid=10
Foreground
process group 20
Background
process
group 32
Background
process
group 40
pid=20
pgid=20
pid=32
pgid=32
pid=40
pgid=40
pid=21
pgid=20
pid=22
pgid=20

## Slide 31: Example of ctrl-c and ctrl-z
bluefish> ./forks 17
Child: pid=28108
Parent: pid=28107
<types ctrl-z>
Suspended
bluefish> ps w
PID TTY STAT TIME COMMAND
27699 pts/8 Ss 0:00 -zsh
28107 pts/8 T 0:01 ./forks 17
28108 pts/8 T 0:01 ./forks 17
28109 pts/8 R+ 0:00 ps w
bluefish> fg
./forks 17
<types ctrl-c>
bluefish> ps w
PID TTY STAT TIME COMMAND
27699 pts/8 Ss 0:00 -zsh
28110 pts/8 R+ 0:00 ps w
STAT (process state) Legend:
First letter:
S: sleeping
T: stopped
R: running
Second letter:
s: session leader
+: foreground proc group
See “man ps” for more
details

## Slide 32: Example of ctrl-c and ctrl-z
bluefish> ./forks 17
Child: pid=28108 pgrp=28107
Parent: pid=28107 pgrp=28107
<types ctrl-z>
Suspended
bluefish> ps w
PID TTY STAT TIME COMMAND
27699 pts/8 Ss 0:00 -zsh
28107 pts/8 T 0:01 ./forks 17
28108 pts/8 T 0:01 ./forks 17
28109 pts/8 R+ 0:00 ps w
bluefish> fg
./forks 17
<types ctrl-c>
bluefish> ps w
PID TTY STAT TIME COMMAND
27699 pts/8 Ss 0:00 -zsh
28110 pts/8 R+ 0:00 ps w
STAT (process state) Legend:
First letter:
S: sleeping
T: stopped
R: running
Second letter:
s: session leader
+: foreground proc group
See “man ps” for more
details

## Slide 33: Sending Signals with kill
void fork12()
{
pid_t pid[N];
int i, child_status;
for (i = 0; i < N; i++)
if ((pid[i] = fork()) == 0)
while(1); /* Child infinite loop (bad style!) */
/* Parent terminates the child processes */
for (i = 0; i < N; i++) {
printf("Killing process %d\n", pid[i]);
kill(pid[i], SIGINT);
}
/* Parent reaps terminated children */
for (i = 0; i < N; i++) {
pid_t wpid = wait(&child_status);
if (WIFEXITED(child_status))
printf("Child %d terminated with exit status %d\n",
wpid, WEXITSTATUS(child_status));
else
printf("Child %d terminated abnormally\n", wpid);
}
}
Notes: The circling of KILL is a popup.

## Slide 34: Default Actions
Each signal type has predefined default action, which is one of:
  Process terminates
  Process terminates and dumps “core” (memory) to a file
    Nowadays dump is suppressed in normal operation
    Was intended for debugging; now usually simpler to rerun under gdb
  Process stops until restarted by a SIGCONT signal
  Process ignores the signal

## Slide 35: Installing Signal Handlers
The obsolete signal function modifies the default action associated with receipt of signal signum:
  handler_t *signal(int signum, handler_t *handler)
Different values for handler:
  SIG_IGN: ignore signals of type signum
  SIG_DFL: revert to default action on receipt of signals of type signum
  Otherwise, handler is address of a signal handler
    Referred to as “installing” the handler
    Called when process receives signal of type signum
    Executing handler is called “catching” or “handling” the signal
    When handler returns, control passes back to instruction in control flow of process that was interrupted by receipt of the signal

## Slide 36: Installing Signal Handlers
The sigaction function modifies the default action associated with receipt of signal signum:
  int *sigaction(int signum, const struct sigaction *act, struct sigaction *oldact)
act is a struct with several useful components:
  sa_mask identifies signals to block while handler runs
  sa_flags controls certain options
  sa_handler is special value or address of a signal handler
    Referred to as “installing” the handler
    Called when process receives signal of type signum
    Executing handler is called “catching” or “handling” the signal
    When handler returns, control passes back to instruction in control flow of process that was interrupted by receipt of the signal
  Special values for sa_handler: SIG_IGN (ignore signal) or SIG_DFL (return to default)

## Slide 37: Obsolete Signal-Handling Example
int main()
{
sigset_t blocks;
sigemptyset(&blocks);
sigaddset(&blocks, SIGINT);
/* Install the SIGINT handler */
sigprocmask(SIG_BLOCK, &blocks, NULL);
if (signal(SIGINT, SIG_IGN) != SIG_IGN)
signal(SIGINT, sigint_handler);
sigprocmask(SIG_UNBLOCK, &blocks, NULL);
/* Wait for the receipt of a signal */
pause();
return 0;
}
sigint.c
/* SIGINT handler */
void sigint_handler(int sig
{
printf("So you think you can stop the bomb with ctrl-c, do you?\n");
sleep(2);
printf("Well...");
fflush(stdout);
sleep(1);
printf("OK. :-)\n");
exit(0);
}

## Slide 38: Signal-Handling Example
int main()
{
struct sigaction action, oldaction;
action.sa_flags = 0;
action.sa_handler = sigint_handler;
sigemptyset(&action.sa_mask);
sigaddset(&action.sa_mask, SIGINT);
/* Install the SIGINT handler */
sigprocmask(SIG_BLOCK, &action.sa_mask,
NULL);
Sigaction(SIGINT, &action, &oldaction);
if (oldaction.sa_handler == SIG_IGN)
sigaction(SIGINT, &oldaction, NULL);
sigprocmask(SIG_UNBLOCK, &action.sa_mask,
NULL);
/* Wait for the receipt of a signal */
pause();
return 0;
}
sigint.c
#include <signal.h>
/* SIGINT handler */
void sigint_handler(int sig)
{
printf("So you think you can stop the bomb with ctrl-c, do you?\n");
sleep(2);
printf("Well...");
fflush(stdout);
sleep(1);
printf("OK. :-)\n");
exit(0);
}
Notes: The sleep(2) system call is also built on signals (SIGALRM).

## Slide 39: Signals Handlers as Concurrent Flows
A signal handler is a separate logical flow (not process) that runs concurrently with the main program
Process A
while (1)
;
Process A
handler(){
…
}
Process B
Time

## Slide 40: Another View of Signal Handlers as Concurrent Flows
Signal delivered
to process A
Signal received
by process A
Process A
Process B
user code (main)
kernel code
user code (main)
kernel code
user code (handler)
context switch
context switch
kernel code
user code (main)
Icurr
Inext

## Slide 41: Nested Signal Handlers
Handlers can be interrupted by other handlers
(2) Control passes to handler S
Main program
(5) Handler T
returns to handler S
Icurr
Inext
(1) Program catches signal s
Handler S
Handler T
(3) Program catches signal t
(4) Control passes to handler T
(6) Handler S
returns to main program
(7) Main program resumes

## Slide 42: Blocking and Unblocking Signals
Implicit blocking mechanism
  Kernel blocks any pending signals of type currently being handled.
  E.g., A SIGINT handler can’t be interrupted by another SIGINT
Explicit blocking and unblocking mechanism
  sigprocmask function
Supporting functions
  sigemptyset – Create empty set
  sigfillset – Add every signal number to set
  sigaddset – Add signal number to set
  sigdelset – Delete signal number from set

## Slide 43: Temporarily Blocking Signals
sigset_t mask, prev_mask;
Sigemptyset(&mask);
Sigaddset(&mask, SIGINT);
/* Block SIGINT and save previous blocked set */
Sigprocmask(SIG_BLOCK, &mask, &prev_mask);
/* Code region that will not be interrupted by SIGINT */
/* Restore previous blocked set, unblocking SIGINT */
Sigprocmask(SIG_SETMASK, &prev_mask, NULL);
…

## Slide 44: Guidelines for Writing Safe Handlers
G1: Keep your handlers as simple as possible
  e.g., Set a global flag and return
G2: Call only async-signal-safe functions in your handlers
  printf, sprintf, malloc, and exit are not safe! (But _exit is)
  (We cheated in the example because we know details of implementation…)
G3: Save and restore errno on entry and exit
  So that other handlers don’t overwrite your value of errno
G4: Protect accesses to shared data structures by temporarily blocking all signals.
  To prevent possible corruption
G5: Declare global variables as volatile
  To prevent compiler from storing them in a register
G6: Declare global flags as volatile sig_atomic_t
  flag: variable that is only read or only written (e.g. flag = 1, not flag++)
  Flag declared this way does not need to be protected like other globals
Notes: Each bullet is a popup.

## Slide 45: Async-Signal-Safety
Function is async-signal-safe if either reentrant (e.g., all variables stored on stack frame, CS:APP3e 12.7.2) or non-interruptible by signals.
Posix guarantees 117 functions to be async-signal-safe
  Source: “man 7 signal-safety”
  Popular functions on the list:
    _exit, write, wait, waitpid, sleep, kill
  Popular functions that are not on the list:
    printf, sprintf, malloc, exit
    Unfortunate fact: write is the only async-signal-safe output function
Notes: The Posix guarantees are animated.

## Slide 46: Shell Programs
A shell is an application program that runs programs on behalf of the user
  sh – Original Unix Bourne shell
  csh – BSD Unix C shell, tcsh – Enhanced C shell (both deprecated)
  bash – “Bourne-Again” shell
  zsh – “Z” shell
int main()
{
char cmdline[MAXLINE];
while (1) {
/* read */
printf("> ");
Fgets(cmdline, MAXLINE, stdin);
if (feof(stdin))
exit(0);
/* evaluate */
eval(cmdline);
}
}
Execution is a sequence of read/evaluate steps

## Slide 47: Simple Shell eval Function
void eval(char *cmdline)
{
char *argv[MAXARGS]; /* argv for execvp() */
int bg; /* should the job run in bg or fg? */
pid_t pid; /* process id */
bg = parseline(cmdline, argv);
if (!builtin_command(argv)) {
if ((pid = Fork()) == 0) { /* child runs user job */
execvp(argv[0], argv);
fprintf(stderr, "%s: Command not found.\n", argv[0]);
exit(1);
}
if (!bg) { /* parent waits for fg job to terminate */
int status;
if (waitpid(pid, &status, 0) == -1)
unix_error("waitfg: waitpid error");
}
else /* otherwise, don’t wait for bg job */
printf("%d %s", pid, cmdline);
}
}

## Slide 48: Problem with Simple Shell Example
Shell correctly waits for and reaps foreground jobs
But what about background jobs?
  Will become zombies when they terminate
  Will never be reaped because shell (typically) will not terminate
  Eventually you hit process limit and can’t do any work
ECF to the rescue:
  SIGCHLD will notify us of child termination
  Ignored by default, so must explicitly catch
  But signal handler must be carefully written (see next two slides)

## Slide 49: Signal Handler Funkiness
Pending signals are not queued
  For each signal type, just have single bit indicating whether or not signal is pending
  Even if multiple processes have sent this signal!
int ccount = 0;
void child_handler(int sig)
{
int child_status;
pid_t pid = wait(&child_status);
ccount--;
printf("Received signal %d from process %d\n",
sig, pid);
}
void fork14()
{
pid_t pid[N];
int i, child_status;
ccount = N;
Signal(SIGCHLD, child_handler); /* Old style */
for (i = 0; i < N; i++)
if ((pid[i] = fork()) == 0) {
/* Child: Exit */
exit(0);
}
while (ccount > 0)
pause(); /* Suspend until signal occurs */
}

## Slide 50: Living With Nonqueuing Signals
Must check for all terminated jobs
  Typically loop with waitpid
void child_handler2(int sig)
{
int child_status;
pid_t pid;
while ((pid = waitpid(-1, &child_status, WNOHANG)) != -1) {
ccount--;
printf("Received signal %d from process %d\n",
sig, pid);
}
}
void fork15()
{
. . .
signal(SIGCHLD, child_handler2);
. . .
}

## Slide 51: Summary
Signals provide process-level exception handling
  Can generate from user programs
  Can define effect by declaring signal handler
Some caveats
  Very high overhead
    >10,000 clock cycles
    Only use for exceptional conditions
  Don’t have queues
    Just one bit for each pending signal type