## Slide 1: Virtual Memory: Systems
Topics
  Simple memory system example
  Case study: Core i7
  Linux memory management
  Memory mapping
CS 105 “Tour of the Black Holes of Computing!”
Notes: Print separate screen notes for this one. The slides are different.

## Slide 2: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  VPN: Virtual page number
  VPO: Virtual page offset
  TLBI: TLB index
  TLBT: TLB tag
Components of the physical address (PA)
  PPN: Physical page number
  PPO: Physical page offset (same as VPO)
  CT: Cache tag
  CI: Cache index
  CO: Byte offset within cache line

## Slide 3: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 4: 1. Simple Memory System TLB
16 entries
4-way set-associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Notes: Mention that they’ll be referring back to this slide and the next two.

## Slide 5: 2. Simple Memory System Page Table
Only shows first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN

## Slide 6: 3. Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 7: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
3
0x03
Notes: Four animations bring up the answers

## Slide 8: 1. Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Notes: Three animations circle the tag, valid bit, and PPN

## Slide 9: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0
0
0
1
1
0
0x0F
3
0x03
Y
N
0x0D
0
0x5
0x0D
1
0
1
0
1
0
Notes: Eight animations bring up answers

## Slide 10: 3. Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
0
11
0
10
1
9
1
8
0
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
Notes: Four animations circle the tag, the valid bit, the byte offset, and the data byte

## Slide 11: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0
0
0
1
1
0
0x0F
3
0x03
Y
N
0x0D
0
0x5
0x0D
Y
0x36
1
0
1
0
1
0
Notes: Two animations bring up the final answer

## Slide 12: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT

## Slide 13: Address Translation Example #2
Virtual Address: 0x0020
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
Notes: Three animations bring up answers

## Slide 14: 1. Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Notes: Two animations circle the tag and the valid bit

## Slide 15: Address Translation Example #2
Virtual Address: 0x0020
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
Notes: One animation brings up the TLB (non-)hit

## Slide 16: 2. Simple Memory System Page Table
Only shows first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
Notes: Two animations bring up the valid bit and the PPN

## Slide 17: Address Translation Example #2
Virtual Address: 0x0020
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
Notes: Six animations bring up the answers through CI/CT

## Slide 18: 3. Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
Notes: Two animations circle the valid bit and cache tag

## Slide 19: Address Translation Example #2
Virtual Address: 0x0020
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem
Notes: Two animations give the final result

## Slide 20: Address Translation Example #2
Virtual Address: 0x0020
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT

## Slide 21: Address Translation Example #3
Virtual Address: 0x0316
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
1
1
0
1
0
0
0
1
1
0
0
0
0
0x0C
0
0x03
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
Notes: Three animations bring up answers

## Slide 22: 1. Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Notes: Two animations circle the tag and the valid bit

## Slide 23: Address Translation Example #3
Virtual Address: 0x0316
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
1
1
0
1
0
0
0
1
1
0
0
0
0
0x0C
0
0x03
N
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
Notes: One animation says TLB miss

## Slide 24: 2. Simple Memory System Page Table
Only shows first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
Notes: One animation circles the invalid page table entry

## Slide 25: Address Translation Example #3
Virtual Address: 0x0316
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
1
1
0
1
0
0
0
1
1
0
0
0
0
0x0C
0
0x03
N
Y
Disk
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
Notes: Two animations answer page fault and the on-disk PPN

## Slide 26: Address Translation Example #3
Virtual Address: 0x0316
  VPN ____ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT

## Slide 27: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge
Notes: We looked at this same diagram (more or less) last week.

## Slide 28: End-to-End Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE
Notes: VA is 64 bits but only 48 bits are sent to the memory system.

## Slide 29: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table. Significant fields:
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 1 PTEs only).
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
XD: Disable or enable instruction fetches from all pages reachable from this PTE.
CD: Disable caching on this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63
Notes: The G bit says that this mapping is global to all processes; clear means it’s process-private. The Linux kernel sets G on its pages but of course sets U/S to supervisor.

## Slide 30: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page. Significant fields:
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
G: Global (used by many processes; don’t flush from TLB unnecessarily)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
XD: Disable or enable instruction fetches from this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 31: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 32: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI are identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available next
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
40
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check
Notes: Note that this is a bottom-to-top diagram (really needs to be redrawn…)

## Slide 33: Virtual Address Space of a Linux Process
Kernel code and data
Memory-mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%rsp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x00400000
Different for each process

## Slide 34: Linux Organizes VM As Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
vm_flags
vm_flags
vm_flags
Stack

## Slide 35: Linux Page-Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a nonexistent page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)
Stack
Notes: Six animations bring up read 1, segfault, write 2, segfault, read 3, normal page fault

## Slide 36: Memory Mapping
VM areas initialized by associating them with disk objects.
  Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 37: Sharing Revisited: Shared Objects
Process 1 maps the shared object
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 38: Sharing Revisited: Shared Objects
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the shared object
Notice how the virtual addresses can be different.

## Slide 39: Sharing Revisited: Private Copy-on-Write (COW) Objects
Two processes mapping a private copy-on-write (COW) object.
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 40: Sharing Revisited: Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault
Handler creates new R/W page
Instruction restarts upon handler return
Copying deferred as long as possible!
  With luck, never
  General principle called “lazy evaluation”
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 41: The fork Function Revisited
VM and memory mapping explain how fork provides private address space for each process
To create virtual address for new process
  Create exact copies of current kernel structures and page tables.
  Flag each page in both processes as read-only, private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new pages using COW mechanism.

## Slide 42: The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
  Programs and initialized data backed by object files
  .bss and stack backed by anonymous files
Set PC to entry point in .text
  Linux will fault in code and data pages as needed
Memory mapped region
for shared libraries
Runtime heap (via malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
Private, demand-zero
libc.so
.data
.text
Shared, file-backed
Private, demand-zero
Private, demand-zero
Private, file-backed
a.out
.data
.text

## Slide 43: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Maps len bytes starting at offset offset of the file specified by file descriptor fd, preferably at address start
  start: may be NULL for “pick an address”
  prot: PROT_READ, PROT_WRITE, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Returns pointer to start of mapped area (might not be start)

## Slide 44: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 45: Example: Using mmap to Implement fgrep
/* mmapcopy driver */
int main(int argc, char **argv)
{
struct stat stat;
int fd;
/* Check for required cmd line arg */
if (argc != 3) {
fprintf(stderr, "usage: %s <pattern> <filename>\n",
argv[0]);
exit(0);
}
/* Open file and find size */
fd = Open(argv[2], O_RDONLY, 0);
Fstat(fd, &stat);
mmapfgrep(fd, argv[1], stat.st_size);
exit(0);
}
Searching a file with no read calls
But it must fit In virtual memory space (256 TB on Core i7)
#include "csapp.h"
void mmapfgrep(int fd, char *pattern, int size)
{
/* Ptr to memory mapped area */
char *bufp;
int i, patlen;
bufp = Mmap(NULL, size,
PROT_READ,
MAP_PRIVATE,
fd, 0);
patlen = strlen(pattern);
for (i = 0; i < size – patlen; i++) {
if (strcmp(bufp[i], pattern) == 0) {
/* Print line containing pattern */
}
}
return;
}
mmapfgrep.c
mmapfgrep.c