## Slide 1: File Systems
Topics
  Design criteria
  Berkeley Fast File System
  Effect of file systems on programs
CS 105 “Tour of the Black Holes of Computing”

## Slide 2: File Systems: Disk Organization
A disk is a sequence of 4096-byte sectors or blocks
  Can only read or write in block-sized units
First comes boot block and partition table
Partition table divides the rest of disk into partitions
  May appear to operating system as logical “disks”
  Useful for multiple OSes, etc.
  Otherwise bad idea; hangover from earlier days
File system: partition structured to hold files (of data)
  May aggregate blocks into segments or clusters
    Typical size: 8K–128M bytes
    Increases efficiency by reducing overhead
    But may waste space if files are small (and most files are small—by the millions)

## Slide 3: Disk Geometry
Disks consist of stacked platters, each with two surfaces
Each surface consists of concentric rings called tracks
Each track consists of sectors separated by gaps
spindle
surface
tracks
track k
sectors
gaps

## Slide 4: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder (this view is outdated but useful)
surface 0
surface 1
surface 2
surface 3
surface 4
surface 5
cylinder k
spindle
platter 0
platter 1
platter 2

## Slide 5: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
spindle
By moving radially, arm can seek, or position read/write head over any track
Read/write head
is attached to end
of the arm and flies over
disk surface on
thin cushion of air
spindle
Notes: Animation moves the head back and forth

## Slide 6: Disk Operation (Multi-Platter View)

## Slide 7: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector
  Typical Tavg seek = 9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under read/write head
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min

## Slide 8: Disk Access Time Example
Given:
  Rotational rate = 7200 RPM (typical desktop or server; laptops usually 5400)
  Average seek time = 9 ms (given by manufacturer)
  Avg # sectors/track = 400
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency
  First byte in a sector is the most expensive; the rest are “free”
  SRAM access time is about 4 ns/64 bits, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM, and
    2,500 times slower than DRAM

## Slide 9: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  Set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller (partly on motherboard, mostly in disk itself)
  Converts requests for logical blocks into (surface,track,sector) triples
Allows controller to set aside spare blocks & cylinders
  Automatically substituted for “bad” blocks
  Accounts for (some of) the difference between “formatted capacity” and “maximum capacity”

## Slide 10: Block Access
Disks can only read and write complete sectors (blocks)
  Not possible to work with individual bytes (or words or…)
  File system data structures are usually smaller than a block
  OS must pack structures together to create a block
Disk treats all data as uninterpreted bytes (one block at a time)
  OS must read block into (byte) buffer and then convert into meaningful data structures
  Conversion process is called serialization (for write) and deserialization
  OS carefully arranges for this to happen by simple C type-casting
Requirement of working in units of blocks affects file system design
  Writing (e.g.) a new file name inherently rewrites other data in same block
  But block writes are atomic  can update multiple values at once

## Slide 11: Aside: Solid-State Disks
They aren’t disks! But for backwards compatibility they pretend to be…
SSDs are divided into erase blocks made up of pages
  Typical page: 4K-8K bytes
  Typical erase block: 128K-512K
Can only change bits from 1 to 0 when writing
  Erase sets entire block to all 1’s
  Erase is slow
  Can only erase 104 to 106 times
  Must pre-plan erases and manage wear-out
Net result:
  Reads are fast (and almost truly random-access)
  Writes are 100X slower (and have weird side effects)
  Flash Translation Layer (FTL) tries to hide all this from OS
Notes: Some newer SSDs allow the OS to bypass the FTL and do the FTL work itself; this can allow the OS to optimize better.

## Slide 12: Design Problems
So, disks have mechanical delays (and SSDs have their own strange behaviors)
Fundamental problem in file-system design: how to hide (or at least minimize) these delays?
Side problems also critical:
  Making things reliable (in face of software and hardware failures)
    People frown on losing data
  Organizing data (e.g., in directories or databases)
    Not finding stuff is almost as bad as losing it
  Enforcing security
    System should only share what you want to share
Notes: “The file system is the only part of your computer that’s not allowed to fail” – Greg Ganger

## Slide 13: Important File Systems
FAT: old Windows and MSDOS standard
NTFS: Windows current standard
FFS: Unix standard since 80’s
AFS: distributed system developed at CMU
LFS: Berkeley redesign for high performance
ZFS: redesigned Unix system, recently released by Sun
ISO 9660: CD-ROM standard
EXT2/EXT3/EXT4: Linux standards, variants of FFS
BtrFS: new Linux kid on the block
(Other OS’s have own file organization: VMS, MVS, )
Notes: “New kid” means less than 20 years old; file systems change slowly because new ones risk losing data.

## Slide 14: Typical Similarities Among File Systems
A (secondary) boot record
A top-level directory
Support for hierarchical directories
Management of free and used space
Metadata about files (e.g., name, size, date & time last modified)
Protection and security

## Slide 15: Typical Differences Between File Systems
Naming conventions: case, length, special symbols
File size and placement
Speed
Error recovery
Metadata details
Support for “special” files and pseudo-files
Snapshot support

## Slide 16: Case Study: Berkeley Fast File System (FFS)
First public Unix (Unix V7) introduced many important concepts in Unix File System (UFS)
  I-nodes
  Indirect blocks
  Unix directory structure and permissions system
UFS was simple, elegant, and slow
Berkeley initiated project to solve the slowness
Many modern file systems are direct or indirect descendants of FFS
  In particular, EXT2 through EXT4

## Slide 17: FFS Headers
Boot block: first few sectors
  Typically all of cylinder 0 is reserved for boot blocks, partition tables, etc.
Superblock: file system parameters, including
  Size of partition or drive (note that this is dangerously redundant)
  Location of root directory
  Block size
Cylinder groups, each including
  Data blocks
  List of inodes
  Bitmap of used blocks and fragments in the group
  Replica of superblock (not always at start of group)

## Slide 18: FFS File Tracking
Directory: file containing variable-length records
  File name
  Inode number
Inode: holds metadata for one file
  Fixed size
  Located by number, using information from superblock (basically, array)
  Integral number of inodes in a block
  Includes
    Owner and group
    File type (regular, directory, pipe, symbolic link, …)
    Access permissions
    Time of last i-node change, last modification, last access
    Number of links (reference count)
    Size of file (for directories and regular files)
    Pointers to data blocks
  Except for pointers, precisely what’s in stat data structure

## Slide 19: FFS Inodes
Inode has 15 pointers to data blocks
  12 point directly to data blocks
  13th points to an indirect block, containing pointers to data blocks
  14th points to a double indirect block (has pointers to single indirect blocks)
  15th points to a triple indirect block
With 4K blocks and 4-byte pointers, the triple indirect block can address 4 terabytes (242 bytes) in one file
Data blocks might not be contiguous on disk
But OS tries to cluster related items in cylinder group:
  Directory entries
  Corresponding inodes
  Their data blocks
Notes: With 4K blocks and 8-byte pointers, triple indirect can address only 0.5 TB. But 8K and 8-byte gives 8 TB. Some new FSes have quad indirect blocks.

## Slide 20: FFS Free-Space Management
Free space managed by bitmaps
  One bit per block
  Makes it easy to find groups of contiguous blocks
Each cylinder group has own bitmap
  Can find blocks that are physically nearby
  Prevents long scans on full disks
Prefer to allocate block in cylinder group of last previous block
  If can’t, pick group that has most available space
  Heuristic tries to maximize number of blocks close to each other

## Slide 21: FFS Fragmentation
Blocks are typically 4K or 8K
  Sector size was only 512
  Amortizes overhead of reading or writing block
  On average, wastes 1/2 block (total) per file
FFS divides blocks into 4-16 fragments
  Free space bitmap manages fragments
  Small files, or tails of files, are placed in fragments
  This turned out to be bad idea
    Complicates OS code
    Didn’t foresee how big disks would get
Linux EXT2/3/4 uses smaller block size (typically 4K) instead of fragments

## Slide 22: File Systems and Data Structures
Almost every data structure you can think of is present in FFS:
  Arrays (of blocks and i-nodes)
  Variable-length records (in directories)
  Heterogeneous records
  Indirection (directories and inodes)
  Reference counting
  Lists (inodes in different cylinder groups)
  Trees (indirect data blocks)
  Bitmaps (free space management)
  Caching

## Slide 23: Effect of File Systems on Programs
Software can take advantage of FFS design
  Small files are cheap: spread data across many files
  Directories are cheap: use as key/value database where file name is the key
    But only if value (data) is fairly large, since size is increments of 4K bytes
  Large files well supported: don’t worry about file-size limits
  Random access adds little overhead: OK to store database inside large file
    But don’t forget you’re still paying for disk latencies and indirect blocks!
FFS design also suggests optimizations
  Put related files in single directory
  Keep directories relatively small
  Recognize that single large file will eat much remaining free space in cylinder group
    Create small files before large ones

## Slide 24: The Crash Problem
File system data structures are interrelated
  Free map implies which blocks do/don’t have data
  Inodes and indirect blocks list data blocks
  Directories imply which inodes are allocated or free
  All live in different places on disk
  Which to update first?
Crash in between updates means inconsistencies
  Block listed as free but really allocated will get reused and clobbered
  Block listed as allocated but really free means space leak
  Allocated inode without directory listing means lost file

## Slide 25: File System Checking
Traditional solution: verify all structures after a crash
  Look through files to find out what blocks are in use
  Look through directories to find used inodes
  Fix all inconsistencies, put lost files in “lost+found”
Problem: takes a long time
  Following directory tree means random access
  Following indirect blocks is also random
  Random == slow
  Huge modern disks  hours or even days to verify
    System can’t be used during check

## Slide 26: Journaled File Systems
One (not only) solution to checking problem
  Before making change, write intentions to journal
    “I plan to allocate block 42, give it to inode 47, put that in directory entry foo”
    Journal writes are carefully kept in single block  atomic
  After making changes, append “I’m done” to journal
Post-crash journal recovery
  Journal is sequential and fairly small  fast scanning
  Search for last “I’m done” record
  Re-apply any changes past that point
    Atomicity means they can’t be partial
    All changes are arranged to be idempotent
  Write an “I’m done” in case of another crash

## Slide 27: Summary: Goals of Unix File Systems
Simple data model
  Hierarchical directory tree
  Uninterpreted (by OS) sequences of bytes
Multiuser protection model
High speed
  Reduce disk latencies by careful layout
  Hide latencies with caching
  Amortize overhead with large transfers
  Sometimes trade off reliability for speed

## Slide 28: Making Disks Bigger and Faster
Problem: Disks have limited size, but want to store lots of data
Problem: Want to be able to read all that data really fast
Solution: Just attach more than one disk to the computer
  Amount of data scales with number of disks
  Can read from multiple drives simultaneously, so bandwidth roughly scales too
Problem: Disks fail
  Failure equates to lost data
  For maximum bandwidth on one file, need to spread it across disks
    Failure of one drive means parts of many files are lost

## Slide 29: RAID
Insight: Disks fail completely (e.g., motor dies or electronics emit smoke)
Idea: Keep a parity drive
  Stores XOR of data on all other drives
  If parity drive fails, obviously easy to reconstruct
  Less obvious: if drive N fails, its contents are just XOR of all other drives with the the parity drive
  Allows any failed drive to be reconstructed!
Making it work is a bit trickier
  Read performance is good (if files spread across drives)
  Write performance drops (must write true data and update parity drive)
  Cost goes up (extra drive)
  Reconstruction is slow
  Can’t handle multiple failures